## Slide 1
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 16
General Purpose Timer and PWM
Exercises ANS
Z. Gu
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Summary of Equations
Timer clock frequency vs. CPU Clock Frequency
Timer frequency with up-counting or down-counting mode:
PWM duty cycle for Mode 1 (Low-True):
Timer frequency with center-aligned counting mode:
PWM duty cycle for Mode 2 (High-True):
Review

## Slide 3: Calculating the ARR
Suppose a 16-bit timer has the following settings
    CPU clock frequency is 4 MHz.
    Prescaler PSC = 39
    Counting direction: center-aligned counting
    Desired timer frequency = 100 Hz
Calculate the ARR.

## Slide 4: Calculating the ARR ANS
Suppose a 16-bit timer has the following settings
    CPU clock frequency is 4 MHz.
    Prescaler PSC = 39
    Counting direction: center-aligned counting
    Desired timer frequency = 100 Hz
Calculate the ARR.
= 0.1 MHz

## Slide 5: Clock Frequency and Timer Frequency
Suppose all registers are 16 bits. CPU clock frequency is 400 MHz.
What is the maximum and minimum Clock Frequency, and Timer Frequency, assuming up-counting mode?

## Slide 6: Clock Frequency and Timer Frequency ANS
Suppose all registers are 16 bits. CPU clock frequency is 400 MHz.
What is the maximum and minimum Clock Frequency, and Timer Frequency, assuming up-counting mode?
PSC, ARR are both in the range [0, 216-1=65535].
(A realistic Timer Frequency should not be higher than 1 KHz. Hardware can generate high frequency timer interrupts, but software latency and Interrupt Service Routine (ISR) overhead are the real constraints.)
=
Notes: Since each timer interrupt triggers an ISR software execution, timer interrupt frequency should not be higher than 1KHz.

## Slide 7: PWM duty cycle
Suppose a 16-bit timer has the following settings
    CPU Clock frequency is 16 MHz.
    Prescaler PSC = 159
    ARR = 1999
    CCR = 499
    Counting direction: up-counting
    Output is set as PWM Mode 2 (High True).
Calculate the timer frequency and PWM duty cycle.

## Slide 8: PWM duty cycle ANS
Suppose a 16-bit timer has the following setting
    CPU clock frequency is 16 MHz.
    Prescaler PSC = 159
    ARR = 1999
    CCR = 499
    Counting direction: up-counting
    Output is set as PWM Mode 2 (High True).
Calculate the timer frequency and PWM duty cycle.
ANS:
=
PWM output is high on when the counter is 499, 500, 501, …, 1999, a total of 1501 cycles. (This statement is not required in the exam.)

## Slide 9: Interrupt (NOT COVERED)
Suppose register i (i ≤ 12) is initialized to have a value of i (e.g. r0 = 0, r1= 1, r2 = 2, r3 = 3, etc.). Assume the main stack (MSP) is used. (Recall: in the interrupt handler, if LR = 0xFFFFFFF9, then the main stack (MSP) is used. If LR = 0xFFFFFFFD, then the process stack (PSP) is used. ) The program status register (PSR) = 0x00000020, PC = 0x08000020, and LR = 0x20008020, when the interrupt occurs.
(1) Show the stack content immediately before the PUSH instruction runs. Suppose the stack pointer SP, i.e. MSP in this case, was 0x20000600 immediately before the system timer interrupt occurs
(2) What are the values of these registers (R0-R12, LR, SP, PC, and PSR) immediately after the interrupt exits?
SysTick_Handler PROC EXPORT SysTick_Handler PUSH {lr, r0, r7} ADD r0, r0, #1 ADD r1, r1, #1 ADD r2, r2, #1 ADD r3, r3, #1 ADD r4, r4, #1 ADD r5, r5, #1 ADD r6, r6, #1 ADD r7, r7, #1 ADD r8, r8, #1 ADD r9, r9, #1 ADD r10, r10, #1 ADD r11, r11, #1 ADD r12, r12, #1 POP {r0, r7, pc} ENDP

## Slide 10: Interrupt ANS (NOT COVERED)
(1)
0x20000600 | 
0x200005FC | 0x00000020 (PSR)
0x200005F8 | 0x08000020 (PC)
0x200005F4 | 0x20008020 (LR)
0x200005F0 | 12 (R12)
0x200005EC | 3 (R3)
0x200005E8 | 2 (R2)
0x200005E4 | 1 (R1)
0x200005E0 | 0 (R0)
0x200005DC |