## Slide 1: Z. Gu Hofstra University
Spring 2026
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 2
Data Representation
Exercises ANS

## Slide 2: Question: Number Conversion
Q: Convert 0x3A56E2F8 into binary
Q: Convert binary number 111010 into hex

## Slide 3: Answer: Number Conversion
Q: Convert 0x3A56E2F8 into binary
A: 0011 1010 0101 0110 1110 0010 1111 1000 (simple table lookup for each hex symbol)
Q: Convert binary number 111010 into hex
A: 0x3A (group 111010 into two parts 0011 1010, followed by table lookup)

## Slide 4: Question: 2’s Complement
For each of the following binary numbers, give the corresponding binary number of the negative of its value, for 2’s-complement system
(a) x=01010101
(b) x=10101010
(c) x=10000000

## Slide 5: Answer: 2’s Complement
For each of the following binary numbers x, give the corresponding binary number of –x in 2’s-complement representation?
(a) x=01010101
  -x = 10101011
(b) x=10101010
  -x = 01010110
(c) x=10000000
  -x = 10000000

## Slide 6: Question: Number Conversion
Q: What is the decimal value of binary number x=10100111 as either unsigned int, or signed int in 2’s complement representation?
What about x=11100001?
What about x=10000000?

## Slide 7: Answer: Number Conversion
Q: What is the decimal value of binary number x=10100111 as either unsigned int, or signed int in 2’s complement representation?
A: if unsigned int, then x=2^7+2^5+2^2+2^1+2^0=167
If signed int, then it is a negative number, since leftmost sign bit is 1. First convert it into its positive counterpart of bitwise NOT plus one to get 01011001, which is equal to decimal 2^6+2^4+2^3+2^0=89. Hence x=-89
Similarly, for x=11100001 (unsigned int 225), first convert it into its positive counterpart of bitwise NOT plus one to get 00011111, which is equal to decimal 31. Hence x=-31
Similarly, for x=10000000 (unsigned int 128), first convert it into its positive counterpart of bitwise NOT plus one to get 10000000, which is equal to decimal 2^7. Hence x=-2^7=-128
 | uint | Int
10100111 | 167 | -89
11100001 | 225 | -31
10000000 | 128 | -128

## Slide 8: Question: Number Conversion
Q: Which number is larger: 1001 or 0011 in binary?
Q: Which number is larger: 0xFFFFFFFF or 0x00000001 in hex?

## Slide 9: Answer: Number Conversion
Q: Which number is larger: 1001 or 0011 in binary?
A: depends on the number system.
  If unsigned int, then 1001 is 9, and 0011 is 3 in decimal, and 9 > 3
  If signed int, then 1001 is -7 (negative of 0111), and 0011 is 3 in decimal, and -7 < 3
Q: Which number is larger: 0xFFFFFFFF or 0x00000001 in hex?
Q: depends on the number system.
  If unsigned int, then 0xFFFFFFFF is 2^32-1, and 0x00000001 is 1 in decimal, and 2^32-1 > 1
  If signed int, then 0xFFFFFFFF is -1 (negative of 0x00000001), and 0x00000001 is 1 in decimal, and -1 < 1
Notes: If they represent signed integers, the latter is greater
(-1 < 1).
If they represent unsigned integers, the former is greater
(232-1 > 1).

## Slide 10: Question: Number Range
Which range of decimals can be expressed with a 6-bit signed integer (assuming Two’s complement representation)?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | -32 … 31

## Slide 11: Answer: Number Range
Which range of decimals can be expressed with a 6-bit signed integer (assuming Two’s complement representation)?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | -32 … 31

## Slide 12: Question: Number Range
Which range of decimals can be expressed with a 6-bit unsigned integer?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | 0 … 63

## Slide 13: Answer: Number Range
Which range of decimals can be expressed with a 6-bit unsigned integer?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | 0 … 63

## Slide 14: Question: Integer arithmetic
Q: What is the result of 1001 + 0011?

## Slide 15: Answer: Integer arithmetic
Q: Consider a 4-bit system. What is the result of 1001 + 0011?
A: 1001 + 0011 = 1100
Value of 1100 depends on the number system.
  If unsigned int, then 1100 is 12, which is equal to 9 (1001) + 3 (0011)
  If signed int, then 1100 is -4 (negative of 0100), which is equal to -7 (1001) + 3 (0011) in decimal

## Slide 16: Question: Addition
Q: Consider a 4-bit system. What is the result of addition 1011+0110, assuming either unsigned integers, or signed integers in 2’s-complement representation？
0001

## Slide 17: Answer: Addition
Q: Consider a 4-bit system. What is the result of addition 1011+0110, assuming either unsigned integers, or signed integers in 2’s-complement representation？
A: 1011+0110 = 10001; the extra leftmost bit is discarded, so the result is 0001 (1 in decimal) for both cases.
1011 is 11 in decimal as unsigned int; -5 in decimal as signed int; 0110 is 6 as either unsigned or signed int. A 4-bit unsigned int has the range [0,24-1]=[0, 15]; a 4-bit signed int has the range [-23, 23-1]=[-8, 7]
For unsigned addition, true result should be 11+6=17 in decimal. Since 17>15, the result is wrong, and Carry flag is set to 1.
For signed addition, true result should be -5+6=1 in decimal. So the result is correct.

## Slide 18: Question: Subtraction
Q: Q: Consider a 4-bit system. What is the result of subtraction 1011-0110, assuming either unsigned integers, or signed integers in 2’s-complement representation？

## Slide 19: Answer: Subtraction
Q: Consider a 4-bit system. What is the result of subtraction 1011-0110, assuming either unsigned integers, or signed integers in 2’s-complement representation？
A: 1011-0110 = 0101, so the computed result is 0101 (5 in decimal) for both cases.
For unsigned subtraction, true result should be 11-6=5 in decimal. So the result is correct
For signed subtraction, true result should be -5-6=-11. Since -11 < -8, the result of 5 is wrong, and Overflow flag is set to 1.

## Slide 20: Question: Subtraction
Q: Consider a 4-bit system. What is the result of subtraction 0110-1011, assuming either unsigned integers, or signed integers in 2’s-complement representation？

## Slide 21: Answer: Subtraction
Q: Consider a 4-bit system. What is the result of subtraction 0110-1011, assuming either unsigned integers, or signed integers in 2’s-complement representation？
A: 0110-1011 = 1011 (borrow bit discarded), so the computed result is 11 in decimal for unsigned, or -5 in decimal for signed.
For unsigned subtraction, true result should be 6-11=-5 in decimal. Since -5 < 0, the result is wrong, and Carry flag is 0 (Borrow flag is 1).
For signed subtraction, true result should be 6-(-5) =11. Since 11 > 7, the result is wrong, and Overflow flag is set to 1.

## Slide 22: Question: True or False
1. Overflow is impossible when subtracting one unsigned number from another.
2. Overflow is impossible when subtracting two signed operands of the same sign.
3. There are two representations of zero in 2’s complement representation.
4. In 2’s complement, the absolute values of full-scale negative and full-scale positive are identical

## Slide 23: Answer: True or False
1. Borrow=1 is impossible when subtracting one unsigned number from another. False
2. Overflow=1 is impossible when subtracting two signed operands of the same sign. True
3. There are two representations of zero in 2’s complement representation. False
4. In 2’s complement, the absolute values of smallest negative and largest positive numbers are identical. False. e.g., [-8, 7] for a 4-bit system
  e.g., for a 4-bit system, the range of signed int is [-8, 7], the range of unsigned int is [0, 15]