## Slide 1: Z. Gu
Fall 2025
CSC111
Final Review
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Data Representation
Integers
  Binary in different bases: binary, octal, hex, decimal
  Signed Integers
    Signed magnitude
    One’s complement
    Two’s complement
  Arithmetic Operations
    N, V, C, Z flags
  Big Endian vs Little Endian
ASCII values
  Null-terminated string
  Converting between numbers and ASCII
  Upper case, lower case
Notes: Fixed point numbers
  Qm.n, UQm.n
  Addition, subtract, multiplication, division
Floating point numbers
  IEEE 754 Standard
  Single Precision, Double Precision

## Slide 3: Signed Integers Method 3: Two’s Complement
Two’s Complement ():
TC of a number can be obtained by its bitwise NOT plus one.
 | Binary | Decimal
Original number | 00011 | 3
Step 1: Invert every bit | 11100 | 
Step 2: Add 1 | + 00001 | 
Two’s complement | 11101 | -3
Example 1: TC(3)

## Slide 4: Adding two integers
-9
6
-3
01001
10110
10111
flip
+1
9
-9
00010
00011
flip
+1
3
Two’s Complement
1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0
1 | 1 | 1 | 0 | 1
Hardware Adder
23
6
29
+
Two’s Complement Counterpart
Same bit patterns, different interpretation.
  Unsigned addition: 23+6=29
  Signed addition: -9+6=-3
This example shows that the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers.
Notes: {{Pause=1}} We will use a very simple example to show that, the hardware adder for adding unsigned numbers, also works correctly for adding signed numbers. {{Pause=0.5}}
Suppose we are adding negative nine and six. {{Pause=0.5}} These two signed numbers are represented in two’s complement in computers. {{Pause=0.5}}
Specifically, we can obtain the two’s complement representation of negative nine by flipping all bits and adding one. {{Pause=0.5}} The two’s complement of a positive number is itself. {{Pause=0.5}}
Let’s see what will happen if the hardware treats these two inputs as unsigned numbers. If these binary bits represent unsigned numbers, they are 23 and 6, respectively. Therefore, the hardware adds 23 and 6, and produces 29, in decimal, {{Pause=0.3}} or one, one, one, zero, one, in binary. {{Pause=0.5}}
If the output represents a signed integer in two’s complement, it actually represents negative 3. This can be proved by inverting all the bits and adding one. The result, negative three, is exactly the sum of the original signed inputs. {{Pause=0.5}}
This example shows that, without any modification, the hardware adder designed for adding unsigned numbers, works correctly for adding signed numbers.

## Slide 5: Basic Assembly Programming
Load-modify-store sequence
Accessing memory
  Memory addressing mode
    Pre-index
    Post-index
    Pre-index with update
Data processing
  Arithmetic, Logic, Comparison, Data Movement
  Barrel Shifter:
    ADD r1, r0, r0, LSL 2
  Bit operations
    Set a bit, Reset a bit, Toggle a bit, Check a bit
  LSL, LSR, ASR, ROR, RRX
Flow control: if, if-then-else, for loop, while loop
  Unconditional Branch: B
  Conditional Branch: CMP, TEQ,TST, BEQ, BNE, BMI, BLS, BHI, etc.
  Conditional Execution: MOVEQ, MOVNE

## Slide 6: Barrel Shifter: Explanations
LSL (logical shift left): shifts left, fills zeros on the right; C gets the last bit shifted out of bit 31. This is multiply by for non-overflowing values.
LSR (logical shift right): shifts right, fills zeros on the left; C gets the last bit shifted out of bit 0. This is unsigned division by .
ASR (arithmetic shift right): shifts right, fills the sign bit on the left to preserving the sign; C gets the last bit shifted out of bit 0. This is signed division by with sign extension
ROR (rotate right): rotates bits right with wraparound; bits leaving bit 0 re-enter at bit 31, and C receives the bit that wrapped. This is a pure rotation without data loss.
RRX (rotate right extended): rotates right by one through the carry flag, treating C as a 33rd bit; new bit 31 comes from old C, and C receives old bit 0.
Notes: Useful for multiword shifts and certain crypto/bit-manip patterns
LSR (used here): Always fills with zeros, converting the negative value to a large positive number
ASR: Would preserve the sign bit, maintaining the negative value (-4096)

## Slide 7: Load/Store a Byte, Halfword, Word
LDR | Load Word | uint32_t/int32_t | unsigned or signed int
LDRB | Load Byte | uint8_t | unsigned char
LDRH | Load Halfword | uint16_t | unsigned short int
LDRSB | Load Signed Byte | int8_t | signed char
LDRSH | Load Signed Halfword | int16_t | signed short int
STR | Store Word | uint32_t/int32_t | unsigned or signed int
STRB | Store Lower Byte | uint8_t/int8_t | unsigned or signed char
STRH | Store Lower Halfword | uint16_t/int16_t | unsigned or signed short
LDRxxx R0, [R1]
; Load data from memory into a 32-bit register
STRxxx R0, [R1]
; Store data extracted from a 32-bit register into memory

## Slide 8: ARM Load Store Summary
Memory address is always in terms of bytes.
How data is organized in memory?
How data is addressed?
Addressing Format | Example | Equivalent
Pre-index | LDR r1, [r0, #4] | r1  memory[r0 + 4], r0 is unchanged
Pre-index with update | LDR r1, [r0, #4]! | r1  memory[r0 + 4] r0  r0 + 4
Post-Index | LDR r1, [r0], #4 | r1  memory[r0] r0  r0 + 4

## Slide 9: Character String
Memory Address | Memory Content | Letter
str + 12 | 0x00 | \0
str + 11 | 0x79 | y
str + 10 | 0x6C | l
str + 9 | 0x62 | b
str + 8 | 0x6D | m
str + 7 | 0x65 | e
str + 6 | 0x73 | s
str + 5 | 0x73 | s
str + 4 | 0x41 | A
str + 3 | 0x20 | space
str + 2 | 0x4D | M
str + 1 | 0x52 | R
str  | 0x41 | A
char str[13] = “ARM Assembly”;
This diagram does not indicate big-endian or little-endian. Endianness is irrelevant for single-byte char arrays.
If you want to detect endianness, you must inspect a multi-byte value in memory, e.g.:
int x = 0x12345678;
That will reveal the byte order.

## Slide 10: Condition Flags
Negative bit
  N = 1 if most significant bit of result is 1
Zero bit
  Z = 1 if all bits of result are 0
Carry bit
  For unsigned addition, C = 1 if carry takes place
  For unsigned subtraction, C = 0 (carry = not borrow) if borrow takes place
  For shift/rotation, C = last bit shifted out
oVerflow bit
  V = 1 if adding 2 same-signed numbers produces a result with the opposite sign
    Positive + Positive = Negative, or
    Negative + negative = Positive
  Non-arithmetic operations does not touch V bit, such as MOV,AND,LSL,MUL
Reserved
ISR number
Program Status Register (PSR)
ICI/IT
T
N
Z
C
V
Q
ICI/IT
GE
Reserved
Notes: N (negative) – set (1) when a signed result is negative, otherwise cleared (0).
Z (zero) – set (1) when a result is 0, otherwise cleared (0).
C (carry) – set (1) when an add-based operation produces an overflow, when a subtract-based operation doesn’t require a borrow; when shifting, holds the last bit that’s been shifted out; otherwise cleared (0).
V (overflow) – set (1) when an add- or subtract-based operation generates a signed overflow, otherwise cleared (0).

## Slide 11: Carry and Overflow Flags w/ Arithmetic Instructions
11
Carry flag C = 1 (Borrow flag = 0) upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition or subtraction if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs; Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
Tip: Convert subtraction to addition with Two’s complement. If two operands have same sign, and the result has opposite sign, then V = 1; else V = 0
 | Unsigned Addition | Unsigned Subtraction | Signed Addition or Subtraction
Carry flag | true result > 2n-1  Carry flag=1 Borrow flag=0 (Result incorrect) | true result < 0  Carry flag=0 Borrow flag=1 (Result incorrect) | N/A
Overflow flag | N/A | N/A | true result > 2n-1-1 or true result < -2n-1 Overflow flag=1 (Result incorrect)
Notes: Convert subtraction to addition with Two’s complement. If two operands have same sign, and the result has opposite sign, then V = 1; else V = 0.”
convert subtraction to addition with Two’s complement. If two operands have same sign, and the result has opposite sign, then V = 1; for all other cases, V = 0
C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. ) or smaller than the minimum signed integer (i.e. ) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.
C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. 2^(𝑛−1)−1) or smaller than the minimum signed integer (i.e. 〖−2〗^(𝑛−1)) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.

## Slide 12: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo (void) {
● ● ●
● ● ●
return;
}
Transfer control to callee
Resume suspended caller
Transfer control to callee
Resume suspended caller

## Slide 13: Passing Arguments and Returning Value
Each argument with size ≤ 32 bits, e.g., 8-bit char, or 16-bit short, or 32-bit int, is passed in a 32-bit register.
  Cannot pack multiple arguments into one register.
The subroutine can take arguments larger than 32 bits. For example, a double-word variable, such as 64-bit long, is passed in two consecutive registers (e.g. R0 and R1, or R2 and R3). A 128-bit variable is passed in four consecutive registers.
  int64_t add_64(int64_t a, int64_t b)
  R0 and R1 are used to store the variable a
The return result is stored in registers (R0-R3), depending on the size of the return variable. If it is less than 32 bits, it is stored in R0. If it is a double-word sized variable, such as long long or double variables in C, it is stored in R0 and R1.
  int128_t multiply_64(int64_t a, int64_t b)
  R0, R1, R2, and R3 are used to store the result

## Slide 14: Callee Saved Registers vs Caller Saved Registers
Callee can freely modify R0, R1, R2, and R3
If caller expects their values are retained, caller should push them onto the stack before calling the callee
Caller expects these values are retained .
If Callee modifies them, callee must restore their values upon leaving the function.
Caller Saved Registers
Callee Saved Registers

## Slide 15: Full Descending Stack

## Slide 16: Stack Recap
PUSH {r3, r1, r7, r2}
POP {r3, r1, r7, r2}
Pop to the smallest-numbered register first.
Largest-numbered register is pushed first but popped last.

## Slide 17: Calling a Subroutine
Caller Program | Subroutine/Callee | 
... BL foo ... | foo PROC ... BX LR EDP | foo PROC PUSH {LR} ... POP {PC} ; pops LR into PC (returns) EDP
Caller: BL label (Branch and Link)
Step 1: LR = PC + 4
Step 2: PC = label
  label is name of subroutine
  Compiler translates label to memory address
  After call, LR holds return address (the instruction following the call)
Callee: BX LR (Branch and Exchange) at end of procedure
PC = LR
  Return to caller by setting PC to LR
Equivalently:
  PUSH {LR} at start of procedure
  POP {PC} at end of procedure

## Slide 18: Caller-saved Registers vs Callee-saved Registers
Not saved by subroutine
Hold arguments/result
Caller expects their values are retained
Callee must save and store it if callee modifies it
Register Bank
Special Registers
Caller-saved registers
Callee-saved registers
Callee-saved registers

## Slide 19: Chapter 8 Subroutines Summary I
How to call a subroutine?
  Branch with link: BL subroutine
How to return the control back to the caller?
  Branch and exchange: BX LR
How to pass arguments into a subroutine?
  Each 8-, 16- or 32-bit variables is passed via r0, r1, r2, r3
  Extra parameters are passed via stack
How to return a value in a subroutine?
  Value is returned in r0
How to preserve the running environment for the caller?
  On the stack

## Slide 20: Chapter 8 Subroutines Summary II
ARM Cortex-M uses full descending stack
How to pass arguments into a subroutine?
  Each 8-, 16- or 32-bit parameter is passed via r0, r1, r2, r3
  Extra parameters are passed via the stack
What registers should be preserved?
  Caller-saved registers vs callee-saved registers
How to preserve the running environment for the caller?
  Via stack

## Slide 21: Timer’s Clock
Current Count
Reload Value
TIMx_CNT
fCL_PSC
ISR
Resume
Interrupt
Reload
TIMx_PSC
TIMx_ARR
Prescaler
fCL_CNT
clock

## Slide 22: PWM Duty Cycle = Ton/Time Period

## Slide 23: Summary of Equations
Timer clock frequency vs. CPU Clock Frequency ()
Timer interrupt frequency with up-counting or down-counting mode:
PWM duty cycle for Mode 1 (Low-True):
Timer interrupt frequency with center-aligned counting mode:
PWM duty cycle for Mode 2 (High-True):