## Slide 1: Z. Gu
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 11
Interrupt Tutorial
Fall 2025
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Polling vs Interrupt
Red & Green LEDs
STM32L4 Discovery Kit
Up
Down
Left
Right
Center
Polling:
You pick up the phone every few seconds to check whether you are getting a call.
Interrupt:
Do whatever you should do and pick up the phone when it rings.
// Polling method
while (1) {
read_button_input;
if (pushed)
exit;
}
turn_on_LED;
// Interrupt method
interrupt_handler(){
turn_on_LED;
exit;
}
Notes: {{Pause=2}} There are two ways to monitor the logic state of an input pin, which is attached to a push button. One is polling, and the other is interrupt. The polling method is like picking up your phone every few seconds, to check whether you are getting a call. The interrupt method is like waiting for the phone to ring. Apparently, the interrupt method is more efficient. You are free to do whatever you should do, and pick up the phone, only when it rings.
{{Pause=1}} Here is a simplified pseudocode of the polling method. In the while loop, software constantly reads the input of {{Pause=0.1}} the pin attached to the push button. It won’t exit the loop until the button is pressed. After the program exits from the while loop, it turns on the LED. The polling method is a busy waiting approach, in which the processor repeatedly reads the input until the button is pressed. It is easy to see, the polling method is simple but inefficient.
{{Pause=1}} The interrupt approach is much more efficient than polling. If the user presses the button, an electrical signal, called interrupt request, is generated. When the processor receives the interrupt request, it automatically suspends the execution of the regular program, and starts the execution of a special defined function called interrupt handler. {{Pause=0.5}} After the interrupt handler completes, the processor restarts the execution of the regular program from where it was stopped. {{Pause=0.5}} Why do we call it an interrupt? {{Pause=0.5}} Because the execution of the regular program is suspended, and the processor is forced to take care of an interrupt request. {{Pause=0.5}} This video explains how interrupts work.

## Slide 3: Memory Map of Cortex-M4
Code
SRAM
Peripheral
External RAM
External Device
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
4 GB
On-chip Flash, for code & data
On-chip RAM, for heap, stack, & code
AHB & APB, such as timers, GPIO
Such as SD card
Off-chip memory for data
NVIC, System Timer, SCB, vendor-specific memory
Notes: {{Pause=2}} Let’s quickly review the memory map. The memory address of ARM Cortex-M has a total of 32 bits, supporting 4 gigabytes of memory space. The memory space is divided into six different pre-defined regions. Each region is given for recommended usage. {{Pause=0.5}} The first region is code region. It is primarily used to store program code. It can also store data. The code region is on-chip memory, typically on-chip flash. The size of on-chip flash is limited to half a gigabyte. The actual size of the on-chip flash varies based on different venders and different chips. {{Pause=0.5}} The second region is Static Random{{Pause=0.1}} Access Memory (SRAM). It is primarily used to store data, such as heaps and stacks. We can also put code here. It supports half a gigabyte. {{Pause=0.5}} The third region is peripheral. These peripherals include AHB peripherals, such as G P I O, and A D C, {{Pause=0.1}} and APB peripherals, such as timers, and USART. {{Pause=0.5}} The next region is for external device, such as SD card. {{Pause=0.5}} The next is external RAM, which is executable region for data. It is off-chip memory, primarily used to store large data blocks. It has a total of 1 gigabyte. {{Pause=0.5}} The last one is system region, which includes the N V I C, system timer, system control block, and vendor-specific memory.

## Slide 4: Data Memory
Code
SRAM
Peripheral
External RAM
External Device
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
Stack
Heap
96 KB
0x20000000
0x3FFFFFFF
Internal
SRAM
Memory
0x20017FFF
Zero-initialized data
Initialized data
Notes: {{Pause=2}} The internal SRAM region, is assigned a space of half a gigabyte. However, the capacity of on-chip SRAM, is often very small. For example, on-chip SRAM on STM32L4 has only 96 kilo-bytes. The SRAM is divided into several segments. {{Pause=0.5}} the initialized data segment. It contains global and static variables, which the program gives some initial values. {{Pause=0.5}} The zero-initialized data segment. It contains all global, or static variables, which are uninitialized, or initialized to zero, in the program. {{Pause=0.5}} The heap segment. It holds all data objects, which an application creates dynamically at runtime. {{Pause=0.5}} The stack segment. Stack is used for various purposes. For example, the stack can store local variables of subroutines, save the runtime environment, and pass arguments to a subroutine.
{{Pause=1}} The stack is placed on the top of the internal SRAM memory, and it grows downwards. The heap is placed at the bottom of the free memory region, and it grows upwards. The stack and the heap, are located at the opposite end of, the free memory region. They grow in the opposite direction. In this way, the stack and the heap can take full advantage of the available memory space. When the stack meets the heap, free memory space is exhausted.

## Slide 5: Instruction Memory
Code
SRAM
Peripheral
External RAM
External Device
System
0x00000000
0x20000000
0.5 GB
0x40000000
0.5 GB
0x60000000
0.5 GB
0xA0000000
1 GB
0xFFFFFFFF
0.5 GB
0xE0000000
1 GB
One Byte (8 bits)
Initial MSP
Interrupt
Vector Table
Reserved
Mapped
(aliasing)
0x08000000
0x080FFFFF
1 MB
0x00000000
0x1FFFFFFF
Internal
Flash
Memory
Initial MSP
Interrupt
Vector Table
Text Section
RO Data Section
RW Data Section
Reserved
Notes: {{Pause=2}} While the code space can have as large as half a gigabyte, much of this space is reserved or not used. For example, STM32L4 chip has, only 1 MB, on-chip flash memory. The memory address of the on-chip flash memory, starts at 8000000 in hex, and ends at 8 0 F F F F F in hex. Typically, the on-chip flash memory stores, the initial value of the stack pointer, {{Pause=0.3}} the interrupt vector table, {{Pause=0.3}} the text section, {{Pause=0.3}} the read-only data section, {{Pause=0.3}} and the read-write data section.
{{Pause=1}} The text section consists of binary machine instructions. The read-only data section that defines the value of variables that cannot change at runtime. The read-write data section that sets the initial values of statically allocated and modifiable variables.
{{Pause=1}} In addition, a small memory region starting at 8000000 in hex, is mapping to, the lowest memory region starting at the address of 0. In other words, two addresses can point to the same data item in this mapped memory region. This mapping region includes the initial value for the main stack pointer, and the interrupt vector table.

## Slide 6: Interrupt Vector Table
PA.3
EXTI3
NVIC
Cortex-M4
Nested-Vectored Interrupt Controller (NVIC)
Interrupt Vector Table
Interrupt Number (8 bits) | Memory Address of ISR (32 bits)
1 | Interrupt Service Routine for interrupt 1
2 | Interrupt Service Routine for interrupt 2
3 | Interrupt Service Routine for interrupt 3
4 | Interrupt Service Routine for interrupt 4
5 | Interrupt Service Routine for interrupt 5
… | …
When interrupt x is triggered, jump to the ISR for interrupt x. (1 ≤ x ≤ 255)
Address of ISR 1
EXTI3_IRQHandler
Interrupt Vector Table
Notes: {{Pause=2}} The Nested Vectored Interrupt Controller (NVIC), prioritizes and handles all interrupts. When we press the push button connected to the pin PA 3, the hardware generates an electrical signal, called interrupt request, E X T I 3. When N V I C receives the interrupt request, it forces the processor to jump to, and execute, a special piece of code, called an interrupt service routine, or an interrupt handler. Specifically, the processor will execute the function named E X T I 3 IRQ Handler. {{Pause=1}} The entry points of all interrupt service routines, are stored in a special table. This special table is called an interrupt vector table. The interrupt vector table is stored at a pre-defined area, in the memory. For ARM Cortex processors, the interrupt vector table starts at the memory address 4. By default, the interrupt vector table is mapped to the lowest address of the internal flash memory. However, software can re-map it to a different location, such as internal SRAM.
{{Pause=1}} To understand interrupts, the concept of interrupt vector table is very important. The interrupt vector table holds an array of memory addresses. Each entry in the interrupt vector table is four bytes long. Each entry contains the starting memory address of an interrupt service routine. To put it simply, the interrupt vector table holds an array of function pointers.
{{Pause=2}} Every type of interrupt is assigned a number, called interrupt number. The interrupt number is used to index into the interrupt vector table. When interrupt x is triggered, N V I C uses the interrupt number x, as the index value, to look up the interrupt vector table, finds the memory address of the corresponding interrupt service routine for interrupt x, and forces the processor to jump to and execute this interrupt service routine.

## Slide 7: Interrupt Vector Table
The Nested Vectored Interrupt Controller (NVIC), prioritizes and handles all interrupts. The IVT holds an array of memory addresses, each entry is a function pointer pointing to the starting memory address of an ISR.
Every type of interrupt is assigned a number, called interrupt number, used to index into the IVT. When interrupt x is triggered, NVIC uses the interrupt number x as the index to look up the memory address of its corresponding ISR, and forces the processor to jump to and execute this ISR.
  When we press the push button connected to the pin PA.3, the hardware generates an electrical signal, called interrupt request EXTI3. When NVIC receives the interrupt request, it forces the processor to jump to and execute, the ISR named EXTI3 IRQ Handler.
Notes: By default, the interrupt vector table is mapped to the lowest address of the internal flash memory. However, software can re-map it to a different location, such as internal SRAM.
For ARM Cortex processors, the IVT starts at memory address 4.
{{Pause=1}} To understand interrupts, the concept of interrupt vector table is very important.

## Slide 8: Interrupt Vector Table
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
0x20000068
0x00000008
0x00000004
0x00000000
Main stack
Memory
address
Memory
content
Initialize MSP (main stack pointer)
Bit 0 is 1, indicating Thumb state.
Reset_Handler(); Initialize PC (program counter)
0x20000068
0x2000020D
0x0800030D
Calculate the address which holds the address of the ISR for interrupt n:
Address of pointer = 64 + 4 × n
Example 1: EXTI3_IRQn = 9
Address of pointer to EXTI3 ISR = 64 + 4 × 9
= 100
= 0x64
Example 2: SysTick_IRQn = -1
Address of pointer to SysTick ISR = 64 + 4 × (-1)
= 60
= 0x3C
For interrupt number n, its ISR is stored at address 64 + 4 x n, in the interrupt vector table.
Notes: {{Pause=2}} How does the N V I C controller use the interrupt number to look up the interrupt vector table? {{Pause=0.5}} The first word in the memory is the initial MSP value. Here is the main stack, typically located in SRAM. {{Pause=2}} The second word in the memory is a pointer to the reset handler, which is the starting memory address, or called entry point, of the function reset handler. The reset handler contains program code, which is executed when the processor is reset. Typically, the reset handler performs some hardware initialization first, and then calls the main function. Immediately after the processor, is reset, the program counter is initialized to this value.
{{Pause=1}} For ARM Cortex-M processors, if the interrupt number is n, the pointer that points the interrupt service routine of interrupt n, is stored at, this address, in the interrupt vector table. {{Pause=0.5}} For example, the interrupt number of E X T I 3, is 9. Then, the address of E X T I 3 IRQ Handler is stored at the memory address: 64 plus, 4 times 9. The result is 100 in decimal, or 64 in hex. Suppose the handler for external interrupt 3, is stored at the memory address, 0 8 0 0 0 3 0 C, in hex. {{Pause=1}} In the interrupt table, the value 0 8 0 0 0 3 0 D, is stored at the location 64 in hex. {{Pause=1}} If E X T I 3 interrupt request arrives, the N V I C controller will read the word stored at the memory address 64, and then set the program counter to that value. In this way, the N V I C controller forces the processor to jump to the interrupt service routine, E X T I 3 IRQ Handler.
{{Pause=1}} Note that, the least-significant bit of these memory addresses is 1. When the processor jumps to a new code, it examines bit 0 of the destination address to determine the processor state. In general, for ARM processor family, if bit 0 of the destination address is 1, the processor will be in the Thumb state. If bit 0 is 0, the processor will switch to the ARM state. However, for ARM Cortex processors, the bit 0 of the destination address must always be 1. This is because ARM Cortex processors, only support Thumb instructions.
{{Pause=1}} Please pay attention that the interrupt number can be negative. For example, the interrupt number of system timer (SysTick) is negative 1.

## Slide 9: Interrupt Service Routine (ISR)
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Memory
address
Memory
content
Initialize SP
Bit 0 is 1, indicating Thumb state.
Initialize PC
interrupt vector table of STM32L4. The first word holds the top of the main stack. The next 15 words hold the pointers of 15 system exception handlers. The next are pointers to vender-specific interrupt handlers.
Notes: {{Pause=2}} Here is the interrupt vector table of STM32L4. {{Pause=0.5}} The first word holds the top of the main stack. {{Pause=0.5}} The next 15 words hold the pointers of 15 system exception handlers. {{Pause=0.5}} The next are pointers to vender-specific interrupt handlers. The size of the interrupt vector table, varies among different processor chips.

## Slide 10: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
EXTI3
Suppose EXTI3 arrives. Assume software has already enabled EXTI3 by setting the corresponding bit in the interrupt Enable Register. The interrupt number of EXTI3 is pre-defined as 9. Interrupt priority register shows that its priority is set to 2.
Notes: {{Pause=2}} Let’s use an example to see how N V I C handles an interrupt. Suppose external interrupt 3 (E X T I 3), arrives at this time instant. Assume software has already enabled E X T I 3 interrupt. An interrupt can be enabled by setting the corresponding bit in the interrupt enable register. {{Pause=0.5}} The interrupt number of E X T I 3 is pre-defined as 9. As you see from the interrupt enable register, external interrupt 3 has already been enabled. The interrupt priority register shows that, the priority of external interrupt 3, is set to 2.

## Slide 11: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC first writes 1 to the pending bit of EXTI3 in the interrupt pending register. NVIC starts to the stacking process, and pushes, 8 registers to preserve the running environment. (If FPU is used, more registers are pushed into the stack during the stacking.)
Notes: {{Pause=1}} N V I C first writes 1 to the pending bit of, external interrupt 3, in the interrupt pending register. Let’s assume the floating-point unit (FPU) has not been used in this example. Then, N V I C automatically starts to the stacking process, and pushes, eight registers to preserve the running environment. If the floating-point unit is used, more registers are pushed into the stack during the stacking.

## Slide 12: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
xPSR | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC first pushes program status register (xPSR) onto the stack.
Notes: N V I C first pushes the program status register (x P S R) onto the stack,

## Slide 13: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC then pushes program counter (PC), which is r15.
Notes: then, pushes the program counter (PC), which is register 15,

## Slide 14: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC then pushes link register (LR), which is r14.
Notes: pushes the link register (LR), which is register 14,

## Slide 15: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC pushes r12 (intra‑procedure call scratch register).
Notes: pushes register 12, Because on Cortex‑M exception entry the hardware automatically stacks the “volatile” call‑clobbered registers R0–R3, R12 (aka IP or t12), LR, PC, and xPSR so an ISR can be written like a normal C function without manually saving them, and R12 is included because it’s a scratch register used by veneers/trampolines and function calls, so preserving it avoids corrupting in‑flight call sequences when an interrupt fires.stackoverflow+1
The fixed hardware stack frame contains exactly eight words: xPSR, ReturnAddress (PC), LR, R12, R3, R2, R1, and R0; this is pushed automatically on interrupt entry before the ISR runs.ece.utexas+1
R12 is designated the intra‑procedure call scratch register on ARM, used by linker‑generated veneers for far calls; since it is call‑clobbered and may hold temporary state during calls, the architecture chooses to save it in the exception frame to guarantee correct resumption after the ISR.interrupt.memfault
添加到后续问题
检查来源
https://stackoverflow.com/questions/42688466/arm-cortex-m-exception-entry-and-stack-framing
https://developer.arm.com/documentation/ddi0403/d/System-Level-Architecture/System-Level-Programmers--Model/ARMv7-M-exception-model/Exception-entry-behavior
https://users.ece.utexas.edu/~valvano/Volume1/E-Book/C12_Interrupts.htm
https://interrupt.memfault.com/blog/cortex-m-rtos-context-switching
https://community.arm.com/support-forums/f/keil-forum/34201/stacking-and-interrupts
https://stackoverflow.com/questions/38292995/what-are-the-registers-pushed-to-the-stack-when-an-interrupt-occurs
https://developer.arm.com/documentation/107706/latest/Exceptions-and-interrupts-overview/Stack-frames
https://interrupt.memfault.com/blog/arm-cortex-m-exceptions-and-nvic
https://www.embeddedrelated.com/showarticle/878.php
https://interrupt.memfault.com/blog/cortex-m-hardfault-debug
https://developer.arm.com/documentation/dui0646/latest/The-Cortex-M7-Processor/Exception-model/Exception-entry-and-return
https://stackoverflow.com/questions/45461739/which-stack-is-used-when-entering-interrupt-handler-from-user-program-for-cortex
https://www.ti.com/lit/pdf/spna218
https://eng.auburn.edu/~nelson/courses/elec5260_6260/slides/ARM%20STM32F476%20Interrupts.pdf
https://developer.arm.com/documentation/107706/latest/Use-case-examples/context-switch-fp/Task-initialization
https://www.reddit.com/r/embedded/comments/c0pmlv/cortex_m3_can_anyone_help_me_understanding_how/
https://www.embeddedrelated.com/showarticle/912.php
https://www.embeddedrelated.com/thread/7406/stack-interrupt-function-call
https://www.sciencedirect.com/topics/engineering/exception-return-mechanism
https://e2e.ti.com/support/microcontrollers/arm-based-microcontrollers-group/arm-based-microcontrollers/f/arm-based-microcontrollers-forum/1094104/lp-am243-printing-the-stack-frame

## Slide 16: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC pushes r3.
Notes: then, register 3,

## Slide 17: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC pushes r2.
Notes: register 2

## Slide 18: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC pushes r1.
Notes: register 1

## Slide 19: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
r0 | 
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
NVIC pushes r0.
Notes: and finally, pushes register 0.

## Slide 20: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | SP + 0x20
xPSR | SP + 0x1C
PC(r15) | SP + 0x18
LR(r14) | SP + 0x14
r12 | SP + 0x10
r3 | SP + 0x0C
r2 | SP + 0x08
r1 | SP + 0x04
r0 | SP
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
1
Full Descending Stack
After NVIC pushes these 8 registers onto the stack, the size of the stack increases by 4*8=32 bytes, and the stack pointer is decremented by 32. (ARM Cortex uses full descending stacks.)
Notes: Note that, ARM Cortex uses full descending stacks. If a 32-bit item is pushed onto the stack, the stack pointer (SP) is decremented by four. After N V I C pushes these eight registers onto the stack, the size of the stack increases by 32 bytes, and the stack pointer is decremented by 32. This stacking process is automatically performed by the N V I C controller, not by the user code.

## Slide 21: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | SP + 0x20
xPSR | SP + 0x1C
PC(r15) | SP + 0x18
LR(r14) | SP + 0x14
r12 | SP + 0x10
r3 | SP + 0x0C
r2 | SP + 0x08
r1 | SP + 0x04
r0 | SP
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
Full Descending Stack
1
0
ISR 9
NVIC looks up interrupt vector table and finds the starting address of ISR 9 for EXTI3. It changes status of interrupt 9, from pending to active state by setting its active bit to 1 in Active Register. It then forces the processor to branch to and start to execute ISR 9.
Notes: {{Pause=1}} Then, N V I C looks up the interrupt vector table, and finds the starting address of the interrupt service routine for external interrupt 3. {{Pause=1}} Next, N V I C changes the status of interrupt 9, from the pending state, to the active state. {{Pause=1}} After that, N V I C forces the processor to branch to the interrupt handler, and starts to execute the interrupt handler.

## Slide 22: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 |  | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
xxxxxxxx | SP + 0x20
xPSR | SP + 0x1C
PC(r15) | SP + 0x18
LR(r14) | SP + 0x14
r12 | SP + 0x10
r3 | SP + 0x0C
r2 | SP + 0x08
r1 | SP + 0x04
r0 | SP
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
SP
Memory
address
Memory
content
Initialize SP
Initialize PC
Stacking
Full Descending Stack
1
0
ISR 9
BX LR
ISR 9 completes its execution by executing BX LR as its last instruction.
Notes: {{Pause=1}} The interrupt service routine, completes its execution, by running the following instruction: {{Pause=0.3}} BX LR.

## Slide 23: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | SP + 0x20
xPSR | SP + 0x1C
PC(r15) | SP + 0x18
LR(r14) | SP + 0x14
r12 | SP + 0x10
r3 | SP + 0x0C
r2 | SP + 0x08
r1 | SP + 0x04
r0 | SP
SP
Full Descending Stack
BX LR
Instruction BX LR informs NVIC to perform the unstacking process. The active bit in Active Register is cleared. The unstacking process pops the values of the 8 registers, out of the stack. Therefore, the processor’s state (running environment) is recovered, to the time instant immediately before ISR started.
Notes: {{Pause=1}} The instruction, BX LR, informs the N V I C controller to perform an {{Pause=0.1}} unstacking process. At the same time, the active bit, in the interrupt active register, is cleared. {{Pause=1}} The unstacking process, automatically pops the values of these eight registers, out of the stack. Therefore, N V I C recovers, the processor’s state, or called running environment, to the time instant immediately before the interrupt handler starts.

## Slide 24: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
r0 | 
SP
BX LR
NVIC pops the 8 registers in the reverse order when they were pushed, thus recovering their original values.
Notes: {{Pause=1}} Let’s see how the unstacking process work. First, N V I C pops register 0 off the stack.

## Slide 25: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
SP
BX LR
Notes: then, pop register 1,

## Slide 26: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
SP
BX LR
Notes: register 2,

## Slide 27: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
SP
BX LR
Notes: register 3,

## Slide 28: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
SP
BX LR
Notes: register 12,

## Slide 29: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
SP
BX LR
Notes: the link register,

## Slide 30: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
xPSR | 
PC(r15) | 
SP
BX LR
Notes: the program counter,

## Slide 31: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
xPSR | 
SP
BX LR
Notes: and, finally pop the program status register off the stack.

## Slide 32: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
0
xxxxxxxx | 
SP
BX LR
After unstacking completes, the running environment has been fully recovered from the stack. All registers have their original values, as if the interrupt has never happened.
Notes: After unstacking completes, the running environment has been fully recovered from the stack. All registers have their original values, as if the interrupt has never happened.

## Slide 33: Single Interrupt
12 | 11 | 10 | 9 | 8
Program
time
ISR 9
Enable Register
0 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 2 | 8
Interrupt Number
...
0x00000064
void EXTI3_IRQHandler{
...
}
0x0800030C
EXTI3
0x20000068
0x00000008
0x00000004
0x00000000
0x20000068
0x2000020D
0x0800030D
stack
Stacking
Unstacking
Memory
address
Memory
content
Initialize SP
Initialize PC
xxxxxxxx | 
SP
Program
BX LR
Afterwards, the processor continues to execute the user program, which was interrupted by EXTI3, ISR 9.
Notes: As result, the processor can successfully continue to execute the user program, which has been interrupted by the external interrupt 3.

## Slide 34: Nested Interrupts: Example of Preemption
Program
time
12 | 11 | 10 | 9 | 8
Enable Register
1 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 | 0 | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 5 | 3
Interrupt Number
EXTI3
xxxxxxxx | 
SP
DMA1_Channel2
EXTI3
Suppose EXTI 3 arrives at this time instant.
Notes: {{Pause=2}} Let’s see how the N V I C controller handles multiple interrupts. Suppose interrupt request 9 (E X T I 3) arrives at this time instant.

## Slide 35: Nested Interrupts: Example of Preemption
Program
time
ISR 9
Stacking
12 | 11 | 10 | 9 | 8
Enable Register
1 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 5 | 3
Interrupt Number
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
r0 | 
SP
DMA1_Channel2
EXTI3
1
NVIC first performs stacking, and pushes 8 registers onto the stack. NVIC then forces the processor to execute ISR 9 for EXTI3.
Notes: {{Pause=2}} N V I C first performs stacking, and pushes these eight registers onto the stack. {{Pause=1}} Then, N V I C forces the processor to execute the interrupt service routine for interrupt 9.

## Slide 36: Nested Interrupts: Example of Preemption
Program
time
ISR 9
Stacking
12 | 11 | 10 | 9 | 8
Enable Register
1 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
 | 0 | 0 | 0 | 0
Priority Register
 | 4 | 7 |  | 3
Interrupt Number
EXTI3
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
r0 | 
SP
DMA1_Channel2
EXTI3
DMA1_Channel2
1
1
3
5
  Lower priority value means higher urgency.
Suppose another interrupt (DMA 1 Channel 2) arrives, before ISR 9 completes. This new interrupt has higher urgency than the current interrupt being served, hence NVIC has to respond to the new coming interrupt.
Notes: {{Pause=2}} Suppose another interrupt request (DMA 1 Channel 2) arrives, before the interrupt service routine 9 completes. In addition, this new coming interrupt, has a higher urgency, than the current interrupt being served. {{Pause=1}} As you see from this table, the interrupt priority value is 3 for interrupt 12, and 5 for interrupt 9. Note that, for ARM Cortex processors, a lower priority value actually represents a higher urgency. Accordingly, N V I C has to respond to the new coming interrupt.

## Slide 37: Nested Interrupts: Example of Interrupt Preemption
Program
time
ISR 9
Stacking
12 | 11 | 10 | 9 | 8
Enable Register
1 | 0 | 0 | 1 | 0
Active Register
 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 5 | 3
Interrupt Number
EXTI3
ISR 12
Stacking
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
r0 | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
r0 | 
DMA1_Channel2
EXTI3
DMA1_Channel2
1
1
SP
NVIC stops the current ISR 9 and performs another stacking by pushing another set of 8 registers, onto the stack. Note that these two sets of registers have different values. The first set holds register values, for the user program. The second set hold register values, for the interrupt service routine 9. After the stacking, NVIC starts to execute ISR 12 of the new coming interrupt.
Notes: {{Pause=2}} Because the new interrupt has a higher urgency, N V I C then stops the current interrupt service routine, and performs another stacking. Again, it pushes another set of eight registers, onto the stack. Note that these two sets of registers have different values. The first set holds register values, for the user program. {{Pause=0.5}} The second set hold register values, for the interrupt service routine 9. {{Pause=1}} After the stacking, N V I C starts to execute, the interrupt service routine of the new coming interrupt. The process of stopping the current interrupt handler, and starting to serve another interrupt, is called interrupt preemption.

## Slide 38: Nested Interrupts: Example of Preemption
Program
time
ISR 9
Stacking
12 | 11 | 10 | 9 | 8
Enable Register
1 | 0 | 0 | 1 | 0
Active Register
 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 5 | 3
Interrupt Number
EXTI3
ISR 12
Stacking
Unstacking
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
r0 | 
DMA1_Channel2
EXTI3
DMA1_Channel2
1
0
SP
After ISR12 completes, NVIC performs unstacking, pops out eight registers from the stack, and recovers the running environment, for ISR 9.
Notes: {{Pause=2}} After the interrupt service routine 12 completes, N V I C performs unstacking, pops out eight registers from the stack, and recovers the running environment, for the interrupt service routine 9.

## Slide 39: Nested Interrupts: Example of Preemption
Program
time
ISR 9
Stacking
12 | 11 | 10 | 9 | 8
Enable Register
1 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 5 | 3
Interrupt Number
EXTI3
ISR 12
Stacking
Unstacking
ISR 9
xxxxxxxx | 
xPSR | 
PC(r15) | 
LR(r14) | 
r12 | 
r3 | 
r2 | 
r1 | 
r0 | 
DMA1_Channel2
EXTI3
DMA1_Channel2
1
SP
NVIC continues execution of ISR 9.
Notes: Then, N V I C continues the execution of interrupt service routine 9.

## Slide 40: Nested Interrupts: Example of Preemption
Program
time
ISR 9
Stacking
Unstacking
Program
12 | 11 | 10 | 9 | 8
Enable Register
1 | 0 | 0 | 1 | 0
Active Register
0 | 0 | 0 |  | 0
Pending Register
0 | 0 | 0 | 0 | 0
Priority Register
3 | 4 | 7 | 5 | 3
Interrupt Number
EXTI3
ISR 12
Stacking
Unstacking
ISR 9
xxxxxxxx | 
SP
DMA1_Channel2
EXTI3
DMA1_Channel2
0
After ISR 9 completes, NVIC performs unstacking to recover the running environment of the user program. The user program then resumes its execution.
Notes: {{Pause=2}} After the interrupt service routine 9 completes, N V I C performs un-stacking to recover the running environment of the user program. After unstacking, the user program resumes the computation.

## Slide 41: Nested Interrupts: Tail Chaining
EXTI3 → ISR 9
EXTI4 → ISR 10
Suppose EXTI4 has lower urgency than EXTI3.
  EXTI4 has a higher numeric priority value than EXTI3.
  If interrupt 4 EXTI4 arrives before the interrupt 3 EXTI3’s handler completes, NVICC will continue the execution of the current ISR 9 for EXTI3. After it completes, unstacking and stacking are performed, before the new ISR 10 for EXTI4 starts.
The middle unstacking and stacking are unnecessary in this example. Tail chaining is an optimization technique to reduce the interrupt latency.
  Typically unstacking and stacking each takes 12 cycles.. However, tail chaining takes only 6 cycles.
1
Program
time
Stacking
Unstacking
Program
Stacking
Unstacking
EXTI3
EXTI4
ISR 9
ISR 10
Program
time
ISR 9
Stacking
Unstacking
Program
ISR 10
EXTI3
EXTI4
Tail Chaining
12 cycles
12 cycles
6 cycles
Notes: {{Pause=2}} In the previous example, we have shown that, an interrupt with higher urgency, can preempt, an interrupt with relatively lower urgency. What would happen if the new coming interrupt request has a lower urgency? {{Pause=1}} Suppose external interrupt 4 has less urgency than exernal interrupt 3. If external interrupt 4 arrives, before the external interrupt 3 Handler completes, N V I C won’t respond the new coming interrupt request. Instead, N V I C will continue the execution of the current interrupt service routine. After the current interrupt service routine completes, unstacking and stacking are performed, before the new interrupt service routine starts.
{{Pause=1}} As you notice, the middle unstacking and stacking processes are unnecessary in this example. Therefore, ARM Cortex-M deploys an optimization technique, called tail chaining, to reduce the interrupt latency. Typically the unstacking process takes 12 cycles. The stacking takes 12 cycles too. However, the tail chaining takes only 6 cycles.