## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 8
Passing Parameters to Subroutines
via Registers
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Overview
How to call a subroutine?
How to return the control back to the caller?
How to pass arguments into a subroutine?
How to return a value in a subroutine?
How to preserve the running environment for the caller?

## Slide 3: Link Register (LR)
Link Register (LR) holds the return address of a subroutine
The processor copies LR to PC after the program is finished.
Link Register
Register Bank
Special Registers

## Slide 4: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo (void) {
● ● ●
● ● ●
return;
}
Transfer control to callee
Resume suspended caller
Transfer control to callee
Resume suspended caller

## Slide 5: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo (void) {
● ● ●
● ● ●
return;
}
r0 | 
r1 | 
r2 | 
r3 | 
. . . | . . .
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Registers
32 bits
0x08000214
0x08000210
0x08000214
0x08000280
0x08000280
Transfer control to callee
LR = PCcurrent + 4
PC = Mem Addr of foo()
PCcurrent
Notes: Suppose PC current represents the memory address of the Branch and Link instruction BL. Since the BL instruction takes four bytes in memory, the memory of the next instruction immediately after BL is PC current plus 4.

## Slide 6: Link Register (LR)
void foo(void) ;
int main(void{
● ● ●
foo();
● ● ●
}
Compiler
● ● ●
BL foo
● ● ●
foo PROC
● ● ●
● ● ●
BX LR
ENDP
void foo (void) {
● ● ●
● ● ●
return;
}
r0 | 
r1 | 
r2 | 
r3 | 
. . . | . . .
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Registers
32 bits
0x08000214
0x08000210
0x08000214
0x08000280
PC = LR
PCcurrent
Resume suspended caller
0x08000214
Notes: Suppose PC current represents the memory address of the Branch and Link instruction BL. Since the BL instruction takes four bytes in memory, the memory of the next instruction immediately after BL is PC current plus 4.

## Slide 7: Procedure Call Standard
What is it?
  Contract between a calling subroutine (caller) and a called subroutine (callee)
Why need it?
  Allows subroutines to be separately written, compiled, assembled but work together
  Allows C program calls an assembly function, or vice versa
This talk focuses on
  How to pass arguments to a subroutine?
  How to return a result from a subroutine?
Notes: The AAPCS defines how subroutines can be separately written, separately compiled, and separately
assembled to work together.

## Slide 8: Passing Arguments and Returning Value
Each argument with size ≤ 32 bits, e.g., 8-bit char, or 16-bit short, or 32-bit int, is passed in a 32-bit register.
  Cannot pack multiple arguments into one register.
The subroutine can take arguments larger than 32 bits. For example, a double-word variable, such as 64-bit long, is passed in two consecutive registers (e.g. R0 and R1, or R2 and R3). A 128-bit variable is passed in four consecutive registers.
  int64_t add_64(int64_t a, int64_t b)
  R0 and R1 are used to store the variable a
The return result is stored in registers (R0-R3), depending on the size of the return variable. If it is less than 32 bits, it is stored in R0. If it is a double-word sized variable, such as long long or double variables in C, it is stored in R0 and R1.
  int128_t multiply_64(int64_t a, int64_t b)
  R0, R1, R2, and R3 are used to store the result

## Slide 9: Passing Arguments Examples
Each argument of 8-bit char, or 16-bit short, is passed in a 32-bit register
R0 | R1 | R2 | R3
Registers
Stack in Memory
foo (int i0, int i1, int i2, int i3)
i0 | i1 | i2 | i3
Registers
Stack in Memory
foo (int i0, char a1, double D)
i0 | a1 | D
Registers
Stack in Memory
foo (int i0, int i1, double D, int i2, int i3)
i0 | i1 | D
i2 | i3 |  |  |  |  | 
Registers
Stack in Memory
Caller passes arguments i0, i1, D in registers R0-R3 directly; pushes additional arguments i2 and i3 on the stack before subroutine call

## Slide 10
r0 | a8
r1 | b8
r2 | c16
r3 | d16
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int32_t sum(uint8_t a8, int8_t b8, uint16_t c16, uint16_t d16);
Register
a8
b8
c16
d16
Subroutine
Register r0
Register r1
Register r2
Register r3
Return Value
Register r0

## Slide 11
r0 | sum
r1 | 
r2 | 
r3 | 
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Return the sum in register r0
int32_t sum(uint8_t a8, int8_t b8, uint16_t c16, uint16_t d16);
Register
a8
b8
c16
d16
Subroutine
Register r0
Register r1
Register r2
Register r3
Return Value
Register r0

## Slide 12: Passing Arguments and Returning Value
int32_t sum(uint8_t a8, int8_t b8, uint16_t c16, uint16_t d16);
Caller
s = sum(1, 2, 3, 4);
MOVS r0, #1 ; a8
MOVS r1, #2 ; b8
MOVS r2, #3 ; c16
MOVS r3, #4 ; d16
BL sum
Callee
sum PROC
ADD r0, r0, r1 ; a8 + b8
ADD r0, r0, r2 ; add c16
ADD r0, r0, r3 ; add d16
BX LR
ENDP

## Slide 13: Returning Value
uint32_t s32;
uint32_t sum(uint8_t a8, uint8_t b8, uint16_t c16, uint16_t d16);
s32 = sum(1, 2, 3, 4) + 100;
MOVS r0, #1 ; 1st argument a8
MOVS r1, #2 ; 2nd argument b8
MOVS r2, #3 ; 3rd argument c16
MOVS r3, #4 ; 4th argument d16
BL sum ; result is returned in r0
ADD r0, r0, #100
LDR r4, =s32 ; Get memory address of s32
STR r0, [r4] ; Save returned result to s32
uint32_t s32 is declared as a C global variable, so the compiler/linker creates storage for it in .data or .bss depending on initialization. You can simply reference it by name in assembly as a label.

## Slide 14
r0 | a[31:0]
r1 | a[63:32]
r2 | b[31:0]
r3 | b[63:32]
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int64_t sum(int64_t a, int64_t b);
Callee
sum PROC
ADDS r0, r2, r0 ; Adding lower 32 bits
ADC r1, r3, r1 ; Adding upper 32 bits
BX LR ; Return in r1:r0
ENDP
r1
r0
r3
r2
r1
r0
Addend1
Addend2
Sum
Upper 32 bits
Lower 32 bits
Carry out
Register

## Slide 15
r0 | sum[31:0]
r1 | sum[63:32]
r2 | 
r3 | 
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Returning sum from a subroutine
int64_t sum(int64_t a, int64_t b);
Callee
sum PROC
ADDS r0, r2, r0 ; Adding lower 32 bits
ADC r1, r3, r1 ; Adding upper 32 bits
BX LR ; Return in r1:r0
ENDP
r1
r0
r3
r2
r1
r0
Addend1
Addend2
Sum
Upper 32 bits
Lower 32 bits
Carry out
Register

## Slide 16
r0 | a1
r1 | a2
r2 | a2
r3 | a3
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int32_t sum6(int32_t a1, int32_t a2, int32_t a3, int32_t a4, int32_t a5, int32_t a6)
sum6(1, 2, 3, 4, 5, 6);
MOVS r0, #5
MOVS r1, #6
PUSH {r0, r1} ; push a5, a6
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum6
ADDS sp, sp, #8 ; pop a4, a6
sum6 PROC
ADD r0, r0, r1 ; sum = a1 + a2
ADD r0, r0, r2 ; sum += a3
ADD r0, r0, r3 ; sum += a4
LDRD r1, r2, [sp] ; load a5, a6
ADD r0, r0, r1 ; sum += a5
ADD r0, r0, r2 ; sum += a6
BX LR ; return in r0
ENDP
sp | xxxx
Memory
Register

## Slide 17
r0 | a1
r1 | a2
r2 | a2
r3 | a3
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int32_t sum6(int32_t a1, int32_t a2, int32_t a3, int32_t a4, int32_t a5, int32_t a6)
sum6(1, 2, 3, 4, 5, 6);
MOVS r0, #5
MOVS r1, #6
PUSH {r0, r1} ; push a5, a6
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum6
ADD sp, sp, #8 ; pop a4, a6
sp+8 | xxxx
sp+4 | a6
sp | a5
Memory
Register
sum6 PROC
ADD r0, r0, r1 ; sum = a1 + a2
ADD r0, r0, r2 ; sum += a3
ADD r0, r0, r3 ; sum += a4
LDRD r1, r2, [sp] ; load a5, a6
ADD r0, r0, r1 ; sum += a5
ADD r0, r0, r2 ; sum += a6
BX LR ; return in r0
ENDP

## Slide 18
r0 | a1
r1 | a2
r2 | a2
r3 | a3
r4 | 
r5 | 
r6 | 
r7 | 
r8 | 
r9 | 
r10 | 
r11 | 
r12 | 
r13 (SP) | 
r14 (LR) | 
r15 (PC) | 
Passing arguments to a subroutine
int32_t sum6(int32_t a1, int32_t a2, int32_t a3, int32_t a4, int32_t a5, int32_t a6)
sum6(1, 2, 3, 4, 5, 6);
MOVS r0, #5 ; MOVS can also be MOV here
MOVS r1, #6
PUSH {r0, r1} ; push a5, a6
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum6
ADD sp, sp, #8 ; pop a4, a6 by restoring sp to its old position before calling PROC
sp | xxxx
 | a6
 | a5
Memory
Register
sum6 PROC
ADD r0, r0, r1 ; sum = a1 + a2
ADD r0, r0, r2 ; sum += a3
ADD r0, r0, r3 ; sum += a4
LDRD r1, r2, [sp] ; load a5, a6
ADD r0, r0, r1 ; sum += a5
ADD r0, r0, r2 ; sum += a6
BX LR ; return in r0
ENDP

## Slide 19: Explanations
Step | r0 | r1 | r2 | r3 | Stack (top first) | Description
Before call | 5 | 6 | — | — | — | a5, a6 prepared
After PUSH | — | — | — | — | a5=5, a6=6 | pushed to stack
Set r0–r3 | 1 | 2 | 3 | 4 | a5=5, a6=6 | a1–a4 in regs
Inside sum6 | 1 | 2 | 3 | 4 | a5=5, a6=6 | entry point
LDRD loads | — | 5 | 6 | — | a5=5, a6=6 | from stack
Return | 21 | — | — | — | a5=5, a6=6 | 1+2+3+4+5+6 = 21
First 4 parameters → registers r0–r3.Extra parameters → pushed onto the stack.
LDRD (Load Register Double) fetches two words (a5, a6) efficiently.
r0 always holds the return value.
Caller cleans up the stack after the function (ADDS sp, sp, #8).

## Slide 20: Quiz
Can I use POP to replace ADD?
MOVS r0, #5
MOVS r1, #6
PUSH {r0, r1} ; push a5, a6
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum6
POP {r0, r1}
; ADD sp, sp, #8

## Slide 21: Quiz ANS
POP {r0, r1} is equivalent to LDMIA sp!, {r0, r1}
  Load [sp] into r0
  Load [sp + 4] into r1
  Then increment sp by 8
This is wrong, because it would overwrite registers r0 and r1 with garbage (the old arguments you pushed), whereas r0 should contain the return value
  After returning from sum6, you do not need those values (a5, a6) anymore. You just want to discard them, so ADD moves stack pointer up by 8 bytes and discards data.
MOVS r0, #5
MOVS r1, #6
PUSH {r0, r1} ; push a5, a6
MOVS r0, #1
MOVS r1, #2
MOVS r2, #3
MOVS r3, #4
BL sum6
POP {r0, r1}
; ADD sp, sp, #8

## Slide 22: Calling Assembly Subroutine in C
If your assembly code follows the procedure call standard, a C code can call an assembly subroutine, and vice versa.
extern int32_t sum3(int32_t a1, int32_t a2, int32_t a3);
int main(void){
int32_t s
...
s = sum3(-1, -2, -3) + sum3(4, 5, 6);
...
}
sum3 PROC
EXPORT sum3
ADD r0, r0, r1 ; sum = a1 + a2
ADD r0, r0, r2 ; sum += a3
BX LR ; return in r0
ENDP

## Slide 23: ARM Procedure Call Standard
Register | Usage | Subroutine Preserved | Notes
r0 | Argument 1 and return value | No | If return has 64 bits, then r0:r1 hold it. If argument 1 has 64 bits, r0:r1 hold it.
r1 | Argument 2 | No | 
r2 | Argument 3 | No | If the return has 128 bits, r0-r3 hold it.
r3 | Argument 4 | No | If more than 4 arguments, use the stack
r4 | General-purpose V1 | Yes | Variable register 1 holds a local variable.
r5 | General-purpose V2 | Yes | Variable register 2 holds a local variable.
r6 | General-purpose V3 | Yes | Variable register 3 holds a local variable.
r7 | General-purpose V4 | Yes | Variable register 4 holds a local variable.
r8 | General-purpose V5 | Yes | Variable register 5 holds a local variable.
r9 | Platform specific/V6 | Yes/No | Usage is platform-dependent.
r10 | General-purpose V7 | Yes | Variable register 7 holds a local variable.
r11 | General-purpose V8 | Yes | Variable register 8 holds a local variable.
r12 (IP) | Intra-procedure-call register | No | It holds intermediate values between a procedure and the sub-procedure it calls.
r13 (SP) | Stack pointer | Yes | SP has to be the same after a subroutine has completed.
r14 (LR) | Link register | No | LR does not have to contain the same value after a subroutine has completed.
r15 (PC) | Program counter | N/A | Do not directly change PC

## Slide 24: Callee Saved Registers vs Caller Saved Registers
Callee can freely modify R0, R1, R2, and R3
If caller expects their values are retained, caller should push them onto the stack before calling the callee
Caller expects these values are retained .
If Callee modifies them, callee must restore their values upon leaving the function.
Caller Saved Registers
Callee Saved Registers

## Slide 25: Example: SSQ(3, 4)
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
...
int SSQ(int x, int y){
int z;
z = x*x + y*y;
return z;
}
R0: first argument
R1: second argument
R0: Return Value
Sum of Square:

## Slide 26: Example: SSQ(3, 4)
R0
R1
0x08000128
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOVS R0,#3
MOVS R1,#4
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...

## Slide 27: Example: SSQ(3, 4)
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
3
R0
R1
0x08000128
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOVS R0,#3
MOVS R1,#4
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 28: Example: SSQ(3, 4)
3
R0
4
R1
0x0800012C
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 29: Example: SSQ(3, 4)
3
R0
4
R1
0x08000130
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
LR
BX LR
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 30: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013B
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
R2
0x08000134
LR
BX LR
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
Address of the next instruction after the branch is saved into LR.
In fact, LR is 0x08000135 because bit 0 of PC should always be 1 for ARM Cortex-M to indicate thumb mode.
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 31: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013B
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
9
R2
0x08000134
LR
BX LR
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 32: Example: SSQ(3, 4)
3
R0
4
R1
0x0800013C
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
9
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 33: Example: SSQ(3, 4)
3
R0
4
R1
0x08000140
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 34: Example: SSQ(3, 4)
25
R0
4
R1
0x08000142
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 35: Example: SSQ(3, 4)
25
R0
4
R1
0x08000144
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 36: Example: SSQ(3, 4)
25
R0
4
R1
0x08000134
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
Copy LR to PC when returning from a subroutine!
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 37: Example: SSQ(3, 4)
25
R0
4
R1
0x08000134
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 38: Example: SSQ(3, 4)
25
R0
4
R1
0x08000136
PC
MOVS R0,R2
MUL R3,...
MOVS R2,R0
BL SSQ
MUL R2,...
B ENDL
ADD R2,R3
25
R2
0x08000134
LR
BX LR
16
R3
SSQ
MOVS R0,#3
MOVS R1,#4
MOVS R0,#3
MOVS R1,#4
BL SSQ
MOVS R2,R0
B ENDL
...
SSQ PROC
MUL R2,R0,R0
MUL R3,R1,R1
ADD R2,R2,R3
MOVS R0,R2
BX LR
ENDP
ENDL ...
0x08000128
0x0800012C
0x08000130
0x08000134
0x08000136
0x08000140
0x0800013B
0x0800013C
0x08000142
0x08000144
Memory Address

## Slide 39: Realities
In the previous example,
  PC is incremented by 2 or 4.
  The least significant bit of LR is always 0.
  Well, I lied!

## Slide 40: Realities
PC is always incremented by 4.
  Each time, 4 bytes are fetched from the instruction memory
  It is either two 16-bit instructions or one 32-bit instruction
    If bit [15-11] = 11101, 11110, or 11111, then, it is the first half-word of a 32-bit instruction. Otherwise, it is a 16-bit instruction.
The least significant bit of LR is always 1 for ARM Cortex-M
  This bit is used to control the processor mode:
    0 = ARM, 1 = THUMB
  Cortex-M only supports THUMB.

## Slide 41: Summary
How to call a subroutine?
  Branch with link: BL subroutine
How to return the control back to the caller?
  Branch and exchange: BX LR
How to pass arguments into a subroutine?
  Each 8-, 16- or 32-bit variables is passed via r0, r1, r2, r3
  Extra parameters are passed via stack
How to return a value in a subroutine?
  Value is returned in r0
How to preserve the running environment for the caller?
  (to be covered)

## Slide 42: Common Coding Patterns
Callee returns a constant in r0.
  mov r0,#17 @ r0 is return value register
  bx lr @ return from function
Callee saves some registers, does some arithmetic, and returns the result in r0.
  push {r4-r7,lr}
  mov r4, #10
  mov r5, #100
  add r0,r4,r5
  pop {r4-r7,pc} @ pop saved lr value into PC to return from function
Callee calls another function (nested function calls)
  push {lr} @ must save LR if we call our own function
  mov r0, #123 @ r0 is first function parameter
  bl print_int @ call function print_int(123)
  pop {pc} @ pop saved lr into PC to return from function
Callee return: restore previously-pushed LR, then jump to LR (POP {lr}; BX lr), or equivalently, pop previously-pushed LR to PC
  POP {pc} ≡ POP {lr}; BX lr
Notes: Because loading the PC from the stack both restores the return address and performs a branch, and BX is the branch that also restores the correct instruction set state.
POP {pc} is defined to read a word from [sp], increment sp, and write that value into PC; writing PC causes an immediate control-flow change to that address, effectively “returning” to the caller [this is how POP-with-PC is specified on ARM/Thumb].
POP {lr}; BX lr does the same in two steps: first restore the saved return address into LR from the stack, then branch-exchange to LR, which updates PC and switches to ARM or Thumb according to bit 0 of LR, just like a return via PC does.
Therefore, POP {pc} ≡ POP {lr}; BX lr, because both end with PC loaded from the saved return address and state (Thumb/ARM) determined by the low bit of that address.
https://developer.arm.com/documentation/dui0489/e/arm-and-thumb-instructions/memory-access-instructions/push-and-pop
https://developer.arm.com/documentation/dui0231/latest/thumb-instruction-reference/thumb-memory-access-instructions/push-and-pop
https://stackoverflow.com/questions/16622877/arm-assembly-instructions-pop-what-means-as-return-of-a-function
https://www.cs.uaf.edu/2012/fall/cs301/lecture/11_26_ARM.html
https://ad2001.gitbook.io/a-noobs-guide-to-arm-exploitation/introduction-to-arm
https://duetorun.com/blog/20230614/arm-stack-modes/
https://keleshev.com/compiling-to-assembly-from-scratch/07-arm-assembly-programming
https://azeria-labs.com/functions-and-the-stack-part-7/

## Slide 43: Common Coding Patterns
Memory access: first put memory address into register, then load memory content at that address
  adr r2, mydata @Compute address of label mydata using a PC‑relative add and put that address in r2
  ldr r0, [r2] @Dereference that address, loading the 32‑bit word stored at mydata into r0
  bx lr
  mydata:
  .word 123
Or
  ldr r2,=mydata @ pseudo‑instruction that loads absolute address of mydata from a nearby literal pool into r2
  ldr r0,[r2]
  bx lr
  mydata:
  .word 123
adr vs. ldr
  If mydata is in range for adr (c.f., ), both forms will leave r2 holding the same address at run time.
  Out‑of‑range labels: adr may fail; ldr =mydata still works, but it incurs one memory access
Note: pseudo-instruction LDR Rd, =X loads a value if X is a constant, and an address if X is a symbol,
  e.g., “LDR r2, =0x55555555” loads the value 0x55555555 from memory
Notes: https://www.cs.uaf.edu/2012/fall/cs301/lecture/11_26_ARM.html
It loads a PC‑relative address to a constant, reads the word stored there into r0, then returns.
adr r2, mydata: Compute the address of label mydata using a PC‑relative add and put that address in r2; adr is a pseudo‑instruction that forms a nearby address without touching memory.
ldr r0, [r2]: Dereference that address, loading the 32‑bit word stored at mydata into r0; after this, r0 = 123.
bx lr: Branch to the address in the link register (lr), i.e., return from the subroutine, preserving ARM/Thumb state via the low bit of lr.
mydata: .word 123: Assembles a 32‑bit literal 123 placed in the code/data section right after the code; adr targets this label so the code can read the literal at runtime.
Short answer: Not always. They can both put the address of mydata into r2, but they work differently and have different limits.
What adr does
adr r2, mydata computes the address of mydata relative to the current PC and places it in r2, producing position‑independent code.
It assembles to a single add/sub with PC and only works if mydata is within the encodable PC‑relative range for that instruction; otherwise it fails to assemble.
What ldr r2,=mydata does
ldr r2,=mydata is a pseudo‑instruction that typically loads the absolute address of mydata from a nearby literal pool into r2.
It is not limited by small PC‑relative ranges but costs an extra memory read and usually produces non‑position‑independent code unless using relocations suited for PIC.
When they are equivalent
If mydata is in range for adr, both forms will leave r2 holding the same address at run time.
When they differ
Out‑of‑range labels: adr may fail; ldr =mydata still works by using a literal pool entry.
Performance/side effects: adr is one instruction and no memory access; ldr =mydata fetches from memory and can be affected by literal pool placement and timing.
Code model: adr yields PC‑relative, PIC‑friendly code; ldr =mydata commonly yields absolute addresses unless assembled/linker‑relocated for PIC.
https://stackoverflow.com/questions/73851756/what-is-the-purpose-of-adr-instructions-in-arm
https://duetorun.com/blog/20230610/arm-adr-ldr/
https://en.eeworld.com.cn/news/mcu/eic302608.html
https://duetorun.com/blog/20230610/arm-adr2ldr/
https://www.youtube.com/watch?v=NJTlN2o2Xuo
https://www.youtube.com/watch?v=rvFqvlPukHg
https://stackoverflow.com/questions/73600196/why-use-adr-and-ldr-x2-var-to-get-the-address-of-a-variable
https://en.eeworld.com.cn/news/mcu/eic281184.html
https://developer.arm.com/documentation/dui0231/latest/writing-arm-and-thumb-assembly-language/loading-addresses-into-registers/direct-loading-with-adr-and-adrl
https://developer.arm.com/documentation/dui0489/latest/arm-and-thumb-instructions/adrl-pseudo-instruction

## Slide 44: References
Lecture 29. Calling a subroutine
  https://www.youtube.com/watch?v=xt2Q9n1Udb4&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=29
Lecture 30. Passing Arguments to a Subroutine
  https://www.youtube.com/watch?v=DGKjFKjxAYs&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=31