## Slide 1: CSC 112: Computer Operating Systems Lecture 7 Memory System I: Cache Exercises ANS
Department of Computer Science,
Hofstra University

## Slide 2: Cache Organization
# ways (associativity)
# sets
2
Tag | Set Index | Offset
#blocks = #ways * #sets
Use Set Index to select a set
Compare Tag to select a way
Tag
Data
(Valid bit omitted)
Use Offset to find Byte address within cache block
(Set Index increases from top to bottom)
Review
SI identifies a set; Tag identifies the block within the set; Offset identifies the byte within the block (if cache hit).

## Slide 3: Key Equations
5/14/2025
Offset
Tag
Set Index
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
SI size determines # sets = 2SI size
Offset size determines Bytes/block = 2Offset size
Tag size does not affect cache capacity; depends on memory address length
Review
3
Notes: Total # cache blocks = Associativity * # sets = #ways (blocks/set) × # sets × Bytes/block C = N × S × B

## Slide 4: Decimal, Binary and Hex
Decimal | Binary | Hex
0 | 0000 | 0x0
1 | 0001 | 0x1
2 | 0010 | 0x2
3 | 0011 | 0x3
4 | 0100 | 0x4
5 | 0101 | 0x5
6 | 0110 | 0x6
7 | 0111 | 0x7
8 | 1000 | 0x8
9 | 1001 | 0x9
10 | 1010 | 0xA
11 | 1011 | 0xB
12 | 1100 | 0xC
13 | 1101 | 0xD
14 | 1110 | 0xE
15 | 1111 | 0xF
Prefix 0x denotes hex
Review
4

## Slide 5: Quiz
Memory hierarchies take advantage of spatial locality by keeping the most recent data items closer to the processor.
  False. This is called temporal locality.
For a given cache size, a larger block size may cause lower hit rate than a smaller one.
  True. The relationship between block size and hit rate is non-monotonic. A large block size leads to fewer cache blocks, so it may cause lower hit rate since useless junk may be brought into cache along with useful data. But it may lead to higher hit rate if the program has good locality.
If you know your computer’s cache size, you can often make your code run faster.
  True. By tuning your code to be cache-aware.
5
Notes: If the block size gets too big, fetches become more expensive and the big blocks force out more useful data.

## Slide 6: Quiz
Q: How many 32-bit integers can be stored in a DM cache with 15 tag bits, 15 index bits, and 2 offset bits?
A: Each cache block is 2^2=4 Bytes and can store one 32-bit integer. The cache has a total number of 2^15=32K blocks, hence it can store 32K integers. (The tag bits are irrelevant here since it is related to memory size, not cache size)
6
Notes: Q: You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 32-line direct-mapped cache with 1 word blocks? (in hex)
A: The cache has TIO breakdown of 9:5:2 (1 word = 4 Bytes  2 Offset Bits; 32-line cache  5 Index Bits; 16-(5+2)=9 Tag Bits.) Memory address 0x3434 in binary is 0011010000110100 (Online hex converter: Online hex converter: http://easycalculation.com/hex-converter.php)
You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 16-line direct-mapped cache with 4 word blocks? (in hex)
You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 1kiB direct-mapped cache with 2 word blocks? (in hex)
What is the ratio of data bits to total bits in a 128 byte write-back direct-mapped cache that has 2-word blocks and is part of a 64-bit byte-addressed memory system?

## Slide 7: Quiz I
Q: Consider 32-bit address space; a direct-mapped cache with size 16KB;each cache block is 4 words. What is the TIO breakdown?
A:
Cache size = 16KB = 16 * 2^10 bytes
Cache block size = 4 words = 4 * 4 bytes = 16 bytes = 2^4
Number of cache blocks= 16 * 2^10 bytes / 16 bytes = 2^10
Index bits = 10
Offset bits = 4
Tag bits = 32 – 10 – 4 = 18
7

## Slide 8: Quiz II
Q: Consider 32-bit address space; a two-way set-associative cache with size 16KB;each cache block is 4 words. What is the TIO breakdown?
A:
Cache size = 16 * 2^10 bytes
cache block size = 16 bytes
Set size = cache block size * set associativity = 16 bytes * 2 = 32 bytes
Number of sets = 16 * 2^10 bytes / 32 bytes = 2^9
Index bits = 9
Offset bits = 4
Tag bits = 32 – 9 – 4 = 19
8

## Slide 9: Quiz
Q: Consider 32-bit address space; a DM cache with size 32 KB; each cache block is 8 words. What is the TIO breakdown?
ANS: T=17, I=10, O=5
  8-word per block => 32 bytes / block => O = 5
  32 KB / (32 bytes / block) = 2^10 blocks total => I = 10
  T = 32 – 10 – 5 = 17
Q: Consider 32-bit address space; a 4-way SA cache with size 32 KB; each cache block is 8 words. What is the TIO breakdown?
ANS: T=19, I=8, O=5 (Tag 19b, Index 8b, Offset 5b)
  8-word per block => 32 bytes / block => O = 5
  32 KB / (32 bytes / block) = 2^10 blocks total
  2^10 blocks / (4 blocks / set) = 2^8 sets total => I = 8
  T = 32 – 8 – 5 = 19
Q: Consider 32-bit address space; an FA cache with size 32 KB; each cache block is 8 words. What is the TIO breakdown?
  ANS: T=27, I=0, O=5
  8-word per block => 32 bytes / block => O = 5
  FA cache => I = 0
  T = 32 – 0 – 5 = 27
9
Notes: Index bits will index into sets
32-bit address space, 32 KB 4-way SA cache with 8-word blocks. What is the breakdown of TIO bits?
32-bit address space, 32 KB FA cache with 8-word blocks.

## Slide 10: Quiz
Q: Consider 32-bit address space; a DM cache with size 16 KB; each cache block is 4 words. What is the TIO breakdown?
ANS: T=18, I=10, O=4
  4-word per block => 16 bytes / block => O = 4
  16 KB / (16 bytes / block) = 2^10 blocks total => I = 10
  T = 32 – 10 – 4 = 18
Q: Consider 32-bit address space; a 2-way SA cache with size 16KB; each cache block is 4 words. What is the TIO breakdown?
ANS: T=19, I=9, O=4
  4-word per block => 16 bytes / block => O = 4
  16 KB / (16 bytes / block) = 2^10 blocks total
  2^10 blocks / (2 blocks / set) = 2^9 sets total => I = 9
  T = 32 – 9 – 4 = 19
Q: Consider 32-bit address space; an FA cache with size 16KB; each cache block is 4 words. What is the TIO breakdown?
  ANS: T=27, I=0, O=5
  4-word per block => 16 bytes / block => O = 4
  FA cache => I = 0
  T = 32 – 0 – 4 = 28
10
Notes: Cache size = 16 * 2^10 bytes
cache block size = 16 bytes
Set size = cache block size * set associativity = 16 bytes * 2 = 32 bytes
Number of sets = 16 * 2^10 bytes / 32 bytes = 2^9
Index bits = 9
Offset bits = 4
Tag bits = 32 – 9 – 4 = 19
A:
Cache size = 16KB = 16 * 2^10 bytes
Cache block size = 4 words = 4 * 4 bytes = 16 bytes = 2^4
Number of cache blocks= 16 * 2^10 bytes / 16 bytes = 2^10
Index bits = 10
Offset bits = 4
Tag bits = 32 – 10 – 4 = 18

## Slide 11: Q: 12-bit DM Cache
Consider 12-bit memory address; DM cache with block size 4B; total of 16 cache blocks, with contents shown below ("—“ means invalid data). All values are in hex. Within each block, B0 refers to Byte address 00, B1 refers to Byte address 01, and so on.
  1. What are the sizes of Tag, Set Index, Offset?
  2. Cache hit or miss for referencing the following memory addresses (individually, not sequentially) ? If cache hit, give the actual value returned: 0x7AC, 0x024, 0x99F
11
IMPORTANT

## Slide 12: A: 12-bit DM Cache
1. What are the sizes of Tag, Set Index, Offset?
# Bytes/block=4, hence Offset size=2
# Sets=(# Blocks for DM cache)=16, hence SI size=4
Tag size=12-4-2=6
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
12
IMPORTANT

## Slide 13: A: 12-bit DM Cache
2. Cache hit or miss for referencing the following memory addresses? If cache hit, give the actual value returned: 0x7AC, 0x024, 0x99F
0x7AC = 0111 1010 1100 (bin). Set Index=1011(bin)=0xB. The set with index 0xB has a single block with Valid=0, hence it is a cache miss (no need to check for tag match. Even though the table shows some data in this block, all data is invalid with Valid=0).
0x024 = 0000 0010 0100 (bin). Set Index=1001(bin)=0x9. The set with index 0x9 has a single block with Valid=1, and the Tag 000000 (bin) = 0x0 matches, hence it is a cache hit. The Byte offset is 00, hence the actual data returned is 0x01 contained in B0.
0x99F = 1001 1001 1111 (bin). Set Index=0111(bin)=0x7. The set with index 0x7 has a single block with Valid=0, hence it is a cache miss (no need to check for tag match).
13
IMPORTANT

## Slide 14: Q: 12-bit 2-way SA Cache
Consider 12-bit memory address; 2-way SA cache with block size 4B; total of 16 cache blocks with contents shown below ("—“ means invalid data). All values are in hex.
  1. What are the sizes of Tag, Set Index, Offset?
  2. If cache hit, give the actual value returned: 0x435, 0x388, 0x0D3
14
IMPORTANT

## Slide 15: A: 12-bit 2-way SA Cache
1. What are the sizes of Tag, Set Index, Offset?
# Bytes/block=4, hence Offset size=2
# Sets=#blocks/#ways=16/2=8, hence SI size=3
Tag size=12-3-2=7
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
15
IMPORTANT

## Slide 16: A: 12-bit 2-way SA Cache
2. Cache hit or miss for referencing the following memory addresses? If cache hit, give the actual value returned: 0x435, 0x388, 0x0D3
0x435 = 0100 0011 0101 (bin). Set Index=101(bin)=0x5. The set with index 0x5 has 2 blocks, but only one block with Valid=1. The Tag 0100001 (bin) = 0x21 matches the valid block Tag, hence it is a cache hit. The Byte offset is 01, hence the actual data returned is 0xAD contained in B1.
0x388 = 0011 1000 1000 (bin). Set Index=010(bin)=0x2. The set with index 0x2 has 2 blocks, both with Valid=1, but the Tag 0011100 (bin) = 0x1C does not match any valid block Tag (0x03, 0x0E), hence it is a cache miss.
0x0D3 = 0000 1101 0011 (bin). Set Index=100(bin)=0x4. The set with index 0x4 has 2 blocks, both with Valid=0, hence it is a cache miss (no need to check for tag match).
16
IMPORTANT

## Slide 17: Q: 12-bit FA Cache
Consider 12-bit memory address; FA cache with block size 4B; contents shown below ("—“ means invalid data). All values are in hex.
  1. What are the sizes of Tag, Set Index, Offset?
  2. If cache hit, give the actual value returned: 0x1DD, 0x719, 0x2AA
17
IMPORTANT

## Slide 18: A: 12-bit FA Cache
1. What are the sizes of Tag, Set Index, Offset?
# Bytes/block=4, hence Offset size=2
# Sets=1 for FA cache, hence SI size=0
Tag size=12-0-2=10
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
18
IMPORTANT

## Slide 19: A: 12-bit FA Cache
2. Cache hit or miss for referencing the following memory addresses? If cache hit, give the actual value returned: 0x1DD, 0x719, 0x2AA
0x1DD = 00001 1101 1101 (bin). The Tag 00001110111 (bin) = 0x77, which matches a block with Valid=1, hence it is a cache hit. The Byte offset is 01, hence the actual data returned is 0x23 contained in B1
0x719 = 0111 0001 1001 (bin). The Tag 0111000110 (bin) = 0x1C6, which matches a block with Valid=1, hence it is a cache hit. The Byte offset is 01, hence the actual data returned is 0x11 contained in B1
0x2AA = 0010 1010 1010 (bin). The Tag 0010101010 (bin) = 0xAA, which does not match any block with Valid=1, hence it is a cache miss.
19
IMPORTANT

## Slide 20: Question: Tag
Assume: DM cache; 6-bit memory address: 2-bit Tag, 2-bit index, 2-bit Offset. Compute cache capacity and memory size.
  2-bit Offset => Bytes/block = 4;
  # sets = 2SI Size = 4
  # cache blocks = # ways * # sets = 1*4 = 4
  cache capacity = # cache blocks * Bytes/block = 4*4 = 16B
Memory size: 2^4 (2-bit tag +2-bit SI) = 16 blocks = 64 Bytes
0
5
1
Byte Within Block
Offset
2
3
Block Within $
4
Mem Block Within $Block
Tag
Set Index
5/14/2025
# ways = # blocks/cache set = associativity
# cache blocks = # ways * # sets
cache capacity = # cache blocks * Bytes/block
Recall:
20
Notes: 16 Memory blocks = 16 words = 64 bytes => 6 bits to address all bytes (Memory and cache blocks always have the same size) 4 Cache blocks, 4 bytes (1 word) per block
4 sets *1 block per set (direct mapped cache) = 4 blocks =
# Memory blocks (16) >> # Cache blocks (4)
  4 Memory blocks map to each cache block
Given a memory block, how to determine which cache set it is mapped to?
  Look at Set Index: middle two bits
A cache set may contain 1 of 4 possible memory blocks, which exact memory block is mapped to it?
  Look at tag: top two bits

## Slide 21: Question: T-SI-O Distribution
Consider 32-bit memory address, DM cache with size 64KB, 16 Bytes/block. What are the bit-widths of Tag-SetIndex-Offset?
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
21

## Slide 22: Answer: T-SI-O Distribution
Consider 32-bit memory address, DM cache with size 64KB, 16 Bytes/block. What are the bit-widths of Tag-Set Index-Offset?
A: 16 Bytes/block  Offset size=4
For DM cache, # Sets = # blocks = 64 KB/16 Bytes/block = 4K  SI size=12
Tag size = 32-12-4=16
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
22

## Slide 23: Question: T-SI-O Distribution
Consider 32-bit memory address, 8-way SA cache with size 64KB, 16 Bytes/block. What are the bit-widths of Tag-Set Index-Offset?
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
23

## Slide 24: Answer: T-SI-O Distribution
Consider 32-bit memory address, 8-way SA cache with size 64KB, 16 Bytes/block. What are the bit-widths of Tag-Set Index-Offset?
A: 16 Bytes/block  Offset size=4
For 8-way SA cache, # Sets = # blocks/8 = (64 KB/16 Bytes/block)/8 = 0.5K  SI size=9
Tag size = 32-9-4=19
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
24

## Slide 25
0 1 2 3
Set Number
Cache
(4 blocks)
DM 2-way SA FA (4-way SA)
In set ? In set ? In set ?
(? blocks) (? blocks) (? blocks)
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
(32 blocks)
Block Number
Q: Alternative Cache Organizations (4-block cache）
Where are possible locations in cache that block #12 in memory can be placed?
0 1 0 1
0
# ways = # blocks/cache set = associativity
# cache blocks = # ways * # sets
cache capacity = # cache blocks * Bytes/block
Recall:
25
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?
(12 mod 4=0) (12 mod 2=0)

## Slide 26
Memory size is 2^5=32 blocks, so memory address is 5 bits (excluding offset)
Memory block #12 (decimal) corresponds to memory address 01100XXXX in binary (we don’t care about block size, so XXXX may be anything like 2, 3, 4…bits)
For DM cache:
  # cache blocks = 4 = # ways (1) * # sets
  => # sets = 4 = 22 => Set Index has 2b => Set Index is 00 (last 2b in 01100)
  Tag (3b); Set Index (2b)
For 2-way SA cache:
  # cache blocks = 4 = # ways (2) * # sets
  => # sets = 2 = 21 => Set Index has 1b => Set Index is 0 (last 1b in 01100)
  Tag (4b); Set Index (1b)
For FA (4-way SA) cache:
  # cache blocks = 4 = # ways (4) * # sets
  => # sets = 1 = 20 => No Set Index
  Tag (5b)
A: Alternative Cache Organizations (4-block cache）
# ways = # blocks/cache set = associativity
# cache blocks = # ways * # sets
cache capacity = # cache blocks * Bytes/block
Recall:
26

## Slide 27
0 1 2 3
Set Number
Cache
(4 blocks)
DM 2-way SA FA (4-way SA)
In set 0 In set 0 In set 0
(1 block) (2 blocks) (4 blocks)
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
(32 blocks)
Block Number
A: Alternative Cache Organizations (4-block cache）
Where are possible locations in cache that block #12 in memory can be placed?
0 1 0 1
0
# ways = # blocks/cache set = associativity
# cache blocks = # ways * # sets
cache capacity = # cache blocks * Bytes/block
Recall:
27
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?
(12 mod 4=0) (12 mod 2=0)

## Slide 28
Set Number
Cache
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Block Number
Q: Alternative Cache Organizations（8-block cache）
Where are possible locations in cache that block #12 in memory can be placed?
DM 2-way SA 4-way SA FA(8-way SA)
In set ? In set ? In set ? In set ?
(? block) (? blocks) (? blocks) (? blocks)
0 1 2 3
4
5
6
7
0 1 2 3
0
1
2
3
0 1 0 1
0
1
0
1
0
# ways = # blocks/cache set = associativity
# cache blocks = # ways * # sets
cache capacity = # cache blocks * Bytes/block
Recall:
28
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?
(12 mod 8=4) (12 mod 4=0) (12 mod 2=0)

## Slide 29
Memory block #12 (decimal) corresponds to memory address 01100XXXX in binary (we don’t care about block size)
For DM cache:
  # cache blocks = 8 = # ways (1) * # sets
  => # sets = 8 = 23 => Set Index has 3b => Set Index is 100 (4) (last 3b in 01100)
  Tag (2b); Set Index (3b)
For 2-way SA cache:
  # cache blocks = 8 = # ways (2) * # sets
  => # sets = 4 = 22 => Set Index has 2b => Set Index is 00 (last 2b in 01100)
  Tag (3b); Set Index (2b)
For 4-way SA cache:
  # cache blocks = 8 = # ways (4) * # sets
  => # sets = 2 = 21 => Set Index has 1b => Set Index is 0 (last 1b in 01100)
  Tag (4b); Set Index (1b)
For FA (8-way SA) cache:
  # cache blocks = 8 = # ways (8) * # sets
  => # sets = 1 = 20 => No Set Index
  Tag (5b)
A: Alternative Cache Organizations (8-block cache）
# ways = # blocks/cache set = associativity
# cache blocks = # ways * # sets
cache capacity = # cache blocks * Bytes/block
Recall:
29

## Slide 30
Set Number
Cache
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Block Number
A: Alternative Cache Organizations（8-block cache）
Where are possible locations in cache that block #12 in memory can be placed?
DM 2-way SA 4-way SA FA(8-way SA)
In set 4 In set 0 In set 0 In set 0
(1 block) (2 blocks) (4 blocks) (8 blocks)
0 1 2 3
4
5
6
7
0 1 2 3
0
1
2
3
0 1 0 1
0
1
0
1
0
# ways = # blocks/cache set = associativity
# cache blocks = # ways * # sets
cache capacity = # cache blocks * Bytes/block
Recall:
30
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?
(12 mod 8=4) (12 mod 4=0) (12 mod 2=0)

## Slide 31
# cache blocks = 32; Block #12 in decimal is 01100 in binary
For DM cache: Tag (2b); Set Index (3b)
  Set Index=100, hence it is set 4 (1 block)
For 2-way SA cache: Tag (3b); Set Index (2b)
  Set Index=00, hence it is set 0 (2 blocks)
For 4-way SA cache: Tag (4b); Set Index (1b)
  Set Index=0, hence it is set 0 (2 blocks)
For FA (8-way SA) cache: Tag (5b)
  Can be anywhere for SA cache
A: Alternative Cache Organizations (4-block cache）
# ways = # blocks/cache set = associativity
# cache blocks = # ways * # sets
cache capacity = # cache blocks * Bytes/block
Recall:
31

## Slide 32: Question: Cache Address Mapping
What are the possible locations in the cache that memory address 0x1833 (0b0001 1000 0011 0011) be mapped? Assuming: 16-bit memory address, Bytes/block=16, # cache blocks=8
For DM cache:
For 2-way SA cache:
For 4-way SA cache:
For FA cache (8-way SA):
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
DM
2-way SA
4-way SA
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
0 |  | 
1 |  | 
0 |  | 
1 |  | 
0 |  | 
1 |  | 
FA (8-way SA)
Set | Tag | Data
0 |  | 
1 |  | 
0 |  | 
1 |  | 
0 |  | 
1 |  | 
0 |  | 
1 |  | 
32
Notes: block size:
16 B
capacity:
8 blocks
address:
16 bits

## Slide 33: Answer: Cache Address Mapping
What are the possible locations in the cache that memory address 0x1833 (0b0001 1000 0011 XXXX) be mapped? Assuming: 16-bit memory address, Bytes/block=16, # cache blocks=8
For DM cache: Tag (9b); Set Index (3b); Offset (4b)
  Set Index=011, hence it is set 3 (1 block)
For 2-way SA cache: Tag (10b); Set Index (2b); Offset (4b)
  Set Index=11, hence it is set 3 (2 blocks)
For 4-way SA cache: Tag (11b); Set Index (1b); Offset (4b)
  Set Index=1, hence it is set 1 (4 blocks)
For FA cache (8-way SA): Tag (12b); Offset (4b)
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
DM
2-way SA
4-way SA
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
0 |  | 
1 |  | 
0 |  | 
1 |  | 
0 |  | 
1 |  | 
FA (8-way SA)
Set | Tag | Data
0 |  | 
0 |  | 
0 |  | 
0 |  | 
0 |  | 
0 |  | 
0 |  | 
0 |  | 
33
Notes: block size:
16 B
capacity:
8 blocks
address:
16 bits

## Slide 34: Question: Cache Capacity 1
Work out the cache capacity :
0
N-1
1
O
2
3
4
Tag
S.I
0
N-1
1
2
3
Tag
S.I
0
N-1
1
2
Tag
DM
2 Way SA
4-way SA (FA)
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
O
O
34

## Slide 35: Answer: Cache Capacity 1
Work out the cache capacity :
0
N-1
1
2
3
4
Tag
S.I
0
N-1
1
2
3
Tag
S.I
0
N-1
1
2
Tag
  # cache blocks = 1 way * 2^2 sets = 4 blocks
  cache capacity = 4 blocks * 4B/block = 16B
DM
2 Way SA
4-way SA
  # cache blocks = 2 ways * 2^1 sets = 4 blocks
  cache capacity = 4 blocks * 4B/block = 16B
  # cache blocks = 4 ways * 2^0 sets = 4 blocks
  cache capacity = 4 blocks * 4B/block = 16B
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
O
O
O
(Just saying FA is not enough to determine cache capacity!)
35

## Slide 36: Question: Cache Capacity 2
Q: What is the cache capacity of a DM cache with 15 Tag bits, 15 Set Index bits, and 2 Offset bits?
Q: What is the cache capacity of a 2-way SA cache with 15 Tag bits, 15 Set Index bits, and 2 Offset bits?
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
36
Notes: Q: You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 32-line direct-mapped cache with 1 word blocks? (in hex)
A: The cache has TIO breakdown of 9:5:2 (1 word = 4 Bytes  2 Offset Bits; 32-line cache  5 Index Bits; 16-(5+2)=9 Tag Bits.) Memory address 0x3434 in binary is 0011010000110100 (Online hex converter: Online hex converter: http://easycalculation.com/hex-converter.php)
You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 16-line direct-mapped cache with 4 word blocks? (in hex)
You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 1kiB direct-mapped cache with 2 word blocks? (in hex)
What is the ratio of data bits to total bits in a 128 byte write-back direct-mapped cache that has 2-word blocks and is part of a 64-bit byte-addressed memory system?

## Slide 37: Answer: Cache Capacity 2
Q: What is the cache capacity of a DM cache with 15 Tag bits, 15 Set Index bits, and 2 Offset bits?
A: Bytes/block = 22; # sets = 215; # cache blocks = 1 way * 215 = 215; cache capacity = 215 blocks * 22 Bytes/block=217 Bytes
Q: What is the cache capacity of a 2-way SA cache with 15 Tag bits, 15 Set Index bits, and 2 Offset bits?
A: Bytes/block = 22; # sets = 215; # cache blocks = 2 ways * 215 = 216; cache capacity = 216 blocks * 22 Bytes/block=218 Bytes
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
37
Notes: Q: You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 32-line direct-mapped cache with 1 word blocks? (in hex)
A: The cache has TIO breakdown of 9:5:2 (1 word = 4 Bytes  2 Offset Bits; 32-line cache  5 Index Bits; 16-(5+2)=9 Tag Bits.) Memory address 0x3434 in binary is 0011010000110100 (Online hex converter: Online hex converter: http://easycalculation.com/hex-converter.php)
You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 16-line direct-mapped cache with 4 word blocks? (in hex)
You are trying to access memory byte address 0x3434 in a system with a 16 bit address space. What are the corresponding tag, index and offset for a 1kiB direct-mapped cache with 2 word blocks? (in hex)
What is the ratio of data bits to total bits in a 128 byte write-back direct-mapped cache that has 2-word blocks and is part of a 64-bit byte-addressed memory system?

## Slide 38: Answer: Cache Capacity 3
For a cache of 64 blocks, each block 4 Bytes in size:
The capacity of the cache is: _256_ bytes.
Given a 2-way SA organization, there are _32_ sets, each of _2_ blocks, and _2_ places a block from memory could be placed.
Given a 4-way SA organization, there are _16_ sets each of _4_ blocks and _4_ places a block from memory could be placed.
Given an 8-way SA organization, there are _8_ sets each of _8_ blocks and _8_ places a block from memory could be placed.
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
38

## Slide 39: Question: Cache Capacity 4
For an N-way SA cache, # cache blocks = B, # sets = S, which statements hold?
(i) The cache has B number of tags
(ii) The cache needs N comparators
(iii) B = N x S
(iv) Size of Set Index (in # bits) = Log2(S)
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
39

## Slide 40: Answer: Cache Capacity 4
For an N-way SA cache, # cache blocks = B, # sets = S, which statements hold true?
(i) The cache has B number of tags
(ii) The cache needs N comparators
(iii) B = N x S
(iv) Size of Set Index (in # bits) = Log2(S)
ANS: All statements are true
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
40
Notes: (ii) The cache needs N comparators
(iii) B = N x S

## Slide 41
32 bit address space, 32KB 4-way SA cache with 8-word blocks. What are the lengths of Tag - Set Index - Offset in the memory address?
ANS: T – 19, SI – 8, O – 5
Bytes/block=8 words=32B => Offset is 5b
cache capacity (32KB) = # cache blocks*32B/block
=> # cache blocks = 1K = 210
# cache blocks (210) = # ways (4) * # sets
=> # sets = 28 => Set Index has 8b
Memory address length (32)
=> T = 32b – (8b+5b) = 19b
Q. Bits in Memory Address 1
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
41
Notes: 8 word blocks => 32 bytes / block => BO = 5
32 KB / (32 bytes / block) = 2^10 blocks total
2^10 blocks / (4 blocks / set) = 2^8 sets total
Index bits will index into sets => I = 8

## Slide 42: Q. Bits in Memory Address 2
32 bit address space, 16KB DM cache with 4-word blocks. What are the lengths of Tag - Set Index - Offset?
ANS: T - 18, SI – 10, O – 4
Bytes/block=4 words=16B => Offset is 4b
cache capacity (16KB) = # cache blocks*16B/block
=> # cache blocks = 1K = 210
# cache blocks (210) = # ways (1) * # sets
=> # sets = 210 => Set Index has 10b
Memory address length (32)
=> T = 32b – (10b+4b) = 18b
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
42
Notes: 8 word blocks => 32 bytes / block => BO = 5
32 KB / (32 bytes / block) = 2^10 blocks total
2^10 blocks / (4 blocks / set) = 2^8 sets total
Index bits will index into sets => I = 8

## Slide 43: Q. Bits in Memory Address 3
We have a cache of size 2 KB with block size of 128 Bytes. If our cache has 2 sets, what is its associativity? If memory address is 16 bits, how wide is the Tag field?
Bytes/block=128B = 27B => Offset has 7b
cache capacity (2KB=211B) = # cache blocks*27B/block
=> # cache blocks = 16 = 24
# cache blocks (16) = # ways * # sets (2)
# ways = 8 = 23
Set Index has 1b
Memory address length (16) = T + SI + O
=> T = 16b – (1b+7b) = 8b
# sets = 2SI size; # Bytes/block=2Offset size
# blocks = # ways (associativity) * # sets
cache capacity = # blocks * # Bytes/block
Recall:
43

## Slide 44
32 bit address space, 32KB DM cache with 8-word blocks
32 bit address space, 16KB 2-way SA cache with 4-word blocks
32 bit address space, 32KB FA cache with 8-word blocks
Question: Bits in Memory Address 4
44

## Slide 45
32 bit address space, 32KB DM cache with 8-word blocks
T - 17, SI - 10, O – 5 (# blocks = # sets = 210 => SI has 10b, T = 32b–(10b+5b)=17b)
32 bit address space, 16KB 2-way SA cache with 4-word blocks
T - 19, SI - 9, O – 4 (# blocks = 210; # sets = 210/2=29 => SI has 9b, T = 32b–(9b+4b)=19b)
32 bit address space, 32KB FA cache with 8-word blocks
T - 27, SI - 0, O – 5 (# blocks = 210; # sets = 1 => SI has 0b, T = 32b–(0b+5b) = 27b)
Answer: Bits in Memory Address 4
45

## Slide 46: Question: Associativity 1
For a cache with fixed total size, if we increase the number of ways by a factor of two, which statement is false:
A : The number of sets is halved
B : The tag width decreases
C : The block size stays the same
D : The set index decreases
5/14/2025
46

## Slide 47: Answer: Associativity 1
For a cache with fixed total size, if we increase the number of ways by a factor of two, which statement is false:
A : The number of sets is halved
B : The tag width decreases
C : The block size stays the same
D : The set index width decreases
5/14/2025
More Associativity (more ways)
Offset
Tag
Set Index
47

## Slide 48: Question: Associativity 2
5/14/2025
Offset
Tag
Set Index
Push red bar right 1 bit
tag_size ?; index_size?; # sets?; # ways/associativity ?;
# HW comparators ?
Push red bar left 1 bit
tag_size ?; index_size ?; # sets ?; # ways/associativity ?;
# HW comparators ?
48

## Slide 49: Answer: Associativity 2
Push red bar right 1 bit
tag_size +1; index_size -1; # sets halved; # ways/associativity doubled;
# HW comparators doubled
Push red bar left 1 bit
tag_size -1; index_size +1; # sets doubled; # ways/associativity halved;
# HW comparators halved
5/14/2025
More associativity (more ways)
Offset
Tag
Set Index
Less associativity (fewer ways)
49

## Slide 50: Question: Associativity vs. Performance
For a cache of fixed capacity and block size, increasing associativity causes __________ in hit time, and __________ in miss rate
5/14/2025
50

## Slide 51: Answer: Associativity vs. Performance
For a cache of fixed capacity and block size, increasing associativity causes _increase_ in hit time, and _decrease_ in miss rate
5/14/2025
51

## Slide 52: Question: Tag bits & Offset bits
Q: Under what condition will we have # Offset bits = 0? Under what condition will we have # Tag bits = 0?
A: # Offset bits = 0 when size of a cache block = 1 Byte
  (not realistic, since it cannot even fit a 16b short or 32b int)
# Tag bits = 0 when we have a DM cache with the same size as memory
  Tag bits are needed to disambiguate among multiple possible memory blocks that may be mapped to one cache block; if there is a 1-to-1 correspondence between cache blocks and memory blocks, then Tag bits are not needed
  (not realistic, since cache must be small in order to be fast)
Main Memory
Cache
Offset
Set Index
52