## Slide 1: CSC 144V: Autonomous Vehicles Lecture 1.1 Introduction Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: SAE levels
For each description, state the SAE level of automation (0–5) and who is responsible for monitoring the driving environment while the feature is engaged (human or system).
# | Description | SAE level | Who monitors the environment?
1 | A highway package that keeps the lane and the speed at the same time. The driver must keep eyes on the road and be ready to steer at any moment. |  | 
2 | A traffic-jam pilot that drives itself below 60 km/h. The driver may read a book, but must take over when the system issues a takeover request. |  | 
3 | A driverless robotaxi without a safety driver that operates only inside a geo-fenced downtown area, in daylight and good weather. |  | 
4 | A vehicle that can drive anywhere and in any condition a human driver can, with no steering wheel and no pedals. |  | 

## Slide 3: Exercise Solution: SAE levels
Level 2: the system steers and controls speed, but the human supervises (monitors) at all times.
Level 3: the system monitors while engaged, but may ask the human to intervene (takeover request).
Level 4: no human fallback, but limited to its ODD (geo-fence, daylight, good weather).
Level 5: unlimited ODD — drives anywhere a human can.
# | Description | SAE level | Who monitors the environment?
1 | A highway package that keeps the lane and the speed at the same time. The driver must keep eyes on the road and be ready to steer at any moment. | Level 2 | Human
2 | A traffic-jam pilot that drives itself below 60 km/h. The driver may read a book, but must take over when the system issues a takeover request. | Level 3 | System (human must be ready to take over)
3 | A driverless robotaxi without a safety driver that operates only inside a geo-fenced downtown area, in daylight and good weather. | Level 4 | System
4 | A vehicle that can drive anywhere and in any condition a human driver can, with no steering wheel and no pedals. | Level 5 | System