## Slide 1: CSC 144V: Autonomous Vehicles Lecture 1.2 AV Sensors and V2X Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: Sensor data rates
A 128-channel lidar produces 1,800 azimuth measurements per channel per revolution and rotates at 10 Hz; each point takes 16 bytes.
A camera has 1920 × 1080 pixels, 3 bytes per pixel (uncompressed RGB) and runs at 30 frames per second.
Use 1 MB = 10⁶ bytes.
(i) Data rate of the lidar in MB/s?
(ii) Data rate of one camera in MB/s?
(iii) An AV carries 8 such cameras and 1 such lidar: total rate in GB/s, and raw TB per hour of driving?
Item | Data rate
Lidar | 
1 camera | 
8 cameras + 1 lidar | 
1 hour of driving | 

## Slide 3: Exercise Solution: Sensor data rates
Lidar: 128 × 1,800 × 10 = 2,304,000 points/s; × 16 B = 36,864,000 B/s
Camera: 1920 × 1080 × 3 B = 6,220,800 B per frame; × 30 fps = 186,624,000 B/s
Total: 8 × 186.6 + 36.9 ≈ 1,530 MB/s
Per hour: 1.53 GB/s × 3,600 s ≈ 5.5 × 10¹² B
One raw camera stream is about 5× the lidar stream: cameras dominate the raw data volume.
Item | Data rate
Lidar | 36.9 MB/s
1 camera | 186.6 MB/s
8 cameras + 1 lidar | 1.53 GB/s
1 hour of driving | ≈ 5.5 TB

## Slide 4: Exercise: Blind curve and V2X
A disabled vehicle is stopped behind a blind curve. Your AV drives at 30 m/s (108 km/h). Its onboard sensors can first detect the stopped vehicle at a distance of 60 m. The total latency from detection to the start of braking is 0.2 s; the AV then brakes with a constant deceleration of 6 m/s².
(i) Compute the total stopping distance.
(ii) Can the AV stop in time using onboard sensors only? Name one V2X communication that could help, and explain why in one sentence.
0 m
(detect)
X
stopped vehicle at 60 m
60 m

## Slide 5: Exercise Solution: Blind curve and V2X
Distance during the latency: 30 × 0.2 = 6 m; braking distance: v²/(2a) = 30²/(2 × 6) = 75 m; total = 6 + 75 = 81 m.
81 m > 60 m, so No. After the 6 m latency distance only 54 m remain, and the AV still hits the vehicle at v = √(30² − 2 × 6 × 54) = √252 ≈ 15.9 m/s ≈ 57 km/h.
V2V warning from the disabled vehicle (DSRC or C-V2X direct): low latency, no line of sight needed, range of several hundred metres, so the warning arrives well before 81 m.
0 m
(detect)
X
stopped vehicle at 60 m
6 m latency
75 m braking
81 m
(stop)