## Slide 1: CSC 144V: Autonomous Vehicles Lecture 1.3 HW/SW Platforms and Ethics Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: Compute platforms
For each requirement, choose the best compute platform (CPU, GPU, FPGA or ASIC/NPU) and give a one-sentence reason.
# | Requirement | Platform | Reason (one sentence)
1 | Batch-1 camera DNN inference with low and deterministic latency; the network may be updated after the vehicle is deployed. |  | 
2 | Mass-produced vehicle with a fixed DNN, where power and cost per TOPS matter most. |  | 
3 | Highly parallel matrix multiplication for large-batch DNN throughput. |  | 
4 | Control-flow-heavy general software: operating system, task scheduling, planning logic. |  | 

## Slide 3: Exercise Solution: Compute platforms
# | Requirement | Platform | Reason (one sentence)
1 | Batch-1 camera DNN inference with low and deterministic latency; the network may be updated after the vehicle is deployed. | FPGA | Low, deterministic latency at batch 1; reprogrammable after deployment.
2 | Mass-produced vehicle with a fixed DNN, where power and cost per TOPS matter most. | ASIC / NPU | Most power- and cost-efficient per TOPS at volume; the price is lost flexibility.
3 | Highly parallel matrix multiplication for large-batch DNN throughput. | GPU | Many parallel compute elements suit matrix multiplication (large batches raise throughput but also latency).
4 | Control-flow-heavy general software: operating system, task scheduling, planning logic. | CPU | Flexible; strong at sequential control flow, OS and scheduling code.

## Slide 4: Exercise: AUTOSAR
Choose AUTOSAR Classic or AUTOSAR Adaptive for each function and give one reason.
(i) The steering-actuator control loop on a resource-constrained ECU.
(ii) A perception service on a high-performance multicore ECU that receives service updates over the network.

## Slide 5: Exercise Solution: AUTOSAR
(i) Classic: hard real-time, statically configured, signal-based (OSEK) software for resource-constrained, safety-critical ECUs.
(ii) Adaptive: runs on high-performance multicore ECUs (POSIX), dynamically configured, service-oriented communication (SOME/IP), and can be updated at run time.
 | AUTOSAR Classic | AUTOSAR Adaptive
Target ECU | Resource-constrained microcontrollers | High-performance multicore
Operating system | OSEK, hard real-time | POSIX
Configuration | Static | Dynamic
Communication | Signal-based | Service-oriented (SOME/IP)
Updates | Fixed at build time | Updatable at run time

## Slide 6: Exercise: Trolley problem
Trolley variant with a probability threshold.
Option A: you kill a pedestrian with probability 1, but it is not your fault.
Option B: you kill a different pedestrian with probability p, and it is your fault.
You choose A if p ≥ p_thr, otherwise B.
(i) Your threshold is p_thr = 0.3 and p = 0.5. Which option do you choose?
(ii) According to the lecture, what has actually caused AV accidents in recent years, rather than trolley-problem-style choices?

## Slide 7: Exercise Solution: Trolley problem
(i) p = 0.5 ≥ p_thr = 0.3, so choose A (kill with probability 1, but not at fault). The threshold encodes how much extra weight is given to “my fault” versus certain harm.
(ii) Failures in sensors or perception algorithms; none of the recent AV accidents involved an ethical decision of the trolley type.