## Slide 1: CSC 144V: Autonomous Vehicles Lecture 4.2 Adversarial Attacks for AD Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: Tracker and max_age
A Kalman tracker runs at 10 Hz with max_age = 5: a track that is unmatched for more than 5 consecutive frames is deleted. Between matches the track is predicted forward with a constant-velocity model.
(a) For how many consecutive frames must the attacker suppress the detections of an object to delete its track? How many seconds is that?
(b) Suppressing 2 frames: is the track deleted?
(c) Per-frame suppression succeeds with probability p (independent frames). What is the probability that 6 consecutive frames are all suppressed?
p (per frame) | P(6 frames suppressed)
0.8 | 
0.9 | 
0.98 | 

## Slide 3: Exercise Solution: Tracker and max_age
(a) Deleted when unmatched > 5 frames: 6 frames = 0.6 s (5 frames are still survived).
(b) No. The filter predicts through the gap and re-matches the next detection; nothing changes.
(c) P = p⁶: p = 0.8 → 0.26; p = 0.9 → 0.53; p = 0.98 → 0.89.
A detection attack that works only 90 % of the time deletes the track just half of the time: attacks must reason about association and track management (Jia et al.: > 98 % detection success may be needed).
p (per frame) | P(6 frames suppressed)
0.8 | 0.26
0.9 | 0.53
0.98 | 0.89

## Slide 4: Exercise: LiDAR spoofing delay
A LiDAR measures R = c·Δt/2 (c = 3 × 10⁸ m/s). An attacker’s photodiode detects the outgoing pulse, waits a delay τ, then fires a spoofed return. The attacker is at distance d = 20 m from the LiDAR (assume zero electronics delay).
(a) What round-trip time Δt does the LiDAR measure for the spoofed return, and what apparent range R follows?
(b) Compute τ so that a phantom appears at 35 m, in the ego lane.
(c) Can this attacker make a phantom appear at 15 m? Why or why not?

## Slide 5: Exercise Solution: LiDAR spoofing delay
(a) The pulse needs d/c to reach the attacker, then τ, then d/c back: Δt = 2d/c + τ, so R = d + cτ/2.
(b) 35 = 20 + (3 × 10⁸ · τ)/2 → τ = 15 / (1.5 × 10⁸) = 100 ns.
(c) No (for a reactive attacker): the earliest possible return is τ = 0, i.e. R = d = 20 m. A closer phantom would need the return to arrive before the pulse reached the attacker.
The sensor trusts any return with the right wavelength and timing; the delay τ chooses the apparent range.

## Slide 6: Exercise: Attack taxonomy
Levels of attack success: 1 model-output error, 2 persistent perception failure (survives tracking and fusion), 3 closed-loop safety violation (collision, lane departure).
For each attack, fill in what the attacker modifies, which stage is attacked, and the highest level shown.
Attack | What the attacker modifies | Stage attacked | Highest level shown
Laser spoofing (CCS 2019) |  |  | 
Dynamic patch vs. MOT |  |  | 
Dirty road patch |  |  | 
Acero |  |  | 

## Slide 7: Exercise Solution: Attack taxonomy
Levels: 1 model-output error, 2 persistent perception failure, 3 closed-loop safety violation.
Dirty road patch: > 97.5 % success, 100 % collision rate in software-in-the-loop and on a real vehicle. Acero: 73.3 % of attacks end in a collision (simulation). Adversarial training and sensor checks are irrelevant to Acero: no pixel, point or signal is modified.
Attack | What the attacker modifies | Stage attacked | Highest level shown
Laser spoofing (CCS 2019) | Injected LiDAR points | LiDAR detection | Level 1
Dynamic patch vs. MOT | Pixels (adversarial patch) | Detection + tracking | Level 1–2
Dirty road patch | Road appearance (physical patch) | Lane detection → steering | Level 3
Acero | Nothing: normal-looking driving maneuvers | Planning / control of the victim | Level 3

## Slide 8: Exercise: Lane-centering toy model
Toy model (Dirty Road Patch): speed 15 m/s, lane half-width 1.8 m, car half-width 0.95 m. A road patch biases the perceived lane center by b; the controller faithfully tracks the perceived center. Assume the car drifts laterally toward the wrong center at 0.3 m/s.
(a) What is the lateral margin before a wheel crosses the lane boundary?
(b) After how many seconds does the car cross the boundary, and how far has it travelled?
(c) Does the car leave the lane for b = 1.4 m? For b = 0.5 m? (The car ends up offset by b.)

## Slide 9: Exercise Solution: Lane-centering toy model
(a) Margin = 1.8 − 0.95 = 0.85 m.
(b) t = 0.85 / 0.3 ≈ 2.8 s; distance = 15 × 2.83 ≈ 42.5 m.
(c) b = 1.4 m > 0.85 m: leaves the lane. b = 0.5 m < 0.85 m: stays inside (margin only 0.35 m left).
The attack objective must be defined on the control error (does the car cross the line?), and evaluated with a vehicle model in the loop, not on the lane-detection error alone.