## Slide 1: CSC 144V: Autonomous Vehicles Lecture 4.3 Latency and Availability Attacks Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: Delay becomes distance
An AV drives at 25 m/s (90 km/h) and brakes with a = 6 m/s². Normal perception latency is 50 ms; a latency attack adds 250 ms (300 ms in total). An obstacle becomes detectable at 58 m.
(a) How far does the AV travel blind because of the extra 250 ms (d = v·Δt)?
(b) Stopping distance (latency distance + v²/2a) without and with the attack?
(c) Does the AV hit the obstacle in each case? If so, at what speed?

## Slide 3: Exercise Solution: Delay becomes distance
(a) d = 25 × 0.25 = 6.25 m.
(b) Braking: 25²/(2 × 6) = 52.1 m. Normal: 25 × 0.05 + 52.1 = 53.3 m. Attack: 25 × 0.3 + 52.1 = 59.6 m.
(c) Normal: 53.3 m < 58 m, stops. Attack: 59.6 m > 58 m, collision. Remaining braking distance 58 − 7.5 = 50.5 m, so v² = 25² − 2 × 6 × 50.5 = 19, v ≈ 4.4 m/s (≈ 16 km/h).
A late output is as dangerous as a wrong output when the margin is small.

## Slide 4: Exercise: Amplification and deadlines
Pipeline latency T = 30 ms, deadline D = 45 ms. A stage with benign share f = 5 % of T is amplified by A = 50. For sequential stages: A_e2e = 1 + f(A − 1); the deadline is missed only if A > 1 + (D/T − 1)/f.
(a) Compute the threshold on A.
(b) Compute A_e2e and the new latency. Is the deadline missed?
(c) An admission cap limits A to 5. New A_e2e and latency?
(d) Repeat (a)–(b) if the amplified stage has f = 1 %.

## Slide 5: Exercise Solution: Amplification and deadlines
(a) Threshold = 1 + (45/30 − 1)/0.05 = 1 + 0.5/0.05 = 11.
(b) A_e2e = 1 + 0.05 × 49 = 3.45; latency = 30 × 3.45 = 103.5 ms > 45 ms: missed (50 > 11).
(c) A_e2e = 1 + 0.05 × 4 = 1.2; latency = 36 ms ≤ 45 ms: not missed.
(d) f = 1 %: threshold = 1 + 0.5/0.01 = 51 > 50; A_e2e = 1.49, latency 44.7 ms: just not missed.
Neither f nor D/T is a property of the model: they belong to the system.

## Slide 6: Exercise: Stage vs. pipeline factor
Reported numbers: SlowTrack: tracking stage 453.8×, whole camera pipeline 28.4×. Groundswell: ≈ 188× more NMS candidates, only 2.7× end-to-end latency. Use A_e2e = 1 + f(A − 1).
(a) Derive the benign share f of the amplified stage for each attack.
(b) For a pipeline with T = 30 ms and D = 45 ms, what stage factor A is needed to miss the deadline for each f? Is the reported A enough?
Attack | A (stage) | A_e2e | f | Threshold A
SlowTrack | 453.8 | 28.4 |  | 
Groundswell | 188 | 2.7 |  | 

## Slide 7: Exercise Solution: Stage vs. pipeline factor
(a) f = (A_e2e − 1)/(A − 1): SlowTrack 27.4/452.8 ≈ 6.1 %; Groundswell 1.7/187 ≈ 0.91 %.
(b) Threshold = 1 + 0.5/f: SlowTrack ≈ 9.3; Groundswell ≈ 56. Both reported factors (453.8, 188) are far above their thresholds, so both would miss the 45 ms deadline.
Unamplified stages dilute the effect: stage-level factors overstate pipeline-level risk, but a large enough factor still breaks the deadline.
Attack | A (stage) | A_e2e | f | Threshold A
SlowTrack | 453.8 | 28.4 | 6.1 % | 9.3
Groundswell | 188 | 2.7 | 0.91 % | 56

## Slide 8: Exercise: Tracker pool accumulation
A tracker has memory: an unmatched false track survives for R = 30 frames after birth. The scene has 20 real objects. The attacker creates 10 fake detections per frame. Association cost ∝ M × N (M tracks, N detections).
(a) Steady-state track pool M under attack, and N?
(b) Association cost vs. the benign case (M = N = 20)?
(c) An admission cap allows at most 2 track births per frame. New M and cost?
Case | M (tracks) | N (detections) | M × N | vs. benign
Benign | 20 | 20 | 400 | 1×
Attack, no cap |  |  |  | 
Attack, 2 births/frame |  |  |  | 

## Slide 9: Exercise Solution: Tracker pool accumulation
(a) M = 20 + R × 10 = 20 + 300 = 320 tracks; N = 20 + 10 = 30 detections.
(b) 320 × 30 = 9,600 vs. 20 × 20 = 400: 24× more work.
(c) M = 20 + 30 × 2 = 80; cost = 80 × 30 = 2,400 (6× benign): 4× lower than uncapped.
A per-frame cap on detections bounds one dimension only; the persistent pool is bounded by capping track admission (TrackShield).
Case | M (tracks) | N (detections) | M × N | vs. benign
Benign | 20 | 20 | 400 | 1×
Attack, no cap | 320 | 30 | 9,600 | 24×
Attack, 2 births/frame | 80 | 30 | 2,400 | 6×