## Slide 1: CSC 144V: Autonomous Vehicles Lecture 6 LiDAR Perception Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: Time of flight and spacing
c = 3 × 10⁸ m/s; range R = c·Δt/2; max pulse rate per channel f ≤ c/(2R_max); neighboring point spacing s = R·tan(Δθ).
Fill in the table: Δθ = 0.2°, R_max = 200 m.
Quantity | Answer
Return time of a 200 m target | 
Timing accuracy for 5 cm range accuracy | 
Max pulse rate per channel | 
Point spacing at 50 m / 100 m | 
Range where spacing = 0.5 m | 

## Slide 3: Exercise Solution: Time of flight and spacing
Δt = 2R/c = 400/(3 × 10⁸) = 1.33 µs.
5 cm → Δt = 2 × 0.05/c = 0.33 ns (1 ns ≈ 15 cm).
f ≤ c/(2R_max) = 3 × 10⁸/400 = 750 kHz.
s(50 m) = 50 tan 0.2° = 0.17 m; s(100 m) = 0.35 m.
R = 0.5/tan 0.2° ≈ 143 m: beyond it a 0.5 m pedestrian gets < 1 beam per scan line.
Quantity | Answer
Return time of a 200 m target | 1.33 µs
Timing accuracy for 5 cm range accuracy | 0.33 ns
Max pulse rate per channel | 750 kHz
Point spacing at 50 m / 100 m | 0.17 m / 0.35 m
Range where spacing = 0.5 m | ≈ 143 m

## Slide 4: Exercise: Coordinates and distortion
A return has range r = 20 m, azimuth θ = 30°, elevation φ = −5°. The LiDAR is mounted 1.8 m above the road. x = r cosφ cosθ, y = r cosφ sinθ, z = r sinφ.
(a) Compute (x, y, z). Is this likely a ground point?
(b) The vehicle drives at 20 m/s and the LiDAR sweeps at 10 Hz. How far does the vehicle move during one sweep? Why does it matter?
(c) An extrinsic rotation error of 0.5° shifts a point at 100 m by how much?

## Slide 5: Exercise Solution: Coordinates and distortion
(a) x = 20 · 0.996 · 0.866 ≈ 17.25 m, y = 20 · 0.996 · 0.5 ≈ 9.96 m, z = 20 · sin(−5°) ≈ −1.74 m. z ≈ −1.8 m (the road height below the sensor) → likely a ground point.
(b) 20 × 0.1 = 2 m. First and last points of a sweep see different poses: deskew each point with the pose at its timestamp, otherwise walls blur and a seam appears.
(c) 100 · tan 0.5° ≈ 0.87 m: calibration errors grow with range.

## Slide 6: Exercise: RANSAC iterations
RANSAC samples a minimal set of s points, counts inliers, and repeats N times. For success probability p = 0.99 and inlier ratio w:
N = ln(1 − p) / ln(1 − wˢ)
(a) Fill in the table (round up).
(b) Why does the ground-plane fit sample only points with z < 0.5 m?
Model | s | w | N
Plane | 3 | 0.5 | 
Plane | 3 | 0.3 | 
Plane | 3 | 0.8 | 
Line | 2 | 0.5 | 

## Slide 7: Exercise Solution: RANSAC iterations
(a) w = 0.5, s = 3: ln 0.01 / ln 0.875 = 34.5 → 35. w = 0.3: 168.2 → 169. w = 0.8: 6.4 → 7. A line (s = 2) with w = 0.5: 16.01 → 17.
(b) It raises the inlier ratio w (fewer walls and cars among the samples) and makes the fitted plane the road, not a wall; a lower w makes N explode.
Model | s | w | N
Plane | 3 | 0.5 | 35
Plane | 3 | 0.3 | 169
Plane | 3 | 0.8 | 7
Line | 2 | 0.5 | 17

## Slide 8: Exercise: DBSCAN by hand
DBSCAN with ε = 1.0 m and minPts = 3 (the point itself counts). Count the neighbors within ε of each point, classify it as core, border or noise, and give its cluster.
Point | (x, y) | # within ε | Type | Cluster
P1 | (0, 0) |  |  | 
P2 | (0.8, 0) |  |  | 
P3 | (1.6, 0.2) |  |  | 
P4 | (2.4, 0.9) |  |  | 
P5 | (4, 2) |  |  | 
P6 | (6, 1) |  |  | 
P7 | (6.7, 1.1) |  |  | 
P8 | (6.3, 1.8) |  |  | 
P9 | (7.5, 1.3) |  |  | 

## Slide 9: Exercise Solution: DBSCAN by hand
Core: ≥ 3 points within ε (incl. itself). Border: not core, but within ε of a core point. Noise: neither. P4 is 1.06 m from P3 → just outside ε → noise.
Point | (x, y) | # within ε | Type | Cluster
P1 | (0, 0) | 2 | border | 1
P2 | (0.8, 0) | 3 | core | 1
P3 | (1.6, 0.2) | 2 | border | 1
P4 | (2.4, 0.9) | 1 | noise | –
P5 | (4, 2) | 1 | noise | –
P6 | (6, 1) | 3 | core | 2
P7 | (6.7, 1.1) | 4 | core | 2
P8 | (6.3, 1.8) | 3 | core | 2
P9 | (7.5, 1.3) | 2 | border | 2

## Slide 10: Exercise: PointNet and pillars
(a) PointNet. Three points have per-point features h(x₁) = (1, 5), h(x₂) = (3, 2), h(x₃) = (2, 4). The global feature is the max over points. Compute it for the order (x₁, x₂, x₃) and for (x₃, x₁, x₂). Why a symmetric function?
(b) Sparsity. Region 80 m × 80 m; one sweep has ≈ 190,000 points. Voxels 0.1 m (z: 4 m height) vs. pillars 0.16 m (no z split). Compute the number of cells and the maximum occupied fraction (pillars: P = 12,000 non-empty).
Representation | Cells | Occupied
Voxels 0.1 m |  | 
Pillars 0.16 m |  | 

## Slide 11: Exercise Solution: PointNet and pillars
(a) max = (max(1, 3, 2), max(5, 2, 4)) = (3, 5) in both orders: the max is symmetric, so the output does not depend on the order of the N! possible orderings.
(b) Voxels: 800 × 800 × 40 = 25.6 M cells; ≤ 0.19 M/25.6 M ≈ 0.74 % occupied → dense 3D conv wastes > 99 % of its work on empty space.
Pillars: 500 × 500 = 250,000; 12,000/250,000 = 4.8 % occupied. Pillar tensor (P, N, D) = (12000, 100, 9) float32 = 10.8 M values ≈ 43 MB; 2D convolutions only.
Representation | Cells | Occupied
Voxels 0.1 m | 25.6 M | ≤ 0.74 %
Pillars 0.16 m | 250,000 | ≤ 4.8 %