## Slide 1: CSC 144V: Autonomous Vehicles Lecture 8 Control Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: PID by hand
Lateral PID with Δt = 1: steer = −Kp·e − Kd·(e − e_prev) − Ki·Σe. Kp = 0.2, Kd = 1.0, Ki = 0.004. Cross-track error: e₀ = 1.0 (initial), e₁ = 0.7, e₂ = 0.3, e₃ = −0.1. Σe includes the current error.
(a) Fill in the table.
(b) What would a P-only controller (Kd = Ki = 0) output at t = 1, 2, 3? What does the D term do?
t | e | e − e_prev | Σe | steer
1 | 0.7 |  |  | 
2 | 0.3 |  |  | 
3 | −0.1 |  |  | 

## Slide 3: Exercise Solution: PID by hand
t = 1: −(0.2 · 0.7 + 1.0 · (−0.3) + 0.004 · 0.7) = −(0.14 − 0.30 + 0.0028) = 0.157; t = 2: −(0.06 − 0.40 + 0.004) = 0.336; t = 3: −(−0.02 − 0.40 + 0.0036) = 0.416.
P-only: −0.14, −0.06, +0.02: it steers back, but reaches zero error with full steering authority → overshoot (the sign flips once e < 0).
The D term opposes the fast decrease of e: it damps the response and reduces overshoot (here it even reverses the steering sign at t = 1).
t | e | e − e_prev | Σe | steer
1 | 0.7 | −0.3 | 0.7 | 0.157
2 | 0.3 | −0.4 | 1.0 | 0.336
3 | −0.1 | −0.4 | 0.9 | 0.416

## Slide 4: Exercise: Effects of PID gains
Fill in the effect of increasing each gain on the step-response metrics (↑ increase, ↓ decrease, – little change).
(b) A car oscillates around the lane center with large overshoot. Which gain do you raise?
(c) On a constant-curvature track the car keeps a persistent offset (steady-state CTE). Which gain removes it?
Gain | Rise time | Overshoot | Settling time | Steady-state error
Kp |  |  |  | 
Ki |  |  |  | 
Kd |  |  |  | 

## Slide 5: Exercise Solution: Effects of PID gains
(b) Kd (derivative): it damps the oscillation and lowers overshoot.
(c) Ki (integral): it accumulates the persistent error until it is eliminated (at the price of more overshoot).
Kp alone trades a faster response for more overshoot; a P-only controller leaves a steady-state error.
Gain | Rise time | Overshoot | Settling time | Steady-state error
Kp | ↓ | ↑ | – | ↓
Ki | ↓ | ↑ | ↑ | eliminated
Kd | – | ↓ | ↓ | –

## Slide 6: Exercise: Kinematic bicycle model
Kinematic bicycle model (rear axle): x ← x + v cosθ Δt, y ← y + v sinθ Δt, θ ← θ + (v/L) tanδ Δt. L = 2.5 m, v = 10 m/s, constant steering δ = 0.1 rad, Δt = 0.1 s, start (0, 0, θ = 0).
(a) Compute the state after steps 1 and 2.
(b) Turning radius R = L/tanδ and lateral acceleration v²/R?
(c) For a comfort limit of 2 m/s² at v = 10 m/s, what is the maximum steering angle?
Step | x (m) | y (m) | θ (rad)
0 | 0 | 0 | 0
1 |  |  | 
2 |  |  | 

## Slide 7: Exercise Solution: Kinematic bicycle model
(a) θ₁ = (10/2.5) · tan 0.1 · 0.1 = 0.0401; x₁ = 1.000, y₁ = 0. Step 2: x₂ = 1 + cos(0.0401) = 1.999, y₂ = sin(0.0401) = 0.0401, θ₂ = 0.0803.
(b) R = 2.5/tan 0.1 ≈ 24.9 m; v²/R = 100/24.9 ≈ 4.0 m/s².
(c) R_min = v²/a = 100/2 = 50 m; δ_max = atan(L/R) = atan(0.05) ≈ 0.05 rad ≈ 2.9°.
Step | x (m) | y (m) | θ (rad)
0 | 0 | 0 | 0
1 | 1.000 | 0.000 | 0.0401
2 | 1.999 | 0.0401 | 0.0803

## Slide 8: Exercise: Pure pursuit and Stanley
Wheelbase L = 2.5 m. Pure pursuit: δ = atan(2 L sinα / L_d), α = angle to the look-ahead point. Stanley: δ = ψ + atan(k e / v).
(a) Pure pursuit with α = 20°, L_d = 5 m: δ?
(b) Same α with L_d = 2 m: δ?
(c) Stanley with heading error ψ = 0.1 rad, cross-track error e = 0.5 m, k = 1.5, v = 6 m/s: δ?
(d) Peak error in a 20 m radius corner (v = 5 m/s): L_d = 2 m → 0.02 m, 5 m → 0.13 m, 10 m → 0.55 m. Trade-off of the look-ahead distance?

## Slide 9: Exercise Solution: Pure pursuit and Stanley
(a) 2 · 2.5 · sin 20° / 5 = 0.342 → δ = atan(0.342) = 0.330 rad ≈ 18.9°.
(b) 5 · 0.342 / 2 = 0.855 → δ = 0.708 rad ≈ 40.6°: a short look-ahead steers much harder.
(c) atan(1.5 · 0.5/6) = atan(0.125) = 0.124; δ = 0.1 + 0.124 = 0.224 rad ≈ 12.9° (both terms steer toward the path).
(d) A large L_d is smooth and stable but cuts corners (peak error grows 0.02 → 0.55 m); a small L_d tracks the path closely but steers aggressively and can oscillate at speed.

## Slide 10: Exercise: LQR trade-offs
Scalar system ẋ = a x + b u with a = 1 (unstable), b = 1; cost ∫ (q x² + r u²) dt. The Riccati equation 2ap − (b²/r)p² + q = 0 gives p; the gain is K = b p / r, u = −K x, and the closed-loop pole is a − bK.
Fill in the table. What do larger q and larger r do?
q | r | p | K | Pole
1 | 1 |  |  | 
4 | 1 |  |  | 
1 | 4 |  |  | 

## Slide 11: Exercise Solution: LQR trade-offs
q = r = 1: −p² + 2p + 1 = 0 → p = 1 + √2 = 2.414, K = 2.414, pole = 1 − 2.414 = −1.414.
q = 4, r = 1: p = 1 + √5 = 3.236, K = 3.236, pole −2.236 (faster).
q = 1, r = 4: p² − 8p − 4 = 0 → p = 8.472, K = 8.472/4 = 2.118, pole −1.118 (slower).
Larger q penalizes state error more: more aggressive. Larger r makes control expensive: gentler. No pole locations are chosen by hand.
q | r | p | K | Pole
1 | 1 | 2.414 | 2.414 | −1.414
4 | 1 | 3.236 | 3.236 | −2.236
1 | 4 | 8.472 | 2.118 | −1.118