## Slide 1: CSC 144V: Autonomous Vehicles Lecture 9.1 SLAM Fundamentals Exercises Solution
Department of Computer Science,
Hofstra University

## Slide 2: Exercise: 1-D EKF-SLAM update
1-D world. Robot x and landmark m on a line; measurement z = m − x + noise (variance 0.09); motion x ← x + u + noise. At x₀ = 0 (known) the robot measures z₀ = 4.8 and initializes m = 4.8 (variance 0.09). Then it moves u = 3.0 (variance 0.16) and measures z₁ = 1.6.
(a) Fill in the table (state x, m and covariance entries) after the initial observation, the prediction, and the update.
(b) Compute the innovation y, S = HPHᵀ + R (H = [−1, 1]) and the Kalman gain K. (c) Why is P_xm ≠ 0 after the update?
Step | x | m | P_xx | P_mm | P_xm
after z₀ |  |  |  |  | 
predict (u = 3) |  |  |  |  | 
update (z₁ = 1.6) |  |  |  |  | 

## Slide 3: Exercise Solution: 1-D EKF-SLAM update
(b) Predicted ẑ = 4.8 − 3.0 = 1.8, so y = −0.2. S = 0.16 + 0.09 + 0.09 = 0.34. K = PHᵀ/S = (−0.16, 0.09)/0.34 = (−0.471, 0.265).
(c) The landmark was initialized from the robot pose, and the measurement depends on both: the update correlates them (ρ = 0.0424/√(0.0847·0.0662) = 0.57). Learning about one now improves the other; P_mm fell from 0.09 to 0.066.
Step | x | m | P_xx | P_mm | P_xm
after z₀ | 0 | 4.8 | 0 | 0.09 | 0
predict (u = 3) | 3.0 | 4.8 | 0.16 | 0.09 | 0
update (z₁ = 1.6) | 3.094 | 4.747 | 0.0847 | 0.0662 | 0.0424

## Slide 4: Exercise: 1-D pose graph
1-D pose graph with x₀ = 0 fixed. Odometry edges: x₁ − x₀ = 2.0 and x₂ − x₁ = 2.0, each with information Ω = 50. Loop-closure edge: x₂ − x₀ = 3.7 with Ω = 100. Initial guess from odometry: x = (2, 4).
(a) Compute the three residuals e and the cost F = Σ Ω e² at the initial guess.
(b) Build H and b for the unknowns (x₁, x₂).
(c) Solve H Δx = −b and give the new x and the new cost.
(d) What is the standard deviation of x₂, from H⁻¹?

## Slide 5: Exercise Solution: 1-D pose graph
(a) e₀₁ = 0, e₁₂ = 0, e₀₂ = 4 − 3.7 = 0.3; F = 100 · 0.3² = 9.0.
(b) H = [[50 + 50, −50], [−50, 50 + 100]] = [[100, −50], [−50, 150]]; b = Σ Ωe Jᵀ = (0, 30) (only the loop edge has a residual).
(c) Δx = −H⁻¹b = (−0.12, −0.24) → x = (1.88, 3.76). Residuals: −0.12, −0.12, +0.06; F = 50·0.0144 + 50·0.0144 + 100·0.0036 = 1.8. One step is exact because the problem is linear.
(d) H⁻¹ = [[0.012, 0.004], [0.004, 0.008]] → σ(x₂) = √0.008 ≈ 0.089 m. The loop closure spread the 0.3 m inconsistency over all three edges, weighted by Ω.

## Slide 6: Exercise: Gating and data association
A predicted landmark has innovation covariance S = [[0.5, 0.1], [0.1, 0.3]]. Three candidate measurements have innovations y_A = (0.8, −0.4), y_B = (1.5, 0.2), y_C = (1.6, 0.9).
(a) Compute d² = yᵀS⁻¹y for each candidate and test it against the χ² gates for 2 DoF (95 %: 5.99, 99 %: 9.21).
(b) Which candidate does nearest-neighbor association choose? What can go wrong?
Candidate | y | d² | 95 % gate | 99 % gate
A | (0.8, −0.4) |  |  | 
B | (1.5, 0.2) |  |  | 
C | (1.6, 0.9) |  |  | 

## Slide 7: Exercise Solution: Gating and data association
(b) Nearest neighbor (smallest d²) picks A. B is also inside the gate, so the association is ambiguous: a wrong choice moves the landmark and the pose the wrong way, and EKF-SLAM cannot undo it (the past is marginalized). Remedies: joint compatibility, multiple hypotheses (FastSLAM), or a verified graph edge.
C is a clear outlier at 95 % but would pass a 99 % gate: a tighter gate rejects more outliers but also more true matches.
Candidate | y | d² | 95 % gate | 99 % gate
A | (0.8, −0.4) | 2.40 | inside | inside
B | (1.5, 0.2) | 4.54 | inside | inside
C | (1.6, 0.9) | 6.32 | outside | inside

## Slide 8: Exercise: EKF vs. FastSLAM cost
EKF-SLAM keeps the pose (3) and N landmarks (2 each) with a full covariance; one update costs about N² operations. FastSLAM with M = 100 particles costs about M log₂N per update. Doubles take 8 bytes.
(a) Fill in the table for N = 1,000 and N = 100,000 landmarks.
(b) At which map size does a full-covariance EKF become impractical, and what do graph SLAM and FastSLAM do differently?
N | State dim | Covariance entries | Memory | EKF ops ≈ N² | FastSLAM ≈ M log₂N
1,000 |  |  |  |  | 
100,000 |  |  |  |  | 

## Slide 9: Exercise Solution: EKF vs. FastSLAM cost
State dimension 3 + 2N; covariance has (3 + 2N)² entries. For N = 10⁵ the covariance alone needs ≈ 320 GB, and each update touches all of it.
(b) EKF is fine up to a few hundred landmarks, hard beyond a few thousand. FastSLAM factors the posterior into N tiny 2×2 EKFs per particle; graph SLAM stores a sparse H (each constraint links two nodes) instead of a dense covariance.
N | State dim | Covariance entries | Memory | EKF ops ≈ N² | FastSLAM ≈ M log₂N
1,000 | 2,003 | 4.0 × 10⁶ | 32 MB | 10⁶ | ≈ 1,000
100,000 | 200,003 | 4.0 × 10¹⁰ | 320 GB | 10¹⁰ | ≈ 1,700

## Slide 10: Exercise: ATE and RPE
Ground-truth and estimated 2-D positions of five poses are given (already aligned). Truth: (0,0), (1,0), (2,0), (3,0), (4,0). Estimate: (0,0), (1.1,0.1), (2.0,0.3), (3.2,0.2), (4.1,0.5).
(a) Compute the position error of each pose and the ATE (RMSE). (b) Compute the RPE of each step (error of the relative motion) and its RMSE.
(c) The estimate looks good locally but bends away: which metric shows it? (d) A false loop closure is added: which would increase most, ATE or RPE?
Pose | Truth | Estimate | Error (m)
1 | (0, 0) | (0, 0) | 
2 | (1, 0) | (1.1, 0.1) | 
3 | (2, 0) | (2.0, 0.3) | 
4 | (3, 0) | (3.2, 0.2) | 
5 | (4, 0) | (4.1, 0.5) | 

## Slide 11: Exercise Solution: ATE and RPE
(a) errors 0, 0.141, 0.300, 0.283, 0.510 → ATE = √((0 + 0.02 + 0.09 + 0.08 + 0.26)/5) = 0.30 m (max 0.51 m).
(b) relative motions (1.1, 0.1), (0.9, 0.2), (1.2, −0.1), (0.9, 0.3) vs. (1, 0): errors 0.141, 0.224, 0.224, 0.316 → RPE RMSE = 0.23 m per step.
(c) ATE measures global consistency (accumulated drift); RPE measures local accuracy. (d) A false loop edge bends the whole trajectory: ATE grows a lot, RPE only near the bad edge. This is why SLAM is evaluated with both, and with several runs.
Pose | Truth | Estimate | Error (m)
1 | (0, 0) | (0, 0) | 0
2 | (1, 0) | (1.1, 0.1) | 0.141
3 | (2, 0) | (2.0, 0.3) | 0.300
4 | (3, 0) | (3.2, 0.2) | 0.283
5 | (4, 0) | (4.1, 0.5) | 0.510