## Slide 1: L1.1 Introduction and Overview
Zonghua Gu
Fall 2026

## Slide 2: Overview of AV Technology
https://www.hollywoodreporter.com/news/general-news/driving-cars-could-add-billions-905966/

## Slide 3: Why Autonomous Driving?
Reduced traffic accidents and fatalities
  In 2019, an estimated 38,800 people lost their lives to car crashes in the US. About 4.4 million people were injured seriously enough to require medical attention in crashes.
Reduced congestion and pollution
More productive time spent on the road
Autonomous Mobility-on-Demand (AMoD) with a fleet of robotaxis
  Low-cost, safe and efficient mode of transportation that may make vehicle ownership obsolete.
  The dream of Uber (and many other companies)

## Slide 4: Advanced Driver Assistance (ADAS)
Since the initial introduction of Cruise Control in 1948, ADAS functions are increasingly prevalent in modern vehicles.
  Adaptive cruise control (ACC), Anti-lock braking system, Collision avoidance system (Pre-crash system), Driver Monitoring System (DMS), Electronic Stability Control (ESC), Forward Collision Warning (FCW), Lane Departure Warning (LDW), Lane Change Assistance, Surround View…

## Slide 5: DARPA Grand Challenges
2004 challenge
  Held in the Mojave Desert region of the USA, along a 150-mile route.
  None of the robot vehicles finished the route. No winner was declared, and the cash prize was not given.
2005 challenge
  Vehicles passed through three narrow tunnels and negotiated more than 100 sharp left and right turns.
  Five vehicles successfully completed the 132 mi course. Stanford’s Stanley won the $2M top prize.
2007 challenge
  The course involved a 60 mi urban area course to be completed in less than 6 hours. Rules included obeying all traffic regulations while negotiating with other traffic and obstacles and merging into traffic.
The 3 Grand Challenge races jump-started the Self-Driving Car industry. Faculty and students from winning teams such as Stanford and CMU later became leaders in SDC projects at companies like Google/Waymo and Uber and numerous startups.

## Slide 6: Highway vs. City Driving
Highway driving is perceived as an easier problem than city driving.
  Has potential of massive displacement of truck driver jobs
  But traffic merging is tricky and may require human operator assistance
 | Highway Driving | City Driving
Travel Speed | High | Low to medium
Traffic Volume | High | Medium to high
Number of Lanes | Large (6-8) | Small (2-4)
Others | Entry and exit points for traffic merging | Many intersections with traffic lights

## Slide 7: Operational Design Domain (ODD)
The ODD defines the conditions under which a vehicle is designed to function and is expected to perform safely. The ODD includes (but isn’t limited to) environmental, geographical, and time-of-day restrictions, as well as traffic or roadway characteristics.
  e.g., an autonomous freight truck might be designed to transport cargo from a seaport to a distribution center 30 Km away, via a specific route, in day-time only. This vehicles ODD is limited to the prescribed route and time-of-day, and it should not operate outside of it

## Slide 8: Five Levels of Automation
L1: ADAS features that either control steering or speed to support the driver.
L2: both steering and acceleration are simultaneously handled by AD system. The human driver still monitors the environment and supervises the support functions.
L3: Conditional automation: the system can drive without the need for a human to monitor and respond. However, the system might ask a human to intervene, so the driver must be able to take control at all times.
L4: These systems have high automation and can fully drive themselves under certain conditions. The vehicle won’t drive if not all conditions are met.
L5: Full automation, the vehicle can drive wherever, whenever, with unlimited ODD.
https://www.wevolver.com/article/2020.autonomous.vehicle.technology.report
Notes: Autonomous Self-Driving Vehicle Levels Explained
https://www.youtube.com/watch?v=LIP4eJAECvU

## Slide 9: State-of-the-Art
Current commercial products are at most L2 (e.g., Tesla Autopilot)
L2 to L3 is perceived to be a giant leap
  Automakers keep pushing the timeline of L3 and above to the future…
Notes: https://www.forbes.com/sites/jamesmorris/2021/03/13/why-is-teslas-full-self-driving-only-level-2-autonomous/?sh=f7ed99c6a320
https://thenextweb.com/shift/2020/02/27/6-levels-autonomous-self-driving-explained-tesla-waymo-autopilot/
https://europe.autonews.com/automakers/lexus-prepares-introduce-level-2-autonomy

## Slide 10: Two Different Paths to L4/5
Tesla starts from L2 and mass deployment, and gradually moves to L4/5.
Waymo, nuTonomy…starts from L4 in limited ODD, and gradually expands deployment
Emilio Frazzoli, nuTonomy

## Slide 11: The Tesla Fatality (May 2016)
A Tesla Model S was driving 74 mph on the highway when it was struck by a truck
Tesla: “Neither Autopilot nor the driver noticed the white side of the truck against a brightly lit sky, so the brake was not applied.”
  A failure of computer vision algorithm for object detection
Notes: The driver’s hands were off the steering wheel for a total of 37 minutes during the 37.5 minutes of time the car was in Autopilot, despite repeated visual warnings

## Slide 12: The Tesla Fatality (Mar 2018)
In 2018, a man died from a high-speed crash because his Tesla Autopilot system steered the car into a median on Highway 101 in CA.
  Limitations on Tesla's Autopilot Lane-Keeping Assistance (LKA) caused the vehicle to veer into the median and failed to provide an alert to the driver in the seconds leading to the crash.
  The collision avoidance system was not designed to detect a crash attenuator, which resulted in a severe crash in which the automatic braking and collision warning systems failed to activate.
  A failure of computer vision algorithm for lane tracking.
Tesla Autopilot 2 almost crashes Into Barrier (similar to this crash)
  https://www.youtube.com/watch?v=TIUU1xNqI8w
https://www.mv-voice.com/news/2020/02/25/ntsb-teslas-autopilot-steered-model-x-into-highway-median-causing-fatal-mountain-view-crash

## Slide 13: Tesla vs. Truck (Jun 2020)
Tesla crashes into overturned truck on a busy highway in Taiwan
Video: https://taiwanenglishnews.com/tesla-on-autopilot-crashes-into-overturned-truck/

## Slide 14: The Uber Pedestrian Fatality (Mar 2018)
Video of Uber collision that killed pedestrian
  https://www.youtube.com/watch?v=q7d90ZFhg28
After the woman was detected on the road (6 sec before crash), she was:
  first classified as unknown object
  then misclassified as a vehicle
  then as a bicycle
1.3 sec before, the Volvo system tried to do emergency braking maneuver
  but Uber had disabled it for testing
The safety driver was not watching the road moments before crash
  It was probably too dark for the driver to see her in time
The AV was equipped with both Lidar and Radar
  “This is exactly the type of situation that Lidar and radar are supposed to pick up. This is a catastrophic failure that happened with Uber’s technology.” – Prof. David King.

## Slide 15: Tesla Wins in Court (Oct 2023)
Tesla won the first U.S. trial over allegations that its Autopilot driver assistant feature led to a death
  In 2019, a Tesla Model 3 suddenly veered off a highway at 65 MPH, struck a palm tree and burst into flames, killing the driver and seriously injuring two passengers
  Tesla argued that the crash was the result of human error — the same stance it’s taken in other Autopilot lawsuits
    https://www.reuters.com/business/autos-transportation/tesla-wins-autopilot-trial-involving-fatal-crash-2023-10-31/

## Slide 16: AD Safety Evaluation by California DMV
A disengagement report is required from the 43 companies currently licensed to test autonomous cars on public roads in California.
  California is currently the only region in the world where we have such data publicly available.
A disengagement can be described as the event when the AV either got stuck and handed over control to a safety driver present in the vehicle, or when a safety driver took control himself.
https://thelastdriverlicenseholder.com/2023/02/17/2022-disengagement-report-from-california/
Number of vehicles deployed per manufacturer in the 2022 reporting period
Notes: https://thelastdriverlicenseholder.com/2023/02/17/2022-disengagement-report-from-california/

## Slide 17: Reports with Safety Drivers (2022)
Number of vehicles deployed per manufacturer in the 2022 reporting period

## Slide 18: Reports with Safety Drivers (2022)
Number of miles driven per manufacturer
Number of miles driven per disengagement

## Slide 19: Driverless Reports (2022)
Seven companies (Apollo, AutoX, Cruise, Nuro, Waymo, WeRide, and Zoox) have driverless licenses in California
  Cruise completed the majority of driverless driving with 546,492 mi in San Francisco.
  No disengagements are given by the manufacturers because, according to the definition, they require the intervention of a safety driver on board.
Cruise’s permit to operate driverless vehicles was revoked by California DMV in Oct. 2023, since it withheld video of a crash
  https://edition.cnn.com/2023/10/24/business/california-dmv-cruise-permit-revoke/index.html
﻿ | Miles | Vehicles
Apollo (Baidu) | 21,774 | 4
Cruise | 546,492 | 222
Nuro | 924 | 9
Waymo | 51,639 | 317
WeRide | 2,859 | 3
﻿Total | 623,689 | 555

## Slide 20: Where is Tesla?
Tesla does not appear in the 2022 report
  “Tesla’s current interpretation of the FSD Beta, which is now in use in more than 300,000 customer vehicles, is that it is a driver assistance system that does not require reporting to the DMV.”
Tesla Surpasses 150 Million Miles Driven with FSD Beta (Apr. 2023)

## Slide 21: Is Miles Driven a Good Metric?
Not All Miles are Equal.
  Driving conditions may be dramatically different.
  Companies may be incentivized to avoid difficult driving conditions.

## Slide 22: When will L5 AD Arrive?
Chris Urmson, CEO of Aurora:
  “In 5 years” - 2009
  “In 5 years” - 2012
  “In 5 years” - 2015
  “In 5 years” - 2018

## Slide 23: Four Major Tasks of an AV
Localization: Where am I?
Detection: What is around me?
Prediction: Where are they going?
Planning and Control: Where should I go?

## Slide 24: AV Processing Pipeline
Perception:
  Understanding the surrounding environment, incl. localization, object detection and tracking, etc.
Behavior prediction:
  Predict objects’ future movements
Planning:
  Plan a path/trajectory for the ego-vehicle in the context of other road users
Control:
  Moving the vehicle to follow the planned trajectory
Perception
Behavior Prediction
Planning
Control
Objects
(Cars, pedestrians,…)
Object
Futures
Ego-vehicle
Trajectory
Control cmds
(throttle, brake, steering)
Sensor Data
(Camera, Lidar, Radar…)

## Slide 25: Perception
Localization
Static object detection
Dynamic object detection and tracking

## Slide 26: Behavior Prediction
Based on state
  Kalman filter
  Particle filter
Data-driven
  ML-based classification
Pedestrian intention prediction
  Based on visual cues such as pose, etc.

## Slide 27: Planning
Mission Planning: use graph search to find a path from source to destination on the map
Behavior Planning: plan the set of high-level driving actions or maneuvers to safely achieve the driving mission under various driving conditions
Local Planning: plan a safe and smooth trajectory (vehicle pose as function of time)

## Slide 28: Control
Velocity controller for longitudinal speed control
Steering controller for lateral speed control
Notes: Common control algorithms
  PID: Proportional Integral Derivative
  MPC: Model-Predictive Control

## Slide 29: ML/DL Applied in the AV Pipeline
Classic AD processing pipeline: separate algorithms for each processing stage
ML, esp. Deep Neural Networks, may be deployed at different stages of the AD processing pipeline
  (b): DNNs deployed in the Perception stage only, the prevalent approach in industry practice.
  (c): end-to-end control, e.g., mapping from input images to control, trained with Imitation Learning or Reinforcement Learning.
  (d): mid-to-mid approach, e.g., a separate perception module outputs Bird’s Eye View as input to downstream modules.
Notes: Classic AD processing pipeline: separate algorithms for each processing stage.
Where does ML/DL come in?
  CNN (Convolutional Neural Networks) for perception is well accepted.
  DNN trained with Imitation Learning (IL) or Reinforcement Learning (RL) is still in the early-research stage.
    “End-to-end” mapping from pixels to control commands
    Many variants of hybrid approaches, e.g., “half-way” mapping from pixels to waypoints used for planning
    Several companies are making a bet on it, incl. Waymo, Voyage, Wayve…
Where does ML/DL come in?
  CNN (Convolutional Neural Networks) for perception is well accepted.
  DNN trained with Imitation Learning (IL) or Reinforcement Learning (RL) is still in the early-research stage.
    “End-to-end” mapping from pixels to control commands
    Many variants of hybrid approaches, e.g., “half-way” mapping from pixels to waypoints used for planning
    Several companies are making a bet on it, incl. Waymo, Voyage, Wayve…