## Slide 1: L5 Planning
Acknowledgement: slides partly based on https://www.coursera.org/learn/motion-planning-self-driving-cars
Zonghua Gu, Umeå University
Nov. 2023

## Slide 2: A Hierarchy of Planners
Mission Planning: map-level navigation
Behavior Planning: choosing a behavior based on environmental conditions
Motion Planning: includes path planning and speed profile generation, generates a reference trajectory to be tracked by controller
Controller (PID, MPC…)
Reference Trajectory

## Slide 3: Outline
Route planning
Behavior planning
Motion Planning
Responsibility-Sensitive Safety (RSS)
Paden B, Čáp M, Yong S Z, et al. A survey of motion planning and control techniques for self-driving urban vehicles[J]. IEEE Transactions on intelligent vehicles, 2016, 1(1): 33-55.
Notes: Safety plan
The safety plan gives an overview of how you are going to achieve a safe system. A few of the major elements include:
  what system is under consideration
  the goal of the project
  what steps will be taken to ensure safety
  the roles and personnel involved in the project
  the project timeline

## Slide 4: Route Planning
Find the optimal path for navigation from Start to Goal on a weighted graph
Graph search algorithms
  Dijkstra’s, A*,…
Notes: Use graph search to find a high-level path from source to destination on the map

## Slide 5: BFS and DFS
https://medium.com/@nihatkoc/dfs-vs-bfs-6b632c381ed6
Breadth-First Search (BFS): at each node, expand all neighbor nodes at the present depth prior to moving on to the nodes at the next depth level. (Left figure)
Depth-First Search (DFS): at each node, expand as far as possible along each branch before backtracking. (Right figure)
BFS and DFS are inefficient since they do not consider edge costs for selecting the next node to expand. BFS is better than DFS for path planning:
  BFS can finish after finding a path to the goal with total cost cost of all other partial paths.
  DFS must expand all nodes of the graph.
They are not used for robotic path planning. Shown here for comparison purposes.
Notes: We will discuss Dijkstra’s and A* algorithm:
  Both can finish after finding a path to goal, and the path is

## Slide 6: Running Example
Shortest path is with length
S
A
B
C
2
3
G
10
12
20

## Slide 7: BFS
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
Cannot finish here, must expand node C, since total cost , cost of the other partial path through C.
Notes: (Cannot finish here, must expand node B
since B’s cost to S 5 is less than 22.)

## Slide 8: DFS
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
Must always expand all nodes.

## Slide 9: Dijkstra’s Algorithm
open[v] is sorted and popped in decreasing order of , cost of partial path to the source node .

## Slide 10: Dijkstra Example
S
A
B
C
2
3
G
10
12
20
Node | Cost to S
S | 0
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
Node | Cost to S
A | 2
C | 10
Node | Cost to S
B | 5
C | 10
Closed set: S
Closed set: S, A

## Slide 11: Dijkstra Example cont’
S
A
B
C
2
3
G
10
12
20
Node | Cost to S
C | 10
G | 25
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
Node | Cost to S
G | 22
Closed set: S, A, B
Closed set: S, A, B, C
extractPath() yields the shortest path with length

## Slide 12: A* Algorithm (Compare to Dijkstra)
open[v] is sorted and popped in decreasing order of , cost of partial path to the source node plus estimated cost-to-go actual cost-to-go (called an admissible heuristic). A* with becomes Dijkstra’s algo.
open[v] is sorted and popped in decreasing order of , cost of partial path to the source node .

## Slide 13: A* Example
S
A
B
C
2
3
G
10
12
20
Node | Cost to S | Est. cost-to-go | Est. total cost
S | 0 | 11.5 (<22 actual) | 11.5
Node | Cost to S |  | Est. total cost
S | 0 | 11.5 (<22 actual) | 11.5
S
A
B
C
2
3
G
10
12
20
S
A
B
C
2
3
G
10
12
20
Closed set: S
Node | Cost to S | Est. cost-to-go | Est. total cost
C | 10 | 10.5 (<12 actual) | 20.5
A | 2 | 22.5 (<23 actual) | 24.5
Node | Cost to S |  | Est. total cost
C | 10 | 10.5 (<12 actual) | 20.5
A | 2 | 22.5 (<23 actual) | 24.5
Closed set: S, C
Node | Cost to S | Est. cost-to-go | Est. total cost
G | 22 | 0 (exact) | 22
A | 2 | 22.5 (<23 actual) | 24.5
Node | Cost to S |  | Est. total cost
G | 22 | 0 (exact) | 22
A | 2 | 22.5 (<23 actual) | 24.5
extractPath() yields the shortest path with length
Closed set: S

## Slide 14: How to Design an Admissible Heuristic?
In the weighted graph representing the road network, edge cost may be travel distance, or travel time taking into account factors such as speed limit, traffic congestion level, etc.
  If objective is to minimize total travel distance from start to goal, then edge cost is travel distance between two locations. We can set to be the straight-line distance to goal.
  If objective is to minimize total travel time from start to goal, then edge cost is travel time between two locations. We can set to be the straight-line distance to goal divided by the maximum speed limit.

## Slide 15: Exercise
Consider the following graph. Number pairs in parenthesis denote Cartesian coordinates of the node. Find the shortest path (green) from s (start) to t (goal) with:
  Dijkstra’s algo
  A* with heuristic function as the straight-line distance to goal.

## Slide 16: A* vs. Dijkstra
Red crosses denote obstacles.
Green circles denote explored positions.
A* search is more efficient, as it is directed towards the target; Dijkstra’s algorithm explores in every direction and less efficient.
Grid Map
A* Algorithm
Dijkstra’s Algorithm

## Slide 17: A* vs. Dijkstra (Animation)
https://github.com/AtsushiSakai/PythonRobotics
More animations https://qiao.github.io/PathFinding.js/visual/
Dijkstra
A*

## Slide 18: Outline
Route planning
Behavior planning
Motion Planning
Responsibility-Sensitive Safety (RSS)
Paden B, Čáp M, Yong S Z, et al. A survey of motion planning and control techniques for self-driving urban vehicles[J]. IEEE Transactions on intelligent vehicles, 2016, 1(1): 33-55.
Notes: Safety plan
The safety plan gives an overview of how you are going to achieve a safe system. A few of the major elements include:
  what system is under consideration
  the goal of the project
  what steps will be taken to ensure safety
  the roles and personnel involved in the project
  the project timeline

## Slide 19: Behavior Planner
Plan the set of high-level driving actions, or maneuvers to safely achieve the driving mission under various driving situations based on:
  Rules of the road (traffic lights, stop signs…)
  Static objects (parked vehicles…)
  Dynamic objects (moving vehicles, cyclists, pedestrians…). Need behavior prediction.

## Slide 20: Driving Maneuvers
Track speed
  Maintain current speed consistent with other vehicles on the road.
Follow leader
  Match speed of the leading vehicle and maintain a safe distance.
Decelerate to stop
  Begin decelerating and stop before a given space.
Stop
  Remain stopped in the current position.
Change lanes
Turn
  Left, right, U-turn…
Pass
  Complex maneuver involving changing lanes, passing, (optional) changing back to ego-lane.
Notes: Choose a maneuver (stop, go straight, turn left, turn right..),

## Slide 21: Behavior Planning Approaches
Finite State Machine-based
  Transitions triggered by inputs
Rule-based: Logical statements with priorities
Reinforcement Learning-based
  Learned from trial-and-error to maximize cumulative reward.
FSM-based example: traffic light changing color
Rule1: green light at intersection drive straight
Rule 2: pedestrian in intersection stop
Rule-based planning example: Rule 2 has higher priority and overrides Rule 1
Notes: Explicitly designed by experts

## Slide 22: An Intersection Scenario without Dynamic Objects
4-way intersection
Two-lane road
Stop sign in every direction
No other dynamic objects
Discretized into
  Approaching zone (red box)
  At zone (green box)
  On zone (orange box)
Size of each zone determined by
  Ego vehicle speed
  Size of the intersection

## Slide 23
✔
✔
Notes: (✔

## Slide 24
To make the state machine more robust to noise in state estimation, may change Ego.Velocity==0 to Ego.Velocity<=StopThreshold
For an intersection with stop signs, there is no transition from “Decelerate to Stop” to “Track Speed”, since vehicle must come to a complete stop at a Stop sign
For an intersection with traffic lights, there should be such a transition, as the light may turn green while vehicle is decelerating.
✔

## Slide 25: An Intersection Scenario with Dynamic Objects
Additional state “Follow Leader” to handle situation when another vehicle is in front of ego-vehicle.
Again, no transition from “Decelerate to Stop” to “Track Speed”, since vehicle must come to a complete stop at a Stop sign

## Slide 26: Handling Multiple Scenarios with Hierarchical FSM
Each driving scenario is modeled as a super-state, which contains a low-level FSM for the scenario.
(Each low-level FSM is specific for the scenario, e.g., the two FSMs in the figure have different trigger conditions not shown)
Entry transitions
Exit
transitions

## Slide 27: Handling Multiple Scenarios with Hierarchical FSM

## Slide 28: Limitations of FSM-based Behavior Planning
State explosion for many and complex scenarios
Dealing with measurement noise and uncertainty of the environment
  Hyperparameters can be used to deal with some noise, but only in some limited situations, e.g., Ego.Velocity<=StopThreshold instead of Ego.Velocity==0
Incapable of dealing with unencountered scenarios
Reinforcement Learning is a promising alternative

## Slide 29: Outline
Route planning
Behavior planning
Motion Planning
Responsibility-Sensitive Safety (RSS)
Paden B, Čáp M, Yong S Z, et al. A survey of motion planning and control techniques for self-driving urban vehicles[J]. IEEE Transactions on intelligent vehicles, 2016, 1(1): 33-55.
Notes: Safety plan
The safety plan gives an overview of how you are going to achieve a safe system. A few of the major elements include:
  what system is under consideration
  the goal of the project
  what steps will be taken to ensure safety
  the roles and personnel involved in the project
  the project timeline

## Slide 30: Vehicle Control Architecture

## Slide 31: Motion Planning
Generate a feasible (smooth and collision-free) trajectory
  A trajectory is a path parametrized by time

## Slide 32: Motion Planning Methods
Also called trajectory planning or local planning, includes path planning and speed profile generation:
  Path planning:
    Plan a path from point A to point B
  Speed profile generation
    Assign a speed value to every point on a given path
  Variational planning: combine both path planning and velocity planning to generate a trajectory in a single-step (omitted)
Notes: Assign speed value to every point on a given path. v
Also called trajectory planning, local planning
  Decomposed into path planning and speed profile generation
  Generating smooth paths

## Slide 33: Occupancy Grid
Discretized grid map encoding occupancy of static objects (e.g., all non-drivable surfaces are occupied, incl. trees, buildings, sidewalks, lawns…), obtained with Lidar or camera
Can be binary encoding (upper left), or probabilistic encoding (upper right), using a belief threshold to convert to binary encoding

## Slide 34: Rapidly-exploring Random Tree (RRT)
Insert start location S in tree
While tree cannot connect to goal
  Sample random point
  Find point in tree that is closest to
  Add branch between and
    Another variant is to add branch of predefined length from in direction of
  If new branch intersects obstacle:
    Discard new branch (or shorten)
Compute path from start (S) to goal (G) through tree
Shortcut path: for any two points in path, add direct line unless direct line intersect an obstacle (collision checking)
1
S
2
3
4
5
6
G
S
G
S
G

## Slide 35: Path Smoothing
Left: an example completed path
Right: smoothed path (green), obtained by iteratively sampling points between nodes on the overall path and then checking if two points could be connected to reduce path length
http://coecsl.ece.illinois.edu/ge423/spring13/RickRekoskeAvoid/rrt.html

## Slide 36: RRT Animation
RRT growth process (with start location but no goal location)
More animations https://www.youtube.com/watch?v=pOFtvZ_qVsA

## Slide 37: Probabilistic Roadmap (PRM)
Map construction:
While # points in roadmap lower than threshold
  Sample random point
  If new point is not in collision:
    Connect new point to all other points in the roadmap with lines, as long as they do not intersect obstacles.
Path finding:
  Connect start location to nearest point in roadmap s.t. connecting line does not intersect obstacle
  Connect goal location to nearest point in roadmap s.t. connecting line does not intersect obstacle
  Find a path between start and goal traversing the roadmap, with algorithms such as as A* or Dijkstra’s algo.
By Eric O. Scott - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=44485745

## Slide 38: RRT vs. PRM
With RRT, each time new start/goal locations are given, an entirely new graph must be generated, which may be inefficient.
PRM builds a roadmap graph for traveling through a region, but relies on A* or Dijkstra’s algo to find the shortest path from start to goal traversing the roadmap. Hence the roadmap is reused each time new start/goal locations are given.
Notes: Repeatedly generating a new graph to find a single path is arguably inefficient, especially if a relatively large area is being explored. An alternative approach that addresses this deficiency is the Probabilistic Roadmap (PRM) algorithm.

## Slide 39: RRT & PRM
Many variants of RRT and PRM are probabilistically complete:
  If a path exists, it will be found in finite time
  But in the worst-case, solution time can be very long (even longer than exhaustive search)
No guarantees on solution quality
  May not find the shortest path
    With PRM, A*/Dijkstra is guaranteed to find the shortest path for the given roadmap, but the roadmap may not be optimal.
  Often needs post-processing (e.g., smoothing)

## Slide 40: Quiz
Which statement is true for RRT and PRM motion planning algorithms?
  A. Both algorithms will produce the shortest path.
  B. Both algorithms can be used for high dimensional spaces
    Robotic motion planning may be high-dimensional; mobile robot path planning is low-dimensional (3 for ground robot, 6 for aerial robot).
  C. PRM always results in a better path than RRT.
  D. The time for computation is consistent and predictable.
ANS: B

## Slide 41: Parametric Curve-based Planning
Non-parametric path: a path is represented as a sequence of points (as in A*, Dijkstra’s algo, RRT/PRM)
Parametric path: a smooth parametric curve that satisfies boundary conditions at 2 end points, constraints on curvature, and optimizes an objective function.
  : pose (position and heading angle) and curvature (, inverse of radius of rotation) of starting and final points
  : curvature has an upper bound for every point on the curve, to help satisfy kinematic/dynamic constraints, and improve rider comfort.
Example: Quintic splines and polynomial spirals
Coursera MOOC Motion Planning for Self-Driving Cars
Notes: Path Representation A smooth path with low curvature is easier to track by the controller, and more comfortable

## Slide 42: Quintic Splines
Path modeled as 5th-order polynomials, with closed-form solutions for boundary conditions
  The curve connects from start point to end point
Pro: path has closed-form equation for given start and end points
Con: curvature function and its derivatives may be discontinuous
https://pythonrobotics.readthedocs.io/en/latest/modules/path_planning.html
Notes: Pro: path has closed-form equation
Con: curvature function and its derivatives may be discontinuous
Pro: path has closed-form equation
Con: curvature function and its derivatives may be discontinuous
  𝜅(𝑢)=(𝑥^′ (𝑢) 𝑦^′′ (𝑢)−𝑦^′ (𝑢) 𝑥^′′ (𝑢))/(𝑥^′ (𝑢)^2+𝑦^′ (𝑢)^2 )^(3/2)

## Slide 43: Polynomial Spirals
Curvature defined as polynomial function (cubic or higher):
  It is smooth and never discontinuous, so constraining a few points often enough to constrain the entire curve.
Path modeled based on curvature function:
Pro: curvature function is smooth, so curvature can be given upper bound constraint.
Con: path has no closed-form equation; Fesnel integrals need to be computed with numerical integration using Simpson’s rule, which divides the integration interval into regions, and evaluates the function at each region boundary:
  (fig below shows example w. )
  Numerical Integration| What is Simpson's Rule? [Intuition] https://www.youtube.com/watch?v=DdNAcv_rezc

## Slide 44: Bending Energy Optimization Objective
Consider curvature modeled as Cubic spiral.
Minimize Bending Energy, defined as integral of squared curvature along the path, to distribute curvature evenly along spiral to promote comfort:
Subject to constraints:
  End point constraints:
    Starting point:
    Ending point:
  Curvature constraints for two intermediate points:
The optimization problem has closed-form solutions

## Slide 45: Soft Constraints
Since it is challenging to satisfy hard equality constraints, they can be softened into penalty terms in the objective function:
  s.t.

## Slide 46: Example Spline vs. Spiral

## Slide 47: Speed Profile Generation
Behavior planner provides reference speed to local planner
  May be current road speed limit
  Or current maneuver (stopping due to Stop sign or red light, following a lead vehicle…)
Time-To-Collision (TTC) can be computed by difference in speeds divided by distance (arc length )
Notes: Need to reach the red point at lead vehicle speed to avoid collision.

## Slide 48: Curvature and Lateral Acceleration
Speed also bounded by max lateral acceleration and curvature
Final reference speed selected as minimum of all upper bounds

## Slide 49: Speed Profile Examples

## Slide 50: Linear Ramp vs. Trapezoidal Profile
Linear ramp profile: constant acceleration to reach reference speed
Trapezoidal profile: constant-0-constant deceleration (e.g., for stopping at red light)

## Slide 51: Linear Ramp Profile
Given path length and initial/final speeds , compute required acceleration :
  Proof: consider a robot with starting speed and constant acceleration . After time , it reaches speed of , and travels a distance of .
May clamp acceleration to improve rider comfort.
For each path segment, compute speed using accumulated path arc length up to that point, to generate the speed profile:

## Slide 52: Trapezoidal Profile
Given total path length , initial/final speeds , and transit speed .
For 1st segment :
  Compute path arc length:
  Then compute speed profile:
For 2nd segment :
  Speed is constant
For 3rd segment ,
  Compute path arc length:
  Then compute speed profile:
Notes: Consider a robot with starting speed and constant acceleration or deceleration . After time , it reaches speed of , and travels a distance of .
(Coursera MOOC contains typos here.)
Consider a robot with starting speed 𝑣 and constant acceleration or deceleration −𝑣 ̇_𝑏. After time 𝑡, it reaches speed of 𝑣−𝑣 ̇_𝑏 𝑡=0, and travels a distance of (𝑣−1/2 𝑣 ̇_𝑏 𝑡)𝑡=1/2 𝑣 ̇_𝑏 𝑡^2=𝑣^2/(2𝑣 ̇_𝑏 ).

## Slide 53: Outline
Route planning
Behavior planning
Motion Planning
Responsibility-Sensitive Safety (RSS)
Paden B, Čáp M, Yong S Z, et al. A survey of motion planning and control techniques for self-driving urban vehicles[J]. IEEE Transactions on intelligent vehicles, 2016, 1(1): 33-55.
Notes: Safety plan
The safety plan gives an overview of how you are going to achieve a safe system. A few of the major elements include:
  what system is under consideration
  the goal of the project
  what steps will be taken to ensure safety
  the roles and personnel involved in the project
  the project timeline

## Slide 54: Avoid collisions at all cost?
But absolute safety is impossible.
In the scenario below, the AV (yellow car in the center lane) can do nothing to ensure absolute safety.
  If the red car swerves into the AV, collision cannot be prevented
To avoid this scenario, should the AV never drive in the center lane? Or should it never leave the garage?
  Avoiding collisions at all cost leads to a useless system.
Notes: Not a useful system

## Slide 55: Explicit Traffic Rules
Hard rules set limits on vehicle operation. Examples:
  Come to complete stop at red lights
  Don’t cross a double-yellow line
  Obey posted speed limits
  Yield to other road users when signaled
  …
These rules can be programmed into the AV.

## Slide 56: Implicit Traffic Rules
A general set of principles applied by the human driver. They are flexible and culturally dependent.
  Keep a safe distance from the car in front of you.
  Drive cautiously under limited visibility.
  Don’t drive slowly in the fast lane.
  Don’t cut off other drivers.
  …
How to formalize and program these rules into the AV?

## Slide 57: Responsibility-Sensitive Safety (RSS)
RSS formalizes human notions of safe driving into a verifiable model with logically provable rules, defines appropriate responses, and ensures that only safe decisions are made by the AV, and clearly assigns blame/responsibility in case of accidents.
Goal: An AV should never be responsible for accidents, meaning:
  It should never cause accidents
  It should properly respond to mistakes of other drivers
RSS is a mathematical, interpretable model, formalizing the implicit rules (common sense) of
  What is a dangerous situation?
  What is the proper response to a dangerous situation?
  Who is responsible for an accident?
Shalev-Shwartz S, Shammah S, Shashua A. On a formal model of safe and scalable self-driving cars[J]. arXiv preprint arXiv:1708.06374, 2017.
  Short intro video: RSS: Safety Assurance for Automated Vehicles
    https://www.youtube.com/watch?v=EceAB6TUYzo
  Long intro video: Mobileye's Responsibility-Sensitive Safety Mathematical Model Explained
    https://www.youtube.com/watch?v=pn88uJbkQqc
Notes: Check on AI outputs open, transparent, technology neutral safety model for autonomous driving
How self-driving cars will learn to make life-or-death decisions
  https://www.youtube.com/watch?v=EW4EqjxzFq4
It is OK for an AV to be involved in accidents, as long as it is not responsible for causing the accident.
open, transparent, technology neutral safety model for autonomous driving

## Slide 58: Five Rules of RSS
1. Do not hit the car in front (safe longitudinal distance. See figure below for example)
2. Do not cut-in recklessly (safe lateral distance)
3. Right-of-Way is given, not taken.
4. Be careful in areas with limited visibility
5. If you can avoid a crash without causing another, you must
Notes: RULE 1. Do not hit the car in front (longitudinal distance)
RULE 2. Do not cut in recklessly (lateral distance)

## Slide 59: RSS: High-Level Description
Define safe distance (longitudinal).
A situation is dangerous if it is non-safe longitudinally.
Blame time: the first moment in which the situation becomes dangerous
Proper response:
  If the longitudinal distance becomes non-safe, brake longitudinally.
Responsibility:
  We prove that a collision can only occur if one of the agents did not respond properly.
  The responsibility is on the agent(s) that did not respond properly.
Notes: If the lateral distance was becomes non-safe, brake longitudinally
and lateral
A situation is dangerous if it is nonsafe both laterally and longitudinally
Soundness: when the model says that the AV is not responsible for an accident, it should clearly match “common sense” of human judgement
Usefulness: it is possible to efficiently create a driving policy that guarantees to never cause accidents, while still maintaining normal flow of traffic.
  Do not avoid collisions at all cost and stay in the garage.
Can we ensure that a driving policy based on RSS does not lead to accidents of our blame?
  Not trivial due to butterfly effects, where a small action leads to a chain of events that lead to an accident.
  But answer is affirmative: use mathematical induction to construct an efficient procedure for guaranteeing RSS.

## Slide 60: Non-safe Lateral Maneuver
Proper response: red should brake laterally,
  since red is cutting into yellow’s lane.
  “Brake laterally” means “brake while steer to the right direction”.

## Slide 61: Non-Safe Longitudinal Maneuver
Proper response: yellow should brake,
  Since yellow is driving too fast and getting too close.

## Slide 62: Responsibility
Hit from behind
  Yellow is not responsible for the accident.
Side hit
  Red is not responsible for the accident.

## Slide 63: Keep Safe Distances
The AV (blue car) should keep safe longitudinal and lateral distances from other cars
  If the front car slams on the brakes, how much longitudinal distance does it need to avoid a rear-end collision?
  If the left or right car suddenly swerves, how much lateral distance does it need to avoid a side collision?

## Slide 64: Rule 1: Safe Longitudinal Distance
Consider two cars travelling in the same direction: front car and rear ego-car . In order to ensure that will never hit from behind, it is the responsibility of to keep a safe longitudinal distance from . The worst-case situation is that suddenly brakes hard, it will take some response time (sensing and reaction delay) to realize this and to start braking as well, and then both cars will decelerate. Assuming known parameters of: : front car ’s speed; : rear ego-car ’s speed; : ’s reaction time; : maximum deceleration rate (due to braking) for ; : minimum deceleration rate for ; : maximum acceleration rate for . The Safe Longitudinal Distance is:
Notes: Consider a single lane road, where cars cannot perform lateral manoeuvres.
Two cars are travelling in the same direction, front car and rear car . How can ensure that it will never hit from behind?
It is the responsibility of to keep a “safe distance” from , and should be large enough so that no matter what, will not hit . In our simple case, the worst-case situation is that will suddenly brake hard, it will take some response time (sensing and reaction delay) to figure this out and to brake as well, and then both cars will decelerate.
The common sense rule is “if someone hits you from behind it is not your fault”. So, a first try would be to define that if a rear car, , hits a front car, , from behind, then is responsbile for the accident.
But, this definition does not always comply with common sense. For example, suppose that both and are driving slowly up a hill, and then slows down and starts rolling backward until it hits . Even though hit from behind, the common sense in this situation is that should be responsible.
until reaching a full stop
The common sense rule is “if someone hits you from behind it is not your fault”. So, a first try would be to define that if a rear car, 𝑐_𝑟, hits a front car, 𝑐_𝑓, from behind, then 𝑐_𝑟 is responsbile for the accident.
But, this definition does not always comply with common sense. For example, suppose that both 𝑐_𝑟 and 𝑐_𝑓 are driving slowly up a hill, and then 𝑐_𝑓 slows down and starts rolling backward until it hits 𝑐_𝑟. Even though 𝑐_𝑟 hit 𝑐_𝑓 from behind, the common sense in this situation is that 𝑐_𝑓 should be responsible.

## Slide 65: Safe Longitudinal Distance: the Proof
Red (black) lines indicate accel/velocity/position of front (rear) car.
At time the initial distance between front car and rear car is , and front car and rear car have initial speeds and , respectively. Assuming , their distance will decrease monotonically with time. To avoid collision, the minimum initial distance can be obtained by assuming both cars will come to a full stop at some time with distance .
Front car: during time interval , front car applies brake with constant deceleration , and travels a distance of (average speed times time-to-stop ).
Rear car: during time interval , rear car accelerates with constant acceleration . At time , it reaches speed of , and travels a distance of . During time interval , rear car applies brake with constant deceleration . At time , it reaches speed of 0, and travels a distance of .
Min initial distance distance traveled by rear car before full stop - distance traveled by front car before full stop= , where .
65
Accel
Velocity
Position
Collision

## Slide 66: Safety vs. Efficiency
RSS allows to formally define the desired balance of safety and efficiency of AVs on the road.
  e.g., is larger if we assume a large deceleration rate for the front car; or larger acceleration rate or smaller deceleration rate for the rear car. So the AV will drive more conservatively, resulting in lower efficiency, and vice versa
These parameters should be determined by regulatory authorities working with the car makers.
  E.g., NHTSA (National Highway Traffic Safety Administration) in USA.
66

## Slide 67: Proper Response
The moment the distance between the two cars is less than , the AV will perform the proper response: after a response time , apply braking of at least until a safe following distance is restored or until the vehicle comes to a complete stop.
RSS can be a proactive safety mechanism that improves Automatic Emergency Braking (AEB). Called Automatic Preventive Braking (APB), it determines the moment when a vehicle enters a dangerous situation, then uses comfortable, subtle braking () to help return the vehicle to a safer position without waiting for an imminent collision to engage maximum braking force. This preventive approach would provide a stopping distance buffer that could prevent a chain reaction of braking and swerving should an emergency stop occur.
Notes: the application of RSS to traditional AEB systems would use formulas to determine the moment when a vehicle enters a dangerous situation. It would

## Slide 68: Other RSS Rules
Rule 2: Safe Lateral Distance
  Safe lateral distance enables AVs to be aware when their lateral safety may be compromised by unsafe drivers turning into their lanes.
Rule 3. Right of way is given, not taken
  On well-marked roads, the right of way is clear. Lane lines, signs, and traffic lights establish priorities for routes as they intersect one another. However, there are other times when the right of way is less clear, and human drivers must negotiate with one another.
Rule 4. Be cautious in areas with limited visibility
  Drivers must proceed cautiously, especially as they approach crosswalks or pass cars parked along the street
Rule 5. If the vehicle can avoid a crash without causing another one, it must
  It covers scenarios where a dangerous situation may have been imposed so suddenly that a collision cannot be avoided unless a more evasive action is taken. e.g., if boxes fall off the front car, and the next lane is free, the following car can take evasive action to avoid the accident.

## Slide 69: Integration into Apollo and CARLA
RSS is open-source as a C++ library. It has been integrated into Baidu Apollo’s planner module, and the driving simulator CARLA
RSS safety sensor in CARLA
  Use the opensource library to evaluate if a driving situations is safe or unsafe according to RSS. In that regard, a driving situation is composed of the ego vehicle (here in this video the ego vehicle is the one focused by the camera), and another traffic participant (e.g. a leading vehicle). The sensor evaluates longitudinal and lateral conflicts, but does not yet cover intersection conflicts.
  The results are highlighted via green (all safe), yellow (only lateral or longitudinal unsafe) and red lines (dangerous situation that requires to a counter measure according to RSS).
  https://www.youtube.com/watch?v=UxKPXPT2T8Q
Notes: https://intel.github.io/ad-rss-lib/

## Slide 70: Summary
RSS formalizes what is dangerous, what is the proper response to danger, and who is responsible for accidents.
Soundness: it complies with the common sense of human judgement.
Usefulness: we give 100% guarantees to never cause accidents and always properly respond to dangerous situations.