## Slide 1: L6 Control
Zonghua Gu, Umeå University
Nov. 2023

## Slide 2: Control in the AD Pipeline
The controller outputs control commands (brake, acceleration, steering) to follow the trajectory output from motion planning
(Local Planning)

## Slide 3: Feedback Control Problem
Given a system and a reference signal, find a control law such that the closed loop system is stable and follows the reference signal
The most common control algorithms in automotive systems are Proportional–Integral–Derivative (PID) and Model Predictive Control (MPC)

## Slide 4: Outline
PID Control
MPC Control
Kinematic bicycle model
Twiddle() for PID control tuning

## Slide 5: PID Control
Tracking Error:
Control input:
Ref: Controlling Self Driving Cars
  https://www.youtube.com/watch?v=4Y7zG48uHRo
https://en.wikipedia.org/wiki/PID_controller

## Slide 6: Step Response Performance Metrics
The control input (reference input) jumps from 0 to a reference value (e.g., 1.0) at time 0, and the controller aims to track it closely
  Rise time: the time it takes the transient response to move to of the steady state response
  Maximum overshoot: the amount (or percentage) by which the maximum value of the transient response exceeds the steady state value
  Peak time: the time at which the maximum overshoot occurs
  Settling time: the time after which the output is within a specified band around the steady state value
https://www.newport.com/n/control-theory-terminology
Notes: https://www.maplesoft.com/content/EngineeringFundamentals/11/MapleDocument_11/Block%20Diagrams,%20Feedback%20and%20Transient%20Response%20Specifications.pdf

## Slide 7: Proportional Term
proportional to error with factor
Increasing leads to:
  Faster response
  Bigger overshoot, oscillations
    System may become unstable
  Smaller but non-zero steady state error

## Slide 8: Integral Term
takes into account history of tracking error, and eliminates steady state error
Increasing leads to:
  Increased overshoot
  More robust to disturbances

## Slide 9: Derivative Term
proportional to error derivative by factor
Increasing leads to:
  Reduced overshoot
  Faster response
  Little effect on steady state
  More sensitive to measurement noise

## Slide 10: Effects of PID Gains
Closed-Loop Response | Rise Time | Overshoot | Settling Time | Steady State Error
Increase | Decrease | Increase | Small increase | Decrease
Increase | Small decrease | Increase | Increase | Large decrease
Increase | Small decrease | Decrease | Decrease | Minor change
Closed-Loop Response | Rise Time | Overshoot | Settling Time | Steady State Error
 | Decrease | Increase | Small increase | Decrease
 | Small decrease | Increase | Increase | Large decrease
 | Small decrease | Decrease | Decrease | Minor change

## Slide 11: Example: Vehicle Lateral Control
State
  : distance to center of lane; : heading angle.
Reference trajectory:
  The vehicle travels straight ahead at center of lane.
Vehicle has constant speed , so the only control input is , the angular velocity.
Assume perfect sensor state estimation:
  Ref. Control Algorithms for Autonomous Vehicles https://www.icloud.com/keynote/035Qivaw_FXYD70xCbD5R9lDA#control_AV
Notes: https://www.icloud.com/keynote/035Qivaw_FXYD70xCbD5R9lDA#control_AV
  Ref. Control Algorithms for Autonomous Vehicles https://www.icloud.com/keynote/035Qivaw_FXYD70xCbD5R9lDA#control_AV

## Slide 12: System and P Control Modeling
Linear system dynamics:
  assuming is small ( linearized kinematic model)
P Controller:
Closed-loop dynamics is obtained by plugging into system dynamics:
Ref trajectory:
Error signal:
Error dynamics:
Control objective: design to drive error to

## Slide 13: P Control Design with Pole Placement (not covered in this course)
Closed-loop poles:
  Solution
Critically-damped dynamics (repeated real roots):
  chosen empirically

## Slide 14: P Control Design Cont’d
Linear systems dynamics relies on the small angle approximation , assuming
Closed-loop dynamics
  Set ,
  where:
Empirical param settings: ,
Notes: For example: to have , set
  Even if the vehicle is very far from center of lane, do not change heading angle too fast (keep small). (A heuristic rule-of-thumb, not a hard guarantee)
For example: to have 𝜃_𝑡ℎ=𝜋/6, set 𝑑_𝑡ℎ=|(𝐾_𝜃 𝜃_𝑡ℎ)/𝐾_𝑑 |
  Even if the vehicle is very far from center of lane, do not change heading angle 𝜃(𝑡) too fast (keep 𝜃 ̇(𝑡) small). (A heuristic rule-of-thumb, not a hard guarantee)

## Slide 15: Simplifying Assumptions
Did not consider:
  Estimation uncertainty due to measurement noise
    We assume perfect state estimation
  Estimation latency:
    Time from measurements to state estimation availability to the controller
  Constraints (e.g., actuator limits)
    Need to impose a maximum curvature radius to simulate a real car.
  Discrete time (multi-rate), non-uniform sampling:
    Our controller is continuous time, but the actual implementation runs in discrete time.
    Sampling rate of the estimator (slower) may be different than that of actuation (faster), or may be variable

## Slide 16: Outline
PID Control
MPC Control
Kinematic bicycle model
Twiddle() for PID control tuning

## Slide 17: MPC (Model-Predictive Control)
Also called Receding Horizon Control
Choose prediction horizon and control horizon
At each time step :
  Set initial state to predicted state
  Solve a constrained optimization problem over lookahead window , to get a sequence of control inputs , while in the time interval
  Apply 1st control command at time step
Control horizon and prediction horizon may be different, but often the same
  denoted as lookahead horizon in the next slides (current time is denoted as )

## Slide 18: MPC Example
Solve for opt control inputs within lookahead horizon to track the blue desired traj
Execute control input
at 1st timestep
Replan a new set of control inputs at next time step
Execute control input at 1st timestep
…
Notes: Input trajectory refers to computed control inputs
Input trajectory refers to computed control inputs U={u_k,…,u_(k+p−1) }

## Slide 19: MPC Illustration Con’t
Yellow: reference trajectory from planner
Green: trajectory from running control inputs computed by MPC based on system model for lookahead horizon
https://medium.com/@david010/vehicle-mpc-controller-33ae813cf3be

## Slide 20: Linear vs. Nonlinear MPC
Linear MPC (no constraints)
  s.t. for
  is the difference between actual state and ref state (assumed to be 0 here), which should be minimized with the term
  is control input, which should be minimized with the term (to reduce control effort)
  Relative magnitudes of and encode relative importance of the two objectives
  Can be solved analytically at each time step
Nonlinear MPC (with constraints)
  s.t. for
  Both objective and system dynamics may be nonlinear
  Cannot be solved analytically; must solve numerically with optimizers, e.g., CasADi
(Note: in , superscript denotes “vector transpose”; subscript denotes “lookahead horizon”)

## Slide 21: MPC Pros and Cons
Pros
  Predictive control with lookahead
    PID is reactive control, like driving your car by looking in the rearview mirror
  Handles constraints explicitly
    PID control cannot handle constraints
  Applicable to both linear and nonlinear systems
    Pole placement for PID control design is applicable to linear systems only
    Empirical PID param tuning is model-free and applicable to any system (blackbox)
Cons
  Requires accurate yet efficient system model (whitebox)
  Optimizer computation may be expensive, esp. for non-linear MPC
    Select lookahead horizon to tradeoff between control performance and computation overhead
    Small myopic behavior, lower overhead; Larger better control performance but higher overhead
Notes: Pole placement for PID control design is applicable to linear systems only

## Slide 22: PID Control Example (No Look-Ahead)
Vehicle accelerates to track setpoint speed of 70 km/h
Then decelerates upon encountering a sharp turn, but it is too late and cannot track the lane
https://uni-tuebingen.de/fakultaeten/mathematisch-naturwissenschaftliche-fakultaet/fachbereiche/informatik/lehrstuehle/autonomous-vision/lectures/self-driving-cars/

## Slide 23: MPC Control Example (Look-Ahead)
MPC computes control actions based on a lookahead window into the future
Vehicle decelerates early in anticipation of the sharp turn
https://uni-tuebingen.de/fakultaeten/mathematisch-naturwissenschaftliche-fakultaet/fachbereiche/informatik/lehrstuehle/autonomous-vision/lectures/self-driving-cars/

## Slide 24: MPC Quiz
Which from the below statement about MPC are true?
  1) Horizon is a finite window of time
  2) Prediction horizon keeps being shifted at each time step
  3) Full optimization over the time horizon is performed at each iteration
  4) Only the first control action from the optimization is applied at time
  5) All of the above
ANS: 5

## Slide 25: Outline
PID Control
MPC Control
Kinematic bicycle model
Twiddle() for PID control tuning

## Slide 26: Kinematics vs. Dynamics
Kinematics is study of motion without considering the forces that affect the motion. It deals with the geometric relationships that govern the system
  A kinematic model:
  Uses position, velocity, acceleration (and/or further derivatives) as control input (e.g. the kinematic bicycle model)
Dynamics is the study of motion taking into account the forces that affect it. It is described by the equations of motion.
  A dynamic model: (Newton’s law with friction)
  Uses force and torque as control input, and takes mass and inertia into consideration.
  e.g., vehicle dynamics model (longitudinal and lateral)
Consider two vehicles with the same geometry but different mass/weight turning a tight corner
  They may have the same kinematic model, but different dynamic model due to different mass .
  Both may be controllable kinematically by control input
    The light vehicle may be controllable dynamically by control input .
    The heavy vehicle may not be controllable dynamically by control input . Due to large , may exceed the max actuator limit.
Orthogonal issue from control algorithm
  Control algorithms, e.g., PID or MPC, may be either kinematic or dynamic control

## Slide 27: Kinematic vs. Dynamic Control
PID controller for kinematic bicycle model with heading angle rate and velocity , constant here) as control input. ( should be controlled indirectly by controlling steering angle , with .)
MPC for dynamic vehicle model (high-level controller) with forces (longitudinal and lateral) as control input.

## Slide 28: Kinematic Bicycle Model
Front wheel steering. Assuming here rear wheel as reference point (may also use front wheel or center of gravity).
State vector: : vehicle pose includes its position and heading angle .
Control inputs: : steering angle and vehicle speed (assumed to be constant).
  : vehicle length (distance between 2 wheels); : rotation radius of Instantaneous Center of Rotation (ICR), equal to distance between ICR and rear wheel. Curvature .
  Line from ICR to each wheel is perpendicular to it.
  Angular velocity is speed divided by rotation radius
Typically, angles are based on counter-clockwise convention w.r.t reference direction.
  In the fig, w.r.t ref direction ; w.r.t ref direction east (horizontal); for counter-clockwise rotation.
(Non-linear in ;
Linear in )

## Slide 29: State Update in Python Code
# apply noise
steering2 = random.gauss(steering, self.steering_noise)
distance2 = random.gauss(distance, self.distance_noise)
# apply steering drift
steering2 += self.steering_drift
# noise and drift are all set to 0, so steering2 is steering angle , distance2 is distance traveled per time step
# Execute motion
turn = np.tan(steering2) * distance2 / self.length ()
if abs(turn) < tolerance: (with small )
# approximate by straight line motion
self.x += distance2 * np.cos(self.orientation) ()
self.y += distance2 * np.sin(self.orientation) ()
self.orientation = (self.orientation + turn) % (2.0 * np.pi) ()%())
else: (with large )
# Circular motion around ICR
radius = distance2 / turn (; can also use )
# compute ICR’s coordinates (cx, cy)
cx = self.x - (np.sin(self.orientation) * radius) ()
cy = self.y + (np.cos(self.orientation) * radius) ()
self.orientation = (self.orientation + turn) % (2.0 * np.pi) ()
# compute vehicle’s x, y coordinate after rotation around ICR
self.x = cx + (np.sin(self.orientation) * radius) ()
self.y = cy - (np.cos(self.orientation) * radius) ()
(modulo ) keeps angles to be within ; It can be omitted since it does not affect results of functions (assuming no numeric overflow).

## Slide 30: State Update Equation
Circular motion around ICR (accurate):
Straight-line motion for small (approximate):

## Slide 31: Straight Line vs. Circular Motion
Straight line motion (with steering angle ) is a special case of circular motion with radius .
  (small steering angle leads to slow angular velocity .)
  We use this special case to improve computational efficiency for small , and avoid division by 0.
  , for small .
  , for small .
Four special cases of straight line motion:
  (east)
  (west)
  (north)
  (south)

## Slide 32: PID Control Lab Setup
Based on Udacity course Lesson AI for Robotics, Lesson 15: PID Control
  https://classroom.udacity.com/courses/cs373/
Lateral control of a car to run along a race track (either straight line or circular) with fixed speed.

## Slide 33: Outline
PID Control
MPC Control
Kinematic bicycle model
Twiddle() for PID control tuning

## Slide 34: Udacity: Racetrack Control
Lesson 16: Problem Set 5, 4. Quiz: Racetrack control.
Cross-track error (cte): lateral distance (of rear wheel) to desired trajectory, defined as:
  if : deviation from the straight horizontal track (with the implicit assumption that the car will not deviate from the track for more than .)
  Otherwise: deviation from each semi-circle track.
For clockwise traversal, cte>0 if car is outside of the track region; cte<0 if inside.
cte>0
cte>0
cte<0
cte<0
Initial pose

## Slide 35: run()
Implements the PID controller for with PID gains
  params[0] as ; params[1] as ; params[2] as .
  Returns actual trajectory as arrays of x_trajectory[], y_trajectory[]; and average error, defined as sum of squared cte
For clockwise travel direction:
  If cte>0, car is outside of track region; steering angle should decrease (turn right according to the counter-clockwise convention)
  If cte<0, car is inside of track region; steering angle should increase (turn left)
  Based on the above, should be positive (this can be a sanity check for your final solution)
This is for straight line track; need to call myrobot.cte() for circular track.
PID control law
Notes: (Minus signs can be removed without affecting correctness.)

## Slide 36: For General
The Python code assumes controller time step size .
  Also, is constant. ’s range is unconstrained (steering wheel can be turned to arbitrary angle).
For general , the following needs to be modified:
  Call myrobot.move(steer, speed*dt), to match its definition move(self, steering, distance,…)
  In the PID control law:
    Differential of error
    Integral of error

## Slide 37: twiddle()
twiddle: “twist, move, or fiddle with (something), typically in a purposeless or nervous way” –Encyclopedia.
Update to and run(). If error decreases, then was updated in the right direction. Keep the update to get , and increase step size to .
If error increases, then was updated in the wrong direction. Update in the opposite direction by to get . Run again.
If error decreases, then was updated in the right direction. Keep the current , and increase step size to .
If error increases, then was updated in the wrong direction. Update in the opposite direction by + to get back the original . Reduce step size to .
Adjust each in turn.

## Slide 38: Changing to P Control
Setting turns it into a P controller, since are initialized to 0 and never changed. is adjusted in twiddle()
twiddle() is a local optimization algorithm, so perf is dependent on parameter initialization. Here are initialized to 0 for simplicity.
  https://classroom.udacity.com/courses/cs373/lessons/91f48b5b-a063-41f9-ace6-5fb9e7508941/concepts/b740218e-b0eb-40dc-80af-343912305293

## Slide 39: twiddle() vs. Pole Placement
twiddle() is a model-free approach to tuning PID controller by Gradient descent. It adjusts each PID gain parameter systematically, gradually decreasing or increasing step of adjustment (the gradient) until convergence to minimum best_err.
Pole placement for PID controller design is model-based, but requires a linear model
  With simplifying assumptions:
    is small
    Simplified kinematic model: as control input instead of