## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 5 Network Layer:
Control Plane
Acknowledgement: Based on the textbook’s website: https://gaia.cs.umass.edu/kurose_ross/index.php
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Re-do of network management slides; redo of Bellman-Ford slides
8.2 (changes over 8.0)
improved animations of Dijkstra’s algorithm and Bellman Ford
various improvements to BGP
SDN: added Google Orion (2021 Google network SDN control plane)

## Slide 2: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 3: Making routing scalable
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice
scale: billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network

## Slide 4: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
intra-AS (aka “intra-domain”): routing among routers within same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
inter-AS (aka “inter-domain”): routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)
IMPORTANT

## Slide 5: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations
IMPORTANT

## Slide 6: Inter-AS routing plays a role in intradomain forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1, but which one?

## Slide 7: Intra-AS routing: routing within an AS
most common intra-AS routing protocols:
RIP: Routing Information Protocol [RFC 1723]
  classic Distance Vector: DVs exchanged every 30 secs
  no longer widely used
EIGRP: Enhanced Interior Gateway Routing Protocol
  DV based
  formerly Cisco-proprietary for decades (became open in 2013 [RFC 7868])
OSPF: Open Shortest Path First [RFC 2328]
  Link-State routing
  IS-IS protocol (ISO standard, not RFC standard) essentially same as OSPF

## Slide 8: OSPF (Open Shortest Path First) routing
“open”: publicly available
classic link-state
  each router floods OSPF link-state advertisements (directly over IP rather than using TCP/UDP) to all other routers in entire AS
  multiple link costs metrics possible: bandwidth, delay
  each router has full topology, uses Dijkstra’s algorithm to compute forwarding table
security: all OSPF messages authenticated (to prevent malicious intrusion)

## Slide 9: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations
area border routers: “summarize” distances to destinations in own area, advertise in backbone
area 1
area 2
area 3
backbone
internal
routers
backbone router: runs OSPF limited to backbone
boundary router: connects to other ASes
local routers:
flood LS in area only
compute routing within area
forward packets to outside via area border router

## Slide 10: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 11: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
intra-AS (aka “intra-domain”): routing among routers within same AS (“network”)
inter-AS (aka “inter-domain”): routing among AS’es
Notes: Each router then locally runs Dijkstra’s shortest-path algorithm to determine a shortest-path tree to all subnets, with itself as the root node.

## Slide 12: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  Neither Distance Vector nor Link-State. It is a ”Path-Vector” protocol
allows AS to advertise its existence, and the destinations it can reach, to rest of Internet: “I am here, here is who I can reach, and how”
BGP provides each AS a means to:
  obtain destination network reachability info from neighboring ASes (eBGP)
  determine routes to other networks based on reachability information and policy
  propagate reachability information to all AS-internal routers (iBGP)
  advertise (to neighboring networks) destination reachability info
Notes: Since an inter-AS routing protocol involves coordination among multiple ASs, communicating ASs must run the same inter-AS routing protocol. In fact, in the Internet, all ASs run the same inter-AS routing protocol, called the Border Gateway Protocol, more commonly known as BGP

## Slide 13: eBGP, iBGP connections
eBGP connectivity
logical iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 14: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 15: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes
Notes: BGP messages exchanged between peers over TCP connection
BGP messages [RFC 4371]:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection
  BGP protocol messages

## Slide 16: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
AS3, X

## Slide 17: BGP path advertisement: multiple paths
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
based on policy, AS1 gateway router 1c chooses path AS3,X and advertises path within AS1 via iBGP
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS3,X
AS3,X
AS3,X

## Slide 18: BGP: populating forwarding tables
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS2,AS3,X
AS3,X
AS3, X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
1
2
dest
interface
…
…
…
…
local link interfaces
at 1a, 1d
at 1d: to get to X, use interface 1
1c
1
X
1
AS3,X
AS3,X
AS3,X

## Slide 19: BGP: populating forwarding tables
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
at 1d: to get to X, use interface 1
dest
interface
…
…
…
…
1c
2
X
2
at 1a: OSPF intra-domain routing: to get to 1c, use interface 2
at 1a: to get to X, use interface 2

## Slide 20: Hot potato routing
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: OSPF chooses local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): intra-domain routing unaware of inter-domain cost
AS3,X
AS1,AS3,X
OSPF link weights
201
112
263

## Slide 21: BGP: achieving policy via advertisements
B
legend:
customer
network:
provider
network
A,B,C are provider networks; x,w,y are their customers
x is B’s customer; y is C’s customer. B wants to route traffic from x but not from y.
A advertises path Aw to B and to C
B chooses not to advertise BAw to C!
  B gets no “revenue” for routing CBAw (red path), since none of C, A, w are B’s customers
C does not learn about CBAw path, so C will route CAw (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,w
A,w
Desirable
Undesirable

## Slide 22: BGP: achieving policy via advertisements (more)
B
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
x is dual-homed: attached to two networks
policy to enforce: x does not want to route from B to C via x (red path) since it gets no “revenue” for this route
  .. so x will not advertise to B a route to C
legend:
customer
network:
provider
network
Desirable
Undesirable

## Slide 23: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 24: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its network
intra-AS: single admin, so policy less of an issue
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy dominates over performance