## Slide 1: Z. Gu
Spring 2026
CSC175 Spring 2026 Final Exam Sample Questions ANS

## Slide 2: Pipe Diagrams – Packet Transmission Delay
Transmission Delay
Transmission Delay
The width of the packet in the pipe represents the transmission delay.
How long it takes to push all the bits onto the link.
Link capacity = Propagation Delay × Bandwidth
Packet size = Transmission Delay × Bandwidth
  For a packet of given size: higher bandwidth  shorter transmission delay (higher bandwidth = fatter pipe = more bits in pipe per unit time = narrower packet in pipe).
Bandwidth
Propagation Delay
Propagation Delay
Bandwidth
IMPORTANT
Notes: okay so this is the picture that I
1:14:21
really care about at the very end so ultimately when people draw these again they don't draw the dots but they will
1:14:28
draw things like this they'll draw a blue rectangle to represent the link and then they will draw these orange squares
1:14:34
that represent the packets themselves and so these are actually the same packets these are three packets each
1:14:41
packet is 20 dots these are also three packets each packet is also 20 dots or
1:14:47
20 bits but notice that because the link itself changed in particular the link
1:14:52
itself received more bandwidth so we're switching to will link with more bandwidth the packets got taller and
1:14:58
narrower they shifted their shape to fit in the new pipe and so something that I
1:15:04
think is really confusing to people when they see these diagrams is that wait a minute when I change the link that I'm
1:15:10
using the packets themselves also change shape and yes that's true they change shapes because they fit in the pipe in a
1:15:17
different way in particular more dots can be stacked and so they get taller
1:15:23
and they get narrower because it takes less time to send them through the pipe the other thing that I think is not
1:15:28
totally intuitive is the transmission delay is the width of the packet so the
1:15:34
width of this packet tells me the transmission delay that is how long does it take to shove this packet into the
1:15:40
pipe and what this picture is showing you is that if you increase the bandwidth now that they can March in t
1:15:46
instead of stacks of five the transmission delay got shorter and that's represented by the fact that the
1:15:51
packet got less wide I know I just said a lot of words at you
1:15:58
this will probably take a little bit of playing around with the demos and watching the animations to make sense if
1:16:03
the dots don't make sense I really just care about the shape of these rectangles but maybe they helped maybe they didn't
1:16:09
complain at me in the comments if you didn't like this but you can't say I didn't try I drew
1:16:15
all the diagrams any questions on this by the way it is kind of a funky topic when I
1:16:21
saw this I had for the first time I had no idea what the pipes look like when I drew the dots in they made a little bit more sense to me but maybe
1:16:28
not but the key idea I think is really confusing is really just the fact that transmission delay is actually the width
1:16:33
of the packet not immediately obvious and the fact that it gets uh shorter as the packet gets
1:16:40
taller okay an attempt was made but let me know on ad or elsewhere if you find
1:16:46
this confusing we can talk about it somewhere

## Slide 3: Lecture 3 - Links
Consider the pipe diagram below, with a single packet in the pipe:
Q1 What is the size of this packet?
Q2 How long does it take to send a packet of the same size as the packet shown? (Count from the time the first byte is sent, to the time the last byte is received.)
Q3 How long does it take to send 7 packets, all of the same size as the packet shown? (Count from the time the first byte of the first packet is sent, to the time the last byte of the last packet is received.)
Q4 (2 points) What is the maximum number of packets that could be in the process of being sent along this link, at any given moment?

## Slide 4: Lecture 3 - Links ANS
Q1 What is the size of this packet?
  ANS: 𝑥𝑦
  Explanation: 𝑥 is Transmission Delay (how many seconds it takes to transmit the packet). 𝑦 is link bandwidth (how many bytes can be sent per second). Multiplying 𝑥 (seconds) and 𝑦 (bytes/second) gives the overall size of this packet.
Q2 How long does it take to send a packet of the same size as the packet shown? (Count from the time the first byte is sent, to the time the last byte is received.)
  ANS: 𝑥 + 𝑧
  Explanation: 𝑥 is Transmission Delay, 𝑧 is Propagation Delay. Adding them gives the total delay for this packet.
Q3 How long does it take to send 7 packets, all of the same size as the packet shown? (Count from the time the first byte of the first packet is sent, to the time the last byte of the last packet is received.)
  ANS: 7𝑥 + 𝑧
  Explanation: It takes 7𝑥 seconds to transmit all 7 packets. 𝑧 is the propagation delay. Adding them gives the total delay for 7 packets.
Q4 (2 points) What is the maximum number of packets that could be in the process of being sent along this link, at any given moment?
  ANS: 𝑧/𝑥
  Explanation:𝑥 is Transmission Delay, 𝑧 is Propagation Delay. The maximum number of packets that can be in flight therefore is 𝑧/𝑥.

## Slide 5: Lecture 3 - Links
Now, consider the topology below. R1 has an infinite-size queue, and R1 continually processes packets in its queue in FIFO order. R1 can only start transmitting a packet once it has received the entire packet. All packets in the question are the same size as the packet shown in the diagram below. A wants to send a packet to B. No other packets are being sent along the links (i.e. suppose the packet in the diagram is not there). In the next two subparts, select how long it takes to send the packet from A to B. Count from the time the first byte of the packet is sent at A, to the time the last byte of the packet is received at B.
Q5 In this subpart, suppose R1 has 1 other packet in its queue when A sends the packet. How long does it take to send a single packet from A to B?
Q6 In this subpart, suppose R1 has 20 other packets in its queue when A sends the packet. How long does it take to send a single packet from A to B? Assume that the queue at R1 is not empty when this packet arrives at R1.
Q7 What is the maximum number of packets that can be queued at R1, such that when the last byte of the A-to-B packet reaches R1, there is no queue at R1? Don’t worry about fractions and rounding (e.g. assume 𝑥, 𝑦, and 𝑧 are defined such that all answer choices are integers).

## Slide 6: Lecture 3 - Links ANS
Q5 In this subpart, suppose R1 has 1 other packet in its queue when A sends the packet. How long does it take to send a single packet from A to B?
  ANS: 2𝑥 + 2𝑧
  Explanation: Since all packets are the same size, by the time A transmits the packet onto the A-to-R1 link, R1 has finished clearing out its queue. Therefore, there will be no queuing delay at R1. The packet takes 𝑥 + 𝑧 time to travel from A to R1 (transmission delay 𝑥 and propagation delay 𝑧). At time 𝑥 + 𝑧, R1 has received the entire packet. R1 then must send the packet along the R1-to-B link, which takes 𝑥 + 𝑧 time again. The total time to transmit the packet from A to B is 2(𝑥 + 𝑧) = 2𝑥 + 2𝑧.
Q6 In this subpart, suppose R1 has 20 other packets in its queue when A sends the packet. How long does it take to send a single packet from A to B? Assume that the queue at R1 is not empty when this packet arrives at R1.
  ANS: 21𝑥 + 𝑧
  Explanation: By the time the A-to-B packet arrives at R1, the queue is not empty (per the assumption). Therefore, we have to account for queuing delay. We have to wait for R1 to finish sending all 20 packets, and then it can send the A-to-B packet. The time it takes for R1 to transmit 21 packets (the 20 in the queue, plus the A-to-B packet) is 21𝑥.
  Then, the time it takes for the A-to-B packet to propagate along the R1-to-B link is 𝑧. Thus, the total packet delay is 21𝑥 + 𝑧. Note that we don’t need to consider the propagation delay on the A-to-R1 link, since it overlaps with the transmission delay 21𝑥 (i.e. the packet was sent from A to R1 while R1 was clearing out its queue).

## Slide 7: Lecture 3 - Links ANS
Q7 What is the maximum number of packets that can be queued at R1, such that when the last byte of the A-to-B packet reaches R1, there is no queue at R1? Don’t worry about fractions and rounding (e.g. assume 𝑥, 𝑦, and 𝑧 are defined such that all answer choices are integers).
ANS: (𝑥+𝑧)/𝑥
Explanation: The time it takes to send the packet from A to R1 is 𝑥 + 𝑧. R1 needs 𝑥 seconds to send out each packet. Therefore, in 𝑥 + 𝑧 seconds, R1 is able to send out (𝑥+𝑧)/𝑥 packets. Therefore, R1 can have at most (𝑥+𝑧)/𝑥 packets in its queue, and all of those packets will be sent out by the time the last byte of the A-to-B packet reaches R1.