## Slide 1
Lecture 12, Spring 2026
Congestion Control, Part 1
Lecture 12 (Transport 3)
Notes: Slides template credit: Josh Hug, Lisa Yan

## Slide 2: Congestion Control: Why do we need it?
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, Spring 2026

## Slide 3: Recall: Congestion at Routers
If two packets arrive at the same time, the router will send one, and buffer the other.
The router maintains a queue of packets that still need to be sent. If too many packets arrive close in time:
The router cannot keep up, and gets congested.
Packets can be delayed (stuck waiting in queue) or dropped (queue is full).
For a typical queuing system with bursty arrivals:
Higher load = more packets sent = higher packet delay.
Delay gets really bad, even before we reach 100% load.
Trade-offs: Need to balance high link utilization and low delay.
B
A
Router
I cannot send both A and B right now.
One of them will have to wait.
Load
100% load
Average Packet Delay
Notes: If the queue is full, and a packet arrives, the packet gets dropped.

## Slide 4: Brief History of Congestion Control
In the 1980s, TCP did not implement congestion control.
Sending rate was only limited by flow control (recipient buffer capacity).
If packets are dropped, resend them over and over, at the same fast rate.
This led to a congestion collapse.
1986: Capacity of a major link dropped to 0.1% of its original capacity.
Why? Network was flooded with thousands of copies of every packet.
Michael Karels and Van Jacobson changed a few lines of TCP code in BSD (an early OS) to fix the problem.
  The fix worked, and everybody quickly adopted it.
Extensive research and improvements since the original patch.
Notes: Recall: TCP is implemented in everybody's OS.

## Slide 5: Congestion Control: Why is it hard?
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, Spring 2026

## Slide 6: Congestion Control Challenges: Depends on Destination
At what rate should A send traffic?
It depends on the destination.
A → C can send at 10 Gbps.
A → F can only send at 2 Gbps.
A
B
R1
R3
R7
R4
R2
R5
R6
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10
Numbers denote bandwidth in Gbps.
Ignore bandwidth of host-to-router LAN links, which is very high compared to router-to-router WAN links.

## Slide 7: Congestion Control Challenges: Depends on Path
At what rate should A → E send traffic?
It depends on the path through the network.
A → E via R3 can send at 10 Gbps.
A → E via R2 can send at 1 Gbps.
A
B
R1
R3
R7
R4
R2
R5
R6
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10

## Slide 8: Congestion Control Challenges: Depends on Competing Flows
At what rate should A → F send traffic?
It depends on others using the network.
A → F and B → E share a link.
B → E can send at 1 Gbps.
A → F can send at 1 Gbps.
A
B
R1
R3
R7
R4
R2
R5
R6
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10

## Slide 9: Congestion Control Challenges: Depends on Indirect Competition
What if G → D starts sending traffic?
Maybe B → E should slow to 0.5 Gbps.
Then A → F could increase to 1.5 Gbps.
G → D and A → F share no links, but they still affected each other's bandwidth.
A
B
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10
R1
R3
R7
R4
R2
R5
R6

## Slide 10: Congestion Control is a Global Problem
The sender's optimal rate depends on:
The destination.
The path to the destination.
Other connections sharing links along that path.
Connections sharing links with those other connections.
And so on...
Congestion control is a global problem.
Connections in the network are highly interdependent.
Solving it optimally requires a global view of the network.

## Slide 11: Congestion Control as Resource Allocation Problem
Fundamentally, congestion control is a resource allocation problem.
Bandwidth is a limited resource.
Each connection demands a certain amount of bandwidth.
We decide how much to allocate to each connection.
Resource allocation is a classic problem (e.g. CPU scheduling, memory allocation).
But, congestion control has additional challenges.
A change in one connection can have a global impact.
Network topology is constantly changing.
Connections are constantly starting and ending.
Everybody must solve it locally. No global view of network.

## Slide 12: Design Goals
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, Spring 2026

## Slide 13: Design Goals
Goals for a good congestion control algorithm:
Avoid congestion: Minimize packet delay and loss.
Efficiency: Maximize link utilization.
Fairness: Connections should share the available bandwidth.
Practical to implement: Scalable, decentralized, adaptive, etc.
Our ultimate goal is a good tradeoff between these metrics.
Notes: Could avoid congestion (1) by sending really slowly.
But then we aren't using all the bandwidth on the link (2).

## Slide 14: Possible Approaches
Reservations:
Connections reserve bandwidth at the start, and release bandwidth at the end.
Requires connections to know bandwidth ahead of time.
Other problems: Hard to implement, inefficient bandwidth usage, etc.
Pricing/priorities:
Analogy: Express toll lanes on the highway. Price changes depending on traffic.
Prioritize traffic from users who pay more.
Requires a payment model.
Dynamic adjustment:
Learn the current congestion level, and adjust your rate accordingly.
Requires good citizenship (no cheating).

## Slide 15: Possible Approaches
3 possible approaches: reservations, pricing, and dynamic adjustment.
All the algorithms we'll see are based on dynamic adjustment.
If we rebuilt the Internet from scratch, another approach might be feasible.
But congestion control was invented as a patch on the existing Internet.
Dynamic adjustment is the best fit for the existing Internet:
  Doesn't require knowing bandwidth ahead of time.
  Doesn't require a payment model.
Congestion Control Protocols
Pricing
Reservations
Dynamic Adjustment

## Slide 16: Dynamic Adjustment: Algorithm Sketch
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, Spring 2026

## Slide 17: Dynamic Adjustment: Discovery
Discovery: Host A discovers it can send data at 10 Gbps.
A
B
R1
R3
R7
R4
R2
R5
R6
G
F
E
D
C
10
2
1
4
4
10
10
4
5
10

## Slide 18: Dynamic Adjustment: Detection and Adjustment
Later, the R1 → R3 link goes down. A's traffic is rerouted.
Detection: A notices that 10 Gbps is congesting the network.
Adjustment: A decides to slow down to 1 Gbps.
A
B
G
F
E
D
C
2
1
4
4
10
10
4
5
10
R1
R3
R7
R4
R2
R5
R6

## Slide 19: Dynamic Adjustment: Detection and Adjustment
Later, G → D starts sending traffic.
Detection: A notices that 1 Gbps is congesting the network.
Adjustment: A decides to slow down to 0.5 Gbps.
A
B
G
F
E
D
C
2
1
4
4
10
10
4
5
10
R1
R3
R7
R4
R2
R5
R6

## Slide 20: Types of Dynamic Adjustment Algorithms
Solutions can be classified into 2 types, depending on where they're implemented:
Host-based congestion control: (TCP uses this one)
Implemented at the end hosts. No special support from routers.
Hosts adjust rate based on implicit feedback from routers.
Router-assisted congestion control:
Routers signal congestion back to end hosts.
Hosts pick rate based on explicit feedback from routers.
Congestion Control Protocols
Pricing
Reservations
Dynamic Adjustment
Router-assisted
Host-based
Today
Next time

## Slide 21: Host-Based Dynamic Adjustment: Algorithm Sketch
Every host independently runs the same algorithm:
Pick an initial rate R. (How do we pick the initial rate?)
Try sending at rate R for some period of time.
  Did I experience congestion in this time period? (How do we detect congestion?)
  If no, increase R.
  If yes, reduce R. (How much do we increase/decrease by?)
  Repeat.
Components of a solution:
Discovering an initial rate.
Detecting congestion.
Reacting to congestion (or lack thereof) by increasing/decreasing rate.

## Slide 22: Detecting Congestion
There are 2 ways for the host to detect congestion.
Remember: The host can't see the whole network.
Congestion Control Protocols
Pricing
Reservations
Dynamic Adjustment
Router-assisted
Host-based
Loss-based
Delay-based

## Slide 23: Detecting Congestion
Loss-based detection: If we lose a packet, declare congestion. (This is what TCP uses.)
Pros:
Unambiguous signal: Every packet is either lost (resent), or not lost.
TCP already detects loss for reliability.
Cons:
Not all loss is caused by congestion. (e.g. checksum error).
A delayed packet could be mistakenly declared lost.
When we detect loss, the network is already congested (queues are full).
Delay-based detection: If packets are delayed, declare congestion.
Challenge: Packet delay length varies with queue size and other traffic.
Long considered tricky to get right.

## Slide 24: Discovering an Initial Rate: Slow Start
Goal for discovering initial rate: Estimate available bandwidth.
Start slow for safety.
Starting too fast would cause congestion.
Ramp up quickly for efficiency.
Example of inefficiency: Suppose we added 0.5 Mbps every 0.1 seconds.
If 1 Mbps available, we'll reach the target in 0.2 seconds.
If 1 Gbps available, we'll reach the target in 200 seconds.
  Lots of time wasted sending at suboptimal rates.
Slow start is an algorithm for discovering the initial rate:
Start with a small rate (could be much less than actual bandwidth).
Increase exponentially (e.g. double rate each time) until we detect loss.
A safe rate is the most recent rate before detecting loss.
  0.5 × rate when loss occurred.
1
2
4
8
16
32
32 was the last safe rate.
64 – congestion detected!

## Slide 25: Reacting to Congestion
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, Spring 2026

## Slide 26: Host-Based Dynamic Adjustment: Algorithm Sketch
Every host independently runs the same algorithm:
Pick an initial rate R. (Slow start.)
Try sending at rate R for some period of time.
  Did I experience congestion in this time period? (Detect packet loss.)
  If no, increase R.
  If yes, reduce R. (How much do we increase/decrease by?)
  Repeat.

## Slide 27: Reacting to Congestion
Rate adjustment: How much do we increase/decrease by?
Critical part of congestion control design.
Determines how quickly a host adapts to changes in available bandwidth.
Determines how effectively bandwidth is consumed.
Determines how bandwidth is shared (fairness).
Goals for rate adjustment:
Efficiency: High utilization of link bandwidth.
Fairness: Each flow gets an equal share of bandwidth.

## Slide 28: Ways to Adjust Rate
At a high level, we can either adjust quickly or slowly.
Fast: Multiplicative changes.
  Increase by doubling: R → 2R
  Decrease by halving: R → R/2
Slow: Additive changes.
  Increase by adding: R → R + 1
  Decrease by subtracting: R → R – 1
We can combine these rates in four ways:
AIAD: Additive Increase, Additive Decrease.
AIMD: Additive Increase, Multiplicative Decrease.
MIAD: Multiplicative Increase, Additive Decrease.
MIMD: Multiplicative Increase, Multiplicative Decrease.

## Slide 29: Why AIMD?
AIMD (Additive Increase, Multiplicative Decrease) is the best option.
Intuition: Sending too much is worse than sending too little.
Sending too much: Congestion, packets dropped and retransmitted.
Sending too little: Somewhat lower throughput.
General approach:
Gentle increase when uncongested. (exploration)
Rapid decrease when congestion detected.
Loss
Loss
Loss
Loss

## Slide 30: Why AIMD? Intuition
Of the four options, AIMD is the only one that ensures fairness.
To see why, let's build a simple model:
Two flows using a single link of fixed capacity C.
Both flows are independently running identical dynamic adjustment algorithms.
Flows are sending at rates X and Y.
  If X + Y > C, the network is congested.
  If X + Y < C, the network is underloaded.
Goals:
  Full link utilization: X + Y = C.
  Fair sharing: X = Y.

## Slide 31: Rate Adjustment Graph
Assume C = 1.
Efficiency line: X + Y = 1
Congestion: X + Y > 1: above the efficiency line.
Unused capacity: X + Y < 1: below the efficiency line.
Fairness line: X = Y
The lines intersect at (0.5, 0.5).
This allocation is both fair and efficient.
1
1
Congested
Inefficient
Fairness Line:
X = Y
Efficiency Line:
X + Y = 1

## Slide 32: Rate Adjustment Graph
(0.2, 0.5) is inefficient (below blue line).
Only 0.7 bandwidth used.
(0.7, 0.5) is inefficient (above blue line).
1.2 bandwidth used (capacity is C = 1).
(0.7, 0.3) is efficient, but unfair.
On blue line, but not on green line.
1 bandwidth used, but, 0.7 ≠ 0.3.
1
1
Fairness Line:
X = Y
Efficiency Line:
X + Y = 1
(0.2, 0.5)
(0.7, 0.5)
(0.7, 0.3)

## Slide 33: Additive Adjustments on Graph
Recall: Both flows independently running identical algorithms.
Suppose current allocation is (X, Y).
If both increase additively: (X + a, Y + a).
If both decrease additively: (X – b, Y – b).
Notice: Allocations always stay on a line with slope = 1.
1
1
Fairness Line:
X = Y
Efficiency Line:
X + Y = 1
(X, Y)
(X+a, Y+a)
(X–b, Y–b)

## Slide 34: Multiplicative Adjustments on Graph
Recall: Both flows independently running identical algorithms.
Suppose current allocation is (X, Y).
If both increase multiplicatively: (cX, cY).
If both decrease multiplicatively: (X/d, Y/d).
Notice: Allocations always stay on a line with slope = Y/X, going through the origin.
1
1
Fairness Line:
X = Y
Efficiency Line:
X + Y = 1
(X, Y)
(cX, cY)
(X/d, Y/d)
Rise
Run
=
cY – Y
cX – X
Y(c – 1)
X(c – 1)
=
Y
X
=

## Slide 35: AIAD (Additive Increase, Additive Decrease) Dynamics
Increase: +1 Decrease: –2 C = 5
Start: X = 1 Y = 3 sum = 4, no congestion
First iteration: X = 2 Y = 4 sum = 6, congested
Second iteration: X = 0 Y = 2 sum = 2, no congestion
Third iteration: X = 1 Y = 3 back to where we started!
Notice: The difference in allocations stays the same!
AIAD maintains the same unfairness across iterations.
Y – X = 2
Y – X = 2
Y – X = 2
Y – X = 2

## Slide 36: AIAD (Additive Increase, Additive Decrease) Adjustments on Graph
Increase: +a Decrease: –b
We keep moving along the line with slope 1.
AIAD does not converge to fairness.
Fairness Line:
X = Y
Efficiency Line:
X + Y = C
(X, Y)
(X+a, Y+a)
(X–b, Y–b)

## Slide 37: MIMD (Multiplicative Increase, Multiplicative Decrease) Dynamics
Increase: ×2 Decrease: ÷4 C = 5
Start: X = 0.5 Y = 1 sum = 1.5, no congestion
First iteration: X = 1 Y = 2 sum = 3, no congestion
Second iteration: X = 2 Y = 4 sum = 6, congestion
Third iteration: X = 0.5 Y = 1 back to where we started!
Notice: The ratio of allocations stays the same!
MIMD maintains the same unfairness across iterations.
Y/X = 2
Y/X = 2
Y/X = 2
Y/X = 2

## Slide 38: MIMD (Multiplicative Increase, Multiplicative Decrease) Adjustments on Graph
Increase: ×c Decrease: ÷d
We keep moving along the line connected to the origin.
MIMD does not converge to fairness.
1
1
Fairness Line:
X = Y
Efficiency Line:
X + Y = 1
(X, Y)
(cX, cY)
(X/d, Y/d)

## Slide 39: MIAD (Multiplicative Increase, Additive Decrease) Dynamics
Increase: ×2 Decrease: –1 C = 5
Start: X = 1 Y = 3 sum = 4, no congestion
First iteration: X = 2 Y = 6 sum = 8, congestion
Second iteration: X = 1 Y = 5 sum = 6, congestion
Third iteration: X = 0 Y = 4 sum = 4, no congestion
Fourth iteration: X = 0 Y = 8 X stuck at 0 forever!
The gap in allocation doubles when we increase. before: Y – X. after: 2Y – 2X = 2(Y – X)
The gap in allocation stays the same when we decrease. (Same as AIAD.)
MIAD is maximally unfair. The gap increases until one person has all the bandwidth!
Y – X = 2
Y – X = 4
Y – X = 4
Y – X = 4
Y – X = 8

## Slide 40: AIMD (Additive Increase, Multiplicative Decrease) Dynamics
Increase: +1 Decrease: ÷2 C = 5
Start: X = 1 Y = 2 sum = 3, ok
First iteration: X = 2 Y = 3 sum = 5, ok
Second iteration: X = 3 Y = 4 sum = 7, congestion
Third iteration: X = 1.5 Y = 2 sum = 3.5, ok
Fourth iteration: X = 2.5 Y = 3 sum = 5.5, congestion
Fifth iteration: X = 1.25 Y = 1.5 sum = 2.75, ok
Sixth iteration: X = 2.25 Y = 2.5 sum = 4.75, ok
Seventh iteration: X = 3.25 Y = 3.5 sum = 6.75, congestion
Eighth iteration: X = 1.625 Y = 1.75 sum = 3.375, ok
Ninth iteration: X = 2.625 Y = 2.75 approaching 2.5 each!
Y – X = 1
Y – X = 1
Y – X = 1
Y – X = 0.5
Y – X = 0.5
Y – X = 0.25
Y – X = 0.25
Y – X = 0.25
Y – X = 0.125
Y – X = 0.125

## Slide 41: AIMD (Additive Increase, Multiplicative Decrease) Dynamics
The gap in allocation stays the same when we increase.
The gap in allocation halves when we decrease.
Before: Y – X
After: (0.5 Y – 0.5 X) = 0.5(Y – X)
The gap approaches 0, so AIMD approaches fairness!
Y – X = 1
Y – X = 1
Y – X = 1
Y – X = 0.5
Y – X = 0.5
Y – X = 0.25
Y – X = 0.25
Y – X = 0.25
Y – X = 0.125
Y – X = 0.125

## Slide 42: AIMD (Additive Increase, Multiplicative Decrease) Adjustments on Graph
Increase: +a Decrease: ÷d
AIMD (slow-start/gentle increase, rapid decrease) converges to fairness!
Of the four options:
AIAD and MIMD retain unfairness.
MIAD approaches maximum unfairness (one person with all the bandwidth).
AIMD is the only one that ensures fairness.
1
1
Fairness Line:
X = Y
Efficiency Line:
X + Y = 1
Notes: Of the four options, AIMD is the only one that ensures fairness.
AIMD embodies gentle increase, rapid decrease.
Yes, all the zig-zags were measured to go through the origin or be at 45 degrees, I don't know why I bothered to do this

## Slide 43: Host-Based Dynamic Adjustment: Algorithm Sketch
Every host independently runs the same algorithm:
Pick an initial rate R. (Slow start.)
Try sending at rate R for some period of time.
  Did I experience congestion in this time period? (Detect packet loss.)
  If no, increase R. (Additive increase.)
  If yes, reduce R. (Multiplicative decrease.)
  Repeat.
Loss
Loss
Loss
Loss
Slow Start
This algorithm creates a sawtooth-shaped graph as the rate is adjusted.
AIMD

## Slide 44: Implementing Congestion Control with Event-Driven Updates
Congestion Control Principles
Why do we need it?
Why is it hard?
Design Goals
Dynamic Adjustment
Algorithm Sketch
Reacting to Congestion (AIMD)
Implementing Congestion Control with Event-Driven Updates
Lecture 12, Spring 2026

## Slide 45: Review: Setting Window Size
The sender maintains a window of W packets in flight.
Pick window size W to balance three goals:
Take advantage of network capacity ("fill the pipe").
  Not actually used (impractical to calculate, and never the minimum).
Don't overload the recipient.
  Receiver window (RWND): Recipient reports how much space it has left.
Don't overload links.
  Congestion window (CWND): Sender runs a congestion control algorithm.
W is the minimum of RWND and CWND.
For today, we'll assume RWND > CWND, so window is determined by CWND.
Often true in practice too.

## Slide 46: Review: Measuring Packets vs. Bytes
Real TCP measures data in bytes.
Thus, real TCP maintains CWND in bytes.
In this lecture, we'll measure CWND in packets for convenience.
To convert to bytes, recall: 1 packet = MSS bytes.
MSS = Maximum Segment Size.
Congestion control is used to set the window size (CWND).
Recall: Rate = CWND / RTT.
Larger window = higher rate.
Notes: Window size and rate are directly correlated.

## Slide 47: Host-Based Dynamic Adjustment: Algorithm Sketch
Every host independently runs the same algorithm:
Pick an initial rate R. (Slow start.)
Try sending at rate R for some period of time.
  Did I experience congestion in this time period? (Detect packet loss.)
  If no, increase R. (Additive increase.)
  If yes, reduce R. (Multiplicative decrease.)
  Repeat.
How long is "some period of time"?
Ideally, each iteration lasts for one RTT.
Problem: RTT is hard to measure, and changes dynamically.
???

## Slide 48: Event-Driven Updates
Instead of updating after "some period of time," CWND updates are event-driven.
Sender adjusts CWND each time something interesting happens in TCP.
We get an ack for new data.
  This means there was no congestion.
  Increase CWND (additive increase in AIMD).
We get 3 duplicate acks and declare a packet lost.
  Probably an isolated loss, since we're still getting subsequent acks.
  Decrease CWND (multiplicative decrease in AIMD).
The timer expires and we declare a packet lost.
  We probably lost several packets – didn't get any duplicate acks. Bad news!
  Abandon current rate and start over from slow-start.

## Slide 49: Event-Driven Slow Start
Conceptual slow start: Double CWND after each RTT.
Event-driven slow start: Increase CWND by 1 after each ack.
Each time we get an ack, we can send one more packet (sliding window).
But, we can also increase CWND by 1 and send another packet.
In total: Each time we get an ack, we can send out 2 packets.
Example: In one RTT, if we get 8 acks, we can send out 16 packets.
t = 0 RTTs: CWND = 1 Send 1 packet
t = 1 RTT: get 1 ack CWND = 2 Send 2 packets
t = 2 RTTs: get 2 acks CWND = 4 Send 4 packets
t = 3 RTTs: get 4 acks CWND = 8 Send 8 packets
t = 4 RTTs: get 8 acks CWND = 16 Send 16 packets

## Slide 50: Event-Driven Slow Start
Sender
Recipient
CWND = 1
CWND = 2
CWND = 3
CWND = 4
CWND = 5
CWND = 6
CWND = 7
CWND = 8
First RTT
Second RTT
Third RTT
Fourth RTT

## Slide 51: Event-Driven Slow Start: SSTHRESH
Increase CWND by 1 after each ack.
Eventually, we encounter a packet loss.
Set CWND = CWND/2.
Set SSTHRESH = CWND/2.
SSTHRESH helps us remember the last safe rate.
Loss
Loss
Loss
Slow Start
AIMD
Loss
SSTHRESH

## Slide 52: Event-Driven AIMD Adjustments: Additive Increase
Conceptual AIMD increase: Add 1 to CWND after each RTT.
Event-driven AIMD increase: Increase CWND by 1/CWND after each ack.
Intuition:
Increase CWND by a fraction of a packet on each ack.
After one RTT's worth of packets, CWND will increase by 1.
Implementation:
CWND ← CWND +
In bytes: CWND ← CWND + × MSS
1
CWND
MSS
CWND
(1/CWND in packets) fraction rewritten in bytes by multiplying top and bottom by packet size: (MSS/CWND in bytes)
Total increase after each RTT should be MSS bytes, not 1 packet.
Note: Technically, increase on each ack is different, but approximation is close enough.
First update: 3.00 + (1/3.00) = 3.33
Second update: 3.33 + (1/3.33) = 3.63
Third update: 3.63 + (1/3.63) = 3.93 ≈ 4

## Slide 53: Event-Driven AIMD Adjustments: Additive Increase
Event-driven AIMD increase: Increase CWND by a fraction after each ack.
After one RTT (aka one window) of packets, CWND increases by 1.
 | Measured in packets: | Measured in bytes: (MSS = 50 bytes)
Old CWND: | 3 packets | 150 bytes (3 packets)
Fraction of increase per ack: | 1/CWND = 1/3 | MSS/CWND = 50/150
Total increase after 1 RTT: | +1 packet | MSS = +50 bytes
Increase after each ack: | +1 packet × 1/3 = +1/3 | +50 bytes × 50/150 = +50/3
Increase after 3 acks: | 3 + (1/3) + (1/3) + (1/3) = 4 packets | 150 + (50/3) + (50/3) + (50/3) = 200 bytes

## Slide 54: Event-Driven AIMD Adjustments: Multiplicative Decrease
Conceptual AIMD decrease: Divide CWND in half when loss detected.
Event-driven AIMD decrease: Divide CWND in half when 3 duplicate acks detected.
Set CWND ← CWND / 2
Set SSTHRESH ← CWND / 2. (Remember the last safe rate.)
CWND should never decrease below 1 packet (MSS bytes).
If dividing by 2 causes CWND to fall below 1, it's okay to round up to 1 packet.

## Slide 55: Event-Driven Adjustments: Timeout
When a packet is lost from timeout, abandon current rate and restart from slow-start.
Rationale: We didn't get any duplicate acks before timing out, so we probably lost multiple packets.
The current CWND might be way off. Safest to rediscover a good rate from scratch.
This design decision errs on the side of caution.
Implementation: When timeout occurs:
Set SSTHRESH ← CWND/2. (Remember the last safe rate.)
Set CWND ← 1 packet, and re-enter slow start mode.

## Slide 56: Event-Driven Updates: SSTHRESH
SSTHRESH helps us remember the last safe rate.
When slow-start detects loss: Update SSTHRESH ← CWND/2.
When a packet times out in AIMD: Update SSTHRESH ← CWND/2.
During slow start: If CWND exceeds SSTHRESH, switch to additive increases.
SSTHRESH = ∞ for first slow-start.
Loss
Loss
Timeout
Slow Start
AIMD
Loss
SSTHRESH
SSTHRESH
Slow Start
AIMD
Loss

## Slide 57: Summary: TCP Congestion Control
Detecting congestion:
Loss-based. (Delay-based is the alternative.)
Discovering an initial rate:
Slow-start. Double rate until loss or safe rate (SSTHRESH) exceeded.
Event-driven: Add 1 to CWND on each ack.
Adapting rate to congestion:
AIMD (additive increase, multiplicative decrease) approaches fairness.
Event-driven:
  Add 1/CWND on each ack. After one RTT, CWND will have increased by 1.
  Divide CWND in half when there are 3 duplicate acks.
When a packet is lost on timeout, restart from slow-start.