## Slide 1
CS 168, Spring 2026 @ UC Berkeley
Slides credit: Sylvia Ratnasamy, Rob Shakir, Peyrin Kao
Congestion Control, Part 2
Lecture 13 (Transport 4)
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Notes: Slides template credit: Josh Hug, Lisa Yan

## Slide 2: Fast Recovery
Congestion Control Implementation
Fast Recovery
State Machine and Variants
TCP Throughput Model
Congestion Control Issues
Router-Assisted Congestion Control
Lecture 15, Spring 2026

## Slide 3: Fast Recovery
Problem: Additive increases are too slow to recover from isolated loss.
This last feature is an optimization to improve performance.
Bit of a hack, but it's effective.

## Slide 4: Fast Recovery: Setting the Stage
✗
101
102
103
104
105
106
107
108
109
110
ack(101) from 102
ack(101) from 103
ack(101) from 104
ack(101) from 105
ack(101) from 106
ack(101) from 107
ack(101) from 108
ack(101) from 109
ack(101) from 110
ack(111) from 101
Resend 101
Consider sending 10 packets.
The first one (101) is dropped.
Acks for 102–110 all say ack(101) because packet 101 is still missing.
After the third duplicate ack(101), sender declares packet #101 is lost, and resends it.
Eventually, ack for the re-sent 101 says ack(111) because packets 102–110 were all received earlier.
What does CWND look like during this process?
Notes: Senario with only TCP and cumulative acks

## Slide 5: Fast Recovery: Windows Without Fast Recovery
...
101
102
103
104
105
106
107
108
109
110
111
112
113
After sending 10 packets: CWND = 10. 101–110 can be in flight.
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
After ack(101) from 102: Can't send anything new.
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
After ack(101) from 103: Can't send anything new.
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
After ack(101) from 104: Can't send anything new.
114
115
...
3 duplicate acks detected. CWND = 5.
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(101) from 105: Can't send anything new.
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Note: We're marking acked packets in green for convenience, but the sender cannot deduce from duplicate acks that these exact packets were received.
Notes: How does CWND respond in our CC algorithm so far.

## Slide 6: Fast Recovery: Windows Without Fast Recovery
After ack(101) from 107: Can't send anything new.
After ack(101) from 108: Can't send anything new.
After ack(101) from 109: Can't send anything new.
After ack(101) from 110: Can't send anything new.
After ack(111) from resent 101: Window slides to first unacked packet (111).
Sender is now able to send 111–115.
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Problem: After we decreased CWND, we had to wait a long time before sending again.
After ack(101) from 106: Can't send anything new.
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Notes: Issue is this huge jump and stuck window. Wasted bandwidth.

## Slide 7: Fast Recovery: Windows Without Fast Recovery
✗
101
102
103
104
105
106
107
108
109
110
ack(101) from 102
ack(101) from 103
ack(101) from 104
ack(101) from 105
ack(101) from 106
ack(101) from 107
ack(101) from 108
ack(101) from 109
ack(101) from 110
ack(111) from 101
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
CWND = 10. 101–110 can be in flight.
114
115
...
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Resend 101
CWND = 5. 101–105 can be in flight.
Problem: In the entire blue area, after CWND decreased, the sender isn't sending anything.
Notes: Blue zone - wasted!

## Slide 8: Fast Recovery: Windows Without Fast Recovery
ack(101) from 102
ack(101) from 103
ack(101) from 104
ack(101) from 105
ack(101) from 106
ack(101) from 107
ack(101) from 108
ack(101) from 109
ack(101) from 110
111
112
113
114
115
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Resend 101
CWND = 5. 101–105 can be in flight.
Secondary problem: Sender has to wait a full RTT for ack(112) to arrive before sending 116+.
ack(111) from 101
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
CWND = 5. 111–115 can be in flight.
Notes: Bursty behavior is also a secondary issue - project example

## Slide 9: The Fast Recovery Problem
The problem, restated again:
After CWND decreased, the window was too small for us to send packets after 110.
The sender must wait (sending nothing) until the re-sent 101 is acked.
The secondary problem, restated again:
When 101 is acked, the window jumps forward, and 111–115 are all sent at once.
The sender must wait again (idling) until ack(111) before sending more.
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
CWND = 10. 101–110 can be in flight.
114
115
...
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
CWND = 5. 101–105 can be in flight.
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
CWND = 5. 111–115 can be in flight.
Notes: Problem restated again!

## Slide 10: The Fast Recovery Problem
The sender can deduce from the duplicate acks that fewer packets are in flight:
Initially: 10 packets in flight.
After ack(101) from 102: 9 packets in flight.
After ack(101) from 103: 8 packets in flight.
After ack(101) from 104: 7 packets in flight.
After ack(101) from 105: 6 packets in flight.
After ack(101) from 106: 5 packets in flight.
After ack(101) from 107: 4 packets in flight.
After ack(101) from 108: 3 packets in flight.
After ack(101) from 109: 2 packets in flight.
After ack(101) from 110: 1 packet in flight. (The packet still in flight is the re-sent 101.)
Notes: Sender assumes that an ack means something made it through

## Slide 11: The Fast Recovery Problem
The sender can deduce from the duplicate acks that fewer packets are in flight.
Even though there are eventually <5 packets left in flight, the sliding window is stopping us from sending more.
Key idea:
Grant the sender a temporary "credit" for each duplicate ack.
When a duplicate ack arrives, we know that one fewer packet is in flight.
Artificially extend the window to let the sender send one more packet.

## Slide 12: Fast Recovery: Windows with Fast Recovery
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
3 duplicate acks detected. CWND = 5.
Extend window to account for the 3 acks: CWND = 5 + 3 = 8.
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(101) from 105: Extend window to CWND = 9.
Can't send anything new.
After ack(101) from 104: Can't send anything new.
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(101) from 103: Can't send anything new.
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(101) from 102: Can't send anything new.
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After sending 10 packets: CWND = 10. 101–110 can be in flight.

## Slide 13: Fast Recovery: Windows with Fast Recovery
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(101) from 110: Extend window to C = 14.
We can send 114!
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(111) from resent 101: Back to normal. C = 5.
We can send 115.
After ack(101) from 109: Extend window to C = 13.
We can send 113!
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(101) from 108: Extend window to C = 12.
We can send 112!
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(101) from 107: Extend window to C = 11.
We can send 111!
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
After ack(101) from 106: Extend window to C = 10.
Can't send anything new.
Notes: Every duplicate ack extends the window

## Slide 14: Fast Recovery: Windows with Fast Recovery
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
...
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Remember: The sender does not know exactly which packets were acked.
The sender only sees duplicate acks.
The sender does know how many packets were acked.
The sender can count duplicate acks.
The artificially extended window ensures that the total number of packets in flight is still 5 (the new CWND).
Size of extended window – number of duplicate acks = 5 (the new CWND).
Notes: Just after isolated loss with 3 duplicated acks

## Slide 15: Fast Recovery: Windows Without Fast Recovery
✗
101
102
103
104
105
106
107
108
109
110
ack(101) from 102
ack(101) from 103
ack(101) from 104
ack(101) from 105
ack(101) from 106
ack(101) from 107
ack(101) from 108
ack(101) from 109
ack(101) from 110
ack(111) from 101
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
CWND = 10. 101–110 can be in flight.
114
115
...
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Resend 101
CWND = 14. 101–114 can be in flight.
The sender is now still sending in the blue area!
Notes: Blue zone is no longer a waste

## Slide 16: Fast Recovery: Windows Without Fast Recovery
ack(101) from 102
ack(101) from 103
ack(101) from 104
ack(101) from 105
ack(101) from 106
ack(101) from 107
ack(101) from 108
ack(101) from 109
ack(101) from 110
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
Resend 101
CWND = 5. 101–105 can be in flight.
Because we sent 111–114 during the blue area, when the new ack(111) arrives, we only have to send 115. Also, ack(112) will arrive sooner so we can keep sending.
ack(111) from 101
...
100
101
102
103
104
105
106
107
108
109
110
111
112
113
114
115
...
CWND = 5. 111–115 can be in flight.

## Slide 17: Fast Recovery: Implementation
Conceptually: When a duplicate ack arrives, artificially extend the window to let the sender send one more packet.
Implementation:
When we receive 3 duplicate acks:
  SSTHRESH ← CWND/2
  CWND = CWND/2 + 3 (artificially extend for the 3 duplicate acks)
While in fast recovery mode, when we receive a duplicate ack:
  CWND = CWND + 1 (artificially extend for each duplicate ack)
Exit fast recovery when we receive a new, non-duplicate ack:
  CWND = SSTHRESH (back to 0.5 × rate when the loss happened)

## Slide 18: State Machine and Variants
Congestion Control Implementation
Fast Recovery
State Machine and Variants
TCP Throughput Model
Congestion Control Issues
Router-Assisted Congestion Control
Lecture 15, Spring 2026

## Slide 19: Putting It All Together: TCP with Congestion Control
The sender maintains 5 values:
dupACKcount for detecting loss. Initialized to 0.
Timer for detecting loss.
RWND for flow control.
CWND for congestion control. Initialized to 1 packet.
SSTHRESH to remember latest safe rate. Initialized to ∞.
The recipient maintains a buffer of out-of-order packets.
The sender responds to 3 events:
Ack for new data (not previously acked).
Duplicate ack.
Timeout.
The recipient responds to receiving a packet: Reply with an ack and a RWND value.

## Slide 20: Putting It All Together: TCP with Congestion Control
Events at sender: new ack, duplicate ack, timeout.
When we receive an ack for new data (not previously acked):
If in slow-start mode:
  CWND ← CWND + 1 packet (so CWND doubles per RTT)
If in fast recovery mode:
  CWND ← SSTHRESH (so we leave fast recovery)
If in congestion avoidance mode:
  CWND ← CWND + 1/CWND (so CWND increases by 1 per RTT)
Reset timer.
Reset duplicate ack count.
If window allows, send new data.

## Slide 21: Putting It All Together: TCP with Congestion Control
Events at sender: new ack, duplicate ack, timeout.
When we receive a duplicate ack:
Increment duplicate ack count.
If dupACKcount = 3: Do fast retransmit.
SSTHRESH ← CWND / 2
CWND ← (CWND / 2) + 3 (the +3 is for fast recovery)
Resend leftmost packet in window.
If dupACKcount > 3: Do fast recovery.
CWND ← CWND + 1

## Slide 22: Putting It All Together: TCP with Congestion Control
Events at sender: new ack, duplicate ack, timeout.
When the timer expires:
SSTHRESH ← CWND / 2
CWND ← 1 packet
Switch to slow-start mode.
Resend leftmost packet in window.

## Slide 23: TCP Congestion Control State Machine
Congestion Avoidance
Fast Recovery
Slow Start
Timeout
Dup ack
New ack
Dup ack x3
Dup ack x3
Timeout
New ack
Dup ack
New ack
Dup ack
CWND > SSTHRESH
Timeout
Notes: Can go to fast recovery from either slow start or congestion avoidance.

## Slide 24: TCP Congestion Control Variants
TCP Tahoe:
CWND = 1 after triple duplicate acks.
TCP Reno:
CWND = 1 on timeout.
CWND = CWND / 2 after triple duplicate acks.
TCP New Reno:
TCP Reno + improved fast recovery.
TCP-SACK:
Adds selective acknowledgements.
Acks describe byte ranges received.
Unless otherwise specified, we're using this one.
Notes: TCP Tahoe - more conservative
TCP Reno - Almost what we learned but no fast recovery
TCP New Reno - Us!
TCP-SACK - Selective acknowledgements with more information about which packets received

## Slide 25: Interoperability Between TCP Congestion Control Variants
How can all these variants co-exist? Don't we need a single, uniform standard?
Congestion control is implemented at the sender.
The sender can run whatever code they want.
What happens if I use Reno, you use Tahoe, and we try to communicate?
This should work fine. The variants change the rate we send data, but the packet format is the same.
What happens if I use Tahoe, and you use SACK?
Problem: You're expecting selective acks, and I'm only providing cumulative acks.

## Slide 26: TCP Throughput Model
Congestion Control Implementation
Fast Recovery
State Machine and Variants
TCP Throughput Model
Congestion Control Issues
Router-Assisted Congestion Control
Lecture 15, Spring 2026

## Slide 27: Our Goal: The TCP Throughput Equation
Given a path through the network, what TCP throughput can we expect?
The congestion control algorithm told us how to adjust rates.
But it didn't tell us what the actual rates are.
We'll derive a simple model that expressed TCP throughput in terms of path properties:
RTT.
p, the packet loss rate.

## Slide 28: TCP Throughput Equation: Simplifying Assumptions
Simplifying assumptions:
There is a single TCP connection.
Ignore the slow-start phase.
We'll assume a single, non-changing path through the network:
RTT is some fixed number.
Bottleneck bandwidth is some fixed number.
Therefore: RTT × bandwidth = Wmax (a constant value).
  When the window size exceeds Wmax, we lose exactly one packet.
  Loss detected by duplicate acks. No timeouts.

## Slide 29: TCP Throughput in Terms of Window Size
From our assumptions: We lose a packet when CWND reaches Wmax.
Window size changing over time:
After detecting loss: (0.5 × Wmax)
One RTT later: (0.5 × Wmax) + 1
Two RTTs later: (0.5 × Wmax) + 2 ...
(0.5 × Wmax) RTTs later: Wmax
After detecting loss: (0.5 × Wmax)
One RTT later: (0.5 × Wmax) + 1
Two RTTs later: (0.5 × Wmax) + 2 ...

## Slide 30: TCP Throughput in Terms of Window Size
Window size changing over time:
Increase linearly from (0.5 × Wmax) to (Wmax).
Drop back down to (0.5 × Wmax).
Repeat.
Average window size is 3/4 × Wmax.
Wmax
0.5 × Wmax
Average: 3/4 × Wmax
Time
Window Size

## Slide 31: TCP Throughput in Terms of Window Size
Unit conversion:
Average window size is 3/4 × Wmax.
This is measured in packets (since we were adding 1 packet per iteration).
Each packet is MSS bytes.
Average window size, in bytes, is 3/4 × Wmax × MSS.
Computing throughput:
Window size tells us how much data we can send per RTT.
To compute rate, divide window size (data) by RTT (time):
Throughput = Wmax ×
Next step: Express Wmax in terms of p, the loss rate.
3
4
MSS
RTT

## Slide 32: Relating Window and Loss Rate
Next step: Express Wmax in terms of p, the loss rate.
We know one packet is lost every (0.5 × Wmax) RTTs.
  This is how long it takes to climb from (0.5 × Wmax) back up to (Wmax).
  Each RTT adds 1, and we have to climb (0.5 × Wmax) in total.
So, we need to figure out how many packets are sent in (0.5 × Wmax) RTTs.
Loss
Loss
Loss
Wmax
0.5 × Wmax
Average: 3/4 × Wmax
(0.5 × Wmax) RTTs
Time between losses
Time
Window Size

## Slide 33: Relating Window and Loss Rate
How many packets are sent in (0.5 × Wmax) RTTs?
Average window size is 3/4 × Wmax. That's how many packets we send per RTT.
Answer: (3/4 × Wmax) × (0.5 × Wmax) = 3/8 × Wmax2 packets.
Can also be computed as the area of the shape (rate × time), or area under the curve (integral of rate).
Loss
Loss
Loss
Wmax / RTT
(0.5 × Wmax) / RTT
Average: (3/4 × Wmax) / RTT
Width = (0.5 × Wmax) RTT
Height = (3/4 × Wmax) / RTT
Time
Rate

## Slide 34: Relating Window and Loss Rate
Next step: Express Wmax in terms of p, the loss rate.
We now know: 3/8 × Wmax2 packets are sent between losses.
One packet lost out of that many packets.
Loss rate = p =
Loss
Loss
Loss
8
3Wmax2
Time
Rate
Wmax / RTT
(0.5 × Wmax) / RTT
Average: (3/4 × Wmax) / RTT
Width = (0.5 × Wmax) RTT
Height = (3/4 × Wmax) / RTT

## Slide 35: Relating Window and Loss Rate
Plug this into our original throughput equation:
Loss rate = p =
8
3Wmax2
This tells us that:
Throughput is inversely proportional to RTT.
  Shorter RTT = higher throughput.
  TCP is unfair when flows have different RTTs.
Throughput is inversely proportional to square root of loss rate.
  Lower loss rate = higher throughput.
A
X
B
Y
RTT = 100ms
RTT = 200ms
R1
R2
A–B gets twice as much bandwidth as X–0Y

## Slide 36: Consequences of Equation (2/2): Rate-Based Congestion Control
Throughput =
TCP throughput is choppy: Rate oscillates between W/2 and W.
Some applications (e.g. video streaming) would prefer sending at a steady rate.
Solution: Equation-based congestion control.
Abandon TCP's adjustment rules, and just follow the equation.
Measure RTT, measure p, and compute the rate accordingly.
Using the equation ensures fairness: We don't use more bandwidth than TCP would.
Look up RFC 5348 for spec.
Notes: Small shifts in our algorithm can make a big difference at internet scale!

## Slide 37: Congestion Control Issues
Congestion Control Implementation
Fast Recovery
State Machine and Variants
TCP Throughput Model
Congestion Control Issues
Router-Assisted Congestion Control
Lecture 15, Spring 2026

## Slide 38: Congestion Control Issues
We'll look at 5 issues (and potential solutions):
Confusing corruption and congestion.
Short connections complete before discovering available capacity.
Router queues get filled up, causing high delays.
Cheating.
Congestion control and reliability are intertwined.

## Slide 39: Issues (1/5): Confusing Corruption and Congestion
TCP detects congestion by checking for loss.
Loss could also occur due to corruption.
TCP will confuse corruption with congestion.
From the equation: Higher loss = lower throughput.
Still true, even if the losses aren't due to congestion!
Equation could be used to analyze how TCP would perform on a lossy link (high corruption rate).

## Slide 40: Issues (2/5): Short Connections
Most real-life TCP connections are really short.
50% of connections send fewer than 1.5 KB.
80% of connections send fewer than 100 KB.
Very few packets (maybe only one) are sent.
Many connections stay in slow-start the whole time.
Short connections likely to suffer from high latency.
Not enough packets to trigger duplicate acks.
Isolated loss may lead to timeouts.
Timeouts can severely increase latency.
Partial fix: Start with a higher initial CWND.
Look up RFC 5348 for experiments on this.
Sender
Recipient
Recall slow start: Start with CWND = 1, double every RTT.
It took ≈2 RTTs to send 3 packets.

## Slide 41: Issues (3/5): Router Queues Get Filled Up
TCP deliberately overshoots capacity until packets get dropped.
Recall: Loss occurs when the queue is full.
By then, the queue is already full, and packets are delayed.
Result: Delays are large for everybody.
Someone is transferring a 10 GB file. Queues are filled with their packets.
You want to download a 100 byte file. You're stuck waiting in the queue.
The problem is even worse if routers keep really long queues.
Bufferbloat: Routers have excessive memory, and maintain long queues.
When loss occurs, everybody is already waiting in a really long queue.

## Slide 42: Issues (3/5): Router Queues Get Filled Up
Possible solution: Google's BBR algorithm (2016).
Detects congestion using delay instead of loss.
Sender learns its minimum RTT.
Sender slows down if it observes RTTs exceeding the minimum.
Congestion Control Protocols
Pricing
Reservations
Dynamic Adjustment
Router-assisted
Host-based
Loss-based
Delay-based
BBR
TCP

## Slide 43: Issues (4/5): Cheating
Nobody is enforcing that users follow the TCP congestion control algorithm.
Cheating strategy: Change the algorithm.
Increase the window faster (+2, instead of +1).
Start with a large initial CWND.
Cheating strategy: Open lots of connections.
TCP shares bandwidth between connections.
If Alice opens 10 connections, and Bob opens 1, then Alice gets 10x more bandwidth.

## Slide 44: Issues (4/5): Cheating
Applying graphical model to a cheating host:
X increases by 2 per RTT.
Y increases by 1 per RTT.
Suppose current allocation is (X, Y).
If both increase additively: (X + 2a, Y + a).
Notice: Slope of this line is now 1/2, not 1.
Fairness/efficiency lines now meet at (2/3, 1/3).
1
1
Fairness Line:
X = 2Y
Efficiency Line:
X + Y = 1
(X, Y)
(X+2a, Y+a)

## Slide 45: AIMD (Additive Increase, Multiplicative Decrease) Adjustments on Graph
Increase: +2 (X), +1(Y) Decrease: ÷2
Because X is cheating, AIMD converges toward a "fairness" line where X has twice as much bandwidth as Y.
1
1
Efficiency Line:
X + Y = 1
Fairness Line:
X = 2Y
Notes: Yes, all the zig-zags were measured to go through the origin or be at 45 degrees, I don't know why I bothered to do this

## Slide 46: Issues (4/5): Cheating
Why hasn't the Internet suffered congestion collapse? Some theories:
Cheaters might get an unfair share of bandwidth, but they still follow basic congestion control rules (e.g. slow down when loss occurs).
  Contrast with the 1980s: Everybody sent at maximum rate, no adjusting.
TCP is implemented in the operating system.
  Most users probably aren't changing their OS code.
How much cheating occurs in practice?
We don't really know. Measuring cheating is hard.
 | Link
Google’s Network Congestion Algorithm Isn’t Fair, Researchers Say | 
Karl Bode | October 31, 2019
Notes: https://www.vice.com/en/article/xwepkw/googles-network-congestion-algorithm-isnt-fair-researchers-say

## Slide 47: Issues (5/5): Congestion Control and Reliability are Intertwined
Mechanisms for congestion control and reliability are tightly coupled.
A design choice from the 1980s. (TCP was patched to stop congestion collapse.)
Example: CWND is adjusted based on acks and timeouts.
Example: We detect loss/congestion with duplicate acks, because TCP uses cumulative acks.
This complicates evolution.
Example: If we wanted to switch from cumulative to selective acks, we'd have to change the congestion control algorithm too.
This is a failure of modularity, not layering.
Sometimes we only want one, but not the other.
Congestion control, no reliability: Video streaming.
Reliability, no congestion control: Lightweight application (one packet per hour).

## Slide 48: Router-Assisted Congestion Control
Congestion Control Implementation
Fast Recovery
State Machine and Variants
TCP Throughput Model
Congestion Control Issues
Router-Assisted Congestion Control
Lecture 15, Spring 2026

## Slide 49: Router-Assisted Congestion Control
Many of our issues could be fixed with some help from routers!
Confusing corruption and congestion.
Short connections complete before discovering available capacity.
Router queues get filled up, causing high delays.
Cheating.
Congestion control and reliability are intertwined.
Two ways routers can help:
Enforce fairness. (Helps with 4.)
Send information to hosts. (Helps with 1, 2, 3.)

## Slide 50: Enforcing Fairness
How can routers ensure each flow gets its fair share?
Consider a single router's actions.
Router classifies incoming packets into flows (TCP connections).
Each flow has its own separate FIFO queue in the router.
Router picks a queue (i.e. flow) in a fair order, and transmits packet from the front of that queue.
What does fair mean exactly?

## Slide 51: Round-Robin (Equal Packet Size)
For now, assume all packets are the same size.
Suppose we have three connections:
A has 8 packets to send:
B has 6 packets to send:
C has 2 packets to send:
Suppose we only have capacity to send 10 packets.
Round-robin service: Take turns sending packets from each queue.
Packets sent:
  We sent: 4x A packets, 4x B packets, and 2x C packets.
Packets not sent:
A1
A2
A3
A4
A5
A6
A7
A8
B1
B2
B3
B4
B5
B6
C1
C2
A5
A6
A7
A8
B5
B6
A1
A2
A3
A4
B1
B2
B3
B4
C1
C2

## Slide 52: Round-Robin (Equal Packet Size)
With round-robin service and capacity 10:
A had 8 packets. We sent 4.
B had 6 packets. We sent 4.
C had 2 packets. We sent 2.
Property: If you don't get your full demand, nobody gets more than you.
C got its full demand.
A and B did not, but they each got an equal share of the remainder.
This is called max-min fairness.

## Slide 53: Max-Min Fairness (Equal Packet Size)
Instead of round-robin, we could mathematically solve max-min fairness.
Resource allocation problem:
Capacity is 10.
A wants 8. B wants 6. C wants 2.
Intuitive solution:
If we split equally, everyone gets 10/3 = 3.33.
But C only wants 2, so let's give C its full demand. C = 2. Now we have 8 left.
If we split equally, A and B each get 8/2 = 4.
We can't meet A or B's demands, so they each get a fair share of the remainder. A = 4, B = 4.

## Slide 54: Max-Min Fairness (Equal Packet Size)
Formal definition:
Input: Total available bandwidth is C.
Input: Each flow i has a bandwidth demand, ri.
Output: Find a fair allocation ai to each flow i.
Max-min allocations are defined as:
ai = min(f, ri), where f is the unique value such that ∑ai = C.
Intuition:
f is the fair share (same value for everybody) if you don't get full demand.
The min term ensures that nobody gets more than they asked for.
The sum ensures that all capacity is used.

## Slide 55: Max-Min Fairness (Equal Packet Size)
Max-min allocations are defined as:
ai = min(f, ri), where f is the unique value such that ∑ai = C.
Applied to the previous example:
C = 10
r1 = 8 r2 = 6 r3 = 2
Solution:
The fair share is f = 4.
a1 = min(4, 8) = 4
a2 = min(4, 6) = 4
a3 = min(4, 2) = 2

## Slide 56: Round-Robin (Unequal Packet Size)
How do we deal with packets of different sizes?
Mental model: bit-by-bit round-robin ("fluid flow").
We can't actually do this in practice!
But we can approximate it. This is what fair queuing routers do.
Fair queuing:
For each packet, compute the time when the last bit of the packet would have left the router, if flows were served bit-by-bit.
This time is called the deadline for that packet.
Then, serve packets in order of their deadlines.

## Slide 57: Fair Queuing (Unequal Packet Size)
A1
Flow 1 (arrival traffic):
B1
Flow 2 (arrival traffic):
B2
B3
B4
B5
A2
A3
Fluid system:
(Too fine-grained switching, not feasible or too much overhead)
B1
B1
B2
B2
A1
B3
A2
B3
A4
A5
A3
B4
A4
B4
A5
B5
A6
B5
A6
Fair queuing system:
B1
B2
A1
A2
A3
A4
A5
A6
B3
B4
B5
(bold = packet deadline)

## Slide 58: Fair Queuing in Practice
Perfect fair queuing is too complex to implement at high speeds.
But several approximations exist.
Example: Deficit Round Robin (DRR)
Today:
Routers typically implement approximate fair queuing (e.g. DRR).
Routers only use a small number of queues.
  This results in coarser-grained isolation.
  Example: Separate queues per customer (not per flow).

## Slide 59: Fair Queuing vs. FIFO Queues
Fair queuing pros:
Isolation: Cheating flows don't benefit.
Bandwidth share doesn't depend on RTT.
Flows can pick any rate adjustment scheme they want.
Fair queuing cons:
More complex than FIFO.
  Separate queues per flow.
  Additional bookkeeping per packet.
Can only be approximated in practice.
Notes: Smaller networks like datacenters benefit from this, but full internet uses TCP and CC

## Slide 60: Fair Queuing Does Not Solve Congestion
Fair queuing does not eliminate congestion.
A → B wants to send at 5 Gbps. X → Y wants to send at 1 Gbps.
R1 implements fair queuing, and gives 0.5 Gbps to each flow.
If A → B runs at 0.5 Gbps, then R2 ends up dropping 0.4 Gbps (sending only 0.1).
R1 fairly allocating didn't help. A needs to slow down.
Fair queuing can manage congestion.
Resilient to cheating, RTT variations, etc.
Congestion and packet drops still occur.
We still want end hosts to discover/adapt to their fair share.
R1
A
X
R2
B
Y
5
1
1
1
0.1
Notes: Talk through what R1 does (0.5 and 0.5) but congestion still due to 0.1

## Slide 61: Fair Queuing: Philosophy of Fairness
Fair queuing gives us per-flow fairness. But is that really what we want?
What if you have 8 flows, and I have 4?
  Why do you get twice the bandwidth?
What if your flow goes over 4 congested hops, and mine only goes over 1?
  Shouldn't you be penalized for using more scarce bandwidth?
What granularity should we enforce fairness at?
  Per TCP connection?
  Per source-destination pair?
  Per source?
Fair queuing is a great way to ensure isolation.
Ensures that no one person hogs all the bandwidth, even in the worst cases.

## Slide 62: Router-Assisted Congestion Control
Two ways routers can help:
Enforce fairness. (Helps with 4.)
  Fair queuing (and approximations like DRR).
Send information to hosts. (Helps with 1, 2, 3.)

## Slide 63: Router-Assisted Rate Adaptation
Why not just let routers tell the end hosts what rate they should use?
Possible design:
Packets carry an extra "rate" field in the header.
Routers insert a flow's fair share in the header.
End hosts set rate according to the header value.
Now, the sender doesn't need to dynamically adjust to find a good rate.

## Slide 64: Router-Assisted Congestion Detection
Explicit Congestion Notification (ECN) bit: Single bit in the IP packet header.
Congested routers can set this bit.
  When recipient gets a packet with ECN on, the ack also has ECN on.
Many options for when routers set the bit.
  Trade-offs between high link utilization and packet delay.
Sender could treat an ECN bit as a packet drop and adjust accordingly.
Pros:
  Doesn't confuse corruption and congestion.
  Allows routers to warn about congestion earlier (e.g. before queue is full). Reduces delays.
  Lightweight to implement.
Used in some, but not all routers.
Most useful in local networks (e.g. datacenters) where all routers use the bit.
Notes: We do have something!