## Slide 1
Slides credit: CS 168@ UC Berkeley
Ethernet, STP
Lecture 16 (End-to-End 1)
DP
DP
DP
DP
R1
DP
DP
DP
DP
RP
R2
RP
RP
R4
R3
RP
R7
BP
R5
RP
BP
RP
R6
Notes: Slides template credit: Josh Hug, Lisa Yan

## Slide 2: Connecting Local Hosts
Lecture 16, Spring 2026
Ethernet
Connecting Local Hosts
Multiple Access Protocols
Sending Packets
Layer 2 Networks
Layer 2 Routing
Naive Approach: Flooding
Learning Switches
Spanning Tree Protocol (STP)
Implementing STP: BPDU Exchanges

## Slide 3: Link Layer
Today: A closer look at Layer 2.
Ethernet: How do we send data inside a local network?
ARP: How do we connect Layer 2 and Layer 3?
DHCP: What happens when you join the network for the first time?
Physical
Data Link
Network
Transport
Application
7
4
3
2
1
(DNS, HTTP)
(TCP, UDP)
(IP)
(Ethernet)
(Optical fiber, copper)

## Slide 4: Connecting Local Hosts
A
B
D
E
C
A
B
C
D
E
How could we connect hosts in a local network?
Mesh: Link between every pair of machines.
For every new host, we have to add new links to every other host.
Need a lot of (physical) ports per host.
Bus: A single wire for all machines.
Introduces a shared media.

## Slide 5: Shared Media
Shared media: Many machines using the same wire.
If multiple machines transmit at the same time, signals will interfere or collide.
Analogy: People talking simultaneously on a group call.
Note: Shared media is not necessarily a wire.
Could be light signals on a shared optical fiber.
Or radio waves on a shared wireless link.
A
B
C
D
E
Blah blah
Blah blah
??!
??!
??!

## Slide 6: Multiple Access Protocols
Ethernet
Connecting Local Hosts
Multiple Access Protocols
Sending Packets
Layer 2 Networks
Layer 2 Routing
Naive Approach: Flooding
Learning Switches
Spanning Tree Protocol (STP)
Implementing STP: BPDU Exchanges
Lecture 16, Spring 2026

## Slide 7: Multiple Access Protocols
CSMA/CD
CSMA
ALOHA
Tokens
Polling
A multiple access protocol allocates the shared media to everyone wanting to use it.
3 types of approaches.
Several protocols of each type.
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 8: Multiple Access Protocols (1/3) – Multiplexing
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Idea: Allocate a fixed slice of resources to each node.
Frequency-based multiplexing: Divide medium into frequency channels.
Time-based multiplexing: Give each node some fixed time slots.
Problem: Can be wasteful.
There's only so much frequency/time available to allocate.
If a node has nothing to say, some frequency/time goes unused.
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 9: Multiple Access Protocols (2/3) – Taking Turns
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Idea: Nodes take turns speaking.
Polling protocols: A coordinator decides when each node can speak.
  Example: I2C.
Token passing: Pass a virtual token around. Only the node with the token can speak.
  Example: IBM Token Ring, FDDI.
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 10: Multiple Access Protocols (2/3) – Taking Turns
Polling protocols: A coordinator decides when each node can speak.
A
B
C
D
Coordinator
A, do you have something to say?
Yes, blah blah blah
A can speak for as long as it needs.
A
B
C
D
Coordinator
B, do you have something to say?
No
B has nothing to say.
Coordinator can immediately move on to C.

## Slide 11: Multiple Access Protocols (2/3) – Taking Turns
Token passing: Pass a virtual token around. Only the node with the token can speak.
A
B
C
D
Blah blah blah
A holds the token.
A can speak for as long as it needs.
When A is done, it passes the token to B.
A
B
C
D
B has nothing to say.
It can immediately pass the token to C.
Token
Token

## Slide 12: Multiple Access Protocols (2/3) – Taking Turns
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Idea: Nodes take turns speaking.
Benefit: No more time wasted on idling.
  If someone has nothing to say, immediately move on.
Problem: Complexity.
  Need to implement inter-node communication.
  How do we elect the central coordinator?
  What if two nodes both think they have the token?
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 13: Multiple Access Protocols (3/3) – Random Access
CSMA/CD
CSMA
ALOHA
Tokens
Polling
Idea: Nodes talk whenever they have something to say.
Deal with collisions when they occur.
Benefit: Simplicity. No coordinators or tokens.
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 14: Multiple Access Protocols (3/3) – Random Access – ALOHA
CSMA/CD
CSMA
ALOHA
Tokens
Polling
ALOHA random access scheme: "rude" version.
If you have a packet, just send it.
  Recipient replies with an ack.
If two nodes send simultaneously, collision corrupts the packets.
  No ack!
If you don't get an ack: Wait some random amount of time, then resend.
  Randomness helps avoid another collision.
Invented at Univ Hawaii in 1968.
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 15: Multiple Access Protocols (3/3) – Random Access – CSMA
CSMA/CD
CSMA
ALOHA
Tokens
Polling
CSMA (Carrier Sense Multiple Access): "polite" version.
First, listen to see if anyone is sending.
Only start sending when it's quiet.
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 16: Multiple Access Protocols (3/3) – Random Access – CSMA and Propagation Delay
CSMA does not necessarily avoid collisions, because of propagation delay.
t=0: B starts sending.
  Signal takes time to reach A, C, D.
t=2: D wants to send.
  Signal hasn't reached D yet!
  D thinks it's quiet and starts sending.
Result: Collision!
A
B
C
D
time
space

## Slide 17: Multiple Access Protocols (3/3) – Random Access – CSMA/CD
CSMA/CD
CSMA
ALOHA
Tokens
Polling
CSMA/CD (Carrier Sense Multiple Access with Collision Detection):
Listen before sending, but also while you're sending.
If you hear someone else sending, stop! Collision detected.
CSMA/CD uses binary exponential backoff:
After every collision, wait up to twice as long before resending.
  After first collision: Wait between 0–4 seconds.
  If resend collides again: Wait between 0–8 seconds.
Resends fast when possible, slowing down when necessary (e.g. many senders).
Multiplexing
Taking Turns
Random Access
Multiple Access Protocols
Frequency
Time

## Slide 18: Sending Ethernet Packets
Ethernet
Connecting Local Hosts
Multiple Access Protocols
Sending Packets
Layer 2 Networks
Layer 2 Routing
Naive Approach: Flooding
Learning Switches
Spanning Tree Protocol (STP)
Implementing STP: BPDU Exchanges
Lecture 16, Spring 2026

## Slide 19: Ethernet MAC Address
Local Area Networks (LANs) are generally Ethernet.
Machines in the same LAN can exchange messages directly at Layer 2!
No need for IPs, routers, forwarding, etc.
Analogy: If we're in the same room, we can talk without using the postal system.
At layer 2, each machine has a MAC address (Media Access Control).
Can be used even if you don't have an IP address.
48 bits, written in hex, e.g. f8:ff:c2:2b:36:16.
Globally unique. Stored permanently on the machine ("burned in").
  Often can be overridden by software.
Allocated according to organization, e.g. manufacturer of the machine.
00
0111111111111101000011
110101000110110001101000
2 bits of flags
22-bit manufacturer ID
24-bit machine ID

## Slide 20: Types of LAN Communication
Ethernet supports three types of communication:
Unicast: Send a packet to a single recipient.
Destination = the recipient's MAC address.
Recall: On a shared medium, everybody gets the signal.
When you get a packet, check the destination to see if it's meant for you.
If not, ignore the packet.
Broadcast: Send a packet to everyone on the local network.
Packet already reaches everybody on the shared medium.
  We just need to make sure everyone knows it's meant for them.
Destination = the broadcast address, FF:FF:FF:FF:FF:FF.
Multicast: Send a packet to everyone in a specific group.
Again, everyone gets the packet – need to ensure the group knows it's for them.
Each group has a group address.
  Individual computer's address: First bit 0.
  Group address: First bit 1.
Broadcast is a special case of multicast, where everyone is in one group.
10
0111111111111101000011
110101000110110001101000
If this bit is 1, it's a group address.
Notes: Unicast: Send a packet to a single recipient.
Broadcast: Send a packet to everyone on the local network.
Multicast: Send a packet to everyone in a specific group.
  Machines in the local network can join groups.
Example of using multicast: Bonjour/mDNS.
Invented by Apple.
All Apple products join a multicast group.
Apple devices can multicast to the group.
  iPhone says: "Hey, local Apple products, can anyone play music?"
  Apple TV says: "Hey, local Apple products, I'm an Apple TV."
Actually uses DNS advertisements that are sent to multicast addresses.
  Uses specific DNS record types (e.g. SRV) to advertise capabilities.

## Slide 21: Ethernet Packet Structure
A data packet in Ethernet is often called a frame.
Many fields (destination, source, type, checksum) similar to IP header.
Need additional fields to separate packets on the wire.
Preamble (7)
SFD (1)
Destination MAC (6)
Source MAC (6)
Type (2)
Payload
FCS (4)
IPG (12)
Signal start of new packet on wire
Destination
Demultiplex (is payload IPv4 or IPv6?)
Source
Signal end of packet on wire
Checksum

## Slide 22: Layer 2 Networks
Ethernet
Connecting Local Hosts
Multiple Access Protocols
Sending Packets
Layer 2 Networks
Layer 2 Routing
Naive Approach: Flooding
Learning Switches
Spanning Tree Protocol (STP)
Implementing STP: BPDU Exchanges
Lecture 16, Spring 2026

## Slide 23: Layer 2 Networks
We could use more than one wire in a local network.
Switches need to forward packets toward their destination.
If a switch receives a broadcast packet: Send it to every neighbor.
Multicast is more complicated. Need to know who's in the group.
Each switch stores a routing table
Destinations are MAC addresses, instead of IP addresses.
S2
S1
A
S3
S3
B
C
D
S2's Table | 
Destination | Next Hop
A | R1
B | R3
C | R3
D | R4
Notes: Problem: MAC addresses can't be aggregated.
Allocated by manufacturer, not geographically.
This is why Layer 2 can't scale to the Internet.
Routing protocols from Layer 3 can also be used at Layer 2.

## Slide 24: Naive Approach: Flooding
Lecture 16, Spring 2026
Ethernet
Connecting Local Hosts
Multiple Access Protocols
Sending Packets
Layer 2 Networks
Layer 2 Routing
Naive Approach: Flooding
Learning Switches
Spanning Tree Protocol (STP)
Implementing STP: BPDU Exchanges

## Slide 25: Naive Approach: Flooding
When you receive a packet, send it out of all ports, except the incoming port.
Will this work?
Yes. The packet will reach everyone, including the destination.
R1
data
Don't send packet back out of the incoming link.
X

## Slide 26: Naive Approach: Flooding
Problems with flooding? Wastes bandwidth in two ways:
Packet is sent to other hosts (not the destination).
  Solution: Use learning switches to build forwarding tables.
Loops create broadcast storms.
  Solution: Use STP to remove loops.
Fixing these 2 problems will result in a good Layer 2 routing protocol.
R1
data
Don't send packet back out of the incoming link.
X

## Slide 27: Learning Switches
Ethernet
Connecting Local Hosts
Multiple Access Protocols
Sending Packets
Layer 2 Networks
Layer 2 Routing
Naive Approach: Flooding
Learning Switches
Spanning Tree Protocol (STP)
Implementing STP: BPDU Exchanges
Lecture 16, Spring 2026

## Slide 28: Learning Switches: Motivation
Problems with flooding? Wastes bandwidth in two ways:
Packet is sent to other hosts (not the destination).
  Solution: Use learning switches to build forwarding tables.
Loops create broadcast storms.
  Solution: Use STP to remove loops.
Fixing these 2 problems will result in a good Layer 2 routing protocol.
We could run a routing protocol to fix this, but we'll instead use learning switches, which are simpler.

## Slide 29: Learning Switches: Routing Process
R2's Table | 
To: | Next-hop:
R2's Table | 
To: | Next-hop:
A | R1
Key idea: When you receive a data packet, you get a clue about where the sender is.
If a packet from host A comes from the west...
...then host A must be to my west!
Use this idea to add a table entry for the sender.
As more packets get sent, more table entries get added.
Note: The packet only helps you learn about the sender (A), not the receiver (B).
R2
R1
R3
R4
From: A, To: B
From: A, To: B
This packet from A came from R1 (to my west).
Therefore, A must be toward R1 (to my west).

## Slide 30: Learning Switches: Forwarding Process
R2's Table | 
To: | Next-hop:
Forwarding is destination-based: Use the destination to decide the next-hop.
If the destination exists in the table: Forward to corresponding next-hop.
If the destination is not in the table: Flood out of all ports (except incoming port).
R2
R1
R3
R5
From: A, To: B
R4
From: A, To: B
R2's Table | 
To: | Next-hop:
B | R3
R2
R1
R3
R5
From: A, To: B
R4
From: A, To: B
Case 1: No entry for B (destination) in table.
Flood the packet to all ports (except incoming port).
Case 2: Entry for B (destination) is in table.
Use table entry to forward to next-hop.

## Slide 31: Learning Switches: Example
A
All tables start empty. Nobody has an entry for B, so the packet gets flooded.
Along the way, everyone gets a clue about A's location, and adds a table entry for A.
R1
R2
R4
R3
R5
B
C
R4's Table | 
To: | Next-hop:
R5's Table | 
To: | Next-hop:
R3's Table | 
To: | Next-hop:
R2's Table | 
To: | Next-hop:
From: A, To: B
From: A, To: B
From: A, To: B
From: A, To: B
From: A, To: B
From: A, To: B
From: A, To: B
From: A, To: B
R1's Table | 
To: | Next-hop:
R1's Table | 
To: | Next-hop:
A | Direct
R2's Table | 
To: | Next-hop:
A | R1
R3's Table | 
To: | Next-hop:
A | R2
R4's Table | 
To: | Next-hop:
A | R1
R5's Table | 
To: | Next-hop:
A | R4
This slide probably needs to be viewed with animation to make sense.

## Slide 32: Learning Switches: Example
R1's Table | 
To: | Next-hop:
A | Direct
R2's Table | 
To: | Next-hop:
A | R1
R3's Table | 
To: | Next-hop:
A | R2
R4's Table | 
To: | Next-hop:
A | R1
R5's Table | 
To: | Next-hop:
A | R4
This packet can get directly forwarded to A (no flooding) using the forwarding tables.
Routers along the B-to-A path get a clue about B's location, and add a table entry for B.
A
R1
R2
R4
R3
R5
B
C
From: B, To: A
From: B, To: A
From: B, To: A
From: B, To: A
This slide probably needs to be viewed with animation to make sense.
R1's Table | 
To: | Next-hop:
A | Direct
B | R2
R2's Table | 
To: | Next-hop:
A | R1
B | R3
R3's Table | 
To: | Next-hop:
A | R2
B | Direct
From: B, To: A

## Slide 33: Learning Switches: Expiring Routes
Each table entry is associated with a TTL. If the TTL reaches 0, the entry is deleted.
This allows invalid routes (e.g. link goes down) to eventually expire.

## Slide 34: Spanning Tree Protocol (STP)
Ethernet
Connecting Local Hosts
Multiple Access Protocols
Sending Packets
Layer 2 Networks
Layer 2 Routing
Naive Approach: Flooding
Learning Switches
Spanning Tree Protocol (STP)
Implementing STP: BPDU Exchanges
Lecture 16, Spring 2026

## Slide 35: Spanning Tree Protocol: Motivation
Problems with flooding? Wastes bandwidth in two ways:
Packet is sent to other hosts (not the destination).
  Solution: Use learning switches to build forwarding tables.
Loops create broadcast storms.
  Solution: Use STP to remove loops.
Fixing these 2 problems will result in a good Layer 2 routing protocol.
We'll now build a protocol for removing loops.
After the loops are removed, we can use learning switches to build forwarding tables and forward packets.

## Slide 36: Spanning Tree Protocol: Motivation
Loops can cause broadcast storms: Packets get forwarded around a loop forever.
Forwarding tables don't help. If the tables are empty, everyone floods the packet.
Learning switches don't help. We can install entries for the sender, but we still don't know where the receiver is, so the packet still gets flooded forever.
Not flooding out of the incoming port doesn't help. Packets could travel in loops of length 3 or more. (See example below.)
A
R1
R3
R2
R4
B
Best viewed in animation. A copy of the packet loops clockwise forever (red), and another copy loops counterclockwise forever (blue).

## Slide 37: Spanning Tree Protocol: Motivation
Our goal: "Disable" links to remove all the loops.
We'll now design the Spanning Tree Protocol (STP) to achieve this.
After the loops are removed, we can use learning switches to route packets.
Some other possible solutions, besides STP:
Drop packets when TTL expires: Won't work, because Ethernet header doesn't have a TTL field.
Drop packets we've seen before: Won't work, because Ethernet header doesn't have an ID field for identifying duplicates.
A
R1
R3
R2
R4
B

## Slide 38: STP Ignores Hosts
Hosts don't participate in STP.
Routers will do the job of disabling links to remove loops.
A
R1
R2
R3
R4
R6
R5
R7
B
C
A
B
C

## Slide 39: Step 1: Electing a Root
R1
Step 1: Elect one of the routers to be a root switch.
Each router is assigned an ID.
The root switch is the router with the lowest ID.
Each router's ID consists of two values, put together:
Priority: Manually set by operator.
MAC address of router. Used as tiebreaker if two routers have the same priority.
How do we pick a root switch?
Manually: Operator sets a low priority on the chosen root.
Default: All routers have the same default priority value. If operator doesn't override the default, the router with the lowest MAC address is the root.
R1
R2
R3
R4
R6
R5
R7
We'll assume the ID is the router number.
Thus, R1 is the root.

## Slide 40: Step 2: Labeling Ports
Step 2: Each router labels each of its ports as one of three types:
DP
R6
R3
RP
R2
R8
DP
BP
BP
R9
R4
Routers distance < x away from the root.
Routers distance > x away from the root.
R4 is x away from root.
Out of the ports leading to routers closer to the root:
The Root Port is the one along the least-cost path to the root.
Blocked Ports are all the other ports (not along least-cost path).
Designated Ports lead to routers further from the root.

## Slide 41: Port Labels: Designated Ports
Designated Ports lead to routers further from the root.
Out of the ports leading to routers closer to the root:
The Root Port is the one along the least-cost path to the root.
Blocked Ports are all the other ports (not along least-cost path).
R3
R7
R2
DP
DP
DP
DP
R1
DP
DP
DP
R5
R4
DP
R6

## Slide 42: Port Labels: Root Ports
Designated Ports lead to routers further from the root.
Out of the ports leading to routers closer to the root:
The Root Port is the one along the least-cost path to the root.
Blocked Ports are all the other ports (not along least-cost path).
DP
DP
DP
DP
R1
DP
DP
DP
DP
RP
R2
RP
RP
R4
R3
RP
R7
R5
RP
RP
R6
Shortest path to root is via R3, not R4.
Shortest path to root is via R6, not R5.

## Slide 43: Port Labels: Blocked Ports
Designated Ports lead to routers further from the root.
Out of the ports leading to routers closer to the root:
The Root Port is the one along the least-cost path to the root.
Blocked Ports are all the other ports (not along least-cost path).
DP
DP
DP
DP
R1
DP
DP
DP
DP
RP
R2
RP
RP
R4
R3
RP
R7
BP
R5
RP
BP
RP
R6

## Slide 44: Step 3: Disabling Links
Each router can now disable its blocked ports.
To disable a port: Do not send/receive data packets with that port.
Why does this work?
Root port is your best path toward root.
Blocked ports are worse, redundant paths toward root. Disable these ports.
Designated ports lead away from the root. Other further-away routers might use this port (along their shortest paths to root), so leave these enabled for further-away routers to use.
DP
DP
DP
DP
R1
DP
DP
DP
DP
RP
R2
RP
RP
R4
R3
RP
R7
BP
R5
RP
BP
RP
R6

## Slide 45: Step 3: Disabling Links
Each link is disabled by only one side.
The further side thinks:
Is this link along my shortest path to root?
If yes, enable it (RP). If no, disable it (BP).
The closer side thinks:
The further side might need this link (it might be along their shortest path to root). So I'll leave it enabled just in case (DP).
DP
R7
BP
R5
I'm on the closer side of this link.
I'll leave this link enabled (DP).
The other side can disable this link if they don't need it.
I'm on the further side of this link.
I don't need this link (not my shortest path to root), so I'll disable it (BP).

## Slide 46: Breaking Ties
What if there are two shortest paths to the root?
Use router ID to tiebreak.
Lower ID = shortest path to root (RP).
Higher ID = not shortest path to root (BP).
R2 and R3 both yield shortest paths to root.
Tiebreak: Choose R2 (lower ID).
DP
DP
R1
DP
DP
RP
R3
R2
RP
RP
R4
BP

## Slide 47: Breaking Ties
If the link leads to a router equally-far from the root as you:
If their ID is higher, they are "further" (DP).
If their ID is lower, they are "closer" (RP or BP).
DP
DP
RP
RP
DP
BP
DP
BP
RP
R4
RP
R5
DP
DP
R3
R2
R1
I'm 1 away from root.
R2 is also 1 away from root, but its ID is lower, so R2 is "closer" (RP/BP).
I'm 2 away from root.
R5 is also 2 away from root, but its ID is higher, so R5 is "further" (DP).
I'm 1 away from root.
R3 is also 1 away from root, but its ID is higher, so R3 is "further" (DP).
I'm 2 away from root.
R4 is also 2 away from root, but its ID is lower, so R4 is "closer" (RP/BP).

## Slide 48: STP With Shared Medium Links
What does "Designated" mean?
Remember: A single link could have multiple hosts/routers connected to it (shared medium).
When hosts on that link send a packet, the packet is received on the DP, but not on the BP.
This approach helps us avoid loops.
If the packet was received on both ports, it could take multiple paths to the destination, creating a loop.
DP
DP
R1
RP
RP
DP
BP
DP
BP
RP
R4
RP
R5
DP
DP
R2
R3

## Slide 49: Implementing STP: BPDU Exchanges
Lecture 16, Spring 2026
Ethernet
Connecting Local Hosts
Multiple Access Protocols
Sending Packets
Layer 2 Networks
Layer 2 Routing
Naive Approach: Flooding
Learning Switches
Spanning Tree Protocol (STP)
Implementing STP: BPDU Exchanges

## Slide 50: Implementing STP with BPDU Exchanges
STP requires global knowledge of the network:
Who is the root (lowest ID)?
Does this link lead closer to the root, or further from the root?
To learn this information, routers exchange control-plane messages.
They have a fancy name: Bridge Protocol Data Units (BPDUs).
Similar to advertisements in distance-vector.

## Slide 51: BPDU Advertisement Rules
Each router keeps track of two things:
Who is the best root I know about? (Recall: "better" = "lower ID".)
How far away is this best root?
When you send a BPDU to your neighbors, include these two things.
When you hear a BPDU from your neighbor, accept it and update your state if:
The advertised root has a lower ID. (Note: Accept the better root, even if cost is worse.)
The advertised root is the same, but the cost to root is better.
R5
R5's State:
Root R3 is 7 away
If advertised root is better than R3: Accept.
If advertised root is R3, and cost is better than 7: Accept.
Else: Reject.

## Slide 52: BPDU Exchange Example
R1
R2
R3
R4
R6
R5
R7
R2's State:
Root R2 is 0 away
R4's State:
Root R4 is 0 away
R5's State:
Root R5 is 0 away
R7's State:
Root R7 is 0 away
R6's State:
Root R6 is 0 away
R3's State:
Root R3 is 0 away
R1's State:
Root R1 is 0 away
Initially, every router only knows about itself, so it thinks the root is itself.

## Slide 53: BPDU Exchange Example
R1
R2
R3
R4
R6
R5
R7
R2's State:
Root R2 is 0 away
R4's State:
Root R4 is 0 away
R5's State:
Root R5 is 0 away
R7's State:
Root R7 is 0 away
R6's State:
Root R6 is 0 away
R3's State:
Root R3 is 0 away
R1's State:
Root R1 is 0 away
Accept if better root, or better cost to same root.
I'm R3.
Root R3 is 0 away.
Found a better root! Accept.
R6's State:
Root R3 is 1 away
I'm R3.
Root R3 is 0 away.
R3 is a worse root. Reject!
Advertisement said R3 is 0 away.
Link cost is 1.
Total cost to R3 must be 0 + 1 = 1.

## Slide 54: BPDU Exchange Example
R1
R2
R3
R4
R6
R5
R7
R2's State:
Root R2 is 0 away
R4's State:
Root R4 is 0 away
R5's State:
Root R5 is 0 away
R7's State:
Root R7 is 0 away
R6's State:
Root R3 is 1 away
R3's State:
Root R3 is 0 away
R1's State:
Root R1 is 0 away
Accept if better root, or better cost to same root.
I'm R1.
Root R1 is 0 away.
Found a better root! Accept.
R2's State:
Root R1 is 1 away
I'm R1.
Root R1 is 0 away.
Found a better root! Accept.
R3's State:
Root R1 is 1 away

## Slide 55: BPDU Exchange Example
R6's State:
Root R3 is 1 away
R6's State:
Root R1 is 2 away
R1
R2
R3
R4
R6
R5
R7
R2's State:
Root R1 is 1 away
R4's State:
Root R4 is 0 away
R5's State:
Root R5 is 0 away
R7's State:
Root R7 is 0 away
R3's State:
Root R1 is 1 away
R1's State:
Root R1 is 0 away
Accept if better root, or better cost to same root.
I'm R2.
Root R1 is 1 away.
Found a better root! Accept.
I'm R3.
Root R1 is 1 away.
Found a better root! Accept.
R4's State:
Root R1 is 2 away
Always accept the better root, even if the cost is worse.

## Slide 56: BPDU Exchange Example
R1
R2
R3
R4
R6
R5
R7
R2's State:
Root R1 is 1 away
R4's State:
Root R1 is 2 away
R5's State:
Root R5 is 0 away
R7's State:
Root R7 is 0 away
R6's State:
Root R1 is 2 away
R3's State:
Root R1 is 1 away
R1's State:
Root R1 is 0 away
Accept if better root, or better cost to same root.
I'm R4.
Root R1 is 2 away.
Found a better root! Accept.
Worse path to R1!* Reject.
R5's State:
Root R1 is 3 away
I'm R4.
Root R1 is 2 away.
If R4 is 2 away, then I must be 3 away. This is worse than my current cost to R1.

## Slide 57: BPDU Exchange Example
R1
R2
R3
R4
R6
R5
R7
R2's State:
Root R1 is 1 away
R4's State:
Root R1 is 2 away
R5's State:
Root R1 is 3 away
R7's State:
Root R7 is 0 away
R6's State:
Root R1 is 2 away
R3's State:
Root R1 is 1 away
R1's State:
Root R1 is 0 away
Accept if better root, or better cost to same root.
I'm R5.
Root R1 is 3 away.
Found a better root! Accept.
R7's State:
Root R1 is 4 away

## Slide 58: BPDU Exchange Example
R1
R2
R3
R4
R6
R5
R7
R2's State:
Root R1 is 1 away
R4's State:
Root R1 is 2 away
R5's State:
Root R1 is 3 away
R7's State:
Root R7 is 0 away
R6's State:
Root R1 is 2 away
R3's State:
Root R1 is 1 away
R1's State:
Root R1 is 0 away
Accept if better root, or better cost to same root.
Found a better cost to same root! Accept.
I'm R6.
Root R1 is 2 away.
R7's State:
Root R1 is 3 away

## Slide 59: BPDU Exchange Example
R1
R2
R3
R4
R6
R5
R7
R2's State:
Root R1 is 1 away
R4's State:
Root R1 is 2 away
R5's State:
Root R1 is 3 away
R7's State:
Root R1 is 3 away
R6's State:
Root R1 is 2 away
R3's State:
Root R1 is 1 away
R1's State:
Root R1 is 0 away
After convergence, periodic advertisements allow you to learn your neighbors' cost-to-root values.
Use your neighbors' cost-to-root values to assign DP, RP, BP.

## Slide 60: Why BPDU Exchanges Work
Why does this work?
The true root has the lowest ID, so advertisements with the true root will always be accepted over worse roots.
Other exchanges might happen (e.g. "I thought root is R7, now I think it's R3"), but eventually, the true root (e.g. R1) will propagate to everybody.

## Slide 61: Spanning Tree Protocol: Recap
Designated Ports lead to routers further from the root.
Out of the ports leading to routers closer to the root:
The Root Port is the one along the least-cost path to the root.
Blocked Ports are all the other ports (not along least-cost path). Disabling BPs helps us remove loops.
Routers exchange information in BPDUs (e.g. "Root R1 is 3 away") to help routers agree on the root and label ports as DP/RP/BP.
When you hear a BPDU from your neighbor, accept it and update your state if:
The advertised root has a lower ID. (Note: Accept the better root, even if cost is worse.)
The advertised root is the same, but the cost to root is better.
DP
DP
DP
DP
R1
DP
DP
DP
DP
RP
R2
RP
RP
R4
R3
RP
R7
BP
R5
RP
BP
RP
R6
Router with lowest ID is elected as the root.