## Slide 1: Architecting the Internet
Internet Design Principles
Architecting the Internet
Narrow Waist, Demultiplexing
End-to-End Principle
Designing Resource Sharing
Statistical Multiplexing
Circuit vs. Packet Switching
Which is Better?
A Brief History
Lecture 2, Spring 2026
Notes: here we go okay okay so this is cs168 second
0:29
lecture all about the internet design principles so to start off with today I
0:36
just want to set the stage for what today's all about last time we showed you how the internet was built we told
0:41
you things like here are some layers and layer three provides best effort and
0:46
routers understand the first three layers and end hosts understand all five layers so we kind of just told you that
0:54
this is how the internet was built and you trusted us that was how the internet's built and everything was
0:59
great so today's question is not how but why why did we make all those choices who
1:05
was it that decided that layer three is all about best effort and that there are no reliability guarantees at layer three
1:12
who was it that decided that there are these five layers and that they're built in this particular way and are there
1:18
other ways that we could have designed the internet

## Slide 2: The Internet Design Principles
The Internet Design Principles:
Decentralized control.
Best-effort service model.
Route around trouble.
Dumb infrastructure (with smart endpoints).
End-to-end principle.
Layering.
Federation via narrow-waist interface.
These are guidelines, not unbreakable rules.
This is just one of many possible designs.
We're still debating the big questions!
Notes: there are seven internet design principles that we've identified and we'll go through each one one by one and
3:16
we'll focus on a few of them today but before we do that I just want to point out that these are guidelines so it's
3:21
not like somebody came along and said these are the rules if you don't follow them you're in trouble no one really
3:27
said these are the rules that we have to follow but but these are kind of the principles that people have settled on
3:32
over time and even today there are people who are questioning some of these principles and saying well what if we
3:38
broke this principle and tried to do things differently how would that affect the current design of the internet could
3:44
we make things better what are the trade us if we break these rules so these are not unbreakable rules people will bend
3:50
them and try to work around them just to see what happens and sometimes it works
3:56
sometimes it doesn't but these are kind of guiding principles that will help us think about the internet and other
4:02
similar design tasks

## Slide 3: The Internet Design Principles
1. Decentralized control.
Each network device (e.g. router) runs on its own. No central mastermind.
2. Best-effort service model.
At Layer 3, routers only offer best-effort delivery.
3. Route around trouble.
Network must be resilient to failures.
If a router or link goes down, find a different path through the network.
4. Dumb infrastructure (with smart endpoints).
Routers forward packets. They don't care about what's inside.
5. End-to-end principle.
Implement features at the end hosts, not at the routers.
Notes: Alternative: Could introduce some "quality-of-service" guarantees.
Alternative: SDN (Software-Defined Networking) centralizes control for performance.
Alternative: DSDN (Distributed SDN) moves back toward decentralization again!
S
o let's go through each one so the first one is decentralized control as mentioned last
4:08
time there is no one Mastermind running the Internet it's not like there's a single computer somewhere and it's
4:14
thinking really hard and it's running all of the internet for you there's no such computer like that so the internet
4:21
is distributed every Network device every router every host is thinking all by itself and by talking to its
4:28
neighbors it's somehow forming the overall Network that's the internet so there is no Central Mastermind that's a
4:35
principle that we found out as we designed the internet but there are alternatives so for example later in the
4:40
class we'll see something called software defined networking where a bunch of people got together and said well why does it have to be like this
4:47
what if there was a central Mastermind how would that change things and so later we'll see an alternative design
4:53
where there is a central Mastermind and then some people came back and said actually the version with the Mastermind
4:58
is good but what if we moved it back toward decentralization and had less of a mastermind so this one is still being
5:05
debated but on the modern internet I think it's safe to say there is no one computer doing all the work the work is
5:12
being distributed
we also saw best effort that's another internet design principle and we mentioned last time
5:17
that at layer three routers only offer best effort that was a design choice and we could have come up with an alternate
5:24
one we could have said actually layer 3 gives you reliability it guarantees that packet are sent and we'll see why you
5:32
might have chosen the best effort service model later today when we talk about the endtoend principle but that's
5:38
another internet design principle

## Slide 4: The Internet Design Principles
6. Layering.
Each layer relies on the layer below, and supports the layer above.
Allows us to innovate at one layer, without disturbing other layers.
Alternative: cross-layer protocols spanning multiple layers let us optimize several layers together.
7. Federation via narrow-waist interface.
Federation works because all operators speak the same Layer 3 protocol.
Notes: and there's two more layering we've seen this one a lot already from last time remember everyone
Different communities can work on different layers.
  Chip designers at Layers 1 and 2.
  Application developers at Layer 7.
7:54
relies on services from the layer below them and they provide services to the layer above of them and this is great
8:00
because it means that different communities can work on different layers so for example if you work in the
8:06
hardware Community you can spend a lot of work and develop new standards at layers one and two and you don't really
8:12
disturb the application developers who are coming up with new protocols at layer 7 so everyone can innovate at the
8:19
same time at different layers that's great it's something we saw last time but later in the class we're actually
8:25
going to see protocols that break this that say you know what it's nice that the layers are separate but what if we
8:30
actually thought about layers seven and four together we made it like one Mega layer that's four and seven together and
8:37
it turns out that might be useful if you're trying to optimize for performance so near the end of the class
8:42
we'll see something called quick quic that's an alternative where they broke this Rule and finally one we see we will
8:49
see today is the narrow waste and basically it's a fancy way of saying there's one layer three protocol and
8:56
that's important for making sure that everyone speaks the same language so those are the seven principles you're
9:01
going to see them throughout the class so it's okay if they don't perfectly make sense just yet but just know that
9:07
these are some things that the people who built the internet spent a lot of time thinking
9:14
About
Questions time !

## Slide 5: Narrow Waist, Demultiplexing
Internet Design Principles
Architecting the Internet
Narrow Waist, Demultiplexing
End-to-End Principle
Designing Resource Sharing
Statistical Multiplexing
Circuit vs. Packet Switching
Which is Better?
A Brief History
Lecture 2, Spring 2026
Notes: okay so I'm not going to go
9:21
through all seven principles and great detail today again they will pop up over and over throughout the class but I will
9:27
call out two of them the narrow waist and the n to end principle because they will bring out some interesting
9:33
questions about internet design that we wanted to talk about

## Slide 6: Layering in the Open Systems Interconnected (OSI) Model
L7: Application
do the thing
L6: Presentation
(ignored here)
L5: Session
(ignored here)
L4: Transport
beyond delivery: (un)reliability, packet assembly, congestion control, ...
L3: Network
global delivery, best-effort
L2: Data link
local delivery, best-effort
L1: Physical
physical transfer of bits
Notes: Distinguish local and global delivery

## Slide 7: Layering in practice
HTTP(S)
TCP
IP
Ethernet
802.11 Wi-Fi
CAN bus
UDP
USB
SSH
Email (IMAP/POP)
...
L7: Application
L6: Presentation
L5: Session
L4: Transport
L3: Network
L2: Data link
L1: Physical
L3.5: research!

## Slide 8: Protocols at Different Internet Layers
Physical
Link
Internet
Layer 1:
Layer 2:
Layer 3:
Transport
Layer 4:
Application
Layer 7:
Multiple protocols exist at each layer.
End hosts can agree on the L4 and L7 protocols they want to use.
Routers on each link can agree on the L1 and L2 protocols they want to use.
Optical
Copper Wire
Radio Waves
Telephone Line
Wi-Fi
Point-to-Point
Ethernet
FDDI
IP
TCP
UDP
SMTP
DNS
HTTP
NTP
Notes: Jan 2025 - Layer 7 box said UDP instead of NTP
we'll start with this narrow waste principle so something
9:40
that I kind of didn't mention in a lot of detail last time but is important is that multiple protocols can exist at
9:47
every layer so it's not like at layer seven you only have one choice there's actually lots of different protocols
9:53
there's SMTP for sending emails there's HTTP there's you know ntp whatever that
9:59
is so you don't need to know what these are but basically there's lots of different things you can do at layer 7even lots of different pieces of
10:06
software that you can run and likewise you have a choice at layer four you have a choice at Layer Two you have a choice
10:12
at layer one so all of these different layers you have a choice of what protocol you want to use and if two
10:19
people want to communicate they can agree on their own stack of protocols so maybe Alice and Bob say we're going to
10:26
use ntp which runs over UDP which runs over IP which runs over Wi-Fi which runs
10:31
over radio waves they can choose that stack

## Slide 9: Protocols at Different Internet Layers
Physical
Link
Internet
Layer 1:
Layer 2:
Layer 3:
Transport
Layer 4:
Application
Layer 7:
Multiple protocols exist at each layer.
End hosts can agree on the L4 and L7 protocols they want to use.
Routers on each link can agree on the L1 and L2 protocols they want to use.
Optical
Radio Waves
Telephone Line
Wi-Fi
Point-to-Point
FDDI
UDP
DNS
HTTP
NTP
Copper Wire
Ethernet
IP
TCP
SMTP
Notes: Jan 2025 - Layer 7 box said UDP instead of NTP
or maybe another pair of users
10:36
says actually we're going to use SMTP which runs over TCP which runs over IP
10:42
which runs over ethernet which runs over copper wire that's great you can choose that too so you can choose any stack
10:49
that you want you know there are some constraints like for example ethernet is a layer 2 protocol that's for wired
10:55
connection so you would use wires at layer one it'd be kind of weird if you used ethernet and somehow used radio
11:02
waves not an important detail but someone last time asked about Layer Two and layer one some Layer Two Protocols
11:08
are connected or closely related to their corresponding layer one protocol which is kind of what this is showing
11:15
not an important detail kind of a digression but the important thing is Two Hosts if they want to communicate
11:20
they can agree on a stack of protocols and they can use that stack of verticals and different pairs of users can pick
11:27
different Stacks

## Slide 10: Protocols at Different Internet Layers
Physical
Link
Internet
Layer 1:
Layer 2:
Layer 3:
Transport
Layer 4:
Application
Layer 7:
The narrow waist: IP (Internet Protocol) is the only protocol at Layer 3.
All hosts and routers understand IP.
This unifies the Internet and enables federation.
Optical
Copper Wire
Radio Waves
Telephone Line
Wi-Fi
Point-to-Point
Ethernet
FDDI
IP
TCP
UDP
SMTP
DNS
HTTP
NTP
Notes: Jan 2025 - Layer 7 box said UDP instead of NTP
so it's not like everyone has to use the same stack but if you stare at this diagram a little
11:33
closely there is one layer where you don't get a choice so you know at Layer Two you have these choices and more that
11:40
we haven't shown but there's one layer where you don't get a choice that is layer three there is no choice here you
11:47
have to use IP Internet Protocol that is the only choice at layer three and this
11:52
is the narrow waste that people talk about you stare at this picture and see kind of it Narrows in the middle that's
11:58
the narrow waste that you're looking at right there and this is important because as we said from last time the
12:04
internet is lots of different companies machines users talking to each other and
12:09
if everyone spoke different languages there would just be no way to connect everyone up together like if AT&T had
12:17
one stack of protocols and Verizon had a totally different stack of protocols we would be out of luck there's no way for
12:23
packets to tra travel between Verizon and AT&T so it's important that in our
12:29
stack there is this one convergence point where everyone speaks the same protocol the same language so this way
12:36
even if Verizon has a packet and we have to forward to AT&T that's no problem because the packets eventually uh get
12:45
sent over IP and that's a protocol that everyone understands so it's very
12:50
important that here there's only one choice if we had tons of different choices we'd get totally incompatible
12:56
Stacks this is good this ensures that when routers want to forward packets everyone is using IP to forward packets
13:03
we can forward things between different companies between different users between different countries but everyone
13:09
knows what IP is that's what it means to have a narrow waste you're staring at
13:15
Questions about narrow waist!!

## Slide 11: Demultiplexing
Physical
Link
Internet
Layer 1:
Layer 2:
Layer 3:
Transport
Layer 4:
Application
Layer 7:
When you receive a packet, you pass it up the stack, to higher-layer protocols.
How did IP know to pass up to TCP, not UDP?
How did TCP know to pass up to HTTP, not SMTP?
Optical
Copper Wire
Radio Waves
Telephone Line
Wi-Fi
Point-to-Point
Ethernet
FDDI
IP
TCP
UDP
SMTP
DNS
HTTP
NTP
Which way?
Which way?
Notes: Jan 2025 - Layer 7 box said UDP instead of NTP
when you have
13:51
packets remember from last time that when you receive a packet it has all of the headers wrapped around it and then
13:57
you send the packet up to higher layers and every time you send the packet up to a higher layer it unwraps a header
14:03
that's from last time so you receive a packet it's a bunch of ones and zeros on the wire and then you unwrap a header
14:10
send it up to layer two layer two unwraps its header sends it to layer three unwraps a header unwraps unwraps
14:17
and we get to the very top but if you stare at this narrow waist architecture there's kind of a problem once you reach
14:23
these higher layers so let's say you're at layer three and you unwrap the packet now there's a TCP protocol and there's a
14:31
UDP protocol and you can think of these as different programs running on your computer which of these two programs do
14:37
you use to process this packet is this packet a TCP packet which means we
14:42
should have the TCP code process it or is it a UDP packet which means the UDP code should process it and likewise once
14:50
the packet reaches TCP and TCP unwraps its layer for header how does TCP know
14:56
that it should pass the packet up to the http code and not the SMTP code or some
15:01
other piece of code so it's kind of like when I work my way up this stack there
15:07
are these points where I'm not really sure which path to take should I go this way should I go this way and likewise
15:13
with TCP should I go this way should I go this way so we need something to tell
15:18
the IP protocol or the TCP protocol which way to send the packet as it goes
15:24
further up the stack what's the next protocol that should handle this packet so this is the problem we have to solve

## Slide 12: Demultiplexing at Layer 3
Demultiplexing:
Add a new header field that tells us what the next (higher) layer protocol is.
Allows the IP code to pass the rest of the packet to the appropriate L4 code.
IP
TCP
UDP
Which way?
From: Alice's computer
To: Bob's computer
Next layer is TCP.
Layer 4 headers
"Potato."
From: Alice's computer
To: Bob's computer
Next layer is UDP.
Layer 4 headers
"Potato."
Notes: it's got a name it's called D multiplexing I have multiple choices and I need to narrow it down to just one so
15:37
D multiplexing says I need to know which way this packet goes and the way we're going to solve this is well we have this
15:43
header already the header tells us a lot of useful information about this packet and maybe another useful piece of
15:50
information might be which way this packet should be passed up so for example at layer three IP we can add a
15:57
new header field that says this packet is a TCP packet so when you unwrap this
16:03
header all the stuff inside in blue and purple this should be passed to the TCP
16:08
code to process this is a TCP header send it to TCP they will handle it or
16:14
maybe the packets a UDP packet in that case the header would say actually the thing inside is a UDP packet so when you
16:21
unwrap this header please send this code to the UDP protocol and the UDP protocol
16:27
will process this packet accordingly so that's called D multiplexing and the way it's implemented at Layer Three is you
16:33
add a new header field one that we didn't have before we have it now and it basically tells you what's the next
16:40
layer protocol that needs to process this packet and so this way we now know
16:45
which way the packet needs to get passed up when you reach the end host does it go to the TCP code the UDP code the
16:51
demultiplexing field tells us

## Slide 13: Demultiplexing at Layer 4
Firefox
Demultiplexing also works at Layer 4.
Each running application on your computer is associated with a port number.
When L4 receives a packet, it uses the port number to pass the packet to the corresponding application.
TCP
Email
Which way?
From: Port 587
To: Port 50000
Stop watching YouTube and answer your email.
From: Port 194
To: Port 60000
you're fired!!!
From: Port 80
To: Port 40000
Here's that YouTube video you asked for.
Slack
More specifically, each open connection on the computer.
(40000)
(50000)
(60000)
Notes: turns out the same idea
16:57
works at layer four so at layer four you get this packet and you can't really tell who this is for is this for HTTP is
17:04
this for SMTP we're actually going to be even more specific here and instead of just saying a protocol we're actually
17:11
going to identify a specific application so for example you can think of well my computer it's running a couple things
17:17
right now it's running Firefox to show you the slides it's running Zoom to record this lecture it's probably
17:24
running other things like an email client to send and receive emails so my Compu is running a lot of programs and
17:31
when my TCP protocol receives a packet it needs to know should this packet be
17:36
passed to Firefox is this a packet for Firefox is this a packet for the email client is this a packet for the slack
17:43
messaging client so that's something else we need to demultiplex as well so
17:48
not only are we demultiplexing the next protocol to handle this packet but at layer seven we're actually
17:55
demultiplexing the next application to process this pack and the way that we're going to label
18:02
these applications is we'll just give each one a number so for example maybe Firefox is number 40,000 and the email
18:09
client is number 50,000 and the slack messaging app is number 60,000 so
18:14
somehow we pick some numbers and then in the header field the header field has a a field the header Has a Field sorry
18:22
that tells us which application this packet is meant for so for example if I receive a packet and it says the pack is
18:29
going to Port 40,000 well then my TCP code knows oh okay this is for Firefox
18:34
so I unwrap the header I take this stuff in purple and I send it to Firefox or if I get a packet that says to Port 60,000
18:42
I think oh okay that's that's slack so what I should do is I should unwrap this header and send this packet over to
18:48
slack

## Slide 14: Ports at Layer 4
Port numbers help us distinguish between applications on the same computer.
IP address (Layer 3) for all the applications is the same.
But each connection is associated with a different port number.
Analogy: Room numbers.
You and your housemate both have the same street address.
If someone sends a letter to your house, who is it for?
Distinguish by assigning room numbers to each housemate.
From: YouTube server
To: Bob's computer
Next layer is TCP.
From: Port 80
To: Port 40000
[cat video]
Demultiplex: Which L4 protocol?
Demultiplex: Which L7 application?
Notes: they're ways to identify different applications on a single computer and then we can use those port numbers to
19:02
Dem Multiplex when you receive a packet at layer four this allows us to send it to the correct end application at layer
19:12
7 so here's an analogy if ports don't make sense yet so what is a port maybe
19:18
another way of putting it is it allows us to distinguish between applications on the same computer so if you think
19:24
about Firefox and my email program both of them are on my my computer which
19:29
means they have the same IP address my computer has an IP address they both get sent to the same IP address so how do I
19:36
know whether the packet is for the mail client or for Firefox well that's where
19:41
the port number comes in each application has a different port number it allows us to distinguish between the
19:47
two applications even though they have the same layer three IP address so the
19:53
analogy that I would come up with based on our favorite postal analogy is think about room numbers so let's say you have
19:59
a housemate there two of you you're living in the same house or the same apartment that means you both have the same street address so if someone sends
20:07
a letter to your house your street address how do we know is it for you is it for your housemate we don't know who
20:13
it's for and the way we're going to fix this is we're going to add room numbers inside of your house so you're going to
20:19
go to your room and tape okay my room is you know room 40,000 and my buddy's room is room 50,000 and this way when we send
20:26
and receive mail the mail will say oh actually this is for room 50,000 and you
20:31
think okay that's my buddy's room it's not for me or okay this Letter's uh got
20:37
a port number of 40,000 so it's for me that's my room number so another way of thinking of these ports is it's room
20:43
numbers within the same house or the same building

## Slide 15: Ports at Layer 4
Both end hosts in a connection have a port number.
A private client (e.g. your computer) can use a randomly-generated port number.
A public server (e.g. YouTube) must use a fixed, well-known port number.
Analogy: Room numbers.
Pick any number for your bedroom. No one cares.
Public room numbers must be fixed and well-known.
From: Bob's computer
To: YouTube server
Next layer is TCP.
From: Port 40000
To: Port 80
give me cat video
From: YouTube server
To: Bob's computer
Next layer is TCP.
From: Port 80
To: Port 40000
[cat video]
Outgoing packet: Bob picks a random port number, but sends to YouTube's fixed port, 80.
Incoming reply: YouTube replies to Bob's chosen port. Bob's computer passes the packet to the correct application (e.g., Firefox).
Notes: so to extend this analogy
20:50
just a little bit more something we should point out is that port numbers actually exist on all the machines so
20:55
not just my computer which has a bunch of applications running but also like public servers so for example YouTube
21:03
there must be some computer over in Google's building that's running YouTube that computer also has a bunch of port
21:09
numbers because that computer is also running a lot of different programs so the main difference between private
21:15
machines like my machine and public servers like the server that's running YouTube is I can use whatever room
21:22
numbers I want I can pick my own port numbers doesn't matter but by contrast the public server should use a fixed
21:29
well-known port number that everyone in the world knows so to go back to our favorite analogy again if I am in my own
21:36
house nobody cares what room number I assign to my bathroom if my bathroom is
21:42
room 50 that's great if my bathroom is room 200 that's fine too it doesn't matter if I change it it doesn't matter
21:48
as long as when I send out a packet the reply goes to that same room number things are good so it doesn't really
21:54
matter what number I pick however if you think about a public building like soda
22:00
Hall those have public room numbers so soda 310 that's a classroom you can't
22:05
just go to soda 310 and like change the number on the room then you're going to confuse a lot of students so you can't
22:10
do that so public room numbers they have to be fixed everyone has to know them
22:16
but by contrast in your own private bedroom you can pick any number you want nobody cares so that's kind of my
22:22
analogy for port numbers on private computers and public servers and to put
22:28
it all together this is what sending packets with port numbers might look like so let's say you're sending an
22:34
outgoing packet so you're private computer I want to load a c video shouldn't be watching c videos during
22:39
lecture but if you are watching One what you would do is you'd pick a port number this is like your own private room
22:45
number so I'm in room 40,000 okay great that's a room number that I picked for
22:50
myself and I'm going to send this to the YouTube server but the YouTube server
22:55
probably has a bunch of different programs running so what particular program on the YouTube server do I
23:01
actually want I want the one at Port 80 80 is a useful number this is a public
23:06
number everyone knows it I know it your computer knows it you now know it everyone knows that Port 80 is the place
23:13
that YouTube is serving videos so my front port number I pick at random
23:19
whatever I want but the destination port number it says it's not just any program
23:24
on YouTube server it's specifically the program running on Port 80 the one that's serving videos and everyone in
23:30
the world knows that YouTube serves videos on Port 80 that's fixed so then
23:36
what's YouTube going to do YouTube receives your packet it sees okay it's for Port 80 so I give the packet to
23:43
YouTube's video processing application it loads the Cat video it gives it back
23:48
to you and in the reply kind of what you'd expect the from field and the two field are reversed it says this is from
23:55
Port 80 this is from the program that's serving YouTube videos and it's to Port
24:00
40,000 that's the room that requested it and remember all of this is at layer four it doesn't mean we can replace
24:07
layer three we need both of them so just like how I can't go to the Post Office and say hey send this mail to room 50
24:15
what are you talking about room 50 of what building so just like how we have to specify both the room number and the
24:22
physical street address in these packets we have multiple layers we have to specify the computer that is the IP
24:29
address at layer three and also we have to specify the port number that is the
24:35
application running on that particular computer so these two layers together specify one application on one computer
24:43
and then they can go back and forth sending videos and whatever else that application wants to do so that's what
24:50

## Slide 16: Caution – Terminology Conflict
In networking, there are two different things, both called "ports."
If it's unclear, we will specify "logical port" or "physical port."
From: Port 80
To: Port 40000
[cat video]
Logical port: A number identifying an application. Exists in software.
Physical port: The hole you plug a cable into. Exists in hardware.
Notes: https://commons.wikimedia.org/wiki/File:Adsl_connections.jpg
okay great one thing I want to call out when we're talking about ports is
26:40
there's actually two things in networking called ports I don't know why they did this it's kind of annoying but
26:46
there just happen to be two things that are both called ports that are completely unrelated to each other so
26:51
the one we have been talking about so far is a logical Port this is something that only exists in software it's not
26:57
like a physical object and it's a number identifying an application so on YouTube
27:03
server the program running cat videos is number 80 and on my computer the web
27:08
browser is number 40,000 those are logical ports they only exist in software later in the class we'll see
27:15
something called a physical Port that's the actual hole that you plug the cable into and it's an actual thing that
27:21
exists in Hardware these two things have literally nothing to do with each other besides the name so it can be tempting
27:28
to confuse them when it's ambiguous we will try our best to specify logical
27:33
port or physical Port but just know that sometimes people will get lazy and call both of these things ports and we just
27:40
have to deal with it it's unfortunate but that's what they named them sorry
27:46

## Slide 17: Implementing Layers in the End Host
Software
Operating
System
Layers 1 and 2 are implemented in hardware, on the network interface card (NIC).
Layers 3 and 4 are implemented in software, in the operating system.
Layer 7 is the applications running in software.
Network Interface Card (Hardware)
IP
TCP
UDP
Firefox
Zoom
Email
Slack
Game
Layers 1–2
Layer 3
Layer 4
Layer 7
Thinks about packets.
Bridges the packet and connection abstractions.
Thinks about connections.
Notes: I don't have a better place to put this slide, so I guess here is okay.
I figured this is a good as time as any to tell you where the layers are implemented so if you actually open up
28:04
your computer and think about where this program is running TCP or where the
28:10
program is running Firefox this is roughly the picture that you would get so at the very lowest layer we have the
28:17
network interface card this is an actual computer chip like a physical piece of
28:22
Hardware that's running on your computer that's responsible for sending and
28:27
receiving packets so this is an actual chip that takes the ones and the zeros and broadcasts them as a radio wave or
28:34
sends them out across a wire that's an actual thing that Hardware has to do and layers one and two that are thinking in
28:40
terms of packets and sending ones and zeros across the wire they are implemented down here in Hardware at the
28:47
network interface card

## Slide 18: Implementing Layers in the End Host
Software
Operating
System
Demultiplexing helps the operating system pass packets to the correct application.
Logical ports identify the attachment point between the application and the OS.
Network Interface Card (Hardware)
IP
TCP
UDP
Firefox
Zoom
Email
Slack
Game
Layers 1–2
Layer 3
Layer 4
Layer 7
Notes: I don't have a better place to put this slide, so I guess here is okay.
then if I move up a little bit layers three and four they're implemented in software these
28:53
are actual pieces of code so it's not like a chip that you actually program
28:58
these are pieces of code that you can run you can even open up your operating system and see the code for TCP in the
29:04
operating system so this is software and it's usually implemented in your operating system so for example if
29:11
you're running Windows the code for Windows itself has an implementation of TCP or the code for Mac itself has an
29:19
implementation of TCP so it's running at the operating system level and finally
29:25
the actual applications these are running on your computer kind of a user level so like if I open a text editor
29:31
and I run a piece of python code that's running in the user space not at the operating system level so those are the
29:38
applications and
maybe another way of looking at this picture is at the very bottom the hardware is thinking in terms
29:44
of packets it's got the packet mindset it thinks about here's a blob of data I send it across the wire okay I received
29:51
a bunch of ones and zeros that's a blob of data so it's thinking really hard in terms of packets doesn't think about
29:57
Connections it doesn't think oh you seem to be talking to this YouTube server a lot it just thinks about every single
30:03
packet independently with no connection between them and here at the very top
30:08
these applications think in terms of connections so for example when I open my web browser my web browser is
30:14
thinking I've made a connection to YouTube and YouTube and I are exchanging lots of data so I can download a video
30:21
so up here at layer 7 it makes sense to think about long-term connections down

## Slide 19: End-to-End Principle
Internet Design Principles
Architecting the Internet
Narrow Waist, Demultiplexing
End-to-End Principle
Designing Resource Sharing
Statistical Multiplexing
Circuit vs. Packet Switching
Which is Better?
A Brief History
Lecture 2, Spring 2026
Notes: another principle that matters it's the end to end principle so we saw a lot of different internet principes we talked about the narrow waste
33:29
principle just now it gave us a chance to talk about mul Dem multiplexing now let's talk about the endtoend principle

## Slide 20: The End-to-End Question
Recall: Layer 3 (Internet) is best-effort.
Routers implement Layers 1–3 only.
Only end hosts implement Layer 4 (reliability).
Why did we choose this design?
Should we implement reliability in the network?
The end-to-end principle will help us answer these questions.
Guides the debate about what functionality the network does or doesn't implement.
Notes: it's going to help us answer the question why was layer three best effort last time we
33:43
told you that's how the internet is built routers think about layers one two three they do their best to forward
33:50
packets but they don't think about layer 4 which means routers have no ability to offer reliability they don't know about
33:57
layer for they don't think about resending packets that are lost fixing packets that are corrupt routers just
34:03
don't think about those things and that's a design choice that someone made so why did they choose that design
34:09
what's the argument for doing this and what would the alternative look like what does it look like if you actually
34:14
go in the network and say no actually the network guarantees that packets show up if a router gets a packet it promises
34:22
to send it to its destination what would that look like and why did we not choose that design so the end to end principle
34:28
is going to help us think about these questions and formulate an answer for why the internet was designed in this
34:36
way

## Slide 21: Running Example – Simple Reliability Protocol
We haven't discussed Layer 4 protocols yet, so let's use a super-simple protocol.
Alice wants to send 10 packets to Bob (in any order).
Alice numbers the packets 1 through 10 and sends them.
Bob can either:
  Receive all 10 packets and declare success, or
  Detect that some packets were lost, and declare failure.
  Bob cannot declare success when packets are lost.
R1
A
R2
R3
B
Sender
Recipient
Router
Router
Router
Notes: okay so to do this we need a reliability protocol unfortunately we don't have one because we haven't talked
34:42
about one yet so let me give you the simplest dumbest reliability protocol that I could think of so later in this
34:48
class we're going to spend four lectures talking about uh TCP which is an industrial grade reliability protocol
34:55
but since you don't know what that is yet here is a extremely simple reliability protocol on one slide so
35:01
here's how it goes Alice would like to send 10 packets to Bob I don't care about the order I just care that they
35:06
arrive so here's what Alice is going to do she's going to stamp the packets with numbers one through 10 and send them
35:13
that's it and Bob has two things that could happen at Bob's end he could either receive the 10 packets and
35:19
declare success. I got the packets they're numbered 1 through 10 everything is good or Bob might notice actually I
35:26
got nine pack I didn't get number six and declare failure those are Bob's two
35:31
choices so at the end of the day when all is said and done either Bob received 10 packets numbered 1 through 10 and
35:38
declared success or he didn't receive all 10 packets he missed a couple and
35:44

## Slide 22: Solution 1 – Reliability in the Network
Solution 1 – Reliability in the network:
Each router checks if it got all 10 packets.
If success, send the 10 packets to the next hop.
If failure, report the failure to the next hop.
Bob trusts whatever the last packet says. He doesn't count the packets himself.
R1
A
R2
R3
B
Sender
Recipient
Router
Router
Router
Got all 10 packets!
Missed a packet. Fail.
Fail.
Fail.
Notes: so let's go through the two options what could possibly happen uh depending on where I put reliability so
36:39
here's the alternate approach the one we didn't choose let's say I actually go into the network and I install
36:45
reliability so what this means is that Alice and Bob they can relax they don't care about things about checking for
36:52
reliability and checking if things show up the network guarantees it so all these routers together and they say we
36:59
promise we're going to deliver your packets trust us you don't have to worry about it just relax when you send
37:06
packets we are going to guarantee that they arrive so these routers are offering a new guarantee that doesn't
37:12
exist in the real internet this is an alternate universe where the network does implement reliability these routers
37:19
guarantee that things will show up so how's that going to work here's how I think about doing it each router is
37:26
going to check if it receives all 10 packets if it receives the 10 packets it will forward the 10 packets over to its
37:32
neighbor and if this router receives 10 packets forward to its neighbor forward to its neighbor if you don't receive 10
37:39
packets you'll just say fail remember failure is an option as long as Bob properly declares failure it's okay so
37:46
if router number two doesn't get all 10 packets it'll just say oops I got nine so that's a fail I'll send it to router
37:53
3 router 3 will say fail router three will tell Bob fail and Bob will correctly identify that a failure
38:00
occurred so again not the greatest reliability protocol but Bob did the
38:05
right thing he declared that there was a failure because there actually was a failure so again what is this protocol
38:12
doing it's offloading all the problems of reliability into the network itself
38:18

## Slide 23: Solution 1 – Reliability in the Network
Surprising fact: Solution 1 cannot guarantee correctness.
Suppose R3 is buggy and always reports success.
Bob doesn't check, so he trusts R3's report...even if it's wrong.
R1
A
R2
R3
B
Sender
Recipient
Router
Router
Router
Got all 10 packets!
Got all 10 packets!
Got all 10 packets!
R3 is buggy! It actually only got 9 packets.
Success!
Notes: here's a fact that's kind of surprising when I saw it for the first time this solution doesn't work there's simply no
39:01
way to make it work so here's an example where this solution just simply will never work let's say this router is
39:08
broken whoever programmed it made a mistake and this router always returns
39:13
true it always declares Victory even if it receives nine packets or eight
39:18
packets or two packets this router is just broken and it always reports that
39:24
it received all 10 packets so if router number three is buggy well then what happens let's say router number one
39:31
sends packets 10 packets router number two sends 10 packets oops some of them got dropped router number three only got
39:37
nine but router number three is buggy so it just celebrates Victory anyway tells Bob and remember Bob just trusts that
39:45
the network works because the network is guaranteeing reliability so Bob also celebrates success even though he only
39:52
got nine packets so here's a case where the network did the wrong thing
39:58
so because router number three is buggy it caused Bob to do the wrong thing he declared success even though he did not
40:05
receive all 10 packets so kind of a surprising fact but it's true because
40:11
routers can be buggy like this we actually cannot guarantee that this
40:16
scheme is correct

## Slide 24: Solution 2 – Reliability at End Hosts
Solution 2 – Reliability at end hosts:
Routers are best-effort. They might drop packets (and not report it).
Bob checks if he got all 10 packets.
R1
A
R2
R3
B
Sender
Recipient
Router
Router
Router
Got all 10 packets!
Notes: so the alternative is checking reliability at
40:28
the end hosts so now these routers don't give any guarantees all bets are off
40:33
this is like what the real internet does these routers say I'll send the packet if it gets there great if it doesn't get
40:39
there sucks to be you so it's best effort and instead of trusting what the routers say Bob is going to do the work
40:46
of actually counting the packets himself so now you can think of almost the code for checking reliability is no longer in
40:53
these routers it's now in Bob's computer so I've moved moved the job of checking
40:58
for reliability out of the routers into Bob's computer so now Bob's the one
41:04
counting and he either counts to 10 and notices I get all 10 packets or he doesn't count to 10 and says a couple
41:11
got missed so this is what the actual internet does we check reliability at the end hosts and Bob is the one to do
41:18
the checking

## Slide 25: Which Solution is Better?
Problem with Solution 1 (only routers check) : The end host (Bob) had to trust the network for correctness.
If the reliability code in the network is buggy, there's nothing Bob can do.
Solution 2 (only end hosts check) can be correct by itself, where Bob only had to rely on himself for correctness.
If the reliability code is buggy, Bob has the power to fix it.
Solution 2 is strictly better!
End hosts checking alone is already sufficient.
Router checks in solution 1 are unnecessary: Extra complexity for the network.
End-to-end principle: Certain application features (e.g. reliability) must be implemented at the end host for correctness.
Notes: so to recap there were two possible solutions one of them was to
End hosts must check either way.
41:42
put the code for checking reliability in the routers which meant that it wasn't in the end hosts the routers do all the
41:49
work and the end host trust whatever the router says unfortunately this does not
41:54
work we already saw that the routers can be be buggy and the only way to really make this work is to have Bob do the
42:01
counting as well but wait a minute if Bob does the counting isn't that just solution two solution two was having Bob
42:08
count so to fix Solution One you basically have to make it solution two
42:14
that's kind of a deep philosophical point but if you stared at a bit you'll see what I mean so Solution One says the
42:21
routers check it doesn't work because routers can be buggy the only way to guarantee correctness is to have B check
42:27
as well but if Bob is checking you've basically just built solution two so why not just use solution two so the second
42:34
fact here is that solution two by itself does work if you have Bob check that he
42:40
received all 10 packets this solution will work so haven't really proven it
42:45
but you can kind of think about it if Bob's the one counting he either counts to 10 declares success or doesn't count
42:51
to 10 it fails so solution two should work fine so these two facts combine
42:56
basic basically tell us that the second solution having the end host check that's the better one and the argument
43:02
goes like this in both Solutions the end host has got to do the checking in solution one having routers by itself
43:09
check it's not going to work you got to have the end host do the checking in solution two the end host are checking
43:15
so the end host have to do the check either way and we also said that in solution two end host checking by
43:21
themselves is already enough if Bob is doing the checking already and that's enough then there is no need to make the
43:27
routers do extra work so this means solution two is strictly better it's kind of a deep philosophical argument
43:34
but that's how it goes end host has got to do the work either way and if OST are going to do the work either way and end
43:40
host checking is enough might as well just have en host do it don't have the routers do it it doesn't matter if you
43:47
have routers check it's going to be extra complexity and it doesn't help with correctness so there's just no
43:53
point having routers check at all all of this argument that I've just presented is called the endtoend principle it
43:59
basically says that there are certain features out there like reliability like we just saw but you could actually make
44:05
a similar argument for things like security that have to be implemented at the end host for correctness that's a
44:11
rule the end host has to do checking in order for it to be correct if you just do it in the network it's just not
44:18
enough the end host have to do it and if the end host do it it will work so there's no point in making the network
44:25
do extra checks that's the end to end principle

## Slide 26: Breaking the End-to-End Principle for Performance
The end-to-end principle can be relaxed.
Could implement reliability in the network as a performance optimization.
Must be done in addition to end-to-end checks, for correctness.
Example: Links can send duplicate packets to improve/optimize network performance. Crrectness is guaranteed by the end-to-end principle regardless of the network performance (by retransmission of lost packets)
10 links, 10% failure rate per link = ~65% end-to-end failure probablity. (Success rate per link = 1−0.1 = 0.9, so end-to-end success probability (when all 10 links must succeed): 0.910 0.35 , hence End-to-end failure rate is 1-0.35 = 0.65.)
If each link sends 2 extra copies of every packet (3 total): 0.1% failure rate per link, ~1% end-to-end failure rate. (A link only fails if all 3 copies fail. Single-copy failure probability: 𝑞 = 0.1. Failure rate per link when all 3 copies fail is: 𝑞3 = 0.001. Success rate per link = 1− 0.001 = 0.999, so end-to-end success rate is: 0.99910= 0.990, hence end-to-end failure rate is 1 - 0.99 = 0.01.)
Sender
Recipient
Notes: End-to-end success probability:
Compute it:
0.9^10 =0.349 success rate, 1 - 0.349 =0.651 or 65% fail rate
If we send 2 copies of every packet, the chance of ALL packets failing at a link is 0.1* 0.1*0.1 =0.001 = 0.1% failure per link (meaning both packets failing at that link), so 0.999^10 = 0.99 success rate, or 1 - 0.99 =0.01 = 1% failure rate
so as we said earlier the end end principle is a design principle it is not a hard and fast rule so it turns
47:07
out there are actually cases where you want to break this rule so you actually can break this Rule and say you know
47:13
what I am going to have these routers guarantee correctness do they have to guarantee correctness no does adding
47:22
reliability make things more correct no but I could still add reliability and
47:28
the main reason I think why you might want to add reliability is for performance so this is not to make
47:33
things more correct it's just to make things perform better and we still have to have the second solution where the
47:39
sender and the recipient check for all 10 packets in order to have correctness so we're not making things more correct
47:46
we're just breaking the endtoend principle as a performance optimization and whether you want to do this or not
47:52
really depends on your network like how reliable are your links do packets get dropped all the time and things like
47:59
that so here's an example where breaking the end to end principle might actually be worthwhile so let's say these links
48:05
are really bad they drop packets all the time like they drop packets 10% of the time you send 10 packets one of them
48:12
gets dropped on average so if you do that only 65% of packets I guess 35% of
48:19
packets will actually reach the destination 65% of them will get dropped along one of these links you don't have
48:26
to know the math but roughly speaking if there are 10 links and each one fails 10% of the time 65% of the time
48:33
something's not getting to its destination in other words your protocol is going to drw packets a lot by
48:40
contrast what if we added a little bit of reliability and again this a super simple reliability protocol more
48:47
complicated ones exist but let's just do a really stupid one that's every link sends two copies of the packet so just
48:53
send two copies of the packet now the failure rate has dropped . 1% and 99% of
48:58
packets reach the end so we went from like 35% of packets reaching the end host to 99% of packets reaching the end
49:06
host just by having these routers think a little bit about reliability so this
49:11
is a case where we took some of the code for implementing reliability and we moved it into the routers and we told
49:17
these routers hey these links suck please send every packet twice and the
49:23
result is actually a better connection so this is the case where we didn't make things more correct the recipient still
49:30
has to count to 10 to check if the packet showed up but we've at least made it more likely that the packet show up
49:36
so I think this is a good choice for breaking the endtoend principle in exchange for better performance it's not
49:43
for correctness the original argument for correctness still holds just for making things perform
49:48
better this is actually something you'll see at the very end when we talk about Wireless links which tend to suck like
49:54
End-to-end success probability: 〖0.9〗^10
Compute it:
〖0.9〗^10≈0.3487
0.9^10 =0.349 success rate, 1 - 0.349 =0.651 or 65% fail rate
If we send 2 copies of every packet, the chance of ALL packets failing at a link is 0.1* 0.1*0.1 =0.001 = 0.1% failure per link (meaning both packets failing at that link), so 0.999^10 = 0.99 success rate, or 1 - 0.99 =0.01 = 1% failure rate
so as we said earlier the end end principle is a design principle it is not a hard and fast rule so it turns
47:07
out there are actually cases where you want to break this rule so you actually can break this Rule and say you know
47:13
what I am going to have these routers guarantee correctness do they have to guarantee correctness no does adding
47:22
reliability make things more correct no but I could still add reliability and
47:28
the main reason I think why you might want to add reliability is for performance so this is not to make
47:33
things more correct it's just to make things perform better and we still have to have the second solution where the
47:39
sender and the recipient check for all 10 packets in order to have correctness so we're not making things more correct
47:46
we're just breaking the endtoend principle as a performance optimization and whether you want to do this or not
47:52
really depends on your network like how reliable are your links do packets get dropped all the time and things like
47:59
that so here's an example where breaking the end to end principle might actually be worthwhile so let's say these links
48:05
are really bad they drop packets all the time like they drop packets 10% of the time you send 10 packets one of them
48:12
gets dropped on average so if you do that only 65% of packets I guess 35% of
48:19
packets will actually reach the destination 65% of them will get dropped along one of these links you don't have
48:26
to know the math but roughly speaking if there are 10 links and each one fails 10% of the time 65% of the time
48:33
something's not getting to its destination in other words your protocol is going to drw packets a lot by
48:40
contrast what if we added a little bit of reliability and again this a super simple reliability protocol more
48:47
complicated ones exist but let's just do a really stupid one that's every link sends two copies of the packet so just
48:53
send two copies of the packet now the failure rate has dropped . 1% and 99% of
48:58
packets reach the end so we went from like 35% of packets reaching the end host to 99% of packets reaching the end
49:06
host just by having these routers think a little bit about reliability so this
49:11
is a case where we took some of the code for implementing reliability and we moved it into the routers and we told
49:17
these routers hey these links suck please send every packet twice and the
49:23
result is actually a better connection so this is the case where we didn't make things more correct the recipient still
49:30
has to count to 10 to check if the packet showed up but we've at least made it more likely that the packet show up
49:36
so I think this is a good choice for breaking the endtoend principle in exchange for better performance it's not
49:43
for correctness the original argument for correctness still holds just for making things perform
49:48
better this is actually something you'll see at the very end when we talk about Wireless links which tend to suck like
49:54

## Slide 27: Designing Resource Sharing: Statistical Multiplexing
Internet Design Principles
Architecting the Internet
Narrow Waist, Demultiplexing
End-to-End Principle
Designing Resource Sharing
Statistical Multiplexing
Circuit vs. Packet Switching
Which is Better?
A Brief History
Lecture 2, Spring 2026
Notes: any thoughts before I move on to the second half of today
Stretch break!!
so in the first half we talked
54:52
about internet AR design principles architecture choices in the second half of today we're going to keep thinking
54:58
about design but we're going to really focus in on one critical question which is resource sharing and we're going to
55:05
see lots of different solutions for resource sharing and why we decided on the one that we did so it's still about
55:11
design but it's about a very specific design question

## Slide 28: Sharing Network Resources
The network must support many simultaneous flows.
Recall: A flow is a stream of packets sent between two end hosts.
This means network resources are shared between end hosts.
R1
A
R2
B
C
D
A and B want to exchange data.
C and D also want to exchange data.
They all have to share routers and links.
Notes: the design question is the internet is shared we all have to
55:18
share so it's not like you have a dedicated router that's sending packets for you so for example this router here
55:25
it's responsible for serving data to both A and C they have to share and for
55:30
example this link right here between R1 and R2 it's being shared by two different flows the one from A to B and
55:38
the one from C to D so if C to D are talking and A to B are also talking
55:43
they're both sharing this link so an important question is how do we share
55:48
like who decides how much a to b gets and how much bandwidth C to D gets is it
55:54
unfair what happens if one of them tries to cheat who enforces that so an important question we have to ask is how
56:00
does sharing work and that's what we're going to spend the rest of today on

## Slide 29: Sharing Network Resources
Two ways to allocate resources to users:
Static allocation: Give a fixed amount to each user.
Statistical multiplexing: Dynamically allocate to users based on their demand.
  Example: Your computer allocates CPU to apps based on demand.
Network resources are statistically multiplexed.
Time
Time
Resources
Resources
Static Allocation
Statistical Multiplexing
Notes: roughly speaking there's two different ways to give resources to users and here we're really abstracting away what
56:12
resources means so it could be as mentioned before bandwidth on a link but
56:17
this kind of idea works for almost any resource you can think of like what about your computer it's got a limited
56:22
amount of CPU and I have five different programs competing for CPU usage how do
56:28
I allocate CPU to my computer or I don't know there's like I can't think of any
56:33
other one but there's all these different uh resource allocation problems in real life and all of them
56:39
kind of have the same character so there's two different ways we can allocate a limited amount of resources
56:45
to lots of users who want them so one way is static allocation everyone gets a
56:51
fixed amount for all time so for example my computer I could say all right my CPU
56:56
can do you know a thousand computations per second and so this application in
57:02
blue gets a third of it this application in red gets a third of it this application in green gets a third of it
57:07
and that's true for all time so it doesn't matter what time it is everyone gets exactly onethird of the available
57:15
capacity by contrast the other option is called statistical multiplexing which is
57:20
a really fancy way of saying you dynamically allocate based on demand so for example at this time the red
57:28
application needs a lot of uh resources so we give the red application a lot of resources and right now the blue
57:34
application doesn't need any so at this particular slice in time blue gets zero red gets a lot green gets some and maybe
57:42
later the blue application starts up and says actually I need a lot too so now the blue application gets some the red
57:49
application gets some and maybe at this lce of time the green application has gone to sleep and it doesn't need any so
57:55
what this picture is showing is that over time the amount of resources that we give out to each of these three users
58:01
is different depending on what they need so those are our two choices either give everyone a fixed amount or dynamically
58:09
change the amount that we give to them based on what they want so which of these is better that's a question that
58:15
we have to answer as we're designing things but as a bit of a spoiler network resources use statistical Multiplex so
58:22
it's not like each of us has a dedicated amount of network that we can use and it's the same all the time for example

## Slide 30: Statistical Multiplexing is More Efficient
Statistical multiplexing (dynamic) is more efficient than static allocation (fixed).
Fixed: You have to give everyone enough for their peak demand.
Dynamic: Give a user more when their demand peaks.
Example:
Alice needs 10 in the morning, and 2 all other times.
Bob needs 10 at night, and 2 all other times.
Fixed: Alice and Bob each get 10 at all times.
  We need 20 to satisfy demand.
  Alice's 10 is wasted most of the time. Same for Bob.
Dynamic: Give each user 10 at their peak time, and 2 at other times.
  We only need 12 to satisfy demand!
Notes: statistical multiplexing is the right choice we're going to make another argument for why that's true so
59:06
as a reminder fixed means everyone gets the same amount dynamic means uh we can
59:12
give people different amounts at different times and the key idea is that
59:17
everyone's demand changes over time so for example Alice might need 10 of the
59:22
resource in the morning and two at all other times or Bob might be a night owl
59:27
he wants 10 at night and at all other times he wants two so how do we give Alice and Bob what they want can we use
59:35
the fixed approach can we use the dynamic approach which is better so think about the fixed approach in the
59:41
fixed approach remember we want to satisfy everyone's demand so in order to satisfy everyone's demand we need to
59:48
allocate for everyone's Peak that is Alice needs 10 at the worst time the
59:53
mornings so we need to give Alice 10 even though most other times she's not using 10 and likewise Bob needs 10 for
1:00:01
his Peak us which is at night even though most of the time he doesn't use it so we have to give Alice 10 and Bob
1:00:07
10 that's the only way to satisfy this demand Alice needs 10 for her Peak Bob needs 10 for his Peak and in total we
1:00:15
need 20 units of this thing could be bandwidth whatever we need 20 of it that's a lot and it turns out most of it
1:00:22
is wasted for example when Alice isn't using 10 and she's only using two the other eight just go to waste no one's
1:00:29
using it and likewise with Bob in the morning when Bob is not using 10 the other eight they go to waste but this is
1:00:35
the only way we can give Alice and Bob all of their demand if we use fixed allocation that is we give them the same
1:00:43
at all times by contrast what's something smarter we could do something
1:00:48
smarter is why don't we just give them 10 when they want it and give them two when they want two why do we have to
1:00:54
allocate 10 for them the whole time let's be smarter and let's just dynamically change what they need so
1:00:59
when the user wants 10 give them 10 when the user wants two give them two and if you do this turns out you only need 12
1:01:07
to satisfy demand because at the worst times Alice needs 10 but Bob only needs two in the mornings and at night Bob
1:01:14
needs 10 Alice needs two so therefore we only need 12 at any time to satisfy
1:01:20
demand so Dynamic allocation means we have to build fewer resources to satisfy
1:01:25
everyone in the fixed approach we'd have to build 20 of whatever this is to satisfy demand in the dynamic approach
1:01:33
we only need 12 and that's nicer so to summarize all of this argument we're
1:01:38
basically saying the peak of aggregate demand is less than the aggregate of
1:01:43
peak demands that's kind of a mouthful to say the thing I just argued but basically what this is saying is if you
1:01:49
add up all the demands together and look for the peak that's going to be less than if I take everyone individual Peaks
1:01:57

## Slide 31: Statistical Multiplexing is More Efficient
In summary: peak of aggregate demand < aggregate of peak demands. max(Σ fi) < Σ max(fi)
Time
Demand
Alice's demand
Bob's demand
Combined demand
Time
Demand
A's peak
B's peak
+
=
Peak of aggregate
Time
Demand
Aggregate of peak
Time
Demand
Notes: practice, peak of aggregate is usually closer to the average of peak demands.1:02:31
statistical multiplexing in picture form so here's Alys demand she needs a lot in
1:02:36
the morning here's Bob's demand he needs a lot at night this axis is time and this axis is demand so there's two ways
1:02:43
I can approach this one way to approach it is to do fixed allocation A's Peak is
1:02:48
10 so that means a needs a fixed 10 all the time and B's Peak is 10 which means
1:02:54
he needs a fixed 10 all the time so if I was doing fixed allocation a needs 10 B
1:02:59
needs 10 and in total we need 20 that's what this picture is showing the aggregate of the peak means I take
1:03:06
everyone's Peak first and then I sum all the Peaks together and I get 20 this is
1:03:11
what the fixed approach looks like at the bottom and people sometimes call it aggregate of peak by contrast up here
1:03:18
this is the peak of aggregate approach that is this is the approach we do if we first sum up their demands and then take
1:03:26
the peak as the Second Step so here we've summed up their demands there's a peak in the morning when Alice needs it
1:03:32
there's a Peak at night when Alice needs it and the peak of this new graph is 12
1:03:37
because Alice needs 10 Bob needs two at that time in total they just need 12

## Slide 32: Statistical Multiplexing
15
12
9
12
15
9
>=
36
12
9
15
15
Sum of the peaks is always (much) greater than the peak of the sums (peak of the aggregate).
Notes: Statistically multiplexed means that we’ll dynamically allocate resources to users based on their demand, instead of partitioning a fixed share of resources to users.
The peak of the aggregate is actually closer to the sum of the average demands, which is much less than the sum of the peak demands. Statistical multiplexing is now everywhere in computer science. For example, in cloud computing, different companies might dynamically share resources in a datacenter.

## Slide 33: Circuit Switching vs. Packet Switching
Internet Design Principles
Architecting the Internet
Narrow Waist, Demultiplexing
End-to-End Principle
Designing Resource Sharing
Statistical Multiplexing
Circuit vs. Packet Switching
Which is Better?
A Brief History
Lecture 2, Spring 2026
Notes: we saw two different ways to share resources and we decided
1:05:36
that statistical multiplexing is the way to go we're not doing the fixed resource thing we're going to dynamically
1:05:42
allocate so that brings up another question how do you dynamically allocate
1:05:47
resources who decides you know when this person wants more give them more when
1:05:53
it's night please give Bob more when it's the mornings give Alice more how do we decide that stuff who decides how to
1:06:00
dynamically allocate resources

## Slide 34: Circuit Switching vs. Packet Switching
There are 2 canonical designs for implementing statistical multiplexing:
Reservations via circuit switching:
  At start of connection, end-hosts explicitly request and reserve resources.
  During connection, use the reserved resources to send packets.
  At end of connection, release resources.
Best-effort via packet switching:
  Just use the resources (send packets) and hope for the best.
Analogy: In a restaurant, reservations vs. first-come, first-serve.
Notes: and it turns out there are two different approaches to dynamically allocating
resources so here I also have an analogy because another place where you dynamically allocate resources is a
1:06:13
restaurant so it's not like a restaurant is fixed resource if the restaurant was fixed resource it means you have a table
1:06:20
there 24 hours a day and you can use it whenever you want no one else can use it I don't know about you I don't know
1:06:26
restaurants that work like that where there's just a table for you no one else can use it and there's a table for someone else and no one else can use it
1:06:33
that's a very silly way to run a restaurant because most of the time the table is not going to be used instead
1:06:39
restaurants do Dynamic allocation they give the tables to the customers based on who needs it and if you don't need it
1:06:46
you don't get a table that's a lot better and in a restaurant there's two different ways to dynamically give
1:06:53
tables to customers that I can think of so one of them is reservations you
1:06:58
customers call ahead of time and say Hey I want to have dinner tonight can I get a table at 6:00 p.m. to 8:00 P.M and the
1:07:04
restaurant says okay well this table's yours from 6: to 8 you can use it and when the reservation is up you're done
1:07:11
and the other approach is first come first serve you show up you get a table if you show up and it's full you got to
1:07:16
wait in line so those are our two choices and in the network we can do both of those things too so in the
1:07:22
network if you implement reservations they don't call it res obervations they call it circuit switching but the idea
1:07:28
is basically the same when you start a connection you explicitly say you have a connection and you say what the demand
1:07:34
is you say I want to use 10 units of resource from 6 p.m. to 800 p.m. that's
1:07:41
mine I want it and during the connection that's all yours no one else can use it and when you're done you release it for
1:07:47
other people to use and the other approach is best effort this is like first come first serve and it basically
1:07:52
says just send the packet and hope for the best and if there's too many packets some packets just have to wait in line
1:07:59
or get turned away they just don't get service so reservations is circuit
1:08:04
switching and first Comfort Service packet switching just send the packets hope for the best if too many packets
1:08:11
are here some of them have to wait in line or get kicked up so those are the two approaches but just remember that
1:08:18
both of them are still statistical multiplexing they're both Dynamic allocation they're not the fixed
1:08:23
approach where everyone has their own table 24 hours a day

## Slide 35: Circuit Switching
Reservations via circuit switching: Reserve capacity for the connection.
A sends a reservation to B. Along the way, routers hear the reservation and allocate resources. Routers establish a circuit, and A can start sending data.
When connection is done, A sends a teardown message to B. Along the way, routers see the message and free up resources.
R5
R6
B
I need 5 Mbps
I need 5 Mbps
I need 5 Mbps
I need 5 Mbps
A
R1
R3
I need 5 Mbps
R2
R4
R5
R6
Done!
Done!
Done!
Done!
R1
A
R2
R4
R3
B
Done!
Notes: o here's the picture form of circuit switching we
1:08:30
reserve capacity ahead of time so let's sayb want to talk well then what they could do is it could say I need five
1:08:37
five what resources megabits per second whatever but uh router a or host a sorry
1:08:44
says I need five and this message gets sent along to B so router one sees it
1:08:50
and says Okay a needs five so I'm gonna set aside five for a okay good and then
1:08:56
router one forwards it over to R2 and router two sees oh A and B want to talk they want five so I'm also going to
1:09:02
reserve five okay good I reserved five send it to router three router three reserves five send it to four four
1:09:08
reserves five it reaches B so along the way routers here oh someone's calling
1:09:14
they want five and they want it at this time and they can allocate resources ahead of time so now routers 1 two 3 and
1:09:20
four have pre-allocated five units of bandwidth ver something for a to use
1:09:27
it's all theirs nobody else can use those five and now and can start sending data back and forth using those five
1:09:34
units of resources dedicated for them it's a reservation nobody else can use

## Slide 36: Packet Switching
Best-effort via packet switching: Allocate resources to each packet independently.
Each router considers the packet independently.
Each packet in the flow is considered independently.
R1
A
R2
R5
R6
R4
R3
B
Potato
Potato
Potato
Potato
Potato
Potato
No circuit!
Notes: here's the other approach packet switching and here there is no reservation so it's not like before
1:10:22
where the router set aside resources for you each router just receives the packet and if they forward it great if they
1:10:29
don't forward it oh well that's it it's what we've already seen it's best effort so we send it and we send it and that's
1:10:35
it there is no reservation nothing is highlighted pink there is no dedicated links for A and B to use and when we say
1:10:43
independent you can almost think of independent in two different ways so we could say independent because these
1:10:48
routers are thinking separately it's not like before where routers 1 2 3 and four
1:10:54
work together to give you the reservation each router is thinking separately so router one sees the packet
1:11:00
if they can handle it great if they can't sorry router 2 then looks at the packet if router two can handle it great
1:11:06
if not oh well so everyone looks at the packet separately and likewise on
1:11:11
another dimension each packet is separate so if a sends 20 packets to B
1:11:17
each packet is processed or dropped separately so everything is independent the routers don't have to think about
1:11:24
each other and the pack don't have to think about each other so everything is separate and that's what best effort
1:11:29
looks like it's what we already saw bit of a spoiler this is what the network uses but today we're going to argue why
1:11:36
the network uses this as opposed to the reservations approach

## Slide 37: Circuit vs. Packet Switching: Which is Better?
Internet Design Principles
Architecting the Internet
Narrow Waist, Demultiplexing
End-to-End Principle
Designing Resource Sharing
Statistical Multiplexing
Circuit vs. Packet Switching
Which is Better?
A Brief History
Lecture 2, Spring 2026
Notes: okay great so one question you might have now is which of these is better we've presented two different approaches
1:12:26
which do we prefer and why is it that packet switching W in the debate between
1:12:32
these two so when we say which is better we kind of have to qualify that and say better in what sense what does it mean

## Slide 38: Circuit Switching vs. Packet Switching: Which is Better?
Which is better? We can compare along several dimensions.
Which one offers a better abstraction to applications?
Which one is more efficient at scale?
Which one is better at handling failures at scale?
Which one is easier (less complex) to implement at scale?
Notes: here are four ways that I can think of things four ways that I
1:12:44
can think of for something to be better than the other so one question we might ask is which of these is better for
1:12:50
applications if you're someone writing a program that has to be connected to the internet which of these two do you
1:12:56
prefer do you want reservations do you want first come first serve what do you prefer another question might be which
1:13:03
of these is more efficient at scale which of these is better at scaling up to the trillions of users on the
1:13:09
internet billions of users another question might be which of these is better at handling failures if things go
1:13:15
wrong which of these is going to support uh the failure better and more gracefully and the final question might
1:13:21
be which of these is easier to implement when I write code to actually Implement reservations or first come first serve
1:13:29
which one is easier to code up so we're going to look at these four and try to make an argument for why the internet
1:13:34
CHS one over the other

## Slide 39: Which is Better? (1/4) – Application Abstraction
As a programmer, circuit switching is more convenient.
You get a guarantee of reserved resources.
More predictable and understandable behavior.
Leads to an intuitive business model for companies.
  Charge a user depending on what they reserve.
Better abstraction to applications?
More efficient at scale?
Better at handling failures at scale?
Easier (less complex) to implement at scale?
Notes: first one which offers a better
1:13:40
abstraction to Applications if you're writing a program do you want a reservation or do you want first come
1:13:46
first serve so none of these are answers that have to be true but they're kind of what we came up with they are certainly
1:13:53
Up For Debate but I would say I was writing a program I want circuit switching I want reservations because I
1:13:59
can reserve something and guarantee that I have that whereas if I do first come first serf who knows if my packets are
1:14:06
going to get there that's not so great so by using circuit switching I guarantee myself that I get some level
1:14:12
of reserved resources that are just for me things are going to be more predictable if I have these resources I
1:14:18
know I can use them whereas in first come first serve I don't know what I'm going to get like when I open a video or
1:14:24
when my users run my program and watch a video I don't know if they're going to get high quality video or lowquality
1:14:30
video I have no idea in packet switching by contrast if I wrote the program with
1:14:36
circuit switching I can guarantee when you run my video program you are going to get high quality video because I'm
1:14:42
going to reserve resources for you so as an application developer it makes sense
1:14:47
that I want to give my user some guarantee give my users predictable behavior and circuit switching is a more
1:14:54
natural model for them that it's also more natural for internet service providers because they can charge you
1:14:59
based on what you reserve so if I reserved 10 megabits per second then I
1:15:04
got to pay 10 bucks and if I reserve 20 megabits per second I got to pay 20 bucks so it makes a lot of sense for
1:15:11
businesses as well they can charge you based on what you reserve so as people writing programs I think circuit
1:15:17
switching wins

## Slide 40: Which is Better? (2/4) – Efficiency
Packet switching is typically more efficient.
Circuit switching takes time for setup/teardown.
  Very inefficient if you don't have much data to send, e.g. short flows.
Circuit switching can lead to wasted resources.
  If I reserve 5 Mbps for an hour, I might not need 5 Mbps the whole hour.
  Other people could be using the resources I'm not using.
  How much better depends on the "burstiness" of the traffic sources.
Better abstraction to applications?
More efficient at scale?
Better at handling failures at scale?
Easier (less complex) to implement at scale?
Notes: okay number two which one is more efficient so here I think packet
1:15:24
switching actually wins here are some arguments for why one of them is circuit switching takes time because I have to
1:15:30
send a setup message and I have to send the tear down message imagine if you only had to send one packet well then to
1:15:37
send the one packet I have to do setup okay good wait for the setup to work out then I send the one packet and then I
1:15:44
have to do a bunch of tear down that's a lot of extra work for sending a single packet I had to send three messages
1:15:50
instead of one because I only had one packet to send but I had to add the setup and the tear down that's not so
1:15:56
great and another reason why circuit switching isn't too efficient is it wastes resources so if you reserve five
1:16:04
you might not need five the whole time other people could have been using the five so that's not so great so another
1:16:10
way that circuit switching is less efficient is you might not be using all of the reservation when you ask for five
1:16:16
you might not be using the whole five

## Slide 41: Which is Better? (2/4) – Efficiency – Packet Burstiness
Circuit switching with bursty traffic leads to inefficient resource allocation.
Capacity = 30
A reserves 13.
B reserves 11.
Not enough for C!
Circuit switching: Must reject one of the flows!
Packet switching: All demands satisfied!
B's Demand
11
C's Demand
12
A's Demand
13
Time
Demand
Capacity = 30
Notes: here's burstiness burstiness basically says um well I have a spike in demand
1:16:37
and all the other times there's not a lot of demand so I have this burst of demand at one time and at all the other
1:16:43
times I don't have a lot of demand that's roughly speaking what bursting means so here's a b and c they're all
1:16:49
very bursty they have one burst of demand and then at all other times they don't really need all that much so if we
1:16:55
were doing reservations what would a b and c encounter a would say I want 13
1:17:01
and the network looks and it says I have 30 I can give you 13 no problem and then B comes along it says I want 11 because
1:17:09
my peak's going to be 11 so I'll ask for 11 and I give B 11 okay great and then C
1:17:16
comes along and says I need 12 my Peak is 12 now we have a problem because a
1:17:21
used 13 B reserved 11 okay what is that that's 24 for you so far that means
1:17:26
there's only six left but C wants 12 nope no good so C actually gets rejected
1:17:32
its reservation does not succeed because A and B just Reserve too much they reserved for the burst and most of this
1:17:40
actually went unused by contrast if we used packet switching everyone just sends whatever they want based on their
1:17:47
current demand There Is No Reservations so in this case all the demands get
1:17:52
satisfied yeah there are some bursts but we hand hand the burst just fine and everything fits in capacity 30 so that's
1:18:00
the argument for why burstiness can make circuit switching less efficient because
1:18:06
it causes all this wasted capacity that's not so good it's still Dynamic allocation because we're allocating 13
1:18:13
based on their demand but it's worse so burstiness causes circuit switching to
1:18:20
really do worse

## Slide 42: Which is Better? (2/4) – Efficiency – Packet Burstiness
If demand over time is constant, circuit and packet switching both work well.
Capacity = 30
A reserves 10.
B reserves 10.
C reserves 10.
Circuit switching: All demands satisfied!
Capacity = 30
Packet switching: All demands satisfied!
B's Demand
10
C's Demand
10
A's Demand
10
Time
Demand
Notes: smooth there's no burst anywhere and in this case both circuit switching and packet switching would do the job they
1:18:32
both successfully give everyone what they want so in the circuit switching case everyone reserves 10 they all get
1:18:37
10 great in packet switching everyone needs 10 they get 10 all is good so in the birthday approach circuit switching
1:18:44
choked but in the smooth approach or when the demands were smooth everyone got what they wanted and life was good

## Slide 43: Which is Better? (2/4) – Efficiency – Packet Burstiness
Flows can be smooth or bursty.
Characterized by the ratio between the flow's peak demand and average demand.
Smooth applications have a small peak-to-average ratio.
  Voice has a ratio of ~3:1.
  This is why the phone network uses reservations!
Bursty applications have a large peak-to-average ratio.
  Data applications tend to be rather bursty.
  Web browsing can have a ratio of 100:1 or more.
Notes: 1:18:51
so to really formally Define what bursty means it's a ratio between the peak
demand and the average demand so in this case the firstus is one the peak demand
1:19:02
and the average demand is the same in this case the ratio is a lot higher because the peak demand is a lot higher
1:19:07
than the average demand so some applications are smooth some applications are bursty in fact um here
1:19:14
are some examples of different applications voice like talking over the phone is actually relatively smooth
1:19:20
because you're talking all the time and there's noise going through the speaker so Voice is pretty smooth it's not that
1:19:26
bursty at all and this is actually why the phone network which is a totally different type of network that people
1:19:32
designed uses reservations it's because phone connections are quite smooth so in
1:19:38
general when you're talking over the phone it looks like this you reserve a bunch of audio bandwidth space and you
1:19:45
use most of it the whole time man's pretty smooth by contrast a lot of web applications are really bursty think
1:19:51
about how you access the web what do you do you load web page and then you spend like 10 minutes reading it and then you
1:19:57
load a web page and then you spend 10 minutes reading it so it's very bursty you have this one bursty moment where
1:20:03
you download all of the web page and then you spend all this time reading it and there's not a lot of Demands so data
1:20:09
applications like web browsing they can be really bursty like ratios of 100 to one there's one burst and then the rest
1:20:16
of the time not a lot of demand so this is another argument for why packet
1:20:21
switching is better because internet applications actually do tend to be quite bursty but hypothetically if the
1:20:28
internet was used to I don't know make phone calls all the time maybe packet switching would be

## Slide 44: Which is Better? (3/4) – Handling Failure
What happens if a link or router fails?
Network must detect failure and send packets along a different route.
Packet switching is better at handling failure.
End hosts don't need to do anything extra.
Circuit switching requires extra work from end hosts.
End host must also detect failure, tear down old reservations, and send new reservation request.
All flows using that link must redo reservations.
  Potentially millions of flows simultaneously re-establishing reservations!
Better abstraction to applications?
More efficient at scale?
Better at handling failures at scale?
Easier (less complex) to implement at scale?
Notes: one other point of comparison that
5:03
we can use to compare packet switching versus circuit switching is handling failure at scale which of these two
5:10
scenarios or approaches to statistical multiplexing is better if links and
5:15
routers fail because we know already that devices can fail and our Network should be resilient to failure in
5:21
particular routers should be able to send Packers along different routes if one particular route fails so if I try
5:28
try thinking about what would circuit switching do if I've already reserved a path and I've said all the packets are
5:34
going to go along this path and this path has reserved a certain amount of resources for me what if that path goes
5:40
down one of the routers goes down or one of the links goes down well first of all you have to know that the link went down
5:47
already it's not too obvious how that you're going to do that you also have to get rid of the reservation because it's
5:52
no longer valid the path no longer exists also not clear how you tear down this reservation and you also have to go
5:58
and find a brand new reservation based on the New Path so that's a lot of stuff you have to do just to handle a failure
6:05
so the end host has to notice that there's a failure cancel the current reservation and make a new reservation
6:11
that's a lot of work for an end host to do also one problem is as we saw earlier
6:18
resources can be shared a lot of people could be using the same link maybe there's only one link connecting the
6:24
United States to Europe everyone who's talking between these two continents is using that same same underwater cable
that same link so if that link goes down there's going to be millions of users who have to reestablish reservations at
6:38
the same time so when that link goes down a million people detect failure and a million people have to go through the
6:45
extra effort of requesting another reservation that's going to be a lot of traffic for the network to handle at one
6:51
instant in one instant suddenly a million requests come in that's going to be pretty chaotic by contrast hacket
6:58
switching we almost don't even have to think about failure if the link goes down the routers will just relearn paths
7:04
through the network and forward packets through a different path of the network in particular the routers are going to
7:11
handle the failure so this means that the end hosts don't have to do anything extra they don't have to detect that
7:17
there was a failure the routers are going to figure it out and find a new path through the network the end host don't have to cancel a reservation
7:23
because there never was one to begin with and the end host don't have to make a new reservation because again there
7:29
wasn't one one one there wasn't One to begin with so packet switching turns out to be the better approach at handling failure because if something goes down the end host doesn't even have to worry about it the routers will find a new
7:40
path through the network and the end host just continues sending packets like nothing happened

## Slide 45: Which is Better? (3/4) – Handling Failure with Packet Switching
If a failure occurs in packet switching:
Routers send packets along a different route.
End hosts don't need to do anything extra.
R1
A
R2
R5
R6
R4
R3
B
Potato
Potato
Potato
Potato
Potato
Potato
R1
A
R2
R5
R6
R4
R3
B
Banana
Banana
Banana
Banana
Banana
Banana
Router R3 goes down!
Notes: so to
7:47
put all of this in a picture here's a picture of a network topology everyone is working just fine but let's say one
7:54
of the routers goes down so here's a packet being sent all is well or just a
8:00
from A to B

## Slide 46: Which is Better? (3/4) – Handling Failure with Circuit Switching
If a failure occurs in circuit switching:
End host must tear down the circuit, and request a new reservation.
What if the new request gets declined?
R5
R6
R3
Router goes down!
Reserved
Reserved
Reserved
Reserved
R1
A
R2
R4
B
R3
R2
R3
Router R3 goes down!
R1
A
R5
R6
R4
B
I need 5
I need 5
I need 5
I need 5
I need 5
Notes: by contrast in the reservation case let's
8:49
say a link goes down just like before
Circuit switching implementation question:
How does R4 know if the previous routers accepted or rejected the packet?
Possible solution: Send a confirmation packet the other way (B to A). If R2 rejects, it drops the confirmation packet, so A doesn't get it.

## Slide 47: Which is Better? (4/4) – Implementation Complexity
Better abstraction to applications?
More efficient at scale?
Better at handling failures at scale?
Easier (less complex) to implement at scale?
Packet switching is easier to implement.
Routers don't have to keep track of reservations.
Circuit switching implementation questions:
How do all the routers know that the request was approved?
What if the request packet gets dropped?
What if the teardown packet gets dropped?
What should the end host do if the request is declined?
What if routers say: "I can't give you 5, but I can give you 3"?
Notes: so far we said that the better abstraction for programmers was
11:00
circuit switching we like having reservations when we write code but packet switching was more efficient and
11:06
it was better at handling failur so packet switching is winning two to one but here's the final one implementation
11:12
complexity which of these two is easier for the network to implement so this is the people writing the code for the
11:18
routers and for the end hosts which of these is easier to implement it turns out packet switching wins this one too
11:25
and we'll see why so first of all the key is this is less for the routers to
do in circuit switching routers have to keep track of what reservations are currently active and which reservations
11:37
are currently not active or have finished that's extra work for the routers they have to remember well right
11:44
now this reservation is in progress and this reservation is valid for another 10 minutes and this one's about to expire
packet switching routers don't have to keep track of that stuff at all it sees the packet it forwards it and end
12:03
of story there's no such thing as reservations in the packet switching approach also if you think about circuit
12:09
switching and you really try to sit down and write code to implement circuit switching you're going to run into a lot
12:16
of pain so here are just some examples of questions you might come up with as you try to write code for routers to
12:23
support reservations via circuit switching one question you might have is how do you know if the request was
12:28
actually approved so when we sent that reservation request from A to B and it
12:34
hit all of the routers along the way how do you know that everyone said yes what if someone said no how do you know that
12:40
someone five routers before you said no we have to figure that out what if the
12:45
request packet itself gets dropped because remember we're still in a best effort environment packets might get
12:51
dropped so what if the request gets sent halfway and it doesn't reach the other routers what happens to the people
12:57
who've already seen the request I don't know open question what if the tear down packets get gets dropped we're
13:03
done with the reservation we send a tear down packet from A to B but only half of the routers hear about the tear down
13:10
what do the other half of the routers do I don't know open question what if their request is declined what do you do in
13:17
that case do you tell the user there's an error do you try again do you look for different paths all of those seem
13:22
like valid or purchase but that's a question you have to answer and notably you don't have to answer that question
13:28
in packet switching or what if routers try to negotiate with you and they say I can't give you five but I can give you
13:35
three if you want it do you take that do you not take that there's a this totally open question of routers negotiating
13:42
with you about how much bandwidth you can have and that's something we haven't really even touched but you can imagine
13:47
that opens up a whole world of complexity who knows how you answer this question so these questions do have
13:52
answers and if you really wanted to implement circuit switching you could sit down and answer these one by one but
13:58
the I want to get across here is just that circuit switching opens up a whole world of questions that just don't exist
14:04
in packet switching so that's an argument for packet switching being easier to write in code when you're the
14:10
network operator and you're programming routers and hosts

## Slide 48: Which is Better? (4/4) – Implementation Complexity in Circuit Switching
Circuit switching implementation question:
What if the teardown packet gets dropped? Doesn't reach R3 and R4.
Possible solution: Reservation expires after some time of inactivity.
R5
R6
Done!
Done!
Done!
Done!
R1
A
R2
R4
R3
B
Dropped!
R3 and R4 haven't torn down the circuit!
Notes: okay another example what if the tear down packet itself gets dropped so
17:16
a says I'm done sends a packet to B indicating that they're done and the goal is to get all the routers along the
17:21
way to hear the done message so that they can tear down the reservation so R1 hears it R2 hears it R3 doesn't hear it
17:29
and neither does R4 so at this point R1 and R2 know that the reservation is over
17:34
but R3 and R4 don't so what do they do do they keep the reservation open how do they learn that the reservation is over
17:42
again one possible solution is to have a timeout and say when the timer goes off the reservation automatically expires
17:48
but maybe that means that the reservation hung around R3 and R4 for longer than it had to is that something
17:55
we could solve maybe maybe not maybe you have this half finished circuit for some time all of this is just to say circuit
18:02
switching is hard to implement and if you really wanted to implement it you would have to solve all of these
18:07
challenges that we are just barely scratching the surface
18:14
of thoughts questions

## Slide 49: Circuit Switching vs. Packet Switching: Which is Better?
Which one offers a better abstraction to applications? (Circuit switching.)
Which one is more efficient at scale? (Packet switching.)
Which one is better at handling failures at scale? (Packet switching.)
Which one is easier (less complex) to implement at scale? (Packet switching.)
Circuit switching pros:
Reservations give applications better performance.
Reservations are more predictable and understandable.
Packet switching pros:
More efficient.
Faster startup to first packet delivered.
Easier recovery from failure.
Simpler implementation.
Notes: okay so to summarize we
18:21
thought about four different ways to debate the question of circuit switching versus packet switching and it turns out
18:27
packet switching won three times circuit switching won once so circuit switching was the winner when we thought about
18:33
providing a useful abstraction to programmers of applications programmers
18:38
would really like to be able to say I have a network connection it's going to give me five units of resources and I
18:45
have that for the full hour that's great because as the programmer I'm guaranteed five whereas in packet switching who
18:50
knows what I get I try to request five or send five units worth of data whether
18:55
or not it shows up who knows and so that's why circuit switching won in the first case packet switching we said was
19:02
more efficient we said it was better at handling failures and we said it was easier to implement so in general packet
19:08
switching there's just less overhead everyone has to think less hard if they do packet switching because they don't
19:14
have to worry about reservations that's kind of the oneline answer for why packet switching was the winner in these
19:19
three cases there's just less to think about in packet switching so that's kind of the rough summary of circuit
19:27
switching versus packet switching in there are Pros to both so it's not like packet switching is the clear winner
19:32
here just because it one and two three and four there are some cases where circuit switching is better for example
19:38
as mentioned if applications have really strong performance requirements maybe you want to go with circuit switching
19:45
but when we're thinking about the general purpose internet these are the things that the designers of the internet thought about and they came up
19:51
with these tradeoffs between circuit switching and packet switching so it's not that one is better but it's that
19:57
these are the trade-offs that the designers of the internet faced when they try to implement one or both of
20:04

## Slide 50: Circuit vs. Packet Switching: A Brief History
Internet Design Principles
Architecting the Internet
Narrow Waist, Demultiplexing
End-to-End Principle
Designing Resource Sharing
Statistical Multiplexing
Circuit vs. Packet Switching
Which is Better?
A Brief History
Lecture 2, Spring 2026
Notes: these so with all of this lesson uh solved we thought about circuit versus
20:09
packet switching and which is better we can now think about which of these actually is used in the internet so we
20:15
kind of spoiled it already because we told you how the internet works and if you think back to the last set of videos
20:21

## Slide 51: Circuit vs. Packet Switching in Practice
Packet switching is the default in the modern Internet.
Circuit switching used in limited settings.
RSVP (Resource Reservation Protocol) inside a local network.
Users can buy a dedicated link, e.g. MPLS circuits, leased lines.
  Companies might buy dedicated links between their offices.
  Very expensive. 10–20 times more than a normal connection.
  Reservation requires manual set-up, and lasts for years.
  Reservation is per-company, not per-flow.
These settings are more constrained than reservations on the whole Internet.
Notes: we never actually said that the internet is circuit switched we never talked
20:26
about reservations we said that packets are best effort so as you might expect packet switching ended up winning
20:32
overall and in the modern internet the vast majority of the internet is Packet switched so when your computer connects
20:40
to the internet your computer does not make a reservation it just starts sending packets and hopes for the best
20:47
so for the reasons we talked about earlier like the fact that packet switching is just easier to implement
20:52
the modern internet eventually gravitated toward packet switching and that's the dominant form today but as we
20:58
mentioned earlier it's a tradeoff and it doesn't mean that circuit switching is a clear loser in fact there are actually
21:04
some places where circuit switching is the right way to go so for example let's say there are two really important
21:12
there's a really important company and they have two buildings on different sides of the country so I don't know
21:18
some famous bank they have a building in San Francisco and they have a building in New York and it's really important
21:24
that this bank is able to send data back and forth to each other very Rel reliably and nothing gets dropped and we
21:31
really have to make sure that they have a guaranteed amount of bandwidth well maybe those two Banks or I guess the two
21:37
buildings of that same bank maybe they want to have a reservation they want to reserve some bandwidth so that they're
21:44
able to talk to each other and always have a guaranteed standard of performance so circuit switching can
21:49
still be useful in limited applications and there are actually protocols out there that exist for reserving bandwidth
21:57
in real life though because the internet is mostly packet switched if you want to reserve things not only do you actually
have to reserve the bandwidth you actually have to build the band with yourself so if these two Banks really
22:09
wanted to communicate to each other they might actually have to pay an internet service provider and say can you please
22:15
build me the actual physical link that crosses the country and when you build it please build it for only us to use so
22:23
it's very expensive to do this and it's not really the same as what we were talking about earlier where you can
22:29
reserve something and then tear it down this is a case where when you reserve something you're buying the actual
22:34
Network and it's going to take years to build the network itself and you're going to use it for years and years and
22:41
years and there really isn't even a notion of tear down so we've kind of evolved Beyond just the circuit
22:46
switching idea that we talked about earlier but you can imagine in real life if someone really needs bandwidth they
22:52
can just go out and tell Comcast or AT&T can you just build me a link and I'll
22:57
pay a lot for it so it's very expensive it's very slow it's not quite the same as dynamically setting up and tearing
23:04
down bandwidth but if you wanted to you can still get a full-time bandwidth link
23:09
that's all yours so these settings as mentioned they're more constrained it's not like the wide internet just lets you
23:16
reserve and tear down things whenever you want it's kind of a very limited set of applications that would want
23:21
reservations to begin with and are willing to pay for it but this just goes to show it's trade-offs some
23:27
applications do want the reservations and if they're willing to pay up for it they can actually achieve it so that's
23:33
what this slide says okay A little bit of brief history by the way on circuit versus packet
23:39
switching as we've kind of alluded to because of these trade-offs it wasn't clear right away that packet switching
23:45
was the way to go so in the 1970s and the 1980s when the internet was first starting up it wasn't immediately clear
23:52
which of these two should be used so in the beginning packet switching was what

## Slide 52: Circuit vs. Packet Switching – A Brief History
Early Internet (1970s, 1980s) used packet switching.
Well-suited for bursty file transfer applications.
Next iteration (late 1980s, 1990s) tried to move toward circuit switching.
Internet control shifted from the US government to companies.
  Circuit switching offers a more intuitive business model.
Envisioned smooth voice/TV applications to dominate traffic.
Spent 10+ years trying to realize the vision of circuit switching, but ultimately failed.
Because of all the reasons we discussed.
Bursty email and web browsing applications ended up dominating traffic.
Users ended up adapting to packet switching realities.
  Example: Video quality decreases if connection is poor. That’s just life.
Notes: A lesson in how technology can transform user behavior!
because of these trade-offs it wasn't clear right away that packet switching
23:45
was the way to go so in the 1970s and the 1980s when the internet was first starting up it wasn't immediately clear
23:52
which of these two should be used so in the beginning packet switching was what
23:57
people used and this was great because the very early internet was all about transferring files it was researchers
24:04
saying hey I want to send a research paper from Stanford to UC Berkeley or something like that so if the idea is to
24:10
transfer files it makes sense to use packet switching for the reasons we mentioned earlier file transfer is very
24:16
bursting you transfer a file and then you read it for a couple of hours and then you transfer another file and read
24:22
it for a couple of hours so this application is very bursty and because that was the dominant application packet
24:28
switching turned out to be the right approach for the very early internet then in the 80s and 90s something
24:34
interesting happened so the internet stopped becoming a research project that was funded by the government and
24:40
research groups and it started to become an actual business so in the very old days of the internet it wasn't like
24:46
researchers were you know trying to make money off of it and saying oh you know my goal is to make money back in the in the early 70s and '
24:54
80s it was more about research and just trying to see what the system could do and that was what the government and
25:00
different universities were funding but once we got to the 80s and 90s the internet became more of a commercial
25:06
Enterprise and that meant that companies actually wanted to make money and sell the internet to average users not just
25:13
researchers playing around with it and seeing what would work and so there was a concerted effort to try and move
25:19
towards circuit switching because the idea was well if we're going to hand off control of the internet to all these
25:25
companies and they want to sell the internet to users it makes sense to have circuit switching
25:30
because circuit switching has a very intuitive business model like we talked about we can say if you want to reserve
25:36
five that's going to cost you $5 you want to reserve 10 it's going to cost you $10 and packet switching doesn't
25:42
offer a similar business model that's so intuitive so there was a real effort to try and move the internet towards
25:48
circuit switching and another reason why circuit switching was anticipated to be the right idea here was because people
25:55
were trying to predict the future and they thought that the future of the internet would be voice and TV
26:01
applications so for example calling people over the Internet or watching TV over the Internet that's what people in
26:07
the 80s and 90s thought that the future would be and they imagined that these applications would be very smooth they
26:13
wouldn't be as bursty as file transfers for example if you're watching TV live you're constantly downloading data it's
26:20
a very smooth connection it's not as bursty so they they re they reason that well if I'm going to have a lot of users
26:27
talking over phone on the Internet or watching TV on the internet they're going to have very smooth applications
26:33
so it makes sense to use circuit switching because as we saw earlier circuit switching has reasonably good
26:39
efficiency if the connection is smooth so that was the reasoning in the 80s and
26:44
90s and at the time it seemed to make sense for all these reasons but ultimately they ran into the same
26:50
problems that we just talked about they ran into all the same implementation challenges that we talked about how do
26:56
you set up a connection how do you tear it down down what about all these failure cases how do you recover from
27:01
failure and because of all those problems ultimately the vision of circuit switching was not really
27:07
implemented didn't really work also something interesting happened so even
27:12
though people in the 80s and90s thought that live TV was going to be the future when we entered the 2000s that actually
27:19
turned out to be false so maybe some of you are too young for this but in the 2000s there was the do boom do you
27:25
remember that that was when web pages kind of became the main source of traffic on the internet people weren't
27:31
really using the internet to watch TV in the early 2000s they were using it to browse the web they wanted to visit
27:37
websites that was a brand new shiny thing that people wanted to do and they wanted to send email that was another
27:43
shiny new application of the internet so in the early 2000s email and web were
27:48
the two dominating sources of internet traffic and both of these are very bursty you download a web page and then
27:54
you stare at it for a lot of time and then you click on a link and go to another website download it and browse
27:59
it for a lot of time so both of these were very bursty applications so it turned out that the prediction of voice
28:05
and TV at least in the 2000s wasn't quite accurate email and web ended up being the dominant applications and
28:12
because those are bursty they ended up working quite well with packet switching also one very interesting thing that
28:18
happened even today is that even though circuit switching might be better for users as we talked about and better for
28:25
programmers because of the reality that packet switching is what we're stuck with people actually change the way that
28:32
they use the internet to adapt to packet switching realities which is kind of interesting so kind of the most resonant
28:39
example I could think of is when you're watching a video if the connection is poor what happens the quality goes down
28:46
so when you're watching a video if the connection gets really spotty the video just suddenly gets worse and you can
28:51
imagine in an alternate universe where we were in the circuit switched world this would be criminal you complet to
28:58
the phone company or the internet company you'd say hey what the heck I reserved five megabits per second and
29:04
suddenly my internet got worse and suddenly the video got worse what is going on you can imagine that users
29:10
really don't like this but what happened in our universe is because packet switching is the reality and packet
29:17
switching means that it's first come first serve and if there's not enough capacity things just get dropped all of
29:23
us as users we just got used to the fact that hey if I'm watching a video it might just worse and we'll just deal
29:29
with it that's totally okay so it's kind of interesting that technology actually transformed user behavior in this case
29:36
so this is the case where it wasn't the case that technology adapted to the users the users adapted to what was
29:42
actually possible and what was possible was not circuit but packet switching so I find that kind of cool so that's your
29:49
little history lesson on how the internet evolved and you can see that people really thought hard about the tradeoffs as they were designing the

## Slide 53: Summary: Internet Design Principles
End-to-end principle: Reliability must be implemented in end hosts (not routers) for correctness.
Reliability could be added to routers as a performance optimization, though.
Narrow-waist for federation: Everyone uses IP at Layer 3.
Demultiplexing is used to pass a packet up to the correct higher-layer protocol.
Ports are used to uniquely identify applications on an end host.
Software
Operating
System
Network Interface Card (Hardware)
IP
TCP
UDP
Firefox
Zoom
Email
Slack
Game
Layers 1–2
Layer 3
Layer 4
Layer 7
From: YouTube server
To: Bob's computer
Next layer is TCP.
From: Port 80
To: Port 40000
[cat video]
Demultiplex: Which L4 protocol?
Demultiplex: Which L7 application?
Notes: okay so to quickly summarize this set of videos we talked about the design principles that went into making the
30:16
internet so we didn't talk about what the internet is or how it's built we talked about why and we really thought
30:22
about the reasons behind building the internet and building the internet the way that we built it so weal Al about
30:28
the nuro waste we showed you a picture of all the protocols that exist and in particular everyone uses the same
30:34
protocol at layer three namely IP and this is very important because even if
30:40
lots of different users are communicating over different Stacks that is different sets of protocols everyone
30:45
using IP ensures that all these different companies and users and network devices everyone has one common
30:53
language that they speak so even if you're being run by a different organization or in a different country
30:59
we all speak the same language we all speak IP and that's what enables the internet to work even though the
31:04
internet is Federated operated by lots of different operators we also talked about Dem multiplexing and that idea was
31:12
well when the end host receives a packet and it reaches layer three it needs to decide which layer four protocol to pass
31:18
the packet to and we add an extra field in the layer three header to tell us which protocol comes next and likewise
31:25
once you reach layer four we also have to to decide which layer 7 application receives this packet and to enable that
31:33
we added port numbers and the port numbers Associated each application with a number on that particular computer and
31:40
we said that on private computers like yours the port numbers can be basically arbitrary but on a server like the
31:47
YouTube server that's serving videos everyone in the world has to know that YouTube is serving videos from Port 80
31:53
for example and so when you send and receive packets in addition to the IP addresses that tell you which computer
32:00
you're talking to at layer three you also need port numbers at layer 4 and those identify on the two computers that
32:07
are communicating to each other which application on the first computer which application on the second computer
32:13
that's what the port numbers tell you we talked about the endtoend principle which told us that reliability has to be
32:19
implemented in the end hosts we used our super simple reliability protocol to convince ourselves that if we had the
32:26
network deal with reli ility and the end host had to trust the network to be correct we could actually never get
32:32
reliability because the end hosts have to trust the routers and the routers could be buggy so it turns out by the
32:39
argument that we made reliability has to be implemented in end hosts you have to put it there anyway for correctness and
32:46
putting it in end host is already enough so there's no need to do anything else might as well put it in the end host it
32:51
is the strictly better solution but reliability could still be added to routers as a minor performance
32:59
optimization

## Slide 54: Summary: Designing Resource Sharing
Statistical multiplexing is more efficient than static allocation.
Circuit switching offers better abstraction. Packet switching is more efficient, better at handling failures, and easier to implement.
Flows can be smooth or bursty. Packet switching is more efficient on bursty flows.
Peak of aggregate
Aggregate of peak
Time
Demand
Time
Demand
Statistical Multiplexing
Static Allocation
Notes: and in the second half of this set of videos we talked about resource sharing and first we said that
33:05
statistical multiplexing Dynamic allocation is more efficient than static allocation where you just give everyone
33:11
some fixed amount of resources for all of time that's not so great statistical multiplexing is the way to go it's what
33:17
the internet does within statistical multiplexing there's two ways to share resources circuit switching reservation
33:24
based packet switching first come first serve and we said that circuit switching
33:29
was the winner for giving programmers a better abstraction but packet switching won in the other dimensions of being
33:35
more efficient being better at handling failures and just being easier to implement we talked about smooth versus
33:41
bursty flows and we said that the gains or the advantages of packet switching are even more clear when the flows are
33:47
bursty and they're a little less pronounced when the flows are smooth and when we talked about statistical
33:53
multiplexing versus static allocation we showed you this picture where we said the p of the aggregate you sum the
33:59
graphs first and then find the maximum that is always going to be less which means you need less bandwidth to meet
34:05
everyone's demands compared to the aggregate of the peak which means you first compute everyone's Peak and then
34:11
sum it and this is strictly worse so that's the summary
any final thoughts on internet design