## Slide 1
Lecture 25, Spring 2026
Slides credit: CS168@UC Berkeley
Cellular
Lecture 25 (Wireless 2)
Notes: Slides template credit: Josh Hug, Lisa Yan
https://en.wikipedia.org/wiki/File:Wifiservice.svg
FILL OUT THE FORM

## Slide 2: Brief History of Cellular Networks
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 3: Why Study Cellular?
Goal: Wireless mobile connectivity, e.g. watching video in a moving car.
Cellular is the dominant approach today.
  Over 50% of web traffic originates from a cellular device!
Other technologies (e.g. satellite) also exist.
Active area of research!
New bandwidth-intensive mobile apps, e.g. virtual reality, self-driving cars.
Cellular network is facing severe scaling challenges.
  Deploying towers and buying spectrum is expensive.
  Traditional operators (AT&T, Verizon) don't have a reputation for rapid innovation.
Mobile Wireless Access
Cellular
Satellite
Free-Space Optics

## Slide 4: Brief History of Cellular Networks
Cellular networks are derived from the old telephone network.
Original purpose: Make phone calls wirelessly.
Martin Cooper made the first mobile call on this Motorola phone.
Sold for $4,000 in 1983 (over $12,000 today).
Apparently worth over $40,000 today as an antique.

## Slide 5: Brief History of Cellular Networks
Roots in the telephone network led to design choices that differ from the Internet.
The Internet:
Best-effort.
Per-flow or per-packet state.
Doesn't really track usage per user.
Cellular networks:
Resource reservations.
Per-user state in the network.
Emphasis on accountability.
In recent years, cellular networks evolved to be more compatible with the Internet.
Today, can think of cellular networks as Layer 2 networks within the Internet.

## Slide 6: Cellular Network Standards
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 7: Cellular Standards Evolution
3GPP (3rd Generation Partnership Project) consortium oversees standardization efforts.
Includes equipment vendors and telecommunications companies.
Everyone must agree on protocols to achieve interoperability.
Standards ratified by ITU (International Telecom Union), part of the United Nations.
New generation every 10 years: 1G, 2G, 3G, 4G, 5G.
5G introduced in 2019, still being deployed.
6G coming in 2030.
Notes: Politics are involved in approving standards!

## Slide 8: Cellular Standards Evolution
Each generation aims for a ~10x improvement along a few different dimensions:
Peak theoretical data rate.
Average data rate experienced by users.
Mobility: Connection while user travels at high speed.
Connection density: Number of devices in a specific era.
Light green = 4G quality along 8 different dimensions.
Dark green = 5G quality along those same dimensions.

## Slide 9: Cellular Standards Evolution
In addition to performance evolution, there's also been an architectural evolution:
1G:
  Analog.
  Designed for voice calls.
2G/3G:
  Mostly circuit-switched.
  Focused on voice traffic. Some texting. Barely any Internet access.
LTE/4G onwards:
  Packet-switched.
  Voice just one of many different applications.
Cellular specifications are long and complicated.
Components/protocols are renamed in every generation!
  "Base station" → "NodeB" → "evolved Node B (eNodeB)“ → next-gen Node B (gNB)
In this class, we’ll use terminology loosely based on the LTE architecture.

## Slide 10: Challenge: Mobility
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 11: Key Challenge: Mobility
What fundamental new requirements does mobility introduce?
Discovery: What cell tower should a mobile device connect to?
Authentication: Should the tower provide service to this device?
Seamless communication: No disruption to new/ongoing application sessions.
Accountability: Enforcing resource limits based on the user's service plan.

## Slide 12: Cellular Infrastructure
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026
Notes: Conceptual overview - not a lot of math, more to give a sense for how cellular works

## Slide 13: Infrastructure Components (1/5): Radio Towers
Radio Tower
Range of tower
Inside a radio tower:
Radio transceiver: Converts data to signals sent over the air interface.
Radio controller: Decides how to allocate radio resources.
  Traditionally near the tower, but sometimes in the cloud now.
Antenna
Transceiver
Controller

## Slide 14: Infrastructure Components (1/5): Radio Towers
Simplified model: Radio controller is like a CPU running a scheduler.
Decide who gets to transmit when, and on what frequency.
Each block represents one part of the spectrum at one time slot.
Time
Frequency
Purple user gets these frequencies...
...at these times.
Notes: Who gets what frequencies at what time?

## Slide 15: Infrastructure Components: Cellular Core
Each operator has a radio access network of many towers.
Neighboring towers are assigned non-overlapping frequency ranges.
Towers in more populated areas can get allocated more frequencies.
The cellular core is the "backend" of the cellular network.
Cellular Radio Access Network (RAN)
R1
R2
P1
Mobility Manager
Database
Cellular Core
To Internet
Notes: How do these towers actually communicate with the internet?

## Slide 16: Infrastructure Components (2/5 and 3/5): Radio Gateway, Packet Gateway
Data-plane components (routers):
Radio gateway: Boundary between RAN and core.
Packet gateway: Boundary between cellular network and rest of Internet.
Cellular Radio Access Network (RAN)
R1
R2
P1
Mobility Manager
Database
Cellular Core
To Internet
R1 and R2 are radio gateways.
P1 is the packet gateway. (There could be multiple).
Wired links between towers and radio gateways.
Notes: Let’s go through the different components.
Wired links between towers and radio gateways

## Slide 17: Infrastructure Components (4/5 and 5/5): Mobility Manager, Database
Control-plane components:
Mobility manager: Handles authentication, mobility, location tracking, etc.
Database: Stores information about customers.
Cellular Radio Access Network (RAN)
R1
R2
P1
Mobility Manager
Database
Cellular Core
To Internet
Manager can access database.
Manager can configure gateways and towers.

## Slide 18: Infrastructure Components: Summary
Cell towers (arranged in a RAN).
Data plane: Radio gateways, packet gateways.
Control plane: Mobility manager, database.
Cellular Radio Access Network (RAN)
R1
R2
P1
Mobility Manager
Database
Cellular Core
To Internet

## Slide 19: High-Level View
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 20: High-Level View (0/4) – Registration
Step 0: Registration.
User registers for the service. Database is updated.
R1
R2
Mobility Manager
Database
P1

## Slide 21: High-Level View (1/4) – Discovery
Step 1: Discovery.
User wants to connect.
User device discovers available towers and picks one.
R1
R2
P1
Database
Mobility Manager

## Slide 22: High-Level View (2/4) – Attachment
Step 2: Attachment.
Device asks the tower to connect.
Tower checks with mobility manager if connection is allowed.
R1
R2
P1
Database
Mobility Manager

## Slide 23: High-Level View (2/4) – Attachment
Step 2: Attachment.
If manager approves request, it configures a path between user and Internet.
R1
R2
P1
Database
Mobility Manager

## Slide 24: High-Level View (3/4) – Data Exchange
Step 3: Data exchange.
User can now send and receive data!
Packets travel along the path configured in previous step.
R1
R2
P1
Database
Mobility Manager

## Slide 25: High-Level View (4/4) – Handover
Step 4: Handover.
Device might move away from old tower, closer to a new tower.
Device, old tower, new tower, and manager work together to switch towers.
R1
R2
P1
Database
Mobility Manager

## Slide 26: High-Level View (4/4) – Handover
Step 4: Handover.
Manager configures a new path through the network for the user.
Handover must be seamless. We can't interrupt the user's connection!
  User's IP address should stay the same.
R1
Database
Mobility Manager
R2
P1

## Slide 27: High-Level View (4/4) – Handover
After handover, user has a new path through the network.
Step 3 (Data Exchange) and Step 4 (Handover) repeat as the user moves around.
R1
Database
Mobility Manager
R2
P1

## Slide 28: High-Level View – Roaming
One last feature is roaming: User connecting to a different network.
Example: User visiting a different country.
Mostly works the same as what we've seen.
Main difference: Managers in the visited and home networks must coordinate.
R1
R2
P1
DB
Manager
Home network
R1
R2
P1
DB
Manager
Visited network
Internet

## Slide 29: Step 0: Registration
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026
Notes: ~30min in

## Slide 30: Identifying User Devices: IMSI
When you register for a service, you receive an IMSI (International Mobile Subscriber Identity).
Uniquely identifies a user's subscription.
Securely stored in hardware (SIM) card.
IMSI stays the same if you switch phones, but keep the same service plan.
MCC (3 digits)
MNC (2–3 digits)
MSIN (9–10 digits)
Mobile Country Code
Mobile Network Code
Mobile Subscriber Identification Number
IMSI (no more than 15 digits)

## Slide 31: Identifying User Devices: IMSI, IMEI, IP, MSISDN
Different ways to identify a user device:
IMSI: Identifies a user subscription.
IP address: Assigned on attachment, typically retained across handovers.
  Can change each time you attach to the network.
IMEI (International Mobile Equipment Identity): Identifies a physical device.
  Identifies device manufacturer and model.
  Burned into hardware. Stays the same even if you switch plans.
MSISDN: Your phone number.
  Operator maps your phone number to your IMSI.

## Slide 32: Step 0: Registration
User registers for the service.
Operator stores user's IMSI and plan information in the database.
Establishes a shared key known only by the user and operator.
  User: Stored in SIM card.
  Operator: Stored in database.
R1
R2
Mobility Manager
Database
P1

## Slide 33: Step 1: Discovery
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 34: Step 1: Discovery
Towers transmit periodic beacons to announce their presence.
Beacons transmitted on a dedicated control channel.
  Avoids interfering with data.
  Each frequency range has its own control channel. Avoids beacons interfering with each other.
Beacons identify the network operator.
  User compares beacon against the network ID (in the user's IMSI).
User measures signal strength to different towers, and picks the tower (belonging to its operator) with the best signal.

## Slide 35: Discovery: Finding Control Channel
Bootstrapping problem: How does the user know which control channel to listen to?
Scan all frequencies.
  Slow, but sometimes unavoidable.
At registration, pre-configure device with a list of frequency channels.
Cache previously-used channels.
Note: During handovers, the old tower tells the user the channel on the new tower.
No need to scan! Handovers take 0.01s–0.1s.
Contrast with attachment, which takes 10s–100s.
Notes: Analogy here is listening to the radio and checking the channels - KALX 90.7, KEXP 92.7 Contrast with attachment, which takes 10s–100s.

## Slide 36: Step 2: Attachment
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 37: Step 2: Attachment
1. User sends attach request to tower, containing user's IMSI.
2. Tower forwards request to mobility manager.
3. Mobility manager processes the request, by looking up the IMSI in database.
Use secret key to authenticate: Is the user who they claim to be?
Use database to check service parameters: Did user pay their bills?
R1
R2
Mobility Manager
Database
P1
1
2
3

## Slide 38: Step 2: Attachment
4. If request is approved, mobility manager configures the data plane.
Assign an IP address to the user.
Tell the tower how many resources to allocate for this user.
Configure tower and routers to create a path from user to Internet.
Initialize counters to track the device's usage.
R1
R2
Database
P1
Mobility Manager

## Slide 39: Step 2: Attachment
5. If request is approved, mobility manager records information in the database, mapping the user's IMSI to their current:
Location (tower).
Path to the Internet (radio gateway, packet gateway).
IP address.
R1
R2
Mobility Manager
Database
P1

## Slide 40: Step 2: Attachment
1. User sends attach request to tower, containing user's IMSI. 2. Tower forwards request to mobility manager. 3. Mobility manager processes the request, by looking up the IMSI in database. 4. If request is approved, mobility manager configures the data plane. 5. If request is approved, mobility manager records information in the database.
Note: All communication so far is over dedicated control channels.
R1
R2
Database
P1
1
4
5
Mobility Manager
2
4
4
3

## Slide 41: Step 3: Data Exchange
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 42: Step 3: Data Exchange
Device can now send and receive packets with its IP address!
How does the network know how to forward packets?
Users are constantly moving.
Traditional routing algorithms (Distance Vector, Link State) won't converge.
R1
R2
P1
Notes: User is driving in a car which means they need to use different towers at different times. This is different from distance vector, link state where end hosts move once and awhile, but not all the time.

## Slide 43: Step 3: Data Exchange with Tunnels
Solution: Mobility manager configures a path from user to Internet using tunnels.
Different from traditional IP networks:
No direct forwarding on the user's IP address!
Requires installing per-user state in the network.
R2
P1
If I get a packet exiting the green tunnel, send it into the blue tunnel.
R1
If I get a packet exiting the pink tunnel, send it into the green tunnel.
Notes: Fix is to not use IP addresses for forwarding
Install tunnels with rules about how to forward. It’s more centralized.
Tunnel could include multiple links.

## Slide 44: Step 3: Data Exchange with Tunnels
User's IP
[Payload]
User's IP
[Payload]
User's IP
[Payload]
How do we tell if a packet is traveling through a tunnel? Use encapsulation.
R1
R2
P1
Blue Tunnel
User's IP
[Payload]
User sends plain IP packet. No need to think about tunnels.
User's IP
[Payload]
Blue Tunnel
Cellular network adds extra header.
Blue Tunnel
User's IP
[Payload]
Packet forwarded through cellular network. No need to think about user IP!
Extra header removed, and plain IP packet sent to rest of Internet.

## Slide 45: Step 4: Handover
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 46: Step 4: Handover
5. Connect to new tower using these slots.
2. Here's my signal strength to other towers.
Old Tower
Device
New Tower
1. Your signal strength is low. Measure signal to other towers.
3. User is coming your way...
4. OK. Here are radio slots for the user.
7. Handover complete!
Mobility Manager
6. I'm the new tower for the user.
Update user location in database. Configure new path between user and Internet.

## Slide 47: Step 4: Handover
Handover is complicated.
Cooperative process between user, towers, manager, and gateways.
More involved when we have to change the radio or packet gateways being used.
Handover must be seamless.
User's IP address cannot change.
User is still sending/receiving data during handover.
Old tower can buffer data it receives during handover.
After handover, old tower transfers buffer to new tower.
Decisions are made by the operator.
Device reports signal strength, but old tower chooses the new tower.
Benefit: Operator has more control, e.g. for load-balancing.
Drawback: Slower, requires extra round-trips.

## Slide 48: Roaming and Other Features
Why is Cellular Different?
Brief History
Standards
Challenge: Mobility
Cellular Networks
Infrastructure
High-Level View
Step 0: Registration
Step 1: Discovery
Step 2: Attachment
Step 3: Data Exchange
Step 4: Handover
Roaming and Other Features
Lecture 25, Spring 2026

## Slide 49: Roaming
Visitor and home networks must establish a roaming agreement.
Visited network uses device's network code (in IMSI) to learn the home network.
Need home network's help to authenticate user.
Need to update home network's database with user's location.
R1
R2
P1
DB
Manager
Home network
R3
DB
Manager
Visited network
Internet
P2
R4
Notes: If you go to Brazil have to use Vivo
Hopefully they have an agreement with Sprint, Verizon, AT&T
Two managers must coordinate

## Slide 50: Roaming
Two common ways to configure path from user to Internet.
Home routing: Tunnel traffic through the home network's packet gateway.
Benefit: Home network can track user.
Drawback: Packets takes longer path to Internet.
R1
R2
DB
Manager
Home network
R3
R4
DB
Manager
Visited network
Internet
P2
P1

## Slide 51: Roaming
Two common ways to configure path from user to Internet.
Local breakout: Tunnel traffic through the visitor network's packet gateway.
Drawback: Harder for home network to track user.
Benefit: Packets takes shorter path to Internet.
R1
R2
P1
DB
Manager
Home network
R3
R4
DB
Manager
Visited network
Internet
P2

## Slide 52: Additional Operations
Other operations in cellular networks:
Lawful intercept:
  Allows law enforcement to wiretap specific subscribers.
  Operators must be able to fulfill wiretap requests.
Stolen phone registries:
  Users can report their phone stolen.
  If someone connects stolen phone to network, the phone can be tracked.
  Use IMEI (burned into phone) to identify the stolen phone.
These operations are possible because of centralized control.
Notes: Cellular networks have to comply with law enforcement in the standard.

## Slide 53: Design Reflections
Stateful networks are complex and challenging!
Must store per-user state in the network.
Must reconfigure tunnels each time the user moves.
Requires extreme optimization to scale well.
Alternate designs:
Change IPs on handover:
  Benefit: Can use standard routing protocols.
  Drawback: TCP connections break when IPs change.
Tunnels.
  Drawback: Must store per-user state for routing.
  Benefit: Can use standard routing protocols.
Possible solution: QUIC is an alternate Layer 4 protocol that allows changing IPs.
Notes: Constantly changing IP

## Slide 54: Summary: Cellular
Cellular networks are based on a very different design philosophy:
Authentication and accountability are primary goals.
Allocation of radio bandwidth is based on reservations.
Lots of in-network state that is dynamic and per-user.
Generality was not an early goal.
Mobility is the central challenge.
Cellular networks have evolved from a standalone voice network, to being an integral part of the Internet.
We've been able to seamlessly integrate cellular networks into the Internet.
Cellular architecture continues to evolve toward the Internet architecture.
Notes: Thank you all for a great summer semester. I really appreciate all the great questions and having you all in class. Hopefully this is just the beginning of your computer networking journey !!