## Slide 1: Bandwidth and Propagation Delay
Links
Bandwidth and Propagation Delay
Pipe Diagrams
Overloaded Links
Lecture 3, Spring 2026
Notes: so here's the outline we're going
38:16
to start by talking about links in a lot of detail think about how you measure the performance of links what makes a
38:21
link good what makes a link bad what are the trade-offs we'll talk about what happens if links get overloaded and then
38:27
the very end now that we finished all of the introduction I can actually give you a preview of all the topics you're going
38:33
to see in a lot more detail so these three sets of lectures have really been about giving you a highlevel 10,000 foot
38:39
picture of what you're going to see this semester and then at the very end I'll show you the exact places where we'll be
38:45
really diving in and talking about things in lots more detail but before we get there let's not get ahead of
38:50
ourselves let's start with talking about links and how to measure their performanc

## Slide 2: Properties of Links
A link connects two devices.
Properties of a link:
Bandwidth: Number of bits sent/received per unit time.
  "Width" of the link.
  Measured in bits per second (bps).
Propagation delay: Time it takes a bit to travel along the link.
  "Length" of the link.
  Measured in seconds.
Bandwidth-delay product: Bandwidth × delay.
  "Capacity" of the link.
B
A
Capacity = Delay × Bandwidth
Bandwidth
Propagation Delay
Notes: so far we've been drawing
38:56
things like this we draw two circles and we draw a line between them and we say this is a link so what is a link well
39:04
it's something that connects two devices and it has some properties so here are some three properties that we care about
39:11
one of them is bandwidth band with says how many bits can you send or receive on
39:17
this link per unit time so the way you measure it is data per unit time and so
39:25
the most common unit of measurement is bits per second BPS and derivations
39:31
thereof so for example Mbps is megabits per second kbps is kilobits per second
39:38
and one thing I want to point out and it's very annoying and it trips me up all the time BPS is bits per second it
39:44
is not bytes per second those are different things and they're off by a factor of eight because there are eight
39:50
bits in a bite so if I see that this link works at 8 bits per second that's
39:56
one byte per second and sometimes in real life people use these two interchangeably which is kind of
40:02
annoying but just remember that to go from bits to btes there's a factor of eight because there are eight bits in a
40:08
bite kind of annoying but something you have to deal with the second property is propagation delay and this property it
40:15
seems like it's the same as bandwidth but if you squinted it they're very different things bandwidth says how many
40:21
bits can I receive per unit time propagation delay by contrast says how
40:26
long does it take to travel across the link so if I just send a single bit how
40:31
long does it take from the instant the bit is sent to the instant that the bit is received and this is just a unit of
40:37
time so we're just measuring how much time it takes to send the bit across the link and if this still doesn't totally
40:43
make sense I have an analogy for you so let's say that this link is like a pipe so you can think of a pipe that's
40:49
carrying water and we can say that the pipe has bandwidth and the bandwidth of
40:55
the pipe would be how wide the pipe this so if this link has very small bandwidth that's equivalent to a pipe that's very
41:02
narrow and if it's very narrow that means that the amount of water you can send through the pipe per unit time is
41:08
very slow you have a very narrow pipe and you pump water through it the amount of water that trickles out on the other
41:15
end it's not going to be a lot of water by contrast if you have a really big pipe it's really big you can like walk
41:21
inside of it then if you try to shove water through this pipe the other side is going to be flooded really quick
41:27
quickly it's going to be flooded with all the water that you're sending through the pipe so intuitively you can
41:32
think of bandwidth as how wide your pipe is how much water can you shove through this pipe per unit Time by contrast
41:40
propagation delay is the length of the pipe so it's saying how long is the pipe if the pipe is connecting me to my next
41:47
door neighbor not very long if the pipe is connecting San Francisco to New York that's a very long pipe and the pipe
41:53
tells us how long does it take for a single drop of water to travel from one end to the other so as I'm sending water
42:00
through the pipe I can start a timer the instant a drop of water enters the pipe and stop the timer when that same drop
42:07
of water exits the pipe and see how long that takes and notice that these two things they're not really connected to
42:13
each other in any way you can increase one and not increase the other they basically change independently of
42:19
independently of each other for example I can make the bandwidth much wider that is I can shove a lot more water through
42:25
the pipe now but the propagation delay stays the same just because I can shove a lot of water through the pipe if the
42:32
pipe is still really long it's still going to take a lot of time for any individual drop to travel across the
42:37
pipe and likewise if I make the propagation delay long or short well
42:42
that doesn't affect the bandwidth it just means that the water takes less time to travel through but if the pipe
42:48
bandwidth stays the same it's still the same amount of water showing up just takes less time for each individual drop
42:54
to show up so all of this is to say bandwidth and obligation delay are two totally separate properties and they're
43:00
not really related to each other in any meaningful way and the third property is
43:06
actually a combination of these two so it's called the bandwidth delay product and it's just taking these two terms and
43:12
multiplying them together so notice that bandwidth is bits per unit time and
43:17
propagation delay is time so if you think about multiplying bits per second
43:22
and you multiply it by seconds the output is just going to be bits just or rearranging the units a little bit but
43:29
basically the bandwidth delay product if you multiply these two values together you'll get roughly the capacity of the
43:35
link and in the water analogy I would think of this as if you freeze time so
43:40
you stop time for one second or however long and you measure the amount of water in the pipe at that instant that's the
43:48
bandwidth delay product that's how much water can fit in the link at any given instant

## Slide 3: Measuring Packet Delay with Timing Diagrams
Suppose we have a link with:
Bandwidth = 1 Mbps. (1,000,000 bits per second.)
Propagation delay = 1 ms. (0.001 seconds.)
How long does it take to send a 100-byte (800-bit) packet?
From the time the first bit is sent,
To the time the last bit is received.
Let's draw a timing diagram to help.
Note: We measure in bits per second, not bytes!
Notes: can start doing performance calculations for how long it takes to send some amount of data through a link so as a
44:35
running example let's say we have a link with a bandwidth of one megabit per
44:40
second and one megabit is 1 million bits so this means that this link can send 1
44:45
million bits per second again remember not to confuse this with bytes these are bits and the propagation delay is 1
44:52
millisecond which is 0.1 seconds that is how long it takes for for a single bite
44:59
to enter the pipe and then exit the pipe so you enter the pipe at any time and it
45:05
leaves one millisecond later okay so the question we're going
45:10
to try to answer is let's say we have a packet that is 100 bytes how long does it take to send this packet from the
45:17
instant that the first bit is sent to the instant that the last bit is received so in total from the instant
45:24
that the sender starts shoving data into the pipe to the instant that the final bite or bit exits the pipe

## Slide 4: Measuring Packet Delay with Timing Diagrams
B
A
Bandwidth: 1,000,000 bps
Delay: 0.001s
t = 0s
t = 0.000001s
Time to transmit each bit:
1/1,000,000s
t = 0.001001s
Each bit arrives 0.001s later.
t = 0.000002s
t = 0.001002s
t = 0.000003s
t = 0.001003s
t = 0.000800s
t = 0.001800s
Time to transmit 800th bit:
800/1,000,000s
Last bit arrives 1.8 ms later.
800-bit packet
Notes: okay so here's the picture there's our link goes
45:56
from A to B the bandwidth as mentioned earlier is 1 million bits per second and the delay is .1 seconds so this diagram
46:05
is going to show us what happens over time so we're going to start with time zero and as you move down this diagram
46:11
time will increase so at Time Zero a is going to send the very first bit so
46:17
there are 800 bits to send and a is going to take that very first bit and throw it into the pipe so in it goes and
46:25
remember that each bit takes one over one million seconds to send because I
46:31
can send one million bits in one second that means that each bit takes one over
46:37
1 million bits or seconds sorry to send so I'm just taking this value inverting
46:42
it or taking the reciprocal this tells me how long it takes to send each bit into the pipe so the bandwidth allows us
46:49
to realize that at Time Zero I throw one bit into the pipe and then one millionth
46:55
of a second later I throw the next bit into the pipe and 1 millionth of a second later I throw the next bit into
47:00
the pipe this is the rate at which I can throw bits into the pipe so one
47:05
millionth of a second later the next bit shows up or rather the first bit I guess
47:10
shows up so this is how long it takes to send each bit at time equals zero I start throwing in the first one and it
47:16
enters the pipe at Time 1 millionth of a second and once it enters the pipe it
47:22
takes 0.1 seconds to pop out of the other side so by the time the packet reaches the
47:28
other side it is now 0.1 seconds later so if you squint at this this is 0.1 the
47:35
amount of time it takes to travel through the pipe plus 1 millionth which is the amount of time it took to send
47:41
this packet or send this bit into the pipe in the first place so that's the
47:46
first bit arriving so this is the time at which the very first bit arrives then what happens next well one
47:53
millionth of a second later sender a sends the next bit into the pipe you throw it into the pipe and again 0.001
48:01
seconds later it shows up on this side and this is going to happen 800 times because there's 800 bits to send so at
48:09
time three millionth we throw another bit into the pipe 01 seconds later shows
48:14
up on the other end so it's 0.1 plus 3 millionth of a second and so this keeps
48:21
going over and over again and eventually we get to the 800th bit and that's going to be sent at 800 millionth of a second
48:29
after the first one so the first one was sent at 1 millionth 2 millionth 3 millionth all the way up to 800
48:36
millionth which happens to be this number it's okay if these numbers don't you don't have to compute these right
48:42
now just tles on the slide and 0.1 seconds later that packet arrives on the
48:48
other side as well and so this is our final answer this is when the final bit arrives at the recipient it arrives at
48:58
0.008 that's when the bit enters the pipe and it arrives at
49:04
0.180 0 that's when it exits the pipe so if you're really careful with these calculations and really do the math
49:10
you'll realize that this packet takes 1.8 milliseconds to arrive at the end

## Slide 5: Measuring Packet Delay with Timing Diagrams
Packet Delay = Transmission Delay + Propagation Delay
= (Packet Size / Bandwidth) + Propagation Delay
B
A
Bandwidth: 1,000,000 bps
Delay: 0.001s
t = 0s
t = 0.000001s
t = 0.001001s
t = 0.000800s
t = 0.001800s
800-bit packet
Transmission Delay
Propagation Delay
Transmission Delay
Propagation Delay
Notes: f you're
50:30
really looking for the formula roughly speaking this is how we computed it so this is the math that we did so we took
50:36
the packet size that was 800 bits and we divided it by the bandwidth so this
50:42
number in red gave us 800 millionth of a second basically tells us when the last
50:48
bite shows up so maybe another way of thinking it of it is one over bandwidth is how long it takes to send one bit and
50:55
you have packets size number of bits so in total if each one takes one over bandwidth to send and you have packet
51:02
size number of bits the total amount of time it will take to just get everyone in the pipe is Packet size over
51:08
bandwidth and that's this time right here this is the amount of time it takes to just get everyone into the pipe
51:14
regardless of what happens on the other side so the sender has to get until T equals 800 millionth of a second just to
51:22
get everyone into the pipe and this term actually also has a special term we call it transmission delay it's the amount of
51:29
time it takes just to shove everyone in the pipe regardless of what time they actually show up on the other side and
51:35
because this is the time it takes to just get everyone in the pipe by the time the last person enters the pipe or
51:41
the last bit we also have to wait one more propagation delay for that last bit to exit so at the time the last bit
51:48
shows up wait one more propagation delay the last bit exits the pipe and that gives us our final answer so in total
delay comes from two sources one is the transmission delay and it's affected by packet size and bandwidth the more
52:01
packets you have the longer it takes to shove everyone in the pipe and the narrower the packet the pipe is the
52:07
longer it takes to shove everyone into the pipe that's the bandwidth and the second term is propagation delay the
52:13
longer the pipe is the longer it takes for packets to show up and we have one term of propagation delay at the end for
52:19
the last packet to show up all the other packets show up earlier so we don't have to add them in this
52:25
calculation that is is to show up up here so if you really needed the magic
52:30
formula it's this but be ready to draw the timing diagrams to really apply your
52:37
knowledge

## Slide 6: Transmission Delay and Propagation Delay
Transmission Delay: How long it takes to push all bits in the packet onto the link
  From the time the first bit enters the link, to the time the last bit enters the link
Depends on packet size and link bandwidth
Propagation Delay (latency): How long it takes for one bit to travel across the link
  Depends on the distance/length of the link, and propagation speed of the link (close to speed of light)
  Does NOT depend on packet size
Capacity = Prop. Delay × Bandwidth
Bandwidth
Propagation Delay
(bits/second)
Notes: End-to-end transmission time of one bit
Transmission – how long it takes computer to actually put bits onto the wire. Depends on how much data you’re sending and the bandwidth
Propagation – normally speed of light.
Queueing – the traffic pattern. Routers are usually receiving/sending many packets on many different connections simultaneously, and this can slow down the network.
  is received.
  Time between when the first bit enters the link, and the last bit enters the link

## Slide 7: Link Tradeoffs
Which link is better? It depends.
Link 1: Bandwidth 10 Mbps Propagation Delay = 10 ms
Link 2: Bandwidth 1 Mbps Propagation Delay = 1 ms
10-byte packet: Link 2 is better.
10.008ms with Link 1. 1.08ms with Link 2.
  Link 1: ttx = 10 byte / 10Mbps = 80 bits / 10Mbps = 0.008ms, tprop = 10ms, Total delay = 10.008ms
  Link 2: ttx = 10 byte / 1Mbps = 80 bits / 1Mbps = 0.08ms, tprop = 1ms, Total delay = 1.08ms
For small packet, transmission delay is negligible. Propagation delay dominates.
10,000-byte packet: Link 1 is better.
18 ms with Link 1. 81 ms with Link 2.
  Link 1: ttx = 10000 byte / 10Mbps = 80000 bits / 10Mbps = 8ms, tprop = 10ms, Total delay = 18ms
  Link 2: ttx = 10000 byte / 1Mbps = 80000 bits / 1Mbps = 80ms, tprop = 1ms, Total delay = 81ms
For large packet, transmission delay dominates.
Notes: okay so now that we know how to calculate the performance of links and use these performance attributes to
52:44
calculate how long it takes to send packets through the network we can now start comparing links if you go to the
52:50
store and try to buy some links you might think which of these is better and as always the answer is there's not a
52:56
clear way there are tradeoffs so for example let's say you go to the store and you have these two choices of links
53:01
one of them has high bandwidth but low Pro but High propagation delay as well so the link is high bandwidth you can
53:07
shove lots of water through it but it's very long takes a lot of time for the packets to show up by contrast the other
53:14
link has smaller bandwidth it's very narrow can't send a lot of water through it at any given time but the propagation
53:20
delay is quite short so each packet that you send in shows up pretty quickly and so immed imately you think which of
53:27
these is better and the answer is it kind of depends on what data you're trying to send so for example let's say
53:33
you're sending a pretty small packet 10 bytes that's a pretty small packet well if you think about sending a 10 byte
53:39
packet you can do the calculations that we just did and in fact if all of this is seeming like just some wizard magic
53:45
maybe you do want to sit down and actually crunch out these calculations you'll get roughly 10 milliseconds for
53:50
link one 1 millisecond for link two so you can actually run some calculations to prove Pro to yourself that link to is
53:58
the winner here but intuitively here's how I think about it this packet is very small so regardless of what the
54:04
bandwidth is the amount of time it takes to shove this packet into the pipe is pretty quick there's only 10 bytes that
54:11
you have to shove into the pipe so regardless of if my bandwidth is 10 megabits per second or 1 megabit per
54:16
second I'm basically going to be done shoving this packet into the bite into the pipe instantly cuz it's so small and
54:23
so this means that most of the delay is going to come from the propagation delay it's going to come from the time it
54:28
takes for this tiny little packet to travel all the way across the pipe so if I just have a little burst of water that
54:34
I have to send in both cases getting the water in the pipe is not the problem it's the amount of time it takes to
54:40
travel across the pipe that's really going to dominate in that case I want the shorter pipe because I want this
54:46
packet to get there as fast as possible and we know propagation delay is the main problem here so pick the one with
54:52
lower propagation delay here's the other case what if the packet is 10,000 bytes very big packet
55:00
well in this case again you can crunch the numbers you'll get roughly 18 milliseconds for link one 81
55:06
milliseconds for link two unless I messed up my math and if I did let me know but intuitively now the
55:13
transmission delay is the one that dominates this is a lot of data to shove into the pipe so now we really want the
55:20
big pipe we want the one where you can shove all the stuff into the pipe as fast as possible and Link one has the wi
55:26
bandwidth it's going to let us get all of these packets into the pipe and yes the propagation delay is worse but in
55:32
this case because there's so much to shove into the pipe the transmission delay dominates and compared to the
55:38
amount of time it takes to shove the packets into the pipe the propagation delay is very small doesn't really make
55:44
a noticeable difference the transmission delay is what you really feel as the limiting factor the one that makes this
55:51
packet transmission slow so it really depends in this case for packets that are small the propagation delay is the
55:57
one that dominates and you really care about optimizing for that but if you're sending large packets maybe the transmission delay dominates and in that
56:04
case you want the one with wider bandwidth and if you're sending mediumsized packets who knows you have to do the calculations yourself and
56:11
really think about what link is best for your purposes so those are some trade-offs and you can see sometimes it
56:17
requires back at the envelope calculations in addition to just thinking about things
56:25
intuitively

## Slide 8: Pipe Diagrams
Links
Bandwidth and Propagation Delay
Pipe Diagrams
Overloaded Links
Lecture 3, Spring 2026
Notes: Questions!!

## Slide 9: Timing Diagrams and Pipe Diagrams
B
A
Bandwidth: 5 bps
Delay: 7s
t = 0s
t = 1s
5 bits transmitted per second.
t = 8s
Each bit arrives 7s later.
t = 2s
t = 9s
t = 3s
t = 10s
t = 10s
t = 17s
10s to transmit 50 bits.
Last bit arrives 17s later.
50-bit packet
Notes: Okay so we've just seen one way to draw out links we saw the timing
57:35
diagrams and we can use those to measure the performance of a link but there's actually an alternate way of drawing
57:41
links and this one honestly kind of threw me off at first so I tried a couple of animations to make it look
57:47
better let me know what you think they might be kind of weird but we'll try it so as a reminder we drew timing diagrams
57:54
and timing diagrams I think they're great the way you read them is relatively simple time starts at the top
58:00
and it works its way down and the way that we drew it is we basically said
58:05
well each line represents some amount of bytes being sent from A to B and we can
58:11
draw the place or the time where that set of bytes is sent and the time at which that set of bytes is received and
58:18
we can use this to help us calculate how long it takes for packets to be sent so for example here's another example with
58:25
slightly more easy to stare at numbers so we have a link with bandwidth that sends five bits per second and a delay
58:32
of 7 seconds is this realistic no is it easier to draw on the slides yes so we'll go with this so here's a case
58:39
where I can send five bits at every second so maybe another way of drawing the timing diagram from before instead
58:44
of drawing each bit individually I can draw well at 1 second five packets enter
58:50
look at the dots 1 2 3 4 5 those are the five bits that entered and each arrives 7s later
58:56

## Slide 10: Timing Diagrams and Pipe Diagrams
B
A
Bandwidth: 5 bps
Delay: 7s
t = 0s
t = 1s
t = 2s
t = 3s
t = 4s
t = 5s
t = 6s
t = 7s
t = 8s
t = 9s
t = 10s
t = 11s
t = 12s
t = 13s
t = 14s
t = 15s
t = 16s
t = 17s
(These diagrams needsto be viewed with animation to make sense.)
The pipe diagram shows the bits on the link at any given moment in time.
B
A
Bandwidth: 5 bps
Delay: 7s
t = 0s
t = 1s
t = 2s
t = 3s
t = 4s
t = 5s
t = 6s
t = 7s
t = 8s
t = 9s
t = 10s
t = 11s
50-bit packet
20-bit packet
Notes: I am showing to you is a frozen moment in time so I am causing the movie to
1:01:27
show you where the bits are at any given time if the bits are on this side outside of the blue pipe they are still
1:01:34
at a waiting to be sent if the bits are on this side outside of the blue pipe
1:01:40
they have been received by B and crucially if they are inside the Blue Zone they are wait or they're currently
1:01:47
being sent through the pipe that's how I drew this and in general when people draw this they mainly draw the thing in
1:01:53
blue and that's going to show you a Frozen in Time picture of the pipe it's
1:01:59
like pausing the movie to see what's going on inside of the pipe so at time equals z none of the bits have been sent
1:02:06
they're all waiting at a to be sent and what happens in time equals 1 well we
1:02:12
can send five bits so look what happened five of the bits entered the pipe there
1:02:17
they are and have they reached B yet no because there's a delay so they're still in the pipe and they're not going to
1:02:23
reach B until 7 seconds later so they're going to enter the pipe now and 7 seconds later they're going to show up
1:02:29
at B so what happens at time two well you guessed it five more bits enter the
1:02:35
pipe check it out five more bits enter the pipe and also the five bits that
1:02:40
entered at time equals 1 that would be these bits right here they took a step they started to approach B so again
1:02:46
we're watching the bits move from A to B we're just doing so with taking snapshots every second so we're pausing
1:02:53
the movie okay so one more second elapses another set of five bits marches
1:02:59
in this set right here marches into the pipe and again the bits that were
1:03:05
already in the pipe take a step forward so what happens next I'm equals four they March again I'm equals 5 they
1:03:12
March again and notice nothing has arrived at B yet because we said the delay is 7 seconds so and we're still at
1:03:18
time equals 5 Seconds nothing has shown up yet okay time 6 something marches in
1:03:24
time seven bite marches in so at this point the pipe is full by the way so before it wasn't now it's full
1:03:30
that's something you can only really observe with these pipe diagrams another reason for drawing these but basically
1:03:35
remember earlier so I'm going to rewind a little bit remember how this one entered at time equals 1 and we said the
1:03:41
delay is seven so if these bits enter at time equals 1 and the delay is seven
1:03:46
well when when's it going to show up on the other side 1 + 7 is8 so we fast
1:03:51
forward back here let check it out at 10 equals 8 those bits show up at B they
1:03:56
exit the pipe B receives them and these bits they entered at time equals 2 right
1:04:02
behind the ones at time equals 1 so if these enter at time equals 2 and they have a delay of 7 Seconds they're going
1:04:08
to show up at 2 + 7 = 9 and there they are they show up at time equals 9 and
1:04:14
you kind of get the idea the next family arrives at time equals 10 and then 11
1:04:19
and 12 and so on and what we're seeing here is that for any given set of bits
1:04:25
they March into the pipe and 7 seconds later they March out on the other end so we basically just watch the bits travel
1:04:32
across the pipe from A to B and by using this picture we got the same answer of
1:04:37
17 seconds it was still 17 seconds from the start to the end you could have also gotten this by plugging it into the
1:04:43
formula or drawing the equivalent timing diagram like we did earlier this is the pipe diagram you draw a rectangle and
1:04:51
the rectangle has bits marching through it it's a little bit weird you have to
1:04:57
stare at it for a little bit and play with the animation a little bit to really get the hang of it but that's what it looks like and I've made this
1:05:05
animation for you to look at you can rewind you can fast forward whatever you want
1:05:11
okay and yes please watch this with animation if you watch this without animation it looks like complete trash
1:05:16
so this makes no sense but if you play with animation it looks great so do that
1:05:21
okay see it's so nice okay enough enough playing with this so uh that's how you view this diagram view with animations

## Slide 11: Pipe Diagrams
B
A
Bandwidth: 5 bps
Delay: 3s
t = 0s
t = 1s
t = 2s
t = 3s
t = 4s
t = 5s
t = 6s
t = 7s
t = 8s
t = 9s
t = 10s
t = 11s
t = 12s
t = 13s
(This diagram needs to be viewed with animation to make sense.)
Shorter propagation delay: Pipe length is shorter.
Notes: so just to convince yourself one more time here's an
1:08:12
example where the pipe length is shorter and so what you'll notice is that the bandwidth is the same still the same
1:08:18
height so what that means is that we can still only March in five bits at any given second that's why it says five
1:08:25
bits per second only five bits can March in but now that the delay is 3 seconds instead of seven the rectangle is
1:08:32
shorter or rather Slimmer less wide so what that means is that when this sequence of five bits
1:08:39
enters the stack we'll notice that at time one it enters and then one two 3
1:08:44
seconds later it shows up on the other side and for any one of these stacks of five let's pick one okay so let's look
1:08:50
at this one right here right now it's here right now it's about to enter the pipe it enters at six 7 8 and at time
1:08:57
equals 9 it exits the pipe let's look at this very last one it enters at time 10 11 12 13 is when it shows up and once
1:09:05
again the timing diagram would have given you the same answer took 13 seconds for this stack of bits this
1:09:12
total packet to travel across the pipe so this pipe represents uh link with the
1:09:18
same bandwidth but lower propagation DeLay So less wide
1:09:26
please view with animation

## Slide 12: Pipe Diagrams
B
A
Bandwidth: 10 bps
Delay: 3s
Higher bandwidth: Pipe height is taller.
t = 0s
t = 1s
(This diagram needs to be viewed with animation to make sense.)
t = 2s
t = 3s
t = 4s
t = 5s
t = 6s
t = 7s
t = 8s
B
A
Bandwidth: 10 bps
Delay: 7s
t = 0s
t = 1s
t = 2s
t = 3s
t = 4s
t = 5s
t = 6s
t = 7s
t = 8s
t = 9s
Notes: okay here's another example now I'm going to keep the propagation delay the same it's
1:09:31
still three so the width of this rectangle is the same but it is now taller because the band width is wider
1:09:37
and again if you think about the water example I've increased the width of the pipe you can now shove in more dots at
1:09:43
once so by making this taller it is now the case that I cannot I can March in not five but 10 dots per second so now
1:09:52
the dots are lined up in stacks of 10 and at any second 10 of them enter and that's allowed because this pipe is now
1:09:59
taller so at time equals 1 the stack of 10 enters but the delay is still three so you still have to count one two three
1:10:07
before that stack of 10 exits and same thing with this last set right here one two three before it exits I think I
1:10:14
count it wrong okay so it enters right there and then one two three it exits and I get a total propagation time of 8
1:10:21
seconds so that's another example of a pipe diagram again people really just
1:10:26
draw the rectangle but I really like Imagining the dots inside of the rectangle to remind myself why the
1:10:32
rectangle looks like this do with animations
1:10:40

## Slide 13: Pipe Diagrams
The pipe diagram shows the bits on the link at any given moment in time.
Height = bandwidth. How many bits we can put in the pipe per unit time.
Width = propagation delay. How long it takes for bits to travel through the pipe.
Area = bandwidth-delay product. How many bits can fit in the pipe (bits in flight on the link) at a given instant.
Examples:
  Long & thin pipe: satellite links → delay dominates, capacity small
  Short & fat pipe: LAN Ethernet → delay negligible, capacity huge
  Long & fat pipe: transoceanic fiber backbones → delay long, but capacity enormous
  Short & thin pipe: local low-rate links (serial bus, IoT, legacy modem) → delay tiny, but bandwidth the bottleneck
B
A
Bandwidth: 5 bps
Delay: 7s
Bandwidth
Propagation Delay
IMPORTANT
Notes: A long-distance satellite link: low bandwidth, long delay  long and thin pipe
A LAN ethernet link: high bandwidth, short delay  short and fat pipe
A Trans-continental fiber-optic link  long and fat pipe (millions of bits in flight)
in real life what they really care about is the
1:05:41
rectangle itself they want to draw this rectangle as a visual representation of
1:05:46
the pipe so that they can analyze what fits in the pipe at any given time and the way that they draw this pipe is or
1:05:53
sorry this pipe yeah H the way that they draw this pipe is based on the rectangle
1:05:58
and the rectangle is based on the two properties that we already talked about so they're going to draw this pipe using
1:06:05
the bandwidth to determine the height and remember we talked about this earlier the bandwidth tells us how many
1:06:11
bits we can fit in the pipe so the reason why I added this crazy animation is because I wanted to show you that if
1:06:17
you increase bandwidth what happens the rectangle gets taller and if the rectangle gets taller what happens it
1:06:24
means more of these bits can line up to enter the pipe at any given unit of time
1:06:30
that's why bandwidth represents the height of this rectangle so the thing that always confuses people is they say
1:06:36
why is bandwidth the height well one intuitive way of saying it is we talked about the water pipe the bandwidth tells
1:06:41
us how wide the pipe is another way of seeing it is if you look at this diagram it tells us that if the bandwidth is
1:06:48
increased it means that you can stack more of these dots which represent bits and more of the bits can enter at any
1:06:54
given time that is exactly what it means to have higher bandwidth that's why the height is determined by the
1:07:00
bandwidth and the width tells us the propagation delay again it's kind of like the water example the width tells
1:07:07
us how long the pipe is and how long it takes for a single drop of water to travel through the pipe but we can see
1:07:13
that through our little animation as well that if you make this rectangle longer these bits are going to have to
1:07:18
March for more time steps before they can exit on the other side and just like we saw earlier bandwidth times
1:07:25
propagation delay if you multiply these two terms together you get the area of this rectangle which is the capacity of
1:07:31
this pipe and again the animation shows us that this is indeed the capacity of the pipe the area of this rectangle
1:07:39
because the bigger this rectangle is whether you make it taller or wider the bigger this rectangle is the more dots
1:07:45
or bits you can fit into this pipe so hopefully with these dots I've convinced you that the pipe diagram is really just
1:07:53
a rectangle where the bandwidth is the height and the propagation delay is the width and the dots are really just there
1:07:59
for clarity but the rectangle is what people really care about when they draw
1:08:05
these and

## Slide 14: Pipe Diagrams – Packet Transmission Delay
Transmission Delay
Transmission Delay
The width of the packet in the pipe represents the transmission delay.
How long it takes to push all the bits onto the link.
Link capacity = Propagation Delay × Bandwidth
Packet size = Transmission Delay × Bandwidth
  For a packet of given size: higher bandwidth  shorter transmission delay (higher bandwidth = fatter pipe = more bits in pipe per unit time = narrower packet in pipe).
Bandwidth
Propagation Delay
Propagation Delay
Bandwidth
IMPORTANT
Notes: okay so this is the picture that I
1:14:21
really care about at the very end so ultimately when people draw these again they don't draw the dots but they will
1:14:28
draw things like this they'll draw a blue rectangle to represent the link and then they will draw these orange squares
1:14:34
that represent the packets themselves and so these are actually the same packets these are three packets each
1:14:41
packet is 20 dots these are also three packets each packet is also 20 dots or
1:14:47
20 bits but notice that because the link itself changed in particular the link
1:14:52
itself received more bandwidth so we're switching to will link with more bandwidth the packets got taller and
1:14:58
narrower they shifted their shape to fit in the new pipe and so something that I
1:15:04
think is really confusing to people when they see these diagrams is that wait a minute when I change the link that I'm
1:15:10
using the packets themselves also change shape and yes that's true they change shapes because they fit in the pipe in a
1:15:17
different way in particular more dots can be stacked and so they get taller
1:15:23
and they get narrower because it takes less time to send them through the pipe the other thing that I think is not
1:15:28
totally intuitive is the transmission delay is the width of the packet so the
1:15:34
width of this packet tells me the transmission delay that is how long does it take to shove this packet into the
1:15:40
pipe and what this picture is showing you is that if you increase the bandwidth now that they can March in t
1:15:46
instead of stacks of five the transmission delay got shorter and that's represented by the fact that the
1:15:51
packet got less wide I know I just said a lot of words at you
1:15:58
this will probably take a little bit of playing around with the demos and watching the animations to make sense if
1:16:03
the dots don't make sense I really just care about the shape of these rectangles but maybe they helped maybe they didn't
1:16:09
complain at me in the comments if you didn't like this but you can't say I didn't try I drew
1:16:15
all the diagrams any questions on this by the way it is kind of a funky topic when I
1:16:21
saw this I had for the first time I had no idea what the pipes look like when I drew the dots in they made a little bit more sense to me but maybe
1:16:28
not but the key idea I think is really confusing is really just the fact that transmission delay is actually the width
1:16:33
of the packet not immediately obvious and the fact that it gets uh shorter as the packet gets
1:16:40
taller okay an attempt was made but let me know on ad or elsewhere if you find
1:16:46
this confusing we can talk about it somewhere

## Slide 15: Overloaded Links
Links
Bandwidth and Propagation Delay
Pipe Diagrams
Overloaded Links
Lecture 3, Spring 2026
Notes: okay for the final topic of
1:16:52
today I want to briefly mention what happened when links themselves get overloaded so sometimes there's a lot of
1:16:59
data to send and the link just can't keep up because its bandwidth isn't enough or his propagation delay isn't enough sometimes the link just cannot
1:17:06
keep up that's something we have to deal with on the internet

## Slide 16: Packet Switching at Routers
Recall: Routers receive packets, and forward them toward their destinations.
For simplicity, consider 2 links with incoming traffic.
For simplicity, consider sending all outgoing traffic out of 1 link.
B1
Router
A1
A2
A3
A4
B2
B3
Notes: so let's talk about that so ultimately we talked about
1:17:13
routers roughly and we're going to talk about them a lot more in this class but at a very high level routers receive
1:17:19
packets and then pick a link to forward them closer to their destination the router says I can't reach the
1:17:25
destination but if I send it to my buddy over here they're going to get this packet closer to the destination for you
1:17:32
so routers ultimately receive packets from links and send them out of links so here's an example where the router has
1:17:37
two incoming links so for Simplicity we'll just assume these two links are being used to send traffic inwards in
1:17:44
reality links might be bidirectional here we're assuming these links are just used for inputting data and then we'll
1:17:50
assume it has just a single outgoing Link in other words this router is going to forward all the packets to the right
1:17:56
in reality there could be multiple outgoing links for now let's just assume one so let's see what happens as we go
1:18:03
through a time and these are pipe diagrams by the way you see these little rectangles they're packets and this
1:18:08
larger rectangle is the pipe itself so we're already using pipe diagrams which is kind of cool so this is a frozen
1:18:14
Moment In Time lots of packets are streaming into the router and the router's goal is to get them all out on
1:18:19
its only outgoing link that's the goal of this particular router so if I look at this type diagram

## Slide 17: Packet Switching at Routers
Recall: Routers receive packets, and forward them toward their destinations.
For simplicity, consider 2 links with incoming traffic.
For simplicity, consider sending all outgoing traffic out of 1 link.
Router
A1
A2
A3
A4
B2
B3
B1
Router
A2
A3
A4
B2
B3
B1
A1
Router
B2
A3
A4
B3
B1
A1
A2
Router
A3
A4
B3
B1
A1
A2
B2
Router
B3
A4
B1
A1
A2
B2
A3
Router
A4
B1
A1
A2
B2
A3
B3
Router
B1
A1
A2
B2
A3
B3
A4
Notes: B1 is the closest
1:18:26
to the router it's going to get there first and the router forwards it out of the link and all the other packets make
1:18:32
their way toward uh the router so they all move toward the router a little bit what comes next well packet A1 is about
1:18:39
to enter the router so at the next time step the router receives A1 sends it out out of the outgoing link and all the
1:18:45
other incoming packets take a step closer okay good and then D1 takes a
1:18:50
step over outwards toward its next top okay good at the next step A2 shows up
1:18:56
great and it gets sent out and then at the next step B2 enters and it gets sent
1:19:02
out A3 enters get sent out B3 and A4 worked out just line at every given time
1:19:08
step the router only had to process one packet and send it out so this router was not overloaded it was able to
1:19:14
successfully handle all of the packets from the incoming links with no problem so the traffic wasn't too heavy the
1:19:20
router was able to process and forward all of the packets and careful viewers might have noticed I think I messed up
1:19:26
this animation but pretend you didn't see it the important thing was just packets coming in and going
1:19:32
out I'll fix it later okay here's an example where the router was going to have some overload

## Slide 18: Transient Overload
What happens if two packets arrive at the router simultaneously?
Can't process both at the same time! Router must queue one for later.
When there are no incoming packets, router can drain the queue.
This is called transient overload, and it's fairly common.
Router
B1
A1
A2
A3
A4
B2
B3
Queued:
Notes: so take a look at
1:19:39
this picture the router has two packets arriving at the exact same time so in this pipe diagram Frozen in Time A1 and
1:19:47
B1 are both about to arrive at the router at the same time they're right there next to the router and on the next
1:19:53
time step they're both going to arrive well that's a problem because this router can't handle two packets at once
1:20:00
can only handle one packet at a time it looks at the packet thinks about where it needs to go forwards the packet so if
1:20:06
this router can only handle one packet at a time what happens if it suddenly gets two at once well it's a problem and
1:20:12
the solution is the router is going to keep a que and the que basically says here are some packets that I've received
1:20:18
but I have not processed so I'm going to save them for processing later and that's actually totally fine happens all
1:20:25
the time in the internet

## Slide 19: Transient Overload
What happens if two packets arrive at the router simultaneously?
Can't process both at the same time! Router must queue one for later.
When there are no incoming packets, router can drain the queue.
This is called transient overload, and it's fairly common.
Router
A1
Queued:
B1
A2
A3
A4
B2
B3
Notes: so what's going to happen is A1 and B1 both arrive we arbitrarily choose to send out A1 and
1:20:31
process it and B1 get stuck in the que how did I choose A1 over B1 open question we'll talk about it some other
1:20:37
day but for now assume that one of them was chosen and at the next time step uh oh we have some trouble A2 and B2 are
1:20:44
also arriving at the same time so the router is going to take both of them and
1:20:49
shove them in the que and in the queue they take B1 and process that one so so
1:20:55
again the exact way that the router figures out what to get queued and what to process is a bit beyond the scope for right for right now but the important
1:21:01
thing is that when packets arrive they first enter the que look A2 and B2 enter

## Slide 20: Transient Overload
What happens if two packets arrive at the router simultaneously?
Can't process both at the same time! Router must queue one for later.
When there are no incoming packets, router can drain the queue.
This is called transient overload, and it's fairly common.
Router
A1
B1
Queued:
B3
A3
A4
A2
B2
Notes: 1:21:07
the que and what was it B1 can get dced so B1 gets dced and gets sent out so
1:21:14
this happens over and over again um

## Slide 21: Transient Overload
What happens if two packets arrive at the router simultaneously?
Can't process both at the same time! Router must queue one for later.
When there are no incoming packets, router can drain the queue.
This is called transient overload, and it's fairly common.
Router
A3
A4
B3
Queued:
B2
A1
B1
A2
Notes: but at this time no packets enter so look
1:21:19
this pipe is empty this pipe is empty so because right now there's no traffic this is a great opportunity to clear out
1:21:25
our que so we clear out A2 we clear out B2 that's great and now A3 enters B3
1:21:30
enters A4 enters

## Slide 22: Transient Overload
What happens if two packets arrive at the router simultaneously?
Can't process both at the same time! Router must queue one for later.
When there are no incoming packets, router can drain the queue.
This is called transient overload, and it's fairly common.
Router
A3
A4
B3
A1
B1
A2
B2
Queued:

## Slide 23: Transient Overload
What happens if two packets arrive at the router simultaneously?
Can't process both at the same time! Router must queue one for later.
When there are no incoming packets, router can drain the queue.
This is called transient overload, and it's fairly common.
Router
B3
A4
A1
B1
A2
B2
A3
Queued:
Router
A4
A1
B1
A2
B2
A3
B3
Queued:
Router
A1
B1
A2
B2
A3
B3
A4
Queued:
Notes: that's called transient overload because temporarily the router
1:21:36
was overloaded and had too much to process but later the router used some downtime to finish training its que so
1:21:42
having a queue is totally fine it just means some of the packets have to wait

## Slide 24: Packet Switching at Routers
Persistent overload: Not enough capacity to handle the incoming packets!
Queue won't help us. If the queue fills up, the router must drop packets.
How do we solve persistent overload?
Operators can detect the overload and (manually) upgrade the link.
Routers can tell the senders to slow down (throttling).
Router
B1
A1
A2
A3
A4
A5
A6
A7
B2
B3
B4
B5
B6
B7
Uh oh...
Notes: but sometimes the router cannot handle
5:02
all the incoming load so if the two pipes that are incoming look like this well this router is doomed it's not
5:09
going to be able to handle all of these packets no matter how much it tries to
5:14
put packets in a queue it's just not going to have enough bandwidth to send out this many packets over a single link
5:22
so this router is in trouble the que is going to build up and build up and eventually the queue itself is going to
5:28
exceed some limit and become to full and at that point this router simply has to give up and it's going to start dropping
5:35
packets which means it receives a packet and just ignores it doesn't get forwarded the packet just gets lost and
5:42
stuff like this by the way is why we said that the internet has best effort at layer three it's because we design
5:48
routers like this and the way that we design routers which is that we allow them to drop packets in cases like this
5:55
is consistent with our design that we said routers only have to offer best effort service so it's a nice case of
6:02
the design matching the implementation because we said that the Internet only provides best effort well then this
6:08
router is allowed to drop packets if it can't handle them because the internet is best effort so you could have a que
6:16
but the que is not going to help you if you try drawing this out with a que the que itself is going to get packed and to
6:22
full and eventually some of these later packets are just going to get dropped so here we call this persistent overload
6:28
because it's not the case that the router temporarily had a little bit too much to do but later it was able to
6:34
clean out the queue this is the case where the queue is never getting clean we just don't have enough capacity this
6:40
router is just not powerful enough or doesn't have enough processing power doesn't have enough outgoing bandwidth
6:47
to process all the packets that are incoming so this is a problem of not enough capacity it's not a problem of a
6:54
temporary overload that gets solved this is a persistent problem that's why people call persistent overload so how
7:01
do you fix this turns out there's not really a great answer one possible answer is the router itself logs
7:09
somewhere for its operator the person operating this router hey I am not able to send out all the packets I have been
7:15
dropping a lot of things lately you might want to consider upgrading me to a better model give me some more
7:21
processing power connect me to some more links so that I can actually handle all the packets but that's a manual process
7:28
it's not something that the router can just automatically do routers don't upgrade themselves automatically someone
7:34
would actually have to come in and rewire this router or install a better one to handle this kind of load and
7:40
something else we'll see later in the semester is this router might actually be able to send a packet backwards to
7:46
the sender and tell the sender you are sending me too much you need to slow down because I can't handle this kind of
7:53
load and that's something we'll spend a lot of time on when we talk about congestion control but for now I just
7:59
wanted to get the point across that routers take in incoming packets they forward them sometimes there is
8:04
transient overload and sometimes there is persistent overload which we will try and solve a lot
8:12
later any thoughts on this stuff

## Slide 25: Life of a Packet
Life of a packet:
Sender puts payload in a packet, adding headers.
Packet travels along a link.
Packet arrives at a router. Router forwards packet to the next hop.
  Store-and-forward: A router can start forwarding a packet only after it has received all bytes of the packet.
  Packet might be queued or dropped.
Repeat the last step until:
  Packet reaches destination.
  Packet is dropped.
Notes: the packet must be fully received at each intermediate router before transmission on the next link starts

## Slide 26: Packet Queuing
How long does it take for your packet to travel through the network?
  Packet delay = Transmission Delay + Propagation Delay + Queuing Delay
  (There is also CPU processing delays, but they are typically very small and can be ignored. We focus on network delays only.)
It depends on…
  how much data you’re sending and the link speed → transmission delay
  your distance from the destination → propagation delay
  the traffic pattern → queuing delay
Notes: 8:18 Queues introduce extra delay.
okay so we actually have to go back now and revisit what a packet does when it
8:24
travels from its source to its destination because remember earlier we said that you send a packet the delay of
8:31
the packet comes from two sources one is the transmission delay that is how long does it take for all of the bits to
8:38
March into the pipe and the propagation delay is how long the pipe is how long does it take for the bits to travel
8:44
across the pipe but there's actually a third term that we've now introduced that we previous previously had not
8:51
thought of which is queuing delay because it could be the case that this packet travels multiple hops to its
8:58
destination and some of the intermediate routers trap the packet in a queue for some time before the packet can get
9:04
forwarded so that actually could introduce additional delay into the time
9:10
it takes to send a packet from a source to a destination so we already saw these
9:15
two terms those are in terms of the link that you have the bandwidth the propagation delay and now we have a
9:21
third term which is the queuing delay and that comes from routers that might have to put this packet in a que so in
9:28
total if you think about what does a packet do from the moment it's created to the moment it's received well the
9:34
sender is the one that creates the packet it wraps the packet around a bunch of headers like we've seen before
9:40
and then it sends the bits of the packet along a link and how long it takes to send the packet along the link depends
9:47
on those two terms eventually the packet arrives at a router and the router has
9:52
to forward the packet closer to its destination so the router says I'm not the Final Destination but the final
9:58
Destin is that way so send it that way so the router is going to forward the packet
10:04
and in doing so the packet might have to wait a little bit in the queue or if this router is totally overwhelmed maybe
10:12
that packet just gets dropped that's also an option and then this just repeats over and over again we get to
10:17
the next router there might be some queuing time the router might drop it and if it doesn't drop then that packet
10:24
gets forwarded to the next router that router cues it for a little bit maybe maybe drops the pack pet forwards it
10:30
again and this repeats over and over again until either the packet reaches its destination because all the routers
10:36
along the path correctly forwarded the packet or the packet got dropped along the way in which case it's not reaching
10:43
its destination the end host will have to do something about that so roughly speaking that is what a packet does from
10:50
the moment it's created to either the moment it drops or the moment it reaches its
10:57
destination any thoughts on this

## Slide 27: How do packet delay and loss occur?
Packets queue in router buffers, waiting for turn for transmission
queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 28: Packet delay: four sources
tq: queueing delay
time waiting at the output link for transmission
depends on congestion level of router
propagation
queueing
ttotal = tq + ttx + tprop
A
B
transmission
ttx: transmission delay:
L: packet length (bits)
B: link bandwidth (bps)
ttx = L/B
tprop: propagation delay:
d: distance of physical link
s: propagation speed
tprop = d/s
IMPORTANT
28
Notes: dproc: nodal processing
check bit errors
determine output linknodal processing
typically < microsecs

## Slide 29: Summary: Links
Packet Delay = (Packet Size / Bandwidth) + Propagation Delay + Queuing Delay
Routers experience transient overload if packets arrive simultaneously. Solution: Packets get queued for later.
Routers experience persistent overload if there's insufficient capacity. Queue gets full, and packets get dropped.
Transmission Delay
Bandwidth
Propagation Delay
Capacity = Delay × Bandwidth
Transmission Delay
Bandwidth: 1,000,000 bps
Delay: 0.001s
t = 0s
0.000001s
0.001001s
0.000800s
0.001800s
800-bit packet
Transmission Delay
Propagation Delay
Notes: Briefly summarize links we talked about this handy little formula
18:16
where we said the packet delay is the sum of the transmission delay that is how long it takes to send all the bits
18:22
across the wire plus the propagation delay how long it takes for a single bit to travel all the way from one end to
18:28
the other end plus the queuing delay in case packets have to wait at a Queue at an intermediate router or multiple
18:35
routers perhaps and we talked about two types of overload transient overload if a couple packets arrive at the same time
18:42
and we queue them and the queue drains or persistent overload where there's just not enough capacity to handle
18:47
everyone incoming and we also spend some time looking at two types of diagrams to help us analyze links we talked about
18:55
these timing diagrams where we draw time going down and and this allows us to check when a packet gets sent and
19:01
received and we also showed you the pipe diagram which shows uh the Link at a
19:07
frozen moment in time and from this you can actually derive some of the properties of the link itself such as
19:13
propagation delay transmission delay bandwidth so that's the summary of links
19:19
any final
19:26
questions