## Slide 1
CS 168, Spring 2026 @ UC Berkeley
Slides credit: Sylvia Ratnasamy, Rob Shakir, Peyrin Kao, Iuniana Oprescu
Link-State Protocols, IP Addressing
Lecture 6 (Routing 3)
4.1
4.2
4.3
4.4
4.5
4.6
Notes: Slides template credit: Josh Hug, Lisa Yan
0:07
okay in this lecture we get to continue our journey through routing this lecture is actually comprised of two separate
0:14
topics so the first half is all about something called link State protocols and then the second half we'll switch to
0:20
a different topic of Ip addressing so it's kind of a twart lecture

## Slide 2: Link-State Protocols
Link-State Protocols
Overview
Computing Paths
Learning Graph Topology
IP Addressing
Hierarchical Addressing
Assigning Addresses
Writing Addresses
Aggregating Routes
IPv6 Changes
Lecture 5.3, Spring 2026
Notes: so we will start with that first
0:27
half where we talk all about link State protocol

## Slide 3: Routing Protocols – Roadmap
Routing protocols can be classified by:
Where they operate. (Intra-domain or inter-domain.)
How they operate. (Distance-vector, link-state, or path-vector.)
Today, we'll look at link-state protocols.
Very common as an Interior Gateway Protocol.
Major examples:
  IS-IS (Intermediate System to Intermediate System).
  OSPF (Open Shortest Path First).
 | Intra-domain (Interior Gateway Protocol) | Inter-domain (Exterior Gateway Protocol)
Distance-vector | RIP | –
Link-state | IS-IS, OSPF | –
Path-vector | – | BGP
Notes: so as a reminder there are lots of
0:32
different routing protocols out there the one we just saw was the distance Vector protocol and real life has a name
0:38
the routing information protocol so that's what we have written in this box
0:44
and today we'll be looking at a different set of protocols
and remember that if you have a routing protocol we
0:51
can classify it in one of two ways one way to classify it as where they operate do they operate within one network or
0:59
across different networks so we're still going to look at intradomain routing protocols that is protocols that work
1:06
inside a network today so we will not be going outside of the network until next time and the second classification we
1:13
can think of is how they operate what style of operation do they do to
1:19
exchange routes between routers last time we saw the distance Vector protocol this time we'll see some link State
1:25
protocols so we are in this box right here on the grid link state is how the protocol operates inter domain is where
1:32
it is operating these Protocols are often used as interior Gateway protocols for intra domain protocols for reasons
1:40
that we'll see soon as a spoiler it doesn't scale very well so it works best inside a specific domain and there are
1:48
two major examples in real life so we'll show you the conceptual version and it's implemented in one of these to actual
1:54
real life protocols

## Slide 4: Link-State Protocols: Definition
Link-state protocols:
Every router learns the full network graph.
Then, each router runs a shortest-path algorithm on the graph to populate the forwarding table.
Distance-vector:
Local data: Each node only knows about part of the network.
Global (distributed) computation: Each node computes part of the solution, working with other nodes.
Link-state:
Global data: Each node knows about the full network graph.
Local computation: Each node computes the full solution by itself.
How do routers learn this?
What algorithm do we run?
Notes: so the link State protocols
2:00
actually relatively simple compared to its cousin the distance Vector protocol there's only two things you have to do
2:06
step one it's step two and you're done so the first step is have every router
2:11
learn the entire network graph this is different from distance Vector you're going to give every router a global
2:18
picture of what the network looks like and how you do that is an open question that will solve coming up and once every
2:25
router has the whole network graph in front of them they can just run their favorite shortest path algorithm to
2:31
populate the forwarding table if you know everything there is to know about the network you can just run your favorite shortest paths algorithm and
2:38
that will give you pass through the network so it's just two steps and we'll break them down coming up but before we
2:44
do I want to contrast distance vector and Link State protocols so in distance
2:49
Vector everyone had a little piece of the solution remember how each router didn't know the entire state of the
2:55
network they only knew advertisements coming in from their neighbors and that's all that they could use to build
3:01
their forwarding table so everyone only had little pieces of information about the network in link State protocols
3:07
we're instead going to give every node Global Information every router is going to know everything there is to know
3:13
about the network graph the other thing we can contrast is distance Vector ends
3:18
up Computing things globally and the way I think of that is every node confuses a
3:24
little piece of the solution and if you take everyone solution and put it all together you get a full solution to the
routing protocol so each person contributes a fraction and if you put it
3:35
together you get the whole by contrast in link State protocols each node will
3:41
compute the full Solution by itself so it's a little bit redundant but
3:46
everyone's going to get a copy of the full solution so that's the key difference distance Vector everyone has
3:51
little pieces that form a whole solution and Link State everyone has all the information and computes the entire
3:58
solution by themselves so with this High Lev picture we just have to solve the
4:04
questions of how to do step one how to do step two and that's it to this protocol

## Slide 5: Global Data
Suppose R3 has learned the full network graph.
We know all the links, their status (up or down?), and their costs.
We know about all the destinations.
R3 can run a graph algorithm to compute paths.
We can populate the forwarding table with the next-hop (in the computed path).
R3
R2
R1
R5
R4
1
1
1
7
2
1
10
A
B
1
R3's Table | 
Destination | Next Hop
A | R2
... | ...
How do routers learn this?
What algorithm do we run?
Notes: econd one then we'll Circle back to the first one so
4:16
let's say somehow magically R3 has learned the entire network graph so that
4:22
means that you know all the links you know all the routers and who is up who is down you know all of their costs you
4:28
know all the hosts and their destinations and if that's the case then all you have to do is run a graph
4:34
algorithm like lra's algorithm or the bman for algorithm and that lets you
4:39
compute paths through the network so I guess this is an example of Link state in action so the first step is R3
4:46
somehow learns everything there is to know about this network and now that it knows the full picture that you and I
4:51
can see it can just run its favorite shortest paths algorithm dyra algorithm whatever else you like and it will
4:58
compute that the shortest path to a is this one in blue and if this is the shortest path to a that means that my
5:04
next top must be R2 because that's the next top along the shortest path that I
5:10
computed so these are the two steps step one step two and we have to answer these two questions and we are done

## Slide 6: Computing Paths
Link-State Protocols
Overview
Computing Paths
Learning Graph Topology
Lecture 5.3, Spring 2026
Notes: so we have two things to solve and they're actually conveniently right there one is Computing paths and
6:03
the second is learning graph topology so let's take care of both of them

## Slide 7: Link-State Algorithms
What graph algorithm do we run to compute paths?
Any single source shortest-path algorithm will work.
Need to find shortest paths from a single source (the router) to every host.
Some possible choices:
Bellman-Ford (the original serial version).
Dijkstra's algorithm.
Breadth-first search.
Dynamic shortest path.
Approximate shortest path.
Parallel single-source shortest path.
Notes: the first question is what graph algorithm
6:09
do you use and it turns out you have a lot of choices you just need some shortest path algorithm that allows you
6:15
to find all the paths from you the router to all the other hosts that are out there and you have all these
6:21
different choices you could use the original version of bellman Ford you don't have to do all the Distributing
6:26
that we did last time you can just use the Bellman Ford that you learn from any data structor class you could use D for
6:33
algorithm breadth for search any variation of a shortest paths algorithm it's really up to you what you want to
6:39
use any of these would work just fine

## Slide 8: Ensuring Consistency
Each router can only influence its next hop.
No guarantee that routers compute the same paths!
We have to ensure that every router is using a "compatible" approach.
R3
R2
R1
R5
R4
A
B
R3
R2
R1
R5
R4
A
B
R2 forwards to R3.
R3 forwards to R2.
Notes: one thing to notice though is even
6:45
though you compute the entire path to the host that is R3 with the full
6:51
picture of the network it computes the entire blue path you cannot influence what other routers do so even though you
6:58
compute this blue path you can't go to R1 and say hey your next top should be this link in blue it doesn't know you're
7:04
only responsible for your own forwarding table so even though you went through all the work of computing this blue path
7:11
the only piece of information that goes into your forwarding table is just my next top to a is R2 that's it you don't
7:19
need to store anything else you don't need to store the rest of the path you don't need to care about what R5 does
7:25
with the packet so even though you've done all the work of calculating the path the only part of the answer you
7:30
need and you can throw the rest away it's just the next top that's the only thing you as R3 have control over you
7:37
don't have control over what happens after R2 gets the packet and this
7:43
actually opens up a problem and the problem is that different routers might compute different paths so check out
7:49
this example where R3 armed with all the information about the network computes this blue path throws away all the
7:56
unnecessary information and just writes down that packets for a should be forwarded via
8:02
R2 and by contrast here we have R2 which also has a full picture of the network
8:08
and it also calculates path through the network and somehow it calculates that this red path is the shortest path to a
8:14
and it throws away the unnecessary information and just writes down that my next hop to a is
8:20
R3 wait a minute R3 is forwarding packets to R2 R2 is forwarding packets to R3 they have formed a routing Loop so
8:28
if we are not careful and different routers are being incompatible in some way it's possible
8:34
that link State protocols introduce unwanted routing Loops like we see here so somehow we need to make sure all the
8:41
routers are thinking about the same thing so that we avoid scenarios like
8:47
this

## Slide 9: Ensuring Consistency
Requirements for routers to produce valid, compatible decisions:
Everyone agrees on the network topology.
Everyone is minimizing the same cost metric.
All costs are positive.
All routers use the same tie-breaking rules.
Routers don't necessarily need to use the same shortest-path algorithm, as long as they follow these rules.
In practice, easier to have everyone use the same algorithm.
Notes: so it turns out these four properties will allow routers to produce
8:53
valid compatible decisions which basically means everyone is Computing shortest paths and you don't provide
8:59
Loops or dead ends or other unwanted things so here are some things that you
9:04
need in order for that to be true one is everyone had better agree on what the network looks like if somehow router a
9:11
or router R1 has a different picture of the network than router R2 there's a link that R1 knows about but R2 doesn't
9:17
know about well that's a problem now they're going to compute different paths because they're using different input
9:22
graphs and that could cause routing Loops dead ends other things you don't want something else that hopefully is
9:28
true is that everyone is minimizing the same cost metric it'd be really bad if one of these links had cost five From
9:34
r3's perspective but from r2's perspective this link costs seven then they could have scenarios like this
9:40
where they compute different paths through the network as usual we want all costs to be positive because we don't
9:46
want loops and in case you're scared about ties you just have to make sure that everyone breaks ties the same not
9:52
something that's the most important here but you can imagine some edge cases where if you break ties one way and I
9:58
break ties other way we might create loops and that's not so good so it turns
10:04
out as long as you follow these rules and you make sure that all the routers are compatible in some way it's
10:09
technically okay if everyone uses slightly different algorithms for example if you use Spellman for I use
10:16
dkas we're probably going to get the same answer as long as we're using the same graph the same costs and so on and
10:22
so forth so it's probably okay if we use different algorithms but in practice it's just way easier to have all the
10:28
routers use the same algorithm so we don't have to worry about inconsistencies between various
10:34
algorithms so you can imagine if you're programming routers you would just put the same code in all the routers so

## Slide 10: Learning Graph Topology
Link-State Protocols
Overview
Computing Paths
Learning Graph Topology
IP Addressing
Hierarchical Addressing
Assigning Addresses
Writing Addresses
Aggregating Routes
IPv6 Changes
Lecture 5.3, Spring 2026
Notes: 10:40
everyone's running the exact same copy of dyra algorithm and that makes it easier for all the routers to be
10:46
compatible with each other well that's it we finished step
10:52
one now we know how to compute paths to the network use any favorite shortest paths algorithm subject to certain
10:58
compatibility constraints so the second thing we have to do is we need to let every router know about the full Network
11:05
graph

## Slide 11: Steps of Learning Network Graph
Link-state protocols:
Every router learns the full network graph.
  Step 1A: Discover my neighbors.
  Step 1B: Tell everybody about my neighbors.
Then, each router runs a shortest-path algorithm on the graph to populate the forwarding table.
How do routers learn this?
Notes: so how do we do that that's step one here I've actually broken it down into two substeps one is you should
11:12
figure out who your neighbors are and then you should tell everyone else about your neighbors

## Slide 12: Steps of Learning Network Graph (1/2) – Learn Neighbors
How do we discover who is adjacent to us and their identity? Say hello!
Routers periodically send hello messages to their neighbors.
If they stop saying hello, assume that they disappeared.
This helps us learn about our direct neighbors, but not the whole network.
  R1 does not know about the rest of the network (e.g. R3).
R1
R2
R3
Hello, I'm R2.
Hello, I'm R2.
Hello, I'm R1.
Hello, I'm R3.
My neighbor is R2.
My neighbor is R2.
My neighbors are R1 and R3.
Notes: so let's see that in action and remember the ultimate goal is
11:19
for routers R1 R2 and R3 to learn about the full topology they want the picture
11:24
that we are seeing namely that they are connected in a chain so the first thing you should do is figure out who you are
11:30
directly connected to who's to my left who's to my right who are all the people who are one link away from me and that's
11:37
not so bad if you want to know who your neighbor is you just walk up to them and say hello that's the intuition so let's
11:43
do that R1 wakes up and it see it has one outgoing link that way so it's going
11:49
to send a hello packet that way don't know where it's going but we'll just say hello I'm R1 send along this particular
11:54
port and it'll eventually reach R2 R2 will also do the same thing it has two
12:00
links connected to it so it will send hello I am R2 out of both of those links
12:05
and then R3 will send hello I'm R3 out of its one and only link and if I finish this job and everyone exchanges H then
12:13
R1 now knows my neighbors R2 because I received a hello from R2 R2 knows that
12:18
its neighbors are R1 and R3 because it received hellos from R1 and R3 and R3
12:24
knows that his neighbor is R2 because it received a hello from R2 so it works pretty much like you'd expect and one
12:30
thing we do have to watch out for just like in distance Vector this is a best effort Network things can get dropped
12:37
and people can leave the network because topologies can change and we fix all of that using the same little trick we did
12:43
earlier which is the periodically send these hellos so send the same packet every five seconds if someone stopped
12:51
saying hello they probably left so that's our super simple way to guarantee
12:56
reliability and adapt to changing Networks one thing to notice though this helps
13:01
you learn your direct neighbors it does not help you learn indirect neighbors so for example R1 at this point it knows
13:08
that its neighbor is R2 but it does not know about people further in the network like R3 so we haven't solved that
13:14
problem yet but we'll do next

## Slide 13: Steps of Learning Network Graph (2/2) – Propagate Neighbor Information
How do we learn about the rest of the network, beyond our neighbors?
Solution: Flood information across the network.
When local information changes, send it to everyone.
When you receive information from your neighbor, send it to everyone.
R1
R1 and R2 are neighbors. Tell everyone!
R1 and R2 are neighbors. Tell everyone!
R2
R1 and R2 are neighbors. Tell everyone!
R3
Notes: so now let's do the Second Step the second step is to tell everyone else about your neighbor
13:29
relationships and the way that you'll do this is you'll Flood information across the network so you have a piece of
13:35
information that you care about namely that R1 and R2 are neighbors here's R1 here's R2 we are neighbors we learned
13:42
that from the previous step and since this is a useful piece of information that we want everybody to know remember
13:48
the ultimate goal is to get everyone a full picture of the network this is information that everyone wants to know
13:54
so what we do is we just flood it out of every link that we have I hypthetically if R1 had a bunch of links what it would
14:01
do is it would send this exact packet out of every single link tell the world that R1 and R2 are neighbors and if R2
14:08
hears the same thing it will also blast this information to everyone and if R3 hears this information it will also
14:14
blast it to everyone so by having this information propagate through the network anytime you hear a piece of
14:19
information that says please tell everyone this fact you send it to everyone you know all of your direct
14:25
neighbors if you repeat this enough times this piece of information should spread to everybody across the network
14:31
and that's sometimes called flooding so this one also works kind of like you'd expect any neighborly relationship that
14:38
you know about you your neighbor and you two are neighbors that's information that you want to tell everyone so you
14:44
flooded across the network and if everybody does this hopefully you end up learning all of the neighbor
14:50
relationships and that allows you to reconstruct the full Network graph

## Slide 14: Avoiding Infinite Flooding
Flooding: When you receive an update, send it to everybody.
We have to be careful of the same update being sent repeatedly.
R1
R2
R5 and R9 are neighbors.
R5 and R9 are neighbors.
R5 and R9 are neighbors.
R5 and R9 are neighbors.
R5 and R9 are neighbors.
Notes: there is one we have to be really careful about and that's avoiding infinite flooding so let's take a look
15:04
at an example where flooding can go wrong so let's say R1 and R2 both have some piece of information it's from
15:10
somewhere else in the network I haven't shown where it's from but let's say that R1 knows that R5 and R9 are neighbors
15:16
that's a fact that everyone should know so R1 receives this information and sends it to everyone that is directly
15:23
connected to which includes R2 and R2 hears this information and says that's a piece of information that everyone
15:29
should know so I will also blast it out to all of my neighbors and then R1 gets this and blast it out to all of his
15:36
neighbors and r two gets it and blast it to all of his neighbors do you see the problem here this packet is going to get
15:41
forwarded back and forth between them forever and that's going to waste a lot of bandwidth and it's very pointless
15:48
given that they both know this information already so we have to avoid a problem like this and sometimes they
15:54
call it infinite flooding

## Slide 15: Avoiding Infinite Flooding
Amplification: When there's a loop, copies of the same message get multiplied.
R1
R2
R3
Notes: Does this animation make any sense or am I just hallucinating?
actually infinite flooding gets even worse if
16:43
there's a loop so this SL is a little bit hard to follow but it the idea hopefully is clear so let's say that R1
16:50
has a piece of information that it wants to tell everyone so it sends it to all of its neighbors R2 and R3 at this point
16:56
R2 has the information and must flood it R3 has the information and must flood so what does R2 do it floods it to both of
17:03
its neighbors what does R3 do it also floods it to both of its neighbors so if
17:08
you stare at this a little bit carefully what happened on this next time step is R1 got that message twice R2 and R3 R2
17:16
got the message from R3 R3 got the message from R2 so everyone has a copy of this message and they have to send it
17:23
out further so R1 got the message twice so it needs to blast it out once twice
17:28
R2 got the message once so it has to blast it at once R3 got the message once so it has to flood it once this is going
17:35
to blow up very quickly so now at this point from this green time step we can
17:40
see that R1 received the packet twice R2 received the packet once twice three
17:46
times and R3 received the packet once twice three times so if you receive
17:51
three of those packets you got to send it out three different times at least according to the protocol we've seen so far when you receive a piece of
17:57
information send it to all your neighbors so R1 sends out two copies R2
18:03
sends out three copies R3 sends out three copies this is blowing up very
18:08
quickly so when you have a loop in the topology like this what actually happens
18:14
is the packet gets Amplified one copy gets two copies which then blows up to
18:19
four copies and so on and so forth

## Slide 16: Avoiding Infinite Flooding
Amplification: When there's a loop, copies of the same message get multiplied.
R1
R2
R3
R1
R3
R1
R2
R2
R3
R1
R2
R2
R3
R1
R3
R1
R2
R1
R3
R1
R2
R2
R3
R2
R3
R2
R3
R1
R3
This edge means, R1 sends the message to R2.
Then, R2 sends it to R1, and so on.
R1
R3
Notes: if this picture doesn't make sense I tried to draw a different one so let me know
18:26
if this is better here's a picture where r one has the packet and it sends it to R2 and R3 so just for this slide only
18:33
I'm using links in a slightly different way this uh line means that R1 sent the
18:39
message to R2 it's not that R1 has a link to R2 although it does this is just R1 sending the packet to its neighbor so
18:46
then what does R2 do R2 sends the packet to R1 and R3 and R3 receives the packet sends it to R1 and R2 again this tree is
18:53
not a network it's just showing you who sends packets to whom so R3 sends a packet to one of two R2 sends a packet
19:00
to one and three when R1 receives the packet it sends to its neighbors when R3 sends it receives the packet it sends to
19:06
its neighbors when R1 receives the packet it sends to its neighbors when R2 receives the packet it sends to its
19:11
neighbors and this goes on for a very long time and you can see a single advertisement blowing up as it gets
19:18
forwarded around in a loop because of this amplification problem
19:27
does so

## Slide 17: Avoiding Infinite Flooding
Problem: Naive solution (send to all neighbors) causes amplification.
Solution:
When local information (about yourself) changes, send it to all neighbors.
When you receive a packet from a neighbor, send it to all neighbors...
...unless you've already seen the packet before.
To identify packets you've seen before, add a timestamp.
Or some other unique identifier, e.g. strictly increasing sequence numbers.
✓ Seen it.
✓ Seen it.
✓ Seen it.
R1
R2
R3
Notes: so the solution to this amplification and infinite flooding problem is to not send packets if you've
19:35
seen them before so if you receive a packet twice you should flood it the first time but don't flood it the second
19:42
time so that's that's all we got to do and if you go back to the loop topology and we try the same amplification trick
19:49
it's not going to work anymore if we only send a packet once so R1 has an
19:55
advertisement and it remembers I've seen this before now it sends out the advertisement to R2 and R3 R2 now has
20:01
seen it so it checks off the fact that it's seen this advertisement before and sends a copy to R1 and R3 and then R3
20:09
receives the advertisement from R1 says yeah I've seen it before and sends it to R1 nr2 and at this point because
20:16
everyone has seen it before they are not going to resend the advertisement again so all you have to do is just keep track
20:22
of advertisements that you have seen before if you've already seen them do not resend them because you will end up
20:28
doing infinite flooding and how do you keep track of packets that you've seen before you have to add some sort of
20:34
unique identifier for example maybe add a Tim stamp in the advertisements and say R2 and R3 are neighbors this message
20:42
was sent at this particular time and if you see that exact same message with the exact same timestamp don't send it a
20:49
second time or you can use sequence numbers or something else that uniquely identifies the
20:55
packets

## Slide 18: Ensuring Reliability
The network is still best-effort. Updates could get dropped.
Recall: We need all routers to agree on topology, or else paths might be invalid.
Solution: Periodically re-send the update.
Notes: a couple more things we need to fix about link State before we're all done so we have avoided the infinite Loop problem uh and the infinite
21:37
advertisement problem one more thing we need to fix is that the network is best effort and updates can get dropped and
21:44
that would be bad because if updates get dropped people have different views of the topology and the paths might be
21:50
invalid so to fix this we play our usual trick of periodically resending advertisements one thing to note by the
21:57
way the checking of duplicate advertisements this avoids infinite flooding where a single advertisement
22:04
gets flooded forever but periodically you do have to reflood it so infinite
22:10
advertisements means that without any sort of time constraint you're just flooding this thing as fast as you possibly can creating tons and tons of
22:17
copies and adding a time stamp solves that but even with the time stamp you
22:22
still have to resend the update every five seconds or so so for example you might have an advertisement that says R5
22:29
and R9 are neighbors written at 6:30 pm and that gets flooded out and no one ref
22:35
floods it avoiding infinite looping but then at 6:35 five minutes later you have to restate that R5 and R9 are neighbors
22:42
you send that out that gets flooded all over again but you don't want to infinite flood any of them so no
22:48
individual advertisement should get Amplified and infinite looped or infinite advertised but you still have
22:56
to periodically resend them every couple of minutes

## Slide 19: Ensuring Convergence
The network could change. What happens if a link goes down?
Wait for routers to detect the failure.
Wait to flood new information.
Wait to recompute paths.
While waiting for convergence, the routing state might be invalid.
Dead ends and loops. Packets using longer routes.
Link is down, but R1 doesn't know!
R1 forwards to R3.
R3 knows about the link failure!
R3 forwards to R1.
R2
R1
R3
A
R2
R1
A
R3
Notes: 23:02
we'll quickly talk about convergence because remember that the network topology can change links can go down
23:09
new hosts can join they can leave and this can actually cause routes to temporarily be invalid it's kind of
23:15
similar to what you saw on the distance Vector protocol when something changes about the network the routing state
23:21
becomes invalid and we have to wait a little bit for the routing to converge again to a new valid state so when
23:27
something breaks everyone has to take some time to adjust to the failure and only after everyone
23:33
adjusts do we arrive at a new steady state and a new valid routing State and
23:38
that exact same pattern happens in link State protocols so for example let's say that the a to R3 link goes down and
23:46
let's say R3 knows about it but at this point R1 doesn't know about it yet maybe r1's further away and it hasn't heard
23:52
about the link going down yet so r1's picture is that all four links are valid
23:57
and in that case if it needs to compute the shortest path to a it might perhaps compute R1 R3 a the path in blue so
24:05
we'll forward packets to R3 by contrast R3 knows that the link has gone down
24:10
because it knows about that fact so it will instead using its full information
24:16
about the network compute this path in red and its next top will be R1 and we are once again in a loop R1 sends
24:23
packets to R3 R3 sends packets to R1 this will eventually get fixed once the
24:29
information about this dead link propagates to everyone else but for now it is not fixed and we have a routing
24:35
Loop until everyone reestablishes agreement of what the network graph looks like so this can happen sometimes
24:42
just like in the distance Vector protocol and we have to deal with
24:48
it so

## Slide 20: Link-State vs. Distance-Vector
Link-state is relatively simple. All the complexity is in the details!
Everyone floods link/destination information.
Everyone has a global map of the network.
Everyone independently computes next-hops.
Why might we want to use link-state over distance-vector?
Link-state gives routers more control over the path they choose.
  Distance-vector: We have to trust what our neighbor says, and we don't know the path they're using.
Link-state might be better at converging.
  Distance-vector: Wait for neighbor to recompute and re-advertise path.
  Link-state: Flood information before recomputing.
Real networks often use a combination of path/distance-vector and link-state.
Notes: so to quickly summarize link State versus dist inspector link State I would
24:53
say is probably the simpler of the two protocols if you think about how long it took us to explain one distance Vector
24:59
took like two hours to explain link state has taken 25 minutes in counting
25:05
so I think it's somewhat simpler there are some details though to make sure that it actually works and that you
25:11
don't run into bugs like infinite advertisements but at a very high level everyone floods the information that
25:17
they receive this gives everyone a global map of the network and everyone independently runs their own shortest
25:24
path algorithm to compute the next tops and to compare which which one is better
25:29
which one you might want to use here are some reasons why you might want to choose one over the other so one thing
25:35
that's nice about link state is that routers have a bit of control over the path that they choose so for example if
25:42
you really dislike R2 for some reason not sure why you would but if R1 thinks
25:47
I really hate R2 it can just send packets using R3 because it has a full picture of the network by contrast in
25:55
distance Vector you have to trust what your neighbor says if your neighbor says I can reach with path two but I can
26:01
reach a with cost two you have to trust what they say maybe they have a bug that
26:06
gets introduced and now you're stuck using incorrect information you don't know what path they're using so link
26:12
State because you have a global picture of the network you get a little bit more control over what path you want to
26:19
choose and compare with distance Vector where you receive advertisements from your neighbors you're not sure if
26:24
they're accurate or not you're not sure exactly what happens to the packet after the next top you just have to trust what
26:30
they say and pick whatever you think is best and arguably this one is kind of
26:35
debatable and depends on your network topology there are some cases where links made is a little bit better at
26:40
converging and the idea would be that in distance Vector the propagation involves computation at every single step so you
26:48
propagate information that a link has gone down you send poison and you have to wait a little bit for everyone to
26:54
compute and update their forwarding tables with a new poison and then they send out that that poison we have to
26:59
wait a little bit for all those routers to accept the poison change their forwarding tables and send out more
27:05
poison so there's a bit of computation and depending on how slow your routers are maybe that computation slows down
27:12
the propagation and by contrast in link State when something goes down that information can propagate faster because
27:18
you just say links down and the next router says oh links down let me tell my friends links down and they receive
27:26
links down message and they tell their friends so forth so they don't have to stop and compute things before they tell their neighbors
27:32
again not always true kind of depends on how fast your routers are at Computing New Paths but under certain assumptions
27:38
it could be the case that link state is a little bit more efficient in real life which do people use turns out it's often
27:45
a mixture of both some networks use one some networks use the other there are some protocols that sort of sit in the
27:50
middle between these two that you can use so you have a bit of a choice