## Slide 1: IP Addressing
IP Addressing
Hierarchical Addressing
Assigning Addresses
Writing Addresses
Aggregating Routes
IPv6 Changes
Lecture 6, Spring 2026
Notes: so we will start with that firstLink-state is relatively simple. All the complexity is in the details!
Everyone floods link/destination information.
Everyone has a global map of the network.
Everyone independently computes next-hops.
Why might we want to use link-state over distance-vector?
Link-state gives routers more control over the path they choose.
  Distance-vector: We have to trust what our neighbor says, and we don't know the path they're using.
Link-state might be better at converging.
  Distance-vector: Wait for neighbor to recompute and re-advertise path.
  Link-state: Flood information before recomputing.
Real networks often use a combination of path/distance-vector and link-state.
0:27
half where we talk all about link State protocol

## Slide 2: Hierarchical Addressing
IP Addressing
Hierarchical Addressing
Assigning Addresses
Writing Addresses
Aggregating Routes
IPv6 Changes
Lecture 6, Spring 2026
Notes: that's the end of link if I can
27:57
take questions
Then we’ll take a short break before moving on to the second part of lecture
okay uh let's go into the second half of today's topics and this is all
28:33
about IP addressing

## Slide 3: Scaling Routing
Can we really scale routing and forwarding to every host on the Internet?
Distance-vector: How many routing calculations does each router do?
Link-state: Can we really store the entire network graph in every router?
How long does it take to re-converge?
The secret to scaling routing is how we do addressing.
R3's Table | 
Destination | Port
A | 0
B | 1
C | 1
D | 2
... | ...
One entry for every possible destination.
The trick: Use more informative names than A, B, C, D for destinations.
Disclaimer: Today is about IP (Layer 3) addresses. Other layers use different addressing systems.
Notes: so to motivate why we are doing this talking about
28:39
addressing let's think about the two protocols we've seen so far distance vector and linking and a question that
28:45
you have probably had as you've been watching this is how do you actually scale this stuff up to the entire
28:52
internet imagine trying to use Link State on the entire internet that's not going to be very fun
28:58
because how many calculations do you have to do you're receiving advertisements from your neighbors for every single destination on the internet
29:06
that's probably not going to be feasible and likewise link State scaling is even
29:11
worse you have to throw the entire network graph and that means that your computer has to store a list of all the
29:17
routers and all the hosts on the internet and all the links that's not happening either and imagine trying to
29:24
reconverge routes when we try to scale these protocols up if there's a link failure somewhere that has to propagate
29:30
outwards and outwards across the entire world who knows how long that's going to take so hopefully we can already see
29:36
that both of these protocols scale pretty poorly and if we actually try to implement these protocols at a global
29:43
level it would just not happen you can also see why this is annoying because if you look at the
29:49
table it has one entry per destination and if you have one destination or one
29:56
entry for every destination in the entire world this table is going to be billions of entries long there's no way
30:03
you're storing that and constantly keeping it updated so we need to fix
30:08
this and it turns out that the trick to actually make routing a scalable process
30:14
is the way that we assign these addresses so right now and so far we've been showing these destinations as a b c
30:21
d but it turns out if instead of ABCD you pick more informative names about
30:27
these destination and where they are you actually might be able to scale routing up more efficiently so by uncovering the
30:35
secrets behind why these are labeled ABCD and what they're really labeled in real life we just might be able to make
30:42
our routing protocols scale better and this is going to be useful because even though distance vector and Link State
30:48
work in local networks when we talk about bgp which works across many networks we are going to have to rely a
30:54
lot on this trick to help us scale routing up o we're seeing it now it can be applied to any protocol you want but
31:01
it's extremely useful when we talk about bgp because that's the one that connects the entire world together

## Slide 4: Hierarchical Addressing – Conceptual
Recall: The Internet is a network of networks.
Leads naturally to a hierarchy of addresses.
Each network gets a number. Then, each host gets a number inside the network.
4.1
4.2
4.3
4.4
4.5
4.6
2.5
2.4
2.6
2.7
2.1
2.2
2.3
1.1
1.2
3.1
3.2
3.3
Network 2
Network 1
Network 3
Network 4
Notes: so the key here is to remember that the internet is a network of networks
31:16
remember each network has its own internal routing protocol its own settings whatever and then each Network
31:22
connects to each other to form this big network of networks so if that's the case this this actually already gives us
31:29
a very intuitive way to assign names to each of these end hosts so far we've
31:35
just been saying a CDE e FG but that didn't really tell us anything about host and where they are so maybe
31:42
something more intelligent to do is what if I gave each of these networks a number your network one your two and
31:48
your three and your four and now what I can do is inside of network one instead of calling these A and B or some
31:55
arbitrary number what if I called them 1.1 and 1.2 and the first one represents
32:02
the fact that they are in network one and network two gets numbers 2.1 2.2 2.3
32:09
all the way to 2.7 and maybe you see where this is going Network Three gets
32:14
addresses that start with three and network four gets addresses that start with four that seems like a pretty
32:20
natural way to assign numbers to these hosts so this is kind of what we're going to do but at a more at a bigger
32:28
scale so let's do it

## Slide 5: Hierarchical Addressing – Conceptual
R9 can summarize all hosts in another network with a single table entry.
Huge scaling improvement! Tables are smaller now.
4.1
4.2
4.3
4.4
4.5
4.6
2.5
2.4
2.6
2.7
2.1
2.2
2.3
1.1
1.2
3.1
3.2
3.3
Network 2
Network 1
Network 3
Network 4
R8
R9
R6
R9's Table | 
Destination | Next Hop
1.* | R6
3.* | R6
4.* | R8
... | ...
Notes: so why is this useful by the way this is useful because
32:33
it allows us to summarize table entries so instead of having one table entry for
32:39
every single router or and every single end host sorry that you see on this graph we can actually summarize some
32:46
information so for example let's say you are R9 if we are doing this naively
32:51
you'd have to have an entry for 1.1 and 1.2 and 4.1 and 4.2 and 4.3 and 4. 4 4.5
32:58
4.6 you would need eight table entries to represent 1 2 3 4 5 six seven eight
33:04
end hosts but if you look at those table entries a lot of them say the same thing how do you get to 4.1 R8 how do you get
33:12
to 4.2 R8 how do you get to 4.3 also R8 it turns out the only way to get to
33:18
network 4 is via R8 or rather that is the shortest way to get to R4 so what we
33:23
can do is instead of writing one entry for 4.1 4.2 4 .3 and they all say that
33:29
the next toop is R8 you can just summarize this and say any destination that's 4 something and it doesn't matter
33:37
what that something is whatever it is the next top is R8 so you have summarized six entries into one and if
33:44
we play this trick enough times we can start to summarize and make our tables more scalable and we can play the same
33:50
trick over here instead of writing an entry for 1.1 and 1.2 both of which
33:56
would have a next toop of r we can just say if you want to reach one point anybody just send it to R six and
34:02
you're done and likewise instead of writing 3.1 3.2 3.3 we can see by
34:08
inspection that the next top is R six so you just say if you want to reach 3 point something go to R six I haven't
34:15
told you how to fill in this table yet you can imagine that this is the end goal is to have a table that's more
34:21
scalable like this and the higher archical addressing the fact that these
34:27
had two numbers in them is kind of what enabled this because we could say if the first number is three send it to R six
34:34
so the hierarchical addressing enabled this if the host had just said ABCD EFG
34:40
this would not have been possible

## Slide 6: Hierarchical Addressing – Conceptual
Hierarchical addressing limits table churn.
Changes inside a network don't affect tables in other networks.
4.1
4.2
4.3
4.4
4.5
2.5
2.4
2.6
2.7
2.1
2.2
2.3
1.1
1.2
3.1
3.2
3.3
Network 2
Network 1
Network 3
Network 4
R8
R9
R6
R9's Table | 
Destination | Next Hop
1.* | R6
3.* | R6
4.* | R8
... | ...
4.6 left the network!
No change in table entry!
Notes: something else that's really
34:45
nice about Hier archol addressing is the fact that the tables change less often
34:51
sometimes people call this table churn so for example if host 4.6 leaves the
34:57
net Network and we were doing this naively and we had an entry for every single end host R9 would have to update
35:03
its table to indicate that 4.6 is gone and no longer reachable and if anyone
35:09
joins and leaves R9 has to update it table entry by contrast look at what
35:15
happens if we use aggregated table entries like this this table entry says if you need to reach 4 point something
35:21
go to R8 if 4.6 leaves the network do you have to change this entry
35:28
no it's still correct to reach 4. anything you still go via R8 so the fact that 4.6 left the network doesn't
35:35
require R9 to change its table entry at all the fact that everyone four point something is a link to R8 stays the same
35:44
so this is nice it means that changes in other networks for example if Network 4
35:50
has more people joining and leaving it doesn't affect R9 at all R9 just always keeps the same information of 4 point
35:57
something something go to R8 that's always true regardless of who joins and leaves Network for so this is nice it
36:04
means that tables change less often and changes in one network don't necessarily have to be propagated into the other one

## Slide 7: Hierarchical Addressing – Conceptual
Network 4
...
Size of the forwarding table scales with number of hosts in the current network, plus number of other networks.
Big scaling improvement! Much better than listing every single host.
Network 2
R4's Table | 
Destination | Next Hop
2.1 | R3
2.2 | R3
2.3 | R3
2.4 | R3
2.5 | R3
2.6 | R5
2.7 | R5
1.* | R9
3.* | R9
4.* | R9
2.1
2.2
2.3
2.5
2.4
R2
2.6
2.7
R3
Network 1
R8
R6
...
R1
R5
R9
R4
Internal destinations.
External destinations.
Notes: okay so to reiterate the point we just made about routers and the scaling
36:50
of their tables we can see that the size of the forwarding table now scales based
36:56
on two things so if you're R4 you are responsible for two sets of entries in
37:02
your table so some of your entries are about ways to get to hosts inside your
37:07
own network so R4 is in network 2 and because you're inside Network 2 you have
37:13
to keep track of different ways to reach 2.1 2.2 2.3 all the way to 2.7 you can
37:20
see that these are internal destinations and R4 has to keep separate entries for
37:25
every internal destination it has to remember if I want to go to 2.4 send it
37:31
to R3 but if I want to go to 2.7 send it to R5 so R4 needs to keep track of one
37:37
entry for every internal destination to other hosts inside the same network and
37:44
the second type of Entry that R2 or R4 needs to keep track of is external
37:49
destinations and these are the aggregated ones that we saw earlier so for example everyone in network one is a
37:56
long path the next top of R9 so if I want to send anything to someone who is 1 something I just send it to R9 and
38:04
they will take care of it likewise anyone in 4 point something or 3 point something not shown here all of them
38:11
have next cops of R9 so I have one entry per external destination so o overall in
38:18
this somewhat conceptual model we can see that you need one entry for every internal destination those cannot be
38:24
combined as of right now and then you need one for every external network and that's how these tables
38:31
scale but this is much better than listing every single host if you listed every single host you have to write 1.1
38:37
1.2 1.3 that's too much and

## Slide 8: Implications of Hierarchical Addressing
Inter-domain routing computes routes between networks.
No need to think about churn inside networks.
Just think about network 1, network 2, etc.
Intra-domain routing computes routes inside a network.
No need to think about other networks.
Just think about 2.1, 2.2, etc.
R4's Table | 
Destination | Next Hop
2.1 | R3
2.2 | R3
2.3 | R3
2.4 | R3
2.5 | R3
2.6 | R5
2.7 | R5
1.* | R9
3.* | R9
4.* | R9
Internal destinations.
External destinations.
Notes: so this also shows us the
38:44
difference between inter domain and intradomain routing and we'll actually put these two together at the very end
38:49
of the unit so once you learn about inter domain routing we're able to put both of them together so this is just
38:55
kind of a preview but for later what you'll see eventually is that inter domain routing is responsible for these
39:01
routes in green and in sorry intra domain is responsible for these routes in green and Inter domain is responsible
39:09
for these routes in blue so for example you could run something like distance
39:14
Vector inside the network that would give you all of these green entries and then you can run something like bgp to
39:21
talk to other networks and that would give you these entries in blue again we'll probably make more sense once you
39:26
know what BG p is but what's great about this again is that it separates out churn in other networks so for example
39:34
if you are thinking about a route to one point something it doesn't matter if people are joining and leaving Network
39:40
one this entry stays the same and likewise if someone joins and leaves Network 4 it's not your problem this
39:46
entry stays the same it's less table churn you just have to think about Network one network 3 Network 4 and it
39:53
doesn't matter what's inside of those networks which is kind of nice and likewise the distance Vector
39:59
protocol doesn't have to worry about other networks it just focus on the host inside of its own network so by dividing
40:06
up the work in this way we get tables that scale more efficiently more on this
40:12
coming soon

## Slide 9: Aggregation – Conceptual
Network 4
...
Sometimes, we can aggregate several rows into a single row.
From R4, any packet to an external network has a next-hop of R9.
*.* wildcard says: For any destination not in the table, forward to R9.
Network 2
2.1
2.2
2.3
2.5
2.4
R2
2.6
2.7
R3
Network 1
R8
R6
...
R1
R5
R9
R4
R4's Table | 
Destination | Next Hop
2.1 | R3
2.2 | R3
2.3 | R3
2.4 | R3
2.5 | R3
2.6 | R5
2.7 | R5
*.* | R9
R4's Table | 
Destination | Next Hop
2.1 | R3
2.2 | R3
2.3 | R3
2.4 | R3
2.5 | R3
2.6 | R5
2.7 | R5
1.* | R9
3.* | R9
4.* | R9
Notes: and actually we can get even more aggressive when it comes to aggregation
40:19
40:19
so maybe you noticed that in this picture right here the only way to leave this network seems to be R9 if you want
40:26
to go to network one it's via R9 if you want to go to network 3 anyone with IP
40:32
address 3 something go to R9 if you want to go to anyone with address 4 point something go to R9 you have three
40:39
entries and they all say R9 so actually you can get even more aggressive and summarize all of these and say actually
40:47
I will have a single entry that says R9 and that's something you can do and later we'll see how address aggregation
40:54
works you can get more aggressive with aggregating a doesn't have to be one entry per Network you can also get more
41:01
creative like this and by the way this star point star it's basically saying
41:08
anything Point anything and so what it's saying is if the destination is one of
41:14
these in the table send it to these Next Tops but if you don't see it in the table just send it to R9 more on this
41:21
later but you can already see that aggregation can actually work more aggressively than just one3 Network you
41:28
can even have one entry for lots of networks at once and if you apply this trick over and over again we're
41:34
eventually able to scale to everyone in the internet

## Slide 10: Aggregation – Conceptual
Network 4
...
From R2, everything is reached through R3, so we can aggregate entries.
The *.* wildcard (everything not in the table) is the default route.
Most hosts only have the default route!
Network 2
2.1
2.2
2.3
2.5
2.4
R2
2.6
2.7
R3
Network 1
R8
R6
...
R1
R5
R9
R4
R2's Table | 
Destination | Next Hop
2.4 | Direct
2.5 | Direct
*.* | R3
R2's Table | 
Destination | Next Hop
2.4 | Direct
2.5 | Direct
2.1 | R3
2.2 | R3
2.3 | R3
2.6 | R3
2.7 | R3
1.* | R3
3.* | R3
4.* | R3
Notes: and in fact aggregation can
41:41
even work like this so for example let's say you are R2 well if you're R2 the decision is even simpler for you so you
41:48
still have to build this table to understand routes to everyone but once you build this table you notice
41:54
something kind of interesting if it's the 2.4 that's Direct directly connected if it's to 2.5 that's directly connected
42:01
but look at everyone else everyone else inside Network to and also everyone else
42:06
inside other networks it all goes to R3 check it out if I want to go to 2.1 next stop is R3 if I want to go to 4.7 next
42:14
toop is also R3 so you can actually get more aggressive like this and just say 2.4 and 2.5 are directly connected
42:22
everyone else just send it to R3 so this wild card is kind of useful it basically
42:27
says everything else that's not in my table just send it to R3 sometimes people call it a default route because
42:34
this is the default if it's not overridden by other table entries so
42:40
when you see this star wild card it's basically saying for every other host not listed here send it to R3 and in
42:47
case you're wondering what hosts do for routing they usually just have one route like this so for example 2.1 if it had a
42:54
routing table what would it say it would just say send everything to R1 it would have one entry that says everyone goes
43:00
to R1 that's why hosts don't have to participate in routing so to close that loop from yesterday
43:07
hosts don't have to participate in routing because they just have to forward everything to their directly connected router and they can use a
43:14
default route to achieve that now you know

## Slide 11: Assigning Addresses
Link-State Protocols
Overview
Computing Paths
Learning Graph Topology
IP Addressing
Hierarchical Addressing
Assigning Addresses
Writing Addresses
Aggregating Routes
IPv6 Changes
Lecture 6, Spring 2026
Notes: so that's the high level idea
43:22
behind hierarchical addressing again it kind of works like you would expect
43:28
Any questions about the approach?
okay so now that we've seen the
43:53
conceptual version of how addressing can be done with a hierarchy let's talk about where those numbers actually come
43:59
from so far I've made them up but they actually come from somewhere

## Slide 12: Assigning Addresses
Hierarchical addressing makes routing scalable.
Hosts that are "close to each other" (in some sense) share part of their address.
Analogy: All third-floor room numbers start with the digit 3.
When a host joins the network, it's assigned an IP address based on its location in the network.
Analogy: When you move to a new house, your address changes.
How do we assign addresses to hosts?
Notes: 44:05
we've already seen is that if Two Hosts are somewhat close to each other for
44:10
some definition of that phrase they should somehow share part of their address that's why everyone in network 4
44:17
was 4 something and the analogy I use here if you're thinking about our favorite post office analogy is that all
44:24
the rooms on the third floor are three something something that first digit tells you what floor you're on and
44:30
that's pretty useful for navigating buildings so we're going to use that same kind of trick to help us assign
44:36
addresses if Two Hosts are somehow close to each other they should share some part of their address whatever that
44:42
means and something else to note since we're here is that when hosts join the network their address is based on where
44:49
they are because we just saw that the addresses have to reflect your location
44:55
people who are nearby should have similar address addresses people who are further away have addresses that are very different so what this means is
45:01
that your address is based on your location and what that also means is when you join the network you receive a
45:08
new IP address based on where you are so it's not the case that your computer has the same IP address everywhere if I
45:15
packed up right now and I got on a plane and I went somewhere in Asia I would get a totally different IP address when I
45:22
rejoin the internet and the analogy here is if you move to a new house your address changes you don't move to the
45:28
new house and keep the address that would be very weird so the question we have to ask ourselves now is where do
45:35
these addresses come from who comes up with these numbers and what does it mean for hosts to be close that's something
45:41
that someone has to Define so let's do that now

## Slide 13: Assigning Addresses, Attempt 1/3 – Early Internet
Addresses are 32 bits long.
Top 8 bits = network ID.
Bottom 24 bits = host ID.
Each organization gets a unique network ID.
AT&T = ID 12.
Apple = ID 17.
Ford = ID 19.
US Department of Defense = IDs 6, 7, 11, 21, 22, 26, 28, 29, 30, 33, 55, 214, 215.
Bob's address: 11010110 10000100 00111010 01101110
Joe's address: 11010110 10010001 00000000 01001101
Network ID
Host ID
Same network ID, so they must be in the same network.
Notes: start with one attempt
45:46
and this is actually what people in the earliest internet did and then we will evolve this to what the modern internet
45:53
does so there's three attempts we're going to make let's start with the very first one that people did in the very
45:58
old days so in the old very old days what people did is they wrote addresses
46:03
as a 32-bit number 32 ones and zeros and they said the top eight bits identify
46:08
the network the bottom 24 bits identify the host this is basically what we just did when we had addresses like
46:16
4.5 these numbers in red would be the four and then these numbers in blue would be the five so they basically did
46:22
the same trick that we just did intuitively and that means that each Network needs a unique ID so for example
46:29
here are some actual numbers that we pulled out AT&T that was an early internet company any computer in AT&T's
46:35
network got id12 so if you signed up to AT&T and connected to the internet your
46:42
address would be something like 12 100 or something Apple got ID 17 Ford
46:48
got 19 whatever something interesting is that the US Department of Defense got quite a few at IDs so it seems like they
46:54
had a lot of networks um not that important but something that we found kind of interesting and what's useful
47:00
about this is we can play the same tricks as before so if we have two people Bob and Joe we notice that they
47:06
have the same network ID so they must be part of the same network just like we saw earlier 4.1 and 4.10 must be in the
47:14
same network similarly here these red bits are the same so they must be in the same
47:21
network

## Slide 14: Assigning Addresses, Attempt 1/3 – Early Internet
Addresses are 32 bits long.
Top 8 bits = network ID.
Bottom 24 bits = host ID.
Problems:
Only 28 = 256 different network IDs.
  And we already gave the US Department of Defense 13 of them.
Imagine a tiny network (Joe's Tire Shop) with 10 hosts.
  If we give them an ID, we're giving them 224 = 16,777,216 addresses!
We're going to run out!
Notes: there's already a problem here maybe you spotted it8 bits gives you 2 to the 8 Network IDs that is 256
47:29
different networks that's not a lot and we already burned 13 of them on the US
47:35
Department of Defense so we are running out very quickly so if you imagine some
47:40
new network that starts up you're running a tire shop for some reason and it's got 10 hosts you're going to claim
47:46
one of those 256 iids that's not a lot to give out to the entire world and if
47:52
we give them an ID even worse is this tire shop now has access to um let's say
47:59
if they get network number 20 they get everything from 20.0 to 20.11 111111 241s so how many
48:09
host IDs live in network number 20 two to the 24 so even this tiny little tire
48:15
shop now has 16 million addresses even though they only have 10 computers that
48:21
the needs to give addresses to so this is very wasteful you just wasted 16 million addresses
48:27
for a network that only has 10 people inside and this is going to run out really quickly so even though this
48:32
worked on the very early internet people very quickly realized that this is probably doomed we're going to move on
48:39
to attempt number two to try and fix this this was the simplest thing they did it's exactly like the intuitive
48:45
thing we saw only problem is it didn't scale very well

## Slide 15: Assigning Addresses, Attempt 2/3 – Classful Addressing
Idea: Allocate different network sizes based on need.
The top bits (0, 10, or 110) tell us how to split up the rest of the bits.
0 | Network (7 bits) |  |  |  |  |  |  | Host (24 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  | Network (14 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  | Host (16 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
110 |  |  | Network (21 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Host (8 bits) |  |  |  |  |  |  | 
Class A:
Class B:
Class C:
~128 networks
~16m hosts per network
~16k networks
~65k hosts per network
~2m networks
~256 hosts per network
Notes: Technically, 254 hosts, not 256, because the all-zeroes address and all-ones address are reserved for special purposes.
so this is try number two what they
48:53
started to realize is that some organizations are larger and some organizations are smaller US
48:59
Department of Defense very big millions of computers joon's tire shop 10 computers very small so now what they've
49:07
done is they've said actually there are three types of addresses some addresses have a seven bit network ID some
49:13
addresses have a 14bit network ID and some addresses have a 21 bit network ID
49:19
and what's nice about this is you can see for example the class c network
49:25
addresses they have only eight bits of host and so what that means is each of
49:31
these networks only can support 256 hosts so if you're a tiny little tire
49:36
shop guess which one you're going to want you're probably going to want Class C and if you're the US Department of
49:41
Defense you probably want Class A because here each Network that you
49:47
allocate has 16 million hosts so basically the idea here is that we're uh
49:52
defining more networks some are larger some are smaller and by allocating the bits in this way
49:59
turns out we get a lot of class C networks millions of them compared to 256 from before now we have millions of
50:06
networks we can support and 16,000 of these somewhat larger networks that can support 65,000 hosts and only 128 of
50:14
these very big networks that can support 16 million hosts per Network and how do
50:19
you tell which type of address you're looking at you look at the top bits and we use this little bit encoding trick where if this is zero it's Class A if
50:26
it's 10 it's Class B if it's 110 it's Class C so that's what the second
50:32
attempt was sometimes called class full addressing because there are three classes and everyone who wants a network
50:39
picks one of the three classes depending on their size

## Slide 16: Assigning Addresses, Attempt 2/3 – Classful Addressing
0 | Network (7 bits) |  |  |  |  |  |  | Host (24 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  | Network (14 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  | Host (16 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
110 |  |  | Network (21 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Host (8 bits) |  |  |  |  |  |  | 
Class A:
Class B:
Class C:
Bob's address: 10010110 10000100 00111010 01101110
Joe's address: 10010110 10000100 00000000 01001101
Host ID
The top bits indicate this is Class B...
Network ID
...so read the next 14 bits as the network ID...
...and read the last 16 bits as the host ID.
Notes: so here's an example of all the
50:46
classes in action the first thing we do is we look at the top bits we see a one we see a zero this must be Class B this
50:53
is one of those mediumsized networks because we're in class B we read the next 14 bits as the network ID and the
50:59
next 16 bits as the host ID so we're still doing network. host like
51:06
4.7 but the top the network bits vary depending on what type of address it is
51:13
and as a consequence each type of network can hold more hosts fewer hosts depending on how many host bits are
51:20
available this was the second attempt at trying to make Network addressing more
51:25
scalable than before for we now have millions of networks to hand out of different sizes as opposed to 256 all
51:33
gigantic

## Slide 17: Assigning Addresses, Attempt 2/3 – Classful Addressing
Class A: ~128 networks. ~16m hosts per network.
Class B: ~16k networks. ~65k hosts per network.
Class C: ~2m networks. ~256 hosts per network.
Problems:
Class A is way too big for most organizations.
Class C is way too small for most organizations.
Class B is the best option for many.
  ~65k hosts is still too big for most organizations.
  ~16k is still not enough networks. We're running out again!
Notes: but it turns out the internet kept growing and it kept growing and
51:38
things started to run out again so let's do the math to see why it ran out the
51:44
main reason it ran out is because it turns out the way that these bits were
51:50
split actually did not work so well because most people don't need Class A
51:55
they don't need a network with 16 million people in and actually most people don't want Class C either because
52:01
Class C only allows you to support 256 hosts and maybe if you're a company you
52:06
want more than that so actually it turns out most people just ended up using Class B and A and C were not really used
52:13
so we ended up back in the situation where we're mostly using one class namely Class B and Class B we saw
52:20
earlier support 16,000 networks and turns out 16,000 is not
52:25
enough so as time went on this number crept closer and closer and we saw that
52:31
if this curve continues going upwards we're going to run out of class B networks as well so once again we have
52:38
another scaling problem although this was a better attempt it's still not great and the reason why we ran out by
52:44
the way is because most people don't need 65,000 posts so we gave you a Class B
52:50
network if you only have 500 posts you're wasting 64,500
52:56
unused addresses that someone else could have used that's our second attempt still not
53:03
great

## Slide 18: Assigning Addresses, Attempt 3/3 – CIDR
With classful addressing, we tried to use convenient 8-bit boundaries.
Class A: 8 bits for class/network. 24 bits for host.
Class B: 16 bits for class/network. 16 bits for host.
Class C: 24 bits for class/network. 8 bits for host.
What if we could assign network IDs of any length?
Leads to CIDR (Classless Inter-Domain Routing).
This is what the Internet uses today.
0 | Network (7 bits) |  |  |  |  |  |  | Host (24 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  | Network (14 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  | Host (16 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
110 |  |  | Network (21 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Host (8 bits) |  |  |  |  |  |  | 
Class A:
Class B:
Class C:
Notes: so let's move to the third and final attempt this is the one that we use today and the idea is why do we have
53:09
to create these arbitrary splits why do we have to split Network and host here and here and here what if I split it
53:16
here or here or anywhere in the middle so that's what we're going to do next instead of defining a b c and defining
53:24
three specific split points between Network and host what if I could assign
53:30
a network ID that's 8 Bits 12 13 15 if I
53:35
can use any number I want instead of just 7 14 21 that can give me more
53:41
control over the size of my network and that allows me to allocate just enough for what I need so if I only need nine
53:48
bits of host I can create a 20 bit network ID for example and this leads to what the modern internet uses it's
53:54
called classless in domain routing here is classless earlier it was class full
53:59
and that idea here is that we are removing the notion of specific classes we making things more
54:07
flexible

## Slide 19: Assigning Addresses, Attempt 3/3 – CIDR
Suppose Joe's Tire Shop has 450 hosts.
Classful addressing:
Class C gives us ~256 hosts. Not enough!
Class B gives us ~65k hosts. Too many!
We have to use Class B (and waste tons of addresses).
Classless (CIDR) addressing:
8 host bits = 256 bits. Not enough!
9 host bits = 512 bits.
Still not exactly 450, so still some wasted addresses.
But much less wasteful!
Network ID (23 bits) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Host ID (9 bits) |  |  |  |  |  |  |  | 
Notes: so how would you do this you'd have to do a little bit of math so for example let's say you have a tire shop
54:13
with 450 hosts in the classful addressing approach you have to choose a
54:18
BC there's multiple choice if you choose C you get 256 hosts that's not enough
54:24
you have 450 if you Class B you get 65,000 that's way too many you're
54:29
wasting lots of unused addresses but you're forced to use B not so great in
54:35
classless addressing you don't have to choose ABC you can say eight bits are not enough but nine bits are enough so
54:42
yeah you do waste some addresses you waste 72 62 addresses but that's okay
54:49
this is still much better than class full addressing so now this boundary doesn't have to be at a fixed Point
54:55
instead of choosing 7 14 21 here we chose 23 because that was the best fit
55:01
for this particular use

## Slide 20: Granular Hierarchical Assignment with CIDR
CIDR enables multi-layered hierarchical assignment of addresses.
ICANN. (Internet Corporation for Names and Numbers)
  Top-level organization that owns all the IP addresses.
  They allocate blocks to...
RIRs. (Regional Internet Registries)
  Representing Europe (RIPE), North America (ARIN), Asia/Pacific (APNIC), South America (LACNIC), and Africa (AFRINIC).
  They give out portions to...
Large organizations or ISPs.
  Sometimes called Local Internet Registries (especially in Europe).
  They give out portions to...
Small organizations and individuals.
  Examples: Hofstra University, Joe's Tire Shop.
Notes: and something else that's very nice
55:06
about the classless version of addressing is you can actually create multi-layered hierarchal assignment so
55:13
instead of just writing 4.2 that is Network 4 Post Number Two you can
55:19
actually get more specific you can say 4.2.1 or you can say 4.2.1 point2 you
55:26
can create multiple layers and play the same trick of hierarchy across multiple layers and in fact that's what we do
55:33
there's actually a very natural hierarchy so let's see it in action so the very top level of the hierarchy is
55:41
the internet Corporation for names and numbers it's some organization that manages IP address IP addresses and they
55:48
own all the IP addresses so at the very start every IP address from all zeros to
55:53
all ones is owned by I can and if you want one you have to go ask them but in fact they're not going to service
56:00
addresses to everyone so instead what they did is they took the address space and they cut it up and they said this
56:06
part goes to Europe this part goes to North America this part goes to Asia this part goes to South America so they
56:13
took the whole pie and they cut it up into slices and each continent got a specific slice and those are called
56:20
Regional internet registries you don't have to remember that but you can imagine those are organizations
56:25
56:25
represent pres ing each specific continent and again we don't want one organization handling all the addresses
56:32
in Europe that's pretty bad so instead uh it's not scalable so instead Europe will take its slice of the pie and cut
56:39
it up into even smaller slices and give those out to local internet registries
56:44
and those are organizations like uh UC Berkeley or isps like AT&T so the
56:51
continent level registry then cuts it up and then gives it out to organization
56:56
and those organizations can give out smaller portions to even smaller organizations so for example maybe the
57:03
UC system cuts out a slice and gives it to UC Berkeley UC Berkeley cuts out a slice gives it to the eeks department so
57:09
you don't have to memorize this exact hierarchy but what this is showing is that in real life hierarchies are
57:16
multi-layer you splits into a bunch of universities each University splits into a bunch of departments each department
57:23
splits into a bunch of classes and so on so just like how real life hierarchies are multi-layered addresses can also be
57:30
multi-layered to model those real life hierarchies which is kind of useful

## Slide 21: Granular Hierarchical Assignment with CIDR
ICANN owns all addresses: ................................
ARIN (North America) owns: 1101............................
4 bits fixed, 228 ≈ 268m addresses.
AT&T (large ISP) owns: 110111001.......................
9 bits fixed, 223 ≈ 8m addresses.
Hofstra owns: 110111001110100010..............
18 bits fixed, 214 ≈ 16k addresses.
SIC owns: 110111001110100010011010........
24 bits fixed, 28 ≈ 256 addresses.
Prof. Gu owns: 11011100111010001001101001011101
All bits fixed, 1 address.
Notes: so
57:36
here's an example of addresses being allocated I can owns the whole Pi so
57:41
here you can imagine a DOT is not fixed so 32 dots means they own every address
57:47
each of these can be a one or a zero and it's originally owned by Ian and then what Ian does is it says I'm going to
57:54
fix the top bits to 1 one0 one the bottom bits can be anything from all zeros to all ones this range this SCE of
58:01
the pi belongs to North America it's yours now do whatever you want with it so the North American registry now owns
58:08
all the addresses starting with 1 one01 that is 268 million addresses because
58:13
you have 28 unfixed bits and then North America says I don't want to handle 268
58:19
million addresses so I am going to give some of them to AT&T in particular I
58:25
will fix five more bits and anything that starts with these nine bits belongs to AT&T so go ask them if you want an
58:32
address in this range now AT&T controls 8 million addresses and this goes on
58:38
AT&T fix some more bits and sends anything starting with this sequence of
58:43
bits to UC Berkeley so now they own this and maybe UC Berkeley fix some more bits
58:48
now anything starting with these 24 bits that's only 256 addresses is owned by
58:53
soda hall and then maybe a specific Prof profess owns a specific address of all
58:58
32 bits fixed so this is a hierarchy it's not real soal doesn't really own
59:04
any IP addresses but you can see that hierarchies in addressing kind of work like hierarchies in real life that we
59:11
see all the time so that's how you assign addresses

## Slide 22: Writing Addresses
Link-State Protocols
Overview
Computing Paths
Learning Graph Topology
IP Addressing
Hierarchical Addressing
Assigning Addresses
Writing Addresses
Aggregating Routes
IPv6 Changes
Lecture 6, Spring 2026
Notes: 59:16
we started with the first attempt and the second attempt they didn't work so well they didn't scale so we moved on to the classless approach that's what
59:23
everyone uses today

## Slide 23: Writing IPv4 Addresses
We could write an IP address as a 32-bit number: 11011100111010001001101001011101
Nobody wants to read that.
Dotted quad notation:
Split into groups of 8 bits.
Write each 8-bit number in decimal, separated by dots.
11011100 11101000 10011010 01011101
220
232
93
154
.
.
.
Notes: his is really just formatting more so than any
59:36
conceptual thing but we should talk about it because you'll have to write these addresses all the time so if you
59:41
want to to you can write 32 bits 32 ones and zeros that's an address I don't want
59:47
to read that you don't want to read that it's really gross so instead what people often do is they use something called
59:53
dotted quad notation you've probably already seen this before and what they do is they take the first eight bits
59:59
convert it into a decimal number then the next eight then the next eight then the next eight so you get four numbers
1:00:05
separated by dots each number ranges from 0 to 255 that's all zeros to eight
1:00:11
ones and it's basically what you'd expect but this is how people write IP addresses but when they write this it's
1:00:18
not because they really want these four numbers it's just a short hand for those 32 bits that are quite hard to
1:00:24
read

## Slide 24: Writing IPv4 Address Ranges
Slash notation for writing ranges of addresses:
Set all unfixed bits to 0. Write as a dotted quad. After the slash, write how many bits are fixed.
Examples:
192.168.1.0/24 means 24 bits are fixed. Range is 192.168.1.0 – 192.168.1.255. (8 bits address range)
192.168.1.0/29 means 29 bits are fixed. Range is 192.168.1.0 – 192.168.1.7. (3 bits address range)
192.168.1.1/32 means 32 bits are fixed. A single address.
11011100 11101000 10010000 00000000
220
232
0
144
.
.
.
11011100 11101000 1001.... ........
Set all unfixed bits to 0.
/20
Number of fixed bits.
Notes: something else is writing ranges of IP addresses so you could actually just
1:00:31
0.0.0.0/0 means no bits are fixed. All addresses.
go out and write the ranges explicitly you might go out and say I own all the IP addresses from
1:00:39
192.168.1.0 all the way to 192.168.1.254 you can go out and say
1:00:45
that but it's kind of a mouthful to write two IP addresses and say you have a range so in real life what people do
1:00:52
is they use something called slash notation and all you have to do here is take the bits that are not set set them
1:00:58
all to zero so look this is the prefix that I care about these are the bits that are unset so I force them to all be
1:01:05
zeros convert that into an IP address which is 2202 32.1
1:01:11
144.000 then I'll write a slash and then after the slash I'll write how many bits were fixed so when you read this read it
1:01:18
like this the top 20 bits are fixed translate this IP address into bits and
1:01:24
write out the top 20 bits those are are fixed everything else is variable from all zeros all ones so it's kind of a
1:01:31
notational note but this is how people write IP ranges here are some examples that I won't say out loud something to
1:01:37
notice is that the boundaries don't have to be exactly on the dots so for example
1:01:42
if you have a slash 29 it means that the top 29 bits are fixed and only the
1:01:48
bottom two bits can change from 00 0 to 111 represents this range if you write
1:01:54
it out if you put sl32 it means all the bits are fixed if you say 0.0.0.0
1:02:00
sl0 that represents all of the addresses so again it's kind of a notational footnote but since you'll see it a lot
1:02:07
it's good to know what they mean and how people write ranges

## Slide 25: Writing IPv4 Address Ranges
Netmask is an alternative to the number after the slash..
Set all fixed bits to 1, and all unfixed bits to 0. Write as a dotted quad.
Useful in code: To extract network ID, bitwise AND the address and netmask.
Slash notation is more convenient for humans.
11111111 11111111 11110000 00000000
255
255
0
240
.
.
.
11011100 11101000 1001.... ........
Set all bits to 0 or 1.
Slash notation: 220.232.144.0/20
Netmask notation: 220.232.144.0 (netmask 255.255.240.0)
Notes: okay a little bit more notational
1:02:14
notes sometimes people don't like writing slash notation so they instead write something called a net mask and
1:02:21
here all you're doing is replacing the slash with a net mask so the original
1:02:26
range you still have to write the prefix so let me try that again you are still
1:02:32
representing a range to write the range you still have to start with the prefix and the way you write the prefix is just
1:02:37
like before you take the prefix you set all the remaining bits to zero and you write it as a dotted quad so notice that
1:02:44
in both notations you write 220 232 1 1440 that has not changed a net mask
1:02:50
only changes the slash so we no longer write slash2 what we instead do is we
1:02:56
set all the fixed bits to one all the unfixed bits to zero we write this as a quad and that's the net mask so this net
1:03:03
mask of 255 255 240 it represents the exact same thing as 20 someone just
1:03:10
wrote it differently they just wrote 21s followed by 12 zeros put a bunch of dots
1:03:16
in between them this rep uh this net mask replaces the 20 it does not replace
1:03:22
everything else here why is this useful by the way I think 20 is easy to read for humans but this is useful because
1:03:28
and we'll see this a little bit later in the class as well this allows you to do bitwise operations let's say you only
1:03:34
care about the network ID and you want to throw away the bottom bits you can just perform a bitwise and and if you
1:03:41
know your bitwise operations that will keep all of the top bits intact and zero out all the bottom bits so computers
1:03:48
often like to use net masks oras humans like to slashes but all of this is just
1:03:53
fancy notation for writing ranges of IP addresses

## Slide 26: Aggregating Routes
Link-State Protocols
Overview
Computing Paths
Learning Graph Topology
IP Addressing
Hierarchical Addressing
Assigning Addresses
Writing Addresses
Aggregating Routes
IPv6 Changes
Lecture 6, Spring 2026
Notes: okay so moving on now that we know how to write the addresses and we know
1:04:53
how addresses are derived from the multi-layer hierarchical classless addressing system now we can talk about
1:05:00
how all of this circles back to routing because remember we went on this whole Adventure talking about IP addresses for
1:05:06
the purpose of enabling scalable routing so let's go back and take what we've
1:05:12
learned about IP addresses and apply it to routing to make it scalable

## Slide 27: Inter-Domain Routing
AT&T
4.0.0.0/8
In inter-domain routing, we're looking for routes to other networks.
Each destination is a network, represented by an IP prefix.
Already better than one entry per host...but we can do even better!
UC Berkeley
130.0.0.0/8
Stanford
146.0.0.0/8
Orange (France)
R6's Table | 
Destination | Next Hop
4.0.0.0/8 | R2
130.0.0.0/8 | R2
146.0.0.0/8 | R2
... | ...
R6
R2
Notes: so we're
1:05:18
starting to move a little bit toward in domain routing so consider this a bit of a preview for the in domain routing that
1:05:24
we're going to see coming up next time and we'll see how aggregating routes is
1:05:29
able to help us make these tables more scalable so let's say you're R six and
1:05:36
you're building a table in the naive version you would have to build one entry for every single destination in
1:05:42
France in the US UC Berkeley and Stanford that is way too much it's not happening so instead what happens is
1:05:50
we'll play the same tricks as before each network instead of having a number like before where we said four .2 that
1:05:56
would have been true in the very early internet but we now know that there's actually multi-layer hierarchies going
1:06:02
on so each organization whether it's UC Berkeley or AT&T they own a range of
1:06:09
addresses so we've generalized the idea of having numbers like 5.3 and 10.2
1:06:16
we've generalized that using class list addressing to say that everyone has a range and remember we can use slash
1:06:22
notation to write the range so AT&T owns all of the addresses with the top eight
1:06:29
bits fixed and if you're wondering what those bits are turn this into ones and zeros you'll find out and you see
1:06:34
Berkeley owns all of the addresses with the top eight bits fixed where the top
1:06:39
eight bits are the top eight bits of this address whatever they are write it out and find out so as before every
1:06:46
network has a range of addresses using classist addressing and when you write
1:06:52
entries in your table all you have to do is write range anybody in the range
1:06:57
4.0.0 sl8 please send it to R2 and anyone in UC Beres range send it to R2
1:07:04
as well and anyone in Stanford's range also send to R2 so it's the exact same
1:07:10
thing as we saw earlier but instead of using the simpler version of hierarchy where there's just two layers we now
1:07:16
have multiple layers of hierarchy to reflect the fact that real life also has multi-layer
1:07:23
hierarchical relationships we can actually do even better than this

## Slide 28: Inter-Domain Routing
AT&T
4.0.0.0/8
With CIDR, AT&T allocates parts of its ranges to UC Berkeley and Stanford.
We can aggregate many networks into a single entry!
4.0.0.0/8 represents AT&T, and all its subordinates.
UC Berkeley
4.12.0.0/16
Stanford
4.29.0.0/16
Orange (France)
R6's Table | 
Destination | Next Hop
4.0.0.0/8 | R2
4.12.0.0/16 | R2
4.29.0.0/16 | R2
... | ...
R6
R2
Notes: so let's do that one thing we'll notice
1:07:30
is that actually what happened here is these numbers didn't really come out of nowhere like here where I just made up
1:07:36
4.0. z.0 sl8 that's all totally made up in real life we already saw that what
1:07:42
actually happens is that addresses get allocated to different people so you cut a slice of your pie and you give it to
1:07:48
someone else so maybe what happened is not that AT&T and UC Berkeley have randomly generated prefixes what really
1:07:56
happened is that AT&T took its range cut a little slice gave it to UC Berkeley
1:08:01
cut another Little Slice gave it to stard and that's what we see here so
1:08:06
actually maybe a more realistic depiction of the relationships is that AT&T owns this whole range gives a small
1:08:13
piece to UC Berkeley gives a different small piece to Stanford and now what we
1:08:18
can do is we'll notice that all three of these ranges they fall in the same
1:08:24
larger range because all of this is just AT&T's range these are just two small slices of it so instead of writing three
1:08:31
separate entries for AT&T and UC Berkeley and Stanford we can just write one entry for anybody in AT&T's range of
1:08:38
which UC Berkeley is a slice and Stanford is a slice please send all of that stuff to R2 so now this represents
1:08:45
AT&T and every organization that AT&T handed a slice of its address range out
1:08:51
to this is all of AT&T's range smaller slices went to other people we can see
1:08:56
already that this is three networks represented by one entry and if AT&T had
1:09:02
millions of slices that it gave out this could be millions of networks represented by a single entry which is

## Slide 29: Inter-Domain Routing
AT&T
4.0.0.0/8
Now, Stanford wants to connect to multiple networks. This is called multi-homing.
We need an entry for both AT&T and Stanford (one of its subordinates).
Multi-homing limits aggregation!
UC Berkeley
4.12.0.0/16
Stanford
4.29.0.0/16
Orange (France)
R6's Table | 
Destination | Next Hop
4.0.0.0/8 | R2
4.12.0.0/16 | R2
4.29.0.0/16 | R7
... | ...
R6
R2
R7
Notes: somewhat annoying point though and it's something we'll come
1:09:14
back to later as well is the idea of multihoming and what multihoming means
1:09:19
is that maybe Stanford doesn't just want to have a slice of or doesn't want to just be serviced by AT&T so yeah it has
1:09:27
the addresses from AT&T but maybe it also wants to be connected to this network in France well in that case it's
1:09:34
no longer enough to say everyone AT&T's network and all of its subordinates should go to R2 in this case you
1:09:42
actually have a shortcut directly to Stanford because R six has a direct link to R7 so in a topology like this where
1:09:49
Stanford is served by both AT&T and this company in France maybe R six has a
1:09:54
shortcut to reach Stanford so now when you read these entries you have to be a little bit more careful because if you
1:10:01
look at this entry what does it really say it says well actually all of AT&T
1:10:07
and its subordinates go to R2 except for one subordinate Stanford it's special that when you have a shortcut go to R
1:10:14
seven so when you have multihoming it limits aggregation and this is something we'll see more we me talk more about
1:10:20
inter domain routing but basically what this is showing is that aggregation works but sometimes you don't want to
1:10:26
aggregate all the way here's the case where if you aggregated all the way you would have lost this neat little
1:10:31
shortcut and by not aggregating Stanford and saying actually Stanford is a separate range you get to keep the
1:10:37
shortcut around that might be useful there's a bit of a tension between multihoming and
1:10:46
aggregation

## Slide 30: Inter-Domain Routing
AT&T
4.0.0.0/8
Ranges in the table might overlap.
Longest prefix matching: If a destination matches many ranges, pick the most specific range.
Example: 4.29.1.2 matches both 4.0.0.0/8 and 4.29.0.0/16 (more specific).
UC Berkeley
4.12.0.0/16
Stanford
4.29.0.0/16
Orange (France)
R6's Table | 
Destination | Next Hop
4.0.0.0/8 | R2
4.12.0.0/16 | R2
4.29.0.0/16 | R7
... | ...
R6
R2
R7
Notes: and one thing you'll notice in multihoming cases and in general is
1:10:51
that these prefixes sometimes overlap and that can be a problem so if you actually write out the ones and zeros
1:10:57
which I will not do here but try it at home if you're interested you will see that actually this range is a super set
1:11:04
of this range put it another way this range 4.29 16 that's a little slice of
1:11:10
4.0.0 point0 so if you want to send a packet to someone in Stanford technically both of these are valid
1:11:16
entries it falls in this range and it also falls in this range because this lower range is a small slice of the
1:11:23
larger range so both of these are valid entries which one do you use to forward
1:11:29
packets to your friend in Stanford you could use either of them and it turns out what you have to do is something
1:11:35
called longest prefix matching so pick the most specific one in this case the
1:11:40
sl16 is more specific it's a smaller range so use that one and don't use the more General one that's something we'll
1:11:46
see again later as well so in the case that an address matches multiple ranges
1:11:52
please pick the most specific one and that allows you to forward packets to a
1:11:58
host that matches multiple entries that's in multiple
1:12:05
ranges

## Slide 31: IPv6 Changes
Link-State Protocols
Overview
Computing Paths
Learning Graph Topology
IP Addressing
Hierarchical Addressing
Assigning Addresses
Writing Addresses
Aggregating Routes
IPv6 Changes
Lecture 6, Spring 2026
Notes: okay we have one final topic we're all done so the final thing I want
1:12:10
to briefly mention is something called IPv6

## Slide 32: Introducing IPv6
IPv4 addresses are 32 bits long. 232 ≈ 4 billion addresses. That is not enough.
IPv6 was introduced in 1998 to deal with IPv4 address exhaustion.
Main difference: Addresses are now 128 bits, instead of 32.
Fundamentally, same addressing structure as IPv4.
WIth 128-bit address
2128 ≈ 3.4 × 1038 possible addresses.
We won't run out again.
Notes: so to fix that we need a new version of Ip and that's what people started to build they actually started
1:14:06
building this in the 1990s because they started to realize that this is going to happen and so the real the main
1:14:13
difference between ipv4 which is what we've been seeing so far and IPv6 is just that addresses are no longer 32
1:14:19
bits they are now 128 bits so IPv6 is mostly the same they didn't really
1:14:25
change that much the main thing that they changed is just the fact that addresses are now 128 bits instead of 32
1:14:33
later we'll see some other very minor changes but for now that's the one you have to know um but overall the
1:14:38
addressing structure is still the same it's still higher archical you can still do multi-layer hierarchy it's all the
1:14:44
same things you just do it with 128 bits instead of 32 so one question you might ask is is
1:14:51
this going to run out are we headed for ipv 8 or n sometime in the future I don't think so
1:14:57
if you do the math 2 to the 128 is an astronomically large number this is like
1:15:03
number of atoms in the universe type number this is enormous and even if you
1:15:08
gave an address to like every second of History you barely use them so these
1:15:14
numbers are mindboggling and it basically means that for the foreseeable future we are never running out of
1:15:19
addresses again IPv6 has solved the problem of running out of addresses and
1:15:25
if you care about what happened to five it was a draft and it never got implemented so it went from four to
1:15:32
six

## Slide 33: IPv6 Addresses
IPv6 uses hexadecimal instead of decimal.
2001:0DB8:CAFE:BEEF:DEAD:1234:5678:9012
Colon between every 4 hex digits (16 bits).
Shorthand:
Omit leading zeros per block: 2001:0DB8:0000:0000:0000:0000:0000:0001 → 2001:DB8:0:0:0:0:0:1
Omit a long string of zeros, once per address: 2001:DB8:0:0:0:0:0:1 → 2001:DB8::1
Can still use slash notation for ranges.
2001:0DB8::/32 has 32 bits fixed, and 296 addresses.
Notes: so a little bit of notation on IPv6 they change the way you write addresses just a little bit and again this is not
1:15:39
the most important thing is just how you write these addresses so instead of using decimal they switch to using
1:15:44
heximal and what that means is you have to write four heximal digits for every
1:15:50
32 or for every 16 bits I can't do math four hex digits represent 16 bits you
1:15:55
write eight of them that gives you 128 bits so this is just a long HEX number
1:16:01
if you convert every hex digit into bits you'll get 128 bits so these are longer
1:16:07
and because they're long sometimes you can get lazy you don't want to write the whole thing you can already see this is quite long so sometimes what people do
1:16:15
is if you have z0000 Z within two colons you can just write one zero and everyone
1:16:21
knows what you're talking about so this zero is really 32 zeros but no one wants
1:16:26
to write that so we just wrote a single zero and sometimes what people do is they can also emit a bunch of zeros so
1:16:32
instead of writing zero colon zero colon zero colon zero they just write a double colon and everyone knows you know I know
1:16:39
we all know that in between these double colons you just fill in zeros to get 128
1:16:44
bits in total you can only do this once if you do it twice it's not clear how many zeros to put in each omitted range
1:16:50
but if you do it once we all know that there these bits on the right these on the left put zeros in between and you
1:16:57
get your address so again not the most important thing but if you go out into the wild and you see addresses now you
1:17:03
know this is the way that they are written and just like an ipv4 you can use slash notation so you write a range
1:17:10
here we use the double colons to be lazy and not write all the zeros and the SL 32 means the top 32 bits are fixed and

## Slide 34: IPv6 Addresses
IPv6 uses the same hierarchical addressing approach as IPv4.
Some changes:
Instead of someone (e.g. ICANN) giving you a prefix, you can pick your own prefix.
  Uses a protocol called SLAAC (Stateless Address Autoconfiguration).
  Pick a random prefix. If someone else is using it, pick another one.
  Works in IPv6 (not IPv4) because there are so many prefixes.
In practice, prefixes usually fix at most 64 bits.
  Even the smallest network has 264 hosts.
Notes: again the hierarchy is generally the same but something nice
1:17:28
about IPv6 is that the range is so enormous like astronomically big that
1:17:35
actually we don't have to play some of those tricks that we did before remember earlier we had to be really careful with
1:17:40
the way we addressed because Class A Class B Class C didn't give us enough 128 is so big that you're basically
1:17:47
never running out no matter what you do within reason so actually there are some
1:17:52
tricks you can play in IPv6 that you cannot do in ipv4 because of the gigantic number of prefixes so something
1:17:59
you can actually do in IPv6 is you can pick your own prefix instead of other people handing you one like they did in
1:18:06
ipv4 where space is limited and someone has to give you one IPv6 the space is so
1:18:12
big that you can just pick your own and there's actually a pretty good probability that no one else is using it
1:18:17
you pick it and with like 99% probability no one else is using it so it's yours and if someone else is using
1:18:24
it just pick another one so we'll actually see this again later in the class but it's a trick that you can play
1:18:29
an IPv6 but not four it's giving yourself a prefix not the most important
1:18:35
thing but kind of cool and in practice because the space is just so big it's
1:18:41
often the case that you just use 64 bits for the network ID 64 bits for the host
1:18:46
ID and that's totally fun you're G to have way more than you need for the number of hosts and the number of
1:18:52
networks on the internet so if only the early internet designers had written 128
1:18:58
instead of 32 we probably wouldn't have had to do any of this but because they chose 32 bits we have to go through all
1:19:04
this redesign

## Slide 35: IPv6 Adoption
IPv6 introduced in the 1990s, but wide adoption started in the 2010s.
Today, ~40% of hosts have adopted IPv6.
Notes: https://www.google.com/intl/en/ipv6/statistics.html
IPv6 adoption really quick note IPv6
1:19:11
is actually not used by everyone so it turns out introducing a new protocol is pretty hard if a computer refuses to
1:19:18
update it software it might be stuck using ipv4 and it doesn't understand IPv6 so actually even even though this
1:19:25
verticle was developed in the 1990s as of 2010 basically nobody used it but as
1:19:32
addresses started to run out people started to realize we probably need to be upgrading our software to understand
1:19:38
IPv6 so newer computer started to understand IPv6 we started to install
1:19:43
IPv6 into older servers and adoptions slowly increased but even as of
1:19:49
2024 it's actually still less than half so over half of all computers still only speak iv4 so you can see that adopting a
1:19:57
new protocol is quite slow especially if you need everybody on Earth to
1:20:03
understand it

## Slide 36: IPv6 Adoption – Challenges
Why is IPv6 adoption hard?
Requires software and hardware upgrades, from both hosts and routers.
IPv4 and IPv6 are not compatible with each other.
  To support both, you need 2 forwarding tables.
  No way to convert between IPv4 and IPv6.
If I support both IPv4 and IPv6, which should I use?
  IPv6 usually faster, but other factors could affect your choice.
Main driver for IPv6 adoption: We're running out of IPv4 addresses!
Notes: why is it hard by the way why
1:20:21
hasn't everyone just immediately switched to IPv6 well one reason is you have to upgrade your computer some
1:20:27
servers are very old and it's just very hard to upgrade them or people are lazy they don't want to update them so you
1:20:32
got to update your software to understand IPv6 the two Protocols are not compatible so you actually have to
1:20:39
support both it's not one or the other so if you want to speak both ipv4 and IPv6 you have to support both there is
1:20:45
no way for six to work with four or anything they're two basically separate
1:20:51
protocols and you would need for example two forwarding tables and if you support both which one should you use it's not
1:20:57
immediately clear maybe you want to use one maybe you want to use the other something you have to think about if
1:21:02
you're installing both but again it's still important that we do this because if the world doesn't move to IPv6 we're
1:21:08
going to run out of addresses it's important that we do this even though it's kind of
1:21:14
painful

## Slide 37: Summary: IP Addressing
Hosts on the Internet have addresses (IPv4, IPv6, or both).
These addresses are hierarchical.
  They are assigned in groups to specific organizations.
Wildcard matching can help forwarding and routing scale better.
Notes: okay let me just quickly summarize for you
1:21:19
host on the internet have addresses ipv4 or IPv6 both of them use higher archical
1:21:25
addressing we saw three different approaches to doing so and we landed on the classless approach because it scales
1:21:31
the best and it matches hierarchies that we see in real life and because of these
1:21:36
hierarchical addressing schemes it allows us to write ranges in our forwarding tables as opposed to
1:21:42
individual addresses and we also saw that the wild card can help us aggregate even further
1:21:48
and more aggressively to get much more scalable tables so that's your a little preview of in domain routing if you come
1:21:54
back next we'll talk about inter domain so that’s that for today