## Slide 1
Inter-Domain Routing
Lecture 8 (Routing 5)
Slides credit: CS 168 @ UC Berkeley
Notes: Slides template credit: Josh Hug, Lisa Yan

## Slide 2: Autonomous Systems
Autonomous Systems
What are ASes?
Business Relationships
Goals of Inter-Domain Routing
Policy-Based Routing
Gao-Rexford Rules
BGP (Border Gateway Protocol)
Importing and Exporting
Aggregation and Path-Vector
Lecture 8, Spring 2026
Notes: so today it's all about
0:17
interdomain routing

## Slide 3: Intra-Domain vs. Inter-Domain Routing
Recall: The Internet is a network of networks.
We used intra-domain routing to compute routes inside each network.
Notes: 0:24
it's the network of networks that we've been talking about and so far we've used algorithms like dist vector and Link
0:31
state to compute routes within the network so our distance Vector protocol was able to find all of the routes
0:37
inside this network that's great but we haven't talked about how to do inter
0:43
domain routing and that's going to be today's Focus

## Slide 4: Intra-Domain vs. Inter-Domain Routing
Autonomous System (AS): One or more local networks, all under a single administrative control. Sometimes informally called "domains. Each AS is assigned a unique AS number (ASN).
Inter-domain topology (or AS graph): A graph of ASes, with the individual routers and hosts abstracted away. Each node is an AS.
Notes: that is finding the paths between the networks and then next time
0:54
we'll talk about how we combine in domain and in domain to think about what
1:00
the routers are actually doing but for today we're going to ignore what's going on inside of these circles and we'll
1:06
just tra this big circle as one unit and we'll think about how all of these networks find paths between each
1:14
other

## Slide 5: Brief History of Autonomous Systems
New ASNs are assigned by Internet Assigned Numbers Authority (IANA).
Number of ASes increases over time: Over 90,000 today!
ASes by country: USA has the most, followed by Brazil.
Notes: https://commons.wikimedia.org/wiki/File:Jon_Postel_(full_frame).jpg
so one question is where do the asn’s come from if you decide to create a
2:53
network you need a new autonomous system number who gives it to you
2:58
early internet it was one one guy that guy and if you wanted an autonomous
3:03
system you would call this guy up and he would give you a number and he would maintain the list of all the numbers of
3:09
course this is not sustainable especially because he passed away so instead we use an organization called
3:16
the I and if you want a new autonomous system you call up this organization and
3:22
they give you a number

## Slide 6: Types of Autonomous Systems
Stub AS: Only sends/receives packets on behalf of hosts inside the AS.
Similar to end hosts in intra-domain model.
Does not forward packets between other ASes.
Examples: Hofstra Univ, local bank.
Most ASes are this type.
Transit AS: Forwards packets on behalf of other ASes.
Similar to routers in intra-domain model.
Can still send/receive packets for hosts inside the AS.
Examples: AT&T, Verizon.
Can vary in scale (global, regional).
Note: Some modern ASes (e.g. Google, Amazon) blur the line between stub and transit.
Notes: we can classify autonomous systems into one of two types there is a stub
4:05
autonomous system and these only send and receive packets on behalf of the users inside that system so you can
4:12
think of these like the end hosts if you comparing to intra domain routing so
4:18
remember how end hosts they didn't forward packets for other people they just sent and rece received their own
4:24
packets so you can think of stub as's as doing the same thing they only send and receive their own packets for the hosts
4:31
inside of their Network and they're not responsible for forwarding packets between other as's so for example UC
4:38
Berkeley is not an internet company we do not forward packets for other people across the world our responsibility is
4:45
only to send and receive packets for our students or the people in our Network
4:50
and most as's in real life are stub as's they're not responsible for forwarding
4:56
packets and they only send and receive their own packets by contrast the other type of as is a
5:03
Transit as these do forward packets on behalf of other as's and you can think
5:08
of these kind of like the routers in the intra domain model so remember that routers were responsible for forwarding
5:15
packets between other hosts that's what a Transit as does now one difference
5:20
between the transit as and the router in the intro domain model is that Transit
5:25
asist still might have hosts inside of them that want to to send and receive packets so so not only do they forward
5:34
packets on behalf of other as's but they also send and receive packets for their
5:39
own hosts and examples of Transit as's might be companies whose responsibility
5:45
has to do with the internet so for example AT&T is an internet company they offer internet service to other people
5:51
and that's why they're a Transit as or Verizon is another example some Transit as's are very large and they span the
5:58
whole world others are limited to just a small region and that's totally fine so
6:04
for the purposes of our class we'll classify all the as's into one of these two types but do note that especially
6:11
nowadays the difference between these two is starting to get a little bit blurry and there are some as's that are
6:17
hard to classify as one of these two so for example these big tech companies like Google and Amazon it's a little bit
6:25
unclear which of these two as's they fall into you could say they're stub as
6:30
because they're sending and receiving traffic for their users but maybe they're also Transit as because they
6:36
offer internet services to other users these companies are just so big and they do so many different things that it's
6:42
just not really clear where they fall into for our class we won't worry about them we'll just think about stub as's
6:48

## Slide 7: Business Relationships
Autonomous Systems
What are ASes?
Business Relationships
Goals of Inter-Domain Routing
Policy-Based Routing
Gao-Rexford Rules
BGP (Border Gateway Protocol)
Importing and Exporting
Aggregation and Path-Vector
Lecture 8, Spring 2026
Notes: so one thing that makes autonomous systems different from everything we've seen so far maybe
7:17
everything you've seen so far in other computer science courses is the fact that they are businesses and the fact
7:23
that they are businesses means that we also have to think about how they make money this is probably not something you
7:29
had to think about when you were programming in data structures or you were thinking about how a computer worked it wasn't really about making
7:36
money it was about making the computer work and making the code do what you want but today we have to think about
7:42
these as's making money so that makes this protocol I think quite different from other ones you've seen before

## Slide 8: Business Relationships
Inter-domain topology is shaped between business relationships between ASes.
Two different ways for a pair of ASes to be related:
Customer-provider relationship:
  The customer pays the provider.
  In exchange, the provider offers to forward traffic to/from the customer.
Peering relationship:
  Peers don't pay each other.
  Peers exchange roughly equal traffic.
Notes: the way that routing works all depends on business relationships it all comes down
7:56
to money and in particular if two parents of as's or of one pair of as's
8:01
two as's are related to each other they have to have a relationship in business
8:07
terms so if two as's have a link between each other we have to specify what kind
8:12
of link it is the link could either be a customer provider link and what that
8:17
means is one of the as's is a customer the other one is a provider the customer
8:23
is paying the provider and in exchange the provider is offering service it's saying I will forward your packets for
8:30
you and I will receive packets and forward them to you but in exchange you must pay me money so some relationships
8:38
in the as graph look like that there are also relationships called puring
8:44
relationships and in this case the two as's are still connected bya link but
8:49
neither side pays the other instead they sign a contract with each other in real life as a business and the contract says
8:57
we don't have to pay each other but in exchange I'll forward you some traffic and you need to forward me roughly the
9:03
same amount of traffic and that's what aing relationship looks like in real life those contracts can get complicated
9:10
but this is how we'll simplify for this class so these are the two types of relationships that a pair of as's can
9:17
have if they have a link between them we have to specify who pays whom or if they
9:22
have a peering relationship that they don't pay each other

## Slide 9: AS Graph with Business Relationships
Representing business relationships in the AS graph:
Provider Customer
Peer Peer
The arrows do not represent direction of packets (e.g. F can send packets to C).
The AS graph forms a hierarchy (all arrows point down).
Service flows down: Higher nodes provide service to lower nodes.
Money flows up: Lower nodes pay money to higher nodes.
A
B
C
D
E
F
G
H
Notes: we can draw them in a graph the way that we're going to draw them is we're going to
9:35
draw arrows from the provider to the customer so for example this picture is
9:40
saying that c is the customer and it is paying a for service and in exchange a
9:47
is agreeing to forward packets on behalf of C so if C wants to send packets to someone else it can forward the packet
9:53
to a A can forward the packet along to its destination and if anyone has packets to send to C they can send the
10:00
packets to a and a will send them along to C so a is forwarding C's traffic but
10:06
in exchange C must pay a and the arrows always point from provider to customer I
10:12
always have a hard time remembering the direction but it's provider to customer and if we ever draw a line with two dots
10:19
on either end that would be a puring relationship so this says that A and B are peers they don't pay each other but
10:27
they can exchange traffic between between each other if they so desire now one common confusion when people see
10:34
these as business graphs for the first time is they think that the arrows represent packets being sent that is
10:41
wrong you don't want to think about packets in that way Ju Just because I draw an arrow from C to F it doesn't
10:48
mean that packets can only go in One Direction in fact packets can get sent from F to C or from C to F so the Arrow
10:56
does not say anything about where you send the packets it only says that f is the customer and C is the provider so
11:04
you got to remember when you stare at these graphs don't think about the arrows in terms of packets being sent
11:10
packets can get sent along the link in both directions just like in any other routing protocol we've seen all of these
11:17
links are bidirectional the graph is just to show the business relationships
11:23
that we were talking about you got to be careful this one always trips people up so now that we've seen this graph we
11:30

## Slide 10: AS Graph with Business Relationships
Stub ASes in this graph: F, G, H.
No outgoing edges: Not providing service to anybody.
Incoming edge(s) shows who they're buying service from.
A
B
C
D
E
F
G
H
A
B
C
D
E
F
G
H
Transit ASes in this graph: A, B, C, D, E.
Outgoing edges indicate they're providing service to somebody.
Notes: can identify which as's are the stub ones and which ones are the transit ones I think these three are the stub as's
11:37
because they have no outgoing arrows to anyone else this means they are not providing service to other people and
11:44

## Slide 11: AS Graph is Acyclic
The AS graph has no cycles.
A cycle means you're paying yourself, which doesn't make sense.
A cycle of peering relationships is okay.
A
B
C
A
B
C
Invalid
Valid
Notes: now one property of an as graph because of these business relationships is that it is a cyclic that means that
13:32
it has no Cycles if an as graph has a cycle it means that you are somehow paying yourself for service which if you
13:39
think about it doesn't really make sense here for example B would be paying a and
13:45
then a would be paying C and then C would be paying B it doesn't really make sense for money to go back to yourself
13:52
so we would say this is an invalid as graph it'd be weird if you paid someone else for service and then they paid you
13:59
for service that's kind of weird that being said cycles of peering relationships are okay so it's okay if a
14:05
B and C are all peers but you cannot have directed Cycles like this where you're paying yourself money and giving
14:13
yourself service that doesn't really work

## Slide 12: Tier 1 ASes
Tier 1 ASes: ASes at the top of the hierarchy.
A Tier 1 AS:
Has no providers (no incoming edges).
Has a peering relationship with every other Tier 1 AS.
  This helps ensure the AS graph is connected (no disconnected components).
~20 Tier 1 ASes in real life.
  USA: AT&T, Verizon
  Europe: Telecom Italia, France Telecom
  Asia: NTT Communications (Japan)
These companies usually own infrastructure spanning the whole world.
A
B
C
Notes: tier one as those are
15:19
the bosses at the very top of the hierarchy so in this picture A and B
15:24
were the Tier 1 as's here A B and C are the tier one as s's you know they're at
15:30
the top because they have no incoming edges there's nobody above them if there was someone above and another incoming
15:37
Edge they would not be tier one but because they're at the very top and there are no more edges pointing at them
15:43
they are a tier one as this means they have no providers they're not paying anyone else for service they are the
15:50
original source of the service if you're a tier one as you have to have a peering
15:56
relationship with all the other tier one as's so for example here A B and C they
16:02
must have all the pairwise peering relationships that are possible so A and
16:07
B must be Pierce B and C must be Pierce A and C must also be Pierce if there was
16:12
a fourth tier one as like d you would have to connect D to c b and a using
16:19
puring relationships for reasons that we will see soon but it's important that all the tier one as's are connected to
16:25
each other because this guarantees that the as graph is is connected if you
16:30
stare at the hierarchy it's not quite a tree because trees have a single distinct root and there is no single
16:37
distinct route here so the way that we guarantee that everything is connected is we have everyone at the top connected
16:44
to each other so there isn't one distinct roote but because everyone at the top layer is connected to each other
16:51
this helps us guarantee that the whole internet is connected as long as you can
16:56
trace your money up to a tier onea s the Tier 1 as should be connected to everyone else

## Slide 13: Properties of AS Graphs
Every non-Tier 1 AS has at least one provider (incoming edge).
Starting at any AS and walking up the graph will eventually lead to a Tier 1 AS.
A
B
C
D
E
F
G
H

## Slide 14: Goals of Inter-Domain Routing: Policy-Based Routing
Autonomous Systems
What are ASes?
Business Relationships
Goals of Inter-Domain Routing
Policy-Based Routing
Gao-Rexford Rules
BGP (Border Gateway Protocol)
Importing and Exporting
Aggregation and Path-Vector
Lecture 8, Spring 2026

## Slide 15: Goals of Inter-Domain Routing
Scalability: Routing must scale to the entire Internet.
Solution: Hierarchical IP addressing.
Privacy: ASes don't want to explicitly announce sensitive information.
I shouldn't have to tell everybody who my provider is.
Companies might not want to reveal information to rivals.
Autonomy: ASes want the freedom to choose their own policies.
Policy is usually based on business goals.
Notes: 19:5"Explicitly" - Some minor leakage is inevitable.
7
next there's a couple Challen challenges that we need to think about as we're designing this routing scheme one is
20:03
scalability so as mentioned earlier we need to make sure that this routing scales to the entire internet we saw
20:09
already that there are close to a 100,000 as's and that number is growing and in order to route to 100,000
20:17
different as's Each of which probably has tons of hosts we need to use hierarchical IP addressing like we
20:24
talked about last time and this will allow us to have a single entry that says something like everybody in Europe
20:30
is that way well that's much easier than writing out every single entry for every single host in Europe you can have a
20:37
single entry that says everybody in Europe with an IP address that starts with these bits just send it that way
20:43
and it summarizes millions of hosts in a single entry so that's something we're going to have to use in order to scale
20:50
this routing scheme up and these two properties that come next are a bit
20:55
newer they're probably things you haven't seen before but they're important now that we're considering as's as businesses in real life as a
21:04
business something you probably don't want to do is reveal all of your secrets
21:09
businesses have secrets and it's probably good to protect them so one thing that we need here that wasn't the
21:16
case in intad domain rounding is privacy the asss should not have to announce
21:21
unnecessary information to its neighbors or anyone else outside of the as so for
21:28
example an as should not have to tell everyone who it's paying for Internet service that could be private
21:34
information maybe as a company you don't want to tell people who you're paying to service your internet so you shouldn't
21:40
have to reveal that as part of this routing protocol and there's also other information we'll see in general we have
21:47
to be careful not to reveal information to other as's if it's potentially
21:53
sensitive that being said there is some leakage that we can't get away with and there is some work done to try and
22:00
reverse engineer some secret information based on the routing protocol so it's not perfect but we'll do our best to
22:08
hide sensitive information when possible even if sometimes we're not able to hide
22:13
every single thing or we leak a little bit of information by accident
22:20
little bit different is autonomy and this means that as's should be able to choose their own policies based on
22:27
business goals so each as should be able to decide what routes it likes better
22:33
and what routes it doesn't like now this is very different from something like the distance Vector protocol or the link
22:39
State protocol where everyone agreed that the goal was to minimize cost everyone agreed you agreed I agreed all
22:46
of the routers agreed that minimizing cost was the best thing to do but now that we have autonomy as's might not
22:54
like least cost maybe they want something a little bit more expensive because they prefer it for some reason
23:00
and we have to support other goals that asss might have so we need scalability
23:05
and we need these two new goals of privacy and
23:11
autonomy

## Slide 16: Policy-Based Routing
Autonomy: ASes want the freedom to choose their own policies.
Recall our routing goals:
Valid paths:
  Intra-domain definition: No loops, no dead ends.
  Inter-domain definition: Same.
Good paths:
  Intra-domain definition: Least-cost paths.
  Inter-domain definitions: Paths that respect every AS's policies.
Notes: so what does policy-based routing mean as mentioned earlier as's have to be able to choose the policies
23:18
that they like and they should be able to choose their favorite paths whatever that means for them so in intra domain
23:26
routing inside of a network we set that a valid path was one that had no loops
23:32
and no dead ends so that's going to be the same every business out there does not want Loops does not want dead ends
23:39
that we can be pretty sure of because if you have a loop you're not sending the packet so we still agree that everyone
23:45
doesn't want a loop everyone doesn't want the dead end that's okay now the difference is what makes the path good
23:52
in in domain everyone agreed it was least cost in interdomain routing we are
23:58
looking in instead for paths that respect every as's preference so if you prefer something and I prefer something
24:04
we should use that path even if it's not the least cost path and we'll also see
24:10
cases where the preferences actually are in conflict and what to do in those cases but in summary we have to respect
24:17
every as's preferences even if those preferences don't lead to least cost paths and that's going to create an
24:24
extra challenge for us

## Slide 17: Policy-Based Routing
Autonomy: ASes want the freedom to choose their own policies.
Examples of policies:
Define how I will handle traffic from others:
  I don't want to carry AS#2046's traffic through my network.
Defines how others should handle my traffic:
  I prefer if my traffic was carried by AS#10 instead of AS#4.
  Don't send my traffic through AS#54 unless absolutely necessary.
We have to find paths that respect every AS's policies.
Notes: so what is a policy it turns out just More creative policies:
  I prefer AS#12 on weekdays, and AS#13 on weekends.
24:31
about anything can be a policy for an as and the protocol will Design supports
24:36
just about any policy you can think of so here are a bunch of examples some policies Define you carrying traffic so
24:44
as a Transit as you have to forward other people's traffic and you can Define policies like I really don't like
24:50
as number 2046 I just don't like them so I refuse to forward their traffic sorry if they
24:57
send traffic I refuse to forward it you cannot use me as a route if the traffic is coming from
25:04
as246 so that's an example of a policy that has to do with forwarding traffic
25:10
there can also be policies that Define how your traffic is handled so this is not you forwarding other people's
25:16
traffic this is you sending and receiving your own traffic you can say when I send packets if you have a choice
25:23
between as 10 and 14 please use 10 because I like 10 better for what reason
25:29
not our problem as's can choose their own preferences or you can say please don't use 54 unless there are no other
25:36
Alternatives then use 54 and there's all sorts of different exotic policies you can come up with you can invent any
25:42
policy you like you could say on weekdays use 12 on weekends use 13 you can do whatever you want but ultimately
25:50
our protocol has to respect whatever policy these as's could possibly think of and that's going to make routing a
25:56
little bit more challenging

## Slide 18: Gao-Rexford Rules
Autonomous Systems
What are ASes?
Business Relationships
Goals of Inter-Domain Routing
Policy-Based Routing
Gao-Rexford Rules
BGP (Border Gateway Protocol)
Importing and Exporting
Aggregation and Path-Vector
Lecture 8, Spring 2026
Notes: most as's follow a pretty
26:44
standard set of rules that we'll call the ga Rexford rules it's not guaranteed
26:49
but most of them do this

## Slide 19: Gao-Rexford Rules: Choosing Routes
Most ASes follow standard conventions: Gao-Rexford Rules.
These conventions reflect real-world business practices:
Making money is good.
Don't do work for free.
Distance-vector protocol: Prefer the shortest path.
Gao-Rexford rules: Prefer the most profitable path.
Best: Path where the next hop is a customer. (They pay me.)
Less good: Path where the next hop is a peer. (I don't make money.)
Worst: Path where the next hop is a provider. (I have to pay.)
Reflects real-world business practice: Making money is good.
Notes: so in theory you can do whatever you want you like 12
26:55
on weekdays 13 on weekends that's great but in real life there are some standard conventions that most people follow and
27:02
they're based on two properties that I think almost every business can agree on so no matter what business you're in I
27:07
think every business in the world could agree that making money is good and I also think that every business in the
27:14
world could agree you should not do work for free you should get paid if you're doing work so that's what these two

## Slide 20: Gao-Rexford Rules: Choosing Routes
Gao-Rexford rules: If I'm offered multiple paths, pick the most profitable one.
S
A (Provider)
B (Peer)
C (Customer)
I prefer the path via C, because C will pay me to forward packets.
D
Notes: 29:07
look like here's you your s and you receive advertisements from three different as's a sends you an
29:15
advertisement saying I can reach autonomous system D and B also sends an advertisement saying I can also reach D
29:22
and C also sends an advertisement saying I can reach D so you receive three different options for how to reach D and
29:31
as the goxer rulle say it doesn't matter what the cost of these links are you decide based on money first so I look at
29:38
this well if I use this link I have to pay for it I don't want to do that if I use this link I don't make any money but
29:45
if I use this link I send the packet to a customer who pays me I like that so I
29:51
will choose this advertisement and accept to forward packets via C so this

## Slide 21: Gao-Rexford Rules: Choosing Routes
Gao-Rexford rules: If I'm offered multiple paths, pick the most profitable one.
S
A (Provider)
B (Peer)
C
I prefer the path via B. I don't make money, but at least I don't have to pay.
D
Notes: 30:02
if that link goes down suddenly this link doesn't exist anymore you no longer have a customer so you should instead
30:08
use the pier because that's free and this one costs you money and it's the worst so we go customer first then peer
30:15
then provider

## Slide 22: Gao-Rexford Rules: Participating in Routes
Distance-vector protocol: I am okay with participating in any route.
"Participating": Being one of the routers forwarding packets along a path.
Gao-Rexford rules: I will only participate in routes where I get paid.
Reflects real-world business relationship: Don't do work for free.
How to check if I get paid:
Look at my two neighbors along the path.
I get paid if and only if one of my neighbors is a customer.
Notes: so in distance Vector protocols everyone participated in
31:30
everything when you receive an advertisement you forward it to everyone because you're happy to be on any path
31:37
if you're the shortest path for someone else that's great you should join and be part of the path so in distance Vector
31:44
protocols there was no restriction on participating in routes if you were a router you could be on any route however
31:52
now that money is a concern you're no longer going to agree to participate in any route that's out there in particular
31:59
you only participate in routes if you make money and this reflects the other goal we talked about which is to not do
32:06
work for free if you want to make money you don't want to do work for free so do not participate in routes where you are
32:13
being forced to work and you're not getting paid now how do you check if you get paid you look at the route that you
32:20
are along so look to your left look to your right look at your two Neighbors on the path and check if one of them is
32:26
paying you if one of them as a customer you're getting paid this is a path you're willing to participate in but if
32:32
you look to your left and you look to your right and neither of them is a customer you are not getting paid you're
32:38
either doing work for free or even worse you're paying to do work we don't want to do that so we will not participate in
32:45
this route and that means that we will not send an advertisement claiming that we can be part of this route

## Slide 23: Gao-Rexford Rules: Participating in Routes
I get paid and participate if and only if at least one of my neighbors is a customer.
B
C (Customer)
A (Customer)
Packet forwarded via A → B → C
A and C are both paying me. I'm gonna be rich!!
✓
B agrees to participate
Notes: so let's
32:52
see what this looks like in practice there's a lot of different cases we'll just run through them all one by one one
32:58
so here's the first case your B you look to your left it's a customer you look to your right it's a customer it's a great
33:05
day you're going to be paid from both sides this is amazing you are definitely going to participate in this path
33:12
because at least one of your neighbors is a customer now one important thing to note again is that this is an as graph
33:19
these arrows don't represent the packets being sent the packets are being forwarded from A to B to C according to
33:27
the slide they could also be forwarded from C to B to a the arrows have nothing to do with
33:32
the packets being sent they have to do with money flowing from A to B so in
33:38
this case you're making money on both sides you will participate in this route

## Slide 24: Gao-Rexford Rules: Participating in Routes
I get paid and participate if and only if at least one of my neighbors is a customer.
B
C (Customer)
A (Peer)
Packet forwarded via A → B → C
A is not paying me, but at least C is paying me.
✓
B agrees to participate
Notes: 33:44
what about this route you'll participate as well because you look to your left you're not making money but you look to
33:49
your right and you are making money so this is a route that you will participate in

## Slide 25: Gao-Rexford Rules: Participating in Routes
I get paid and participate if and only if at least one of my neighbors is a customer.
In this scenario: I get paid by C, but I have to pay A.
I should still participate because this is how I offer service to my customers.
B
C (Customer)
A (Provider)
Packet forwarded via A → B → C
I'm getting paid by C. I might have to send some of it to A but that's okay.
✓
B agrees to participate
Notes: now this one's kind of
33:56
strange you look to your right there's a customer that will pay you and you look to your left and there's a provider that
34:02
you have to pay so at first glance you might say I don't know if I want to participate in this because I'm making
34:09
money but then I'm paying some of it to a but you should still participate in this and the reason why is because if
34:16
you don't participate in this how do you give service to C remember that c is
34:21
paying you for service and if you refuse routes like this you are refusing to
34:27
send packets up the hierarchy to the tier one as's to reach other destinations so you could reject these
34:35
but you'd be a very bad provider because you are not accepting routes that offer connectivity to far away places and you
34:42
just can't reach a bunch of the internet so this route is important to accept
34:47
because this is how you offer service to your customers It Is by accepting routes toward your providers who then send the
34:54
packet to other far away places so at first glance you might be tempted to not participate but you have to participate
35:01
to give your customer service

## Slide 26: Gao-Rexford Rules: Participating in Routes
I get paid and participate if and only if at least one of my neighbors is a customer.
Peers do not provide transit between other peers.
B
C (Peer)
A (Peer)
Nobody is paying me to do this. I won't participate.
✗
B refuses to participate
Packet forwarded via A → B → C
Notes: 35:33
these now let's look at the cases where we don't accept here's a case where you don't accept to your left is a peer to
35:40
your right is a pier there no good nobody is sending you money there is no point in participating in this path and
35:47
what that means is that peers don't provide Transit between other peers so a packet will not hop across a big chain
35:54
of peers because all of the peers along the chain will will refuse to participate they'll say I'm not making
36:00
money I will not do this for you for free so that's a property has a
36:05
consequence of this picture peers do not forward packets between other peers
36:10
because they don't make money here's another case where you don't make money you look to your right it's a provider
36:16
that you have to pay you look to your that was your left you look to your right it's a peer and they're not
36:22
sending you any money either so once again you don't participate nobody is making you money it's no good

## Slide 27: Gao-Rexford Rules: Participating in Routes
I get paid and participate if and only if at least one of my neighbors is a customer.
If one of my neighbors is a peer, the other neighbor must be a customer.
An AS only carries traffic to/from its own customers over a peering link.
B
C (Peer)
A (Provider)
Packet forwarded via A → B → C
I have to pay A, and I am not paid by C. No thanks.
✗
B refuses to participate
Notes: what this means is that if you receive packets or send packets along appearing link what can you conclude about this
36:36
other side it must be a customer so something useful to conclude here is if you receive a packet from aing link that
36:44
means that one of the sides is a peer the other side must be a customer because someone has to pay you money and
36:51
the peer isn't paying you so this other side must be a customer to pay you that's what these words say it's a small
36:57
consequence of the way that we've designed this

## Slide 28: Gao-Rexford Rules: Participating in Routes
I get paid and participate if and only if at least one of my neighbors is a customer.
Routes are valley-free.
Travelling downhill, and turning around and going back uphill is not allowed.
B
C (Provider)
A (Provider)
Packet forwarded via A → B → C
I have to pay both A and C. Only a fool would participate.
✗
B refuses to participate
Notes: the final one is where
37:03
both sides are providers now this is terrible because you have to pay the left side to participate and you have to
37:08
pay the right side to participate you would simply never do this so B will not
37:13
participate in this path and a consequence of this is that routes are valy free that will be defined more
37:20
concretely later but intuitively what that means is if you draw paths through the graph the paths will never dip down
37:28
and then turn around and go back up because if your path ever goes down and then back up in the hierarchy you're
37:34
forcing someone to pay both sides and they would never do so so this is another path that no one would
37:40
participate in because it doesn't make them
37:46
money

## Slide 29: Policy-Based Routing Example
D and E want to exchange traffic along this path.
Will the transit ASes (A, B, C) agree to participate?
A
B
C
D
E

## Slide 30: Policy-Based Routing Example
D and E want to exchange traffic along this path.
Will the transit ASes (A, B, C) agree to participate?
Yes, each transit AS has an adjacent customer.
A
B
C
D
E
I get paid by D.
I paý A.
I get paid by B and C.
I get paid by E.
I paý A.
Notes: 39:39
B looks at both of its neighbors and says yes I get paid by one of them namely D so I will participate C also
39:47
says yes I get paid by E so I will participate and a it's lucky day it
39:52
won't get paid by both sides so it will also participate therefore this is a valid route everyone will
40:00
participate

## Slide 31: Policy-Based Routing Example
Suppose we add a new link (B and C establish a peering relationship).
Will the transit ASes (B, C) agree to participate in this new route?
A
B
C
D
E
Notes: [changelog] 3/3/25: swapped orders for slides 39 and 40

## Slide 32: Policy-Based Routing Example
Suppose we add a new link (B and C establish a peering relationship).
Will the transit ASes (B, C) agree to participate in this new route?
Yes, each transit AS has an adjacent customer.
A
B
C
D
E
I get paid by D.
I get paid by E.

## Slide 33: Policy-Based Routing Example
With the new link, B and C save money (they don't have to pay A anymore).
Trade-off: B and C have to pay to build that link.
A
B
C
D
E
A
B
C
D
E

## Slide 34: Properties of Routes with Gao-Rexford Rules
Routes are single-peaked.
We first climb 0 or more uphill links.
Then, we reach a peak, and traverse 0 or 1 peering links.
Then, we go strictly downhill all the way to the destination.
A
B
C
D
F
E
Packet forwarded via A → B → C → D → E → F
Notes: 42:09
okay so if you put all these properties together there is a useful property you can derive which is that all of the
42:16
routes have a single Peak this is a consequence of all the things we've talked about previously and if you take
42:22
everything we've said about participating in routes and you summarize it it would look something like this well it's not a new property
42:29
it's a derivation of things we've already talked about and every path that you could possibly draw in the as
42:35
hierarchy that everyone agrees to participate in they will all take a form like this you'll start somewhere and
42:43
you'll first start climbing up so there's zero or more uphill links so you start at a and you climb up going from
42:50
customers to Providers and that also means money is Flowing upwards and then
42:56
eventually once you get to the peak you can Traverse zero peering links that's okay or you can Traverse a single
43:03
peering link that's it why can you not Traverse multiple peering links because if you're staying up here and there a
43:09
long Plateau a chain of peers well then all the intermediate peers would refuse to participate so that's not possible

## Slide 35: Proving Reachability and Convergence with Gao-Rexford
If all of these are true:
Starting from any AS and moving up the hierarchy will lead to a Tier 1 AS.
The AS graph has no cycles.
All ASes follow the Gao-Rexford rules.
Then we can guarantee these two properties:
Reachability: Any two ASes in the graph can communicate.
Convergence: All ASes agree on paths.
These properties hold in steady-state.
Steady-state: Network topology and policies remain unchanged.
If something changes, it might take some time for ASes to reconverge.
If ASes pick arbitrary policies (not following Gao-Rexford), we can't guarantee these properties.
Notes: well there's a useful proof that G and
47:38
Rexford came up with so what they noticed is that all of the as's tend to follow these set of rules that have to
47:45
do with making money and they were able to construct a proof based on these as
47:51
properties so here are the assumptions and the proof we say if all three of these statements are true then we get
47:57
these two nice properties so what are the statements the prerequisites for this proof are as follows number one
48:05
starting from any as and climbing up the hierarchy must lead to a tier one as
48:10
that's something we talked about earlier it is true in the modern internet now you could build some weird as graph that
48:16
doesn't obey that but in the modern as graph on the internet it is true that wherever you start if you climb up you
48:23
end up at a tier one as that's fact number one fact number two the as graph has no Cycles again this is true in the
48:30
modern internet you could certainly create a weird alternate universe internet where this is not true but in
48:36
the modern internet the as graph has no Cycles you cannot pay yourself assumption number three is that everyone
48:43
follows the rules that we just talked about you only participate in paths if you get paid and when you have a choice
48:49
of paths you choose the most profitable one so we need all three of these things to be true and if they are true gow and
48:56
Rexford wrote a whole paper look up their names and you'll find it and the paper says if these three things are
49:01
true you get these two nice properties one property is that the entire as graph
49:07
is connected any two as's in the graph can communicate and in particular they
49:13
can communicate on a path that everyone agrees to participate in so you get something called reachability very
49:20
roughly intuitively this is not the proof but you can try to connect this to the single Peak path that we talked
49:27
about if you build the as hierarchy the way that we've been talking about and everyone follows the gal Rexford rules
49:33
you can always draw a graph like this in the as graph between any pair of as's
49:39
doesn't matter where a and F are in the as graph you can always draw a path that
49:44
climbs up to the Tier 1 as hops over to a different Tier 1 as and goes back down
49:50
to the destination so you get a property called reachability any two as's can talk to each other along a path that
49:58
makes everybody happy that's nice this is why the internet actually works and we don't say you can't reach Asia it's
50:05
because of this property right here and the other nice property is Convergence that means all the asss agree on the
50:11
paths so if you think of them as having forwarding tables which is not something we've talked about yet but if they had
50:17
imaginary forwarding tables those forwarding tables would be consistent so everyone agrees on the path that is
50:24
being taken and that's something we'll dive into more next time but that's the proof it says if the as graph is built
50:30
the way we talked about it don't do weird things like have cycles and if everyone follows the rules then we get
50:37
reachability and convergence now one minor note about this proof is it only
50:42
guarantees these properties in steady state so if the network topology and the policy stay the same forever you do get
50:50
these properties but if something changes like a new as appears it might take some time for everyone to recp
50:56
compute the paths and reconverge on something but eventually it will converge as long as everyone continues
51:03
to follow these rules and this also means that if you break any of these three assumptions you
51:09
lose this proof so if any as goes out there and says actually I love losing
51:14
money well suddenly you can't guarantee these properties because they are not following the rules

## Slide 36: Summary: Autonomous Systems, Policy-Based Routing
AS topology reflects business relationships between ASes.
Business relationships impact what routes are chosen, and what routes are acceptable.
Inter-domain routing design must support:
  Scalability
  Autonomy (support policy choices)
  Privacy
Notes: so to summarize the first part of today we talked about autonomous systems that reflect business relationships
51:40
between as's and we said that those business relationships impact what route you choose that is when you receive
51:48
advertisements which one do you like and also what routes are acceptable which means when you're asked to participate
51:55
in a route do you agree or not and we saw that scalability autonomy and privacy were important
52:05
considerations

## Slide 37: BGP: Importing and Exporting
Autonomous Systems
What are ASes?
Business Relationships
Goals of Inter-Domain Routing
Policy-Based Routing
Gao-Rexford Rules
BGP (Border Gateway Protocol)
Importing and Exporting
Aggregation and Path-Vector
Lecture 8, Spring 2026

## Slide 38: A Brief History of BGP
Least-cost routing algorithms are based on old ideas.
  Shortest-path algorithms predate the Internet: Dijkstra's (1956), Bellman-Ford (1958).
Autonomous systems grew out of necessity.
  Internet control transferred from the US government to various companies.
  The Internet grew too big for least-cost routing algorithms.
BGP is the one and only inter-domain routing protocol.
  Remember: Everyone must agree on the same one.
Notes: Autonomous systems were a new idea to computer science.
  No precedent for "find paths according to business policy."
  Ideas behind BGP were developed on the fly (1989–1995).
It's not perfect, but it's stood the test of time.

## Slide 39: Starting Point: Distance-Vector or Link-State?
Distance-vector or link-state: Which would be a better starting point?
Link-state is a bad choice.
No privacy: I have to reveal my policies to everybody else.
No autonomy: Everyone has to agree on a metric (e.g. least-cost) for consistency.
Distance-vector is a better choice.
BGP extends distance-vector to accommodate policy.
BGP and distance-vector are similar:
  Advertisements are specific to one destination (i.e. one prefix).
  No global sharing of network topology.
  Iterative and distributed convergence on paths.

## Slide 40: Importing and Exporting Paths
New terminology for old ideas:
Advertise (export) the best route to one or more of your neighbors.
Select (import) the best route you hear about.
Use policy to decide which route to import, and who to export routes to.

## Slide 41: Importing Paths
Gao-Rexford import policy: Pick the route advertised by customer > peer > provider.
Contrast with distance-vector: Pick the shortest route.
Import decision determines where an AS sends its outbound traffic.
Why? Because this involves choosing a route.
S
A (Provider)
B (Peer)
C (Customer)
"I can reach D."
"I can reach D."
"I can reach D."
I prefer the path via C, because C will pay me to forward packets.
Packets for D get forwarded this way.
D
Notes: Changelog:
[3/5/25] changed “customer > provider > peer” to “customer > peer > provider”
if you receive multiple advertisements which one do you pick you pick the one from the customer
1:01:22
if there is one otherwise pick the one from the peer otherwise pick the one from the provider it's something you've
1:01:28
already seen and if you want to compare it to distance Vector distance Vector said pick the shortest one we now say
1:01:35
pick the one that makes you the most money this is an import decision that's just a fancy word for accepting
1:01:42
advertisements so this is something you've already seen and yeah you've
1:01:47
already seen it now something to note by the way is that the import decision determines how you forward packets that
1:01:55
might sound a little bit confusing I think it's less confusing than it sounds it basically says when you accept an
1:02:01
advertisement that determines where you're forwarding packets that makes sense if you receive advertisements from
1:02:06
a b and c and you choose C that is you import C that means you're forwarding
1:02:13
packets to see because you chose their advertisement now what about exporting
1:02:19
this one's a little bit trickier so this is where we have to think about whether we participate in a route because we
1:02:26
should only export a route and tell all of our neighbors if the route makes us
1:02:31
money and we agree to participate so now we're going to link up the idea of participation into an actual policy

## Slide 42: Exporting Paths
Gao-Rexford export policy: I only export a route if participating in it makes me money.
Contrast with distance-vector: Advertise a route to all neighbors.
Export decision determines what traffic an AS will carry.
Why? Advertising a route means I'm letting others forward traffic through me.
S
A (Provider)
B (Peer)
C (Customer)
D
Packets for D get forwarded this way.
I have a route to D, but should I tell A, B, C about it?
Notes: okay so the
1:02:45
difference here is that in distance Vector protocols everyone participated in anything nobody said I refuse to
1:02:51
participate everyone agreed to participate in any path and that was reflected in the fact that you advertise
1:02:58
routes to all of your neighbors you tell everyone anyone can send packets to me I
1:03:04
will participate in whatever route you like if you want to send packets that's great I participate if you want to send
1:03:09
packets that's great I will also participate the distance Vector was very nice it let everyone participate by
1:03:16
contrast in bgp you will not let everyone participate you will only let
1:03:21
people participate if it makes you money

## Slide 43: Exporting Paths From Customers
Gao-Rexford export policy: I only export a route if participating in it makes me money.
If I receive a route from a customer, export it to everybody.
The resulting route will be profitable: There's a customer on one end.
S
A (Provider)
B (Peer)
C (Customer)
D (Customer)
All three of these routes make me money.
Packets for D get forwarded this way.

## Slide 44: Exporting Paths From Customers
Gao-Rexford export policy: I only export a route if participating in it makes me money.
If I receive a route from a customer, export it to everybody.
The resulting route will be profitable: There's a customer on one end.
S
A (Provider)
B (Peer)
C (Customer)
D (Customer)
I'll tell everyone about this route.
"I can reach D."
"I can reach D."
"I can reach D."
Packets for D get forwarded this way.

## Slide 45: Exporting Paths From Peers
Gao-Rexford export policy: I only export a route if participating in it makes me money.
If I receive a route from a peer, only export it to a customer.
The peer isn't paying, so I only profit if the person on the other end is a customer.
S
A (Provider)
B (Peer)
C (Customer)
D (Peer)
Only the green route makes me money.
Packets for D get forwarded this way.

## Slide 46: Exporting Paths From Peers
Gao-Rexford export policy: I only export a route if participating in it makes me money.
If I receive a route from a peer, only export it to a customer.
The peer isn't paying, so I only profit if the person on the other end is a customer.
S
A (Provider)
B (Peer)
C (Customer)
D (Peer)
I'll only tell C about this route.
"I can reach D."
Packets for D get forwarded this way.

## Slide 47: Exporting Paths From Providers
Gao-Rexford export policy: I only export a route if participating in it makes me money.
If I receive a route from a provider, only export it to a customer.
I pay the provider, so I only profit if the person on the other end is a customer.
S
A (Provider)
B (Peer)
C (Customer)
D (Provider)
Only the green route makes me money.
Packets for D get forwarded this way.

## Slide 48: Exporting Paths From Providers
Gao-Rexford export policy: I only export a route if participating in it makes me money.
If I receive a route from a provider, only export it to a customer.
I pay the provider, so I only profit if the person on the other end is a customer.
S
A (Provider)
B (Peer)
C (Customer)
D (Provider)
I'll only tell C about this route.
"I can reach D."
Packets for D get forwarded this way.

## Slide 49: Exporting Paths From Providers
Gao-Rexford export policy: I only export a route if participating in it makes me money.
Key idea: The route needs a customer on at least one side.
If a customer advertised the route, we already have a customer on one side. The other side can be anybody.
If a peer/provider advertised the route, we're still missing a customer. The other side must be a customer.
Route advertised by... | Export route to...
Customer | Everyone (providers, peers, customers)
Peer | Customers only
Provider | Customers only

## Slide 50: BGP: Aggregation and Path-Vector
Autonomous Systems
What are ASes?
Business Relationships
Goals of Inter-Domain Routing
Policy-Based Routing
Gao-Rexford Rules
BGP (Border Gateway Protocol)
Importing and Exporting
Aggregation and Path-Vector
Lecture 8, Spring 2026
Notes: now there are two more changes we need and we will have arrived at a pretty nice bgp protocol so once we
1:10:10
fix these two things we're all done for today

## Slide 51: Modifications from Distance-Vector to BGP
Changes we've made so far:
Import paths based on policy (e.g. prefer customer > peer > provider), instead of based on least-cost.
Export paths based on policy (e.g. only advertise profitable routes), instead of advertising all routes.
We need to make two more changes:
Aggregating prefixes for scalability.
Changing from distance-vector to path-vector.

## Slide 52: Modification #1: Aggregating Prefixes
Recall: For scalability, each forwarding table entry maps a range of IPs to a next hop.
Each AS is addressed by a prefix (all machines inside the AS share the same prefix).
BGP can aggregate multiple entries into one, combining ranges into one larger range.
Destination Prefix | Next hop
12.1.0.0/16 | Physical port #1
12.2.0.0/16 | Physical port #1
12.3.0.0/16 | Physical port #1
Destination Prefix | Next hop
12.0.0.0/8 | Physical port #1
Notes: so remember that things have
1:10:52
to be scalable this has to support the entire internet and reachability to
1:10:57
thousands and thousands of as's and so you cannot have a table with a 100,000
1:11:03
entries it's just too big to maintain and store so instead all of the
1:11:08
forwarding tables are going to be a they can be aggregated so what that means is
1:11:15
if you ever have a lot of prefixes with the same next toop you should aggregate them all into a longer prefix right here
1:11:23

## Slide 53: Modification #1: Aggregating Prefixes
Recall: Aggregation scales because addresses are hierarchical.
Multi-homing: An AS having multiple providers.
Multi-homing limits aggregation.
AT&T
4.0.0.0/8
Verizon
UCLA
4.78.0.0/16
UCB
4.24.0.0/16
UCSF
4.91.0.0/16
4.0.0.0/8 is this way.
4.24.0.0/16 is this way.

## Slide 54: Modification #2: Distance-Vector → Path-Vector
Problems with distance-vector-based BGP:
There might be loops.
  Least-cost routing guaranteed no loops.
  Switching to policy-based routing caused us to lose that guarantee.
We can support Gao-Rexford rules, but not arbitrary policies.
  Suppose my policy is: "My traffic should never pass through AS#2019.
  I get an announcement: "I am AS#20 and I can reach D with cost 10.
  How do I know if this route satisfies my policy?
B
C
B's policy: "I like sending packets via C."
C's policy: "I like sending packets via B."

## Slide 55: Modification #2: Distance-Vector → Path-Vector
Solution: Change from distance-vector to path-vector.
Instead of advertising distance to destination, advertise the whole AS path.
Example: "I am A, and I have a path to D via A → B → C → D."
This solves both of our problems.
Loop detection: Check if adding myself to the path creates a loop.
  If I'm C, adding myself to the path creates a cycle: C → A → B → C → D.
  If the path has a cycle (after adding myself), reject the advertisement.
Arbitrary policies: The entire path is available for checking against policy.
  If my policy is "don't send my packets through B," I can check the path and reject the advertisement.

## Slide 56: Stub ASes Use Default Routes
If a stub AS is connected to a single provider, it doesn't need to run BGP.
The stub AS default-routes everything to the provider.
The provider advertises that they can reach the stub AS's prefix.
  The provider is advertising on behalf of the stub.
Provider
Stub
Forwarding table:
Send everything to provider.
Forwarding table:
Send stub packets ↓ this way ↓

## Slide 57: Summary: Inter-Domain Routing
In the AS graph, edges reflect physical connections and business relationships.
  Customers pay providers.
  Peres don't pay each other.
Paths are selected based on policy.
Policy (e.g. Gao-Rexford rules) reflects business goals.
  Making money is good.
  Don't do work for free.
  Good stuff (reachability, converge) happens if you follow Gao-Rexford rules.
BGP extends distance-vector to implement inter-domain routing.
  Destinations are IP prefixes that can be aggregated.
  Each AS advertises its path to a prefix.
  Policy dictates which paths an AS selects (import policy), and which paths it advertises (export policy).